## Slide 1
1. Whether server side certificate-based TLS authentication is mandatory, or optional?
UE’s requirements:
the implemented TLS implicitly support this feature.
No requirement to retrieve its own certification and private key.
UE needs to be in possession of the root certification used for server-side certificate verification.
ECS/EES’s requirements:
With certificate and private key to be configured. It is the basic requirements of the server.
YES？
NO？
2. Whether the GSPI verification is required? If needed, which mechanism is agreeable?
YES？
if yes, AKMA and UE ID API?
NO？
Discussion 1: Conclusion on KI#2.1

## Slide 2
Discussion 2: Conclusion on KI#2.2
Support for selected/preferred Authentication method information in the ECS/EES configuration information + Authentication method negotiation using TLS 1.3 (All Conclusions 1, 1A, 1B, 2, 2A & 2B in draft_S3-230334-r1)
Support for selected/preferred Authentication method information in the ECS/EES configuration information (Conclusions 1, 1A & 1B in draft_S3-230334-r1)
Authentication method negotiation using TLS 1.3 without optimization (negotiation every time) (Conclusion 2 only in draft_S3-230334-r1)
Authentication method negotiation using TLS 1.3 with optimization (Conclusions 1, 2, 2A & 2B in draft_S3-230334-r1)
1) The UE determines the authentication method based on the information in the ECS/EES configuration information, if information on selected authentication method is present in the ECS/EES configuration information.
1A) The selected authentication method in the ECS configuration information can be provided by the core network as detailed in solution#3 and solution#6.
1B) The selected authentication method in the EES configuration information can be provided by the ECS as detailed in solution#4.
2) If no information on selected authentication method is present in the ECS/EES configuration information, then the UE reuses TLS 1.3 to negotiate AKMA or GBA or any other methods to be used between the EEC and ECS/EES as detailed in solution #22.
2A) Once an authentication method is selected using TLS 1.3, the UE stores the selected algorithm in the ECS/EES configuration information.
2B) UE is aware of security capability of the HN. Only the details of the HN supported methods are included in the ClientHello.