3GPP TSG-T1 Meeting #10 	Tdoc T1-010106

Copenhagen, Denmark, 8-9 February, 2001

3GPP TSG-T1/SIG Meeting #15 	T1S-010019

# Copenhagen, Denmark, 5-7 February 2001

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 34.123-1 | CR | CR-Num | ( rev |  | ( Current version: | 3.2.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE | X | Radio Access Network |  | Core Network |  |
| Title: ( | Updates to clause 8 of TS 34.123-1 version 3.2.0 |
| Source: ( | Matsushita Communication Industries (MCI) |
| Work item code: ( |  |  | Date: ( | 5 February 2001 |
| Category: ( | F |  | Release: ( | R99 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | To update RRC test cases for terminal conformance testing, so as to be compatible with the latest version of RRC core specification (TS 25.331 version 3.5.0) |
| Summary of change: ( | Following a proposed change (by Ericsson) to the default RF settings for multiple cell environment specified in TS 34.108 clause 6.1, tables are added into “test procedures” sub-clauses of measurement test cases to clearly state the downlink power of each cell at various stages of test execution. As such, the “method of test” and “test requirements” clauses found in measurement test cases are revised. This CR provides an update to the existing RRC test cases found in clause 8 of TS 34.123-1 version 3.2.0, in accordance to the following CRs to RRC core specification (TS 25.331 version 3.4.1) approved during RAN2 #16 and RAN2#17 meetings. CR-544r1: IE “CFN-SFN observed time difference” in IE “Cell measured results” is renamed to “Cell synchronisation information”, while the same IE in IE “Cell reporting quantities” is renamed to “Cell synchronisation information reporting indicator”. At the same time, all IEs in IE “Cell reporting quantities” are appended with “reporting indicator” to explicitly show that these are flags for reporting quantities, rather than the reported quantities themselves. CR-545r1: Sub-IEs in IE “Downlink information common for all radio links” are revised. IE “Timing Indication” is mandatory and IE “CFN-targetSFN frame offset” is absent if IE “Timing Indication” is set to “Maintain”. CR-548r1: Establishment cause and paging cause are revised. The enumeration of Paging cause is removed. The expression as “PS data call” or “CS data call” are revised. Clause 8.1.2.5, 8.1.2.7. Paging cause for SMS is revised as “Low Priority Signalling”. CR-549: A possible deadlock can occur when all cells in the active set are forbidden to affect the reporting range. It was decided in RAN2 that the UE shall continue to update the reporting range in this case. This scenario was not previously considered in TS 34.123-1. A new test case is added to check for the UE’s conformance in this aspect. Clause 8.4.1.14 is added. CR-573r1: “Flow id” concept is removed. Message routing will be performed using the CN domain identity. The content of clause 8.1.9 Signaling Connection Release Request is revised. UPLINK DIRECT TRANSFER and INITIAL DIRECT TRANSFER messages have been revised. SIGNALLING CONNECTION RELEASE REQUEST message is moved from clause 9 in TS34.108 to clause 8 in TS34.123-1. CR-587r2: A series of changes are carried out in accordance to the modifications introduced in CR-587r1. They are listed below: IE “Measurement identity number” in MEASUREMENT CONTROL and MEASUREMENT REPORT messages is renamed to “Measurement identity” in all specific message contents of clause 8.4.X. The MEASUREMENT CONTROL FAILURE messages in clauses 8.4.1.9 and 8.4.1.10 shall have identical values for IE “RRC transaction identifier”, as that found in the respective MEASUREMENT CONTROL messages. IE “Measured Results on RACH” is added as an optional IE to MEASUREMENT REPORT messages. The purpose of this addition is to allow the UE to append neighbouring cell measurements to uplink RACH messages, in the case of traffic volume measurement reporting in CELL_FACH state. Since traffic volume measurements are currently not being tested, this optional IE is set to “Not Present” in all MEASUREMENT REPORT messages. The name of IE “Cell selection and re-selection info for SIB 11/12” is incorrect. It is corrected to “Cell selection and re-selection info”. IE “TGCFN” is added as a mandatory present IE into IEs “DPCH Compressed Mode Info” and “DPCH Compressed Mode Status Info”. All affected messages in the specific message content sub-clauses are updated to reflect this addition. IE “FACH measurement occasion info” has been re-structured. The corresponding IEs found in SIB type 11 or 12 in the specific message contents sub-clauses are updated. Both “Inter-frequency cell info list” and “Intra-frequency cell info list” IEs are changed to allow the possibility of removing all previously stored inter-frequency cells. The affected messages containing these IEs in the specific message content sub-clauses are updated. It is proposed in RAN2 that event-triggered periodic reporting be disallowed for inter-frequency type measurements. Therefore, IEs “Amount of reporting” and “Reporting interval” are removed from IE “Inter-frequency reporting criteria”. MEASUREMENT CONTROL messages containing these IEs are updated. IE “Inter-system measurement” and its sub-IEs found in specific message contents of clause 8.4.1.9.4 are revised. All IEs with name containing the phrase “inter-system …” are renamed to “inter-RAT …” In IE “Intra-frequency measurement reporting criteria”, a new trigger condition (triggering condition 2) is defined on top of the existing condition (triggering condition 1). Affect messages are revised. It was decided in RAN2 that if “Measurement validity” IE is present in a message, the associated measurement task should be resumed in the state specified in “UE state” IE. Otherwise, if “Measurement validity” IE is absent in the message, the UE shall deleted the associated measurement task. Hence the sub-IE “resume/release” found in “Measurement validity” IE is no longer needed and deleted from all messages. IE “Reporting cell status” is rephrased and modified to include detected set. Affected messages containing this IE are revised. CR-595r4: This CR states example of state-transition with RB control. According to this CR, two new test cases, RB set up from CELL_DCH to CELL_PCH and RB setup from CELL_DCH to URA_PCH are introduced. Clause 8.2.2.19 and 8.2.2.20 are added. Physical Channel Reconfiguration from CELL_FACH to CELL_PCH (clause 8.2.6.21), Physical Channel Reconfiguration from CELL_FACH to URA_PCH (clause 8.2.6.22), Transport Channel Reconfiguration from CELL_FACH to CELL_PCH (clause 8.2.4.22), Transport Channel Reconfiguration from CELL_FACH to URA_PCH (clause 8.2.4.23) are removed. CR-596r1: IE “References to other system information blocks” are removed from all instances of SIB messages in the specific message content sub-clauses. This is because RAN2 decided that only MIB and SB 1 or SB 2 contain system information scheduling information. Also, IE “SIB12 indicator” is inserted into SIB Type 11 messages. The value of this IE in SIB Type 11 is set to “FALSE” so that the UE will read only SIB Type 11 in connected state. IE “UE Timers and constants in connected mode” has been moved from SIB type 2 to SIB type 1. CR-597r5: The following areas are revised due to this approved CR: In RRC Connection Establishment procedure, clause 8.1.2.9 is added to test for physical channel failure condition. All the definition and test cases in RRC connection re-establishment procedure are removed because these concept is moved to CELL UPDATE procedure. Since RRC connection re-establishment procedure has been removed, test cases that use this procedure have been revised using cell-update procedure. The possibility to assign PRACH and SCCPCH in UE dedicated messages for CELL_FACH, CELL_PCH and URA_PCH states has been removed since there is no Iur support. A RB control message cannot assign IE Downlink information for each radio link and PRACH info for state transition to CELL FACH, CELL PCH, URA PCH. The test-cases with transiton to CELL FACH, CELL PCH, URA PCH are revised. Clauses 8.2.1.8, 8.2.1.16, 8.2.2.8, 8.2.2.17, 8.2.3.7, 8.2.3.15, 8.2.4.7, 8.2.6.7 and 8.2.6.15. IE “DRX Indicator” has been changed to IE “RRC State Indicator”. The variables of IE “RRC State Indicator” have been totally removed and new variables have been added.“no DRX”, “DRX with cell updating” and “DRX with URA updating” are removed. “CELL_DCH”, “CELL_FACH”, “CELL_PCH” and “URA_PCH” are added. All message content that contains IE “DRX Indicator” are revised. Clarifications of when procedures end, has caused many test cases to be corrected. Cell update due to RB control response has been removed, hence the related test case has been removed.Clause 8.3.1.14 is removed. Two new causes for cell update has been added. They are “radio link failure” and “RLC unrecoverable error”. Therefore new test cases for these two causes have been added. T306 has been removed and all T306 timers have been replaced with T305 timers. In cell update, condition for invalid configuration has been added. Therefore, new clause 8.3.1.20 has been added. In active set update, the condition for unsupported configuration in the UE has been change and condition for invalid configuration has been added. Clause 8.3.4.4 has been revised to cater for this change. In active set update, the condition for subsequently received active set update messages and for incompatible simultaneous reconfiguration has been removed. Clause 8.3.4.6 has therefore been removed. IE “URA update cause” with value of “change of URA” has been changed to “URA reselection”. T303 has been removed and all T303 timers have been replaced with T302 timers. V303 has been removed and all V303 constants have been replaced with V302 constant. N303 has been removed and all N303 constants have been replaced with N302 constants. In cell updating the UE shall respond to CELL UPDATE CONFIRM message on downlink CCCH with valid IE “U-RNTI” in the same way it respond to message sent on downlink DCCH. CR-598: The name of IE in “Paging record” is revised. CR-600r3: The following areas are revised due to this approved CR: Invalid configuration condition has been added to all RB procedures, therefore new test procedures have been added to current test cases. Clauses 8.2.1.7, 8.2.1.15, 8.2.2.6, 8.2.2.15, 8.2.3.6, 8.2.3.14, 8.2.4.6, 8.2.4.15, 8.2.5.4, 8.2.6.6, 8.2.6.14 are affected. Cell re-selection condition has been added to all RB procedures. Test cases concerning failure to access the assigned physical channel during the transition from CELL_FACH to CELL_DCH have been revised. Clauses 8.2.1.9, 8.2.2.9, 8.2.2.18, 8.2.3.8, 8.2.4.9, 8.2.4.17, 8.2.6.8, 8.2.6.16 are affected. Test cases concerning failure to revert to the old configuration after the detection of physical channel failure during the transition from CELL_DCH to CELL_FACH has been revised. Clauses 8.2.1.5, 8.2.1.13, 8.2.2.4, 8.2.2.13, 8.2.3.4, 8.2.3.12, 8.2.4.4, 8.2.4.13, 8.2.6.4, 8.2.6.12 are affected. IE “suspend/resume” change to “stop/continue”. Some changes in the word used are made. Test cases concerning the control of uplink transmission by RB reconfiguration messages have been revised. Clauses 8.2.2.7, 8.2.2.16 are affected. CR-602: Many IEs are revised. DRX indicator ( RRC state indicator RRC transaction identifier is added. Critical spare values in downlink messages removed, conditions for creating invalid message reception test scenario have been revised. Clauses 8.1.1.7, 8.1.2.8, 8.1.3.5, 8.1.5.1, 8.1.5.4, 8.1.6.1, 8.1.6.2, 8.1.7.1, 8.1.7.2, 8.1.8.1, 8.1.8.2, 8.2.1.7, 8.2.1.15, 8.2.2.6, 8.2.2.15, 8.2.3.6, 8.2.3.14, 8.2.4.6, 8.2.4.15, 8.2.6.6, 8.2.6.14, 8.3.1.13 are affected. CR-604r2: IE “FACH measurement occasion info” has been re-structured. The corresponding IEs found in SIB type 11 or 12 in the specific message contents sub-clauses are updated. CR-641: Downlink outer loop control procedure has been removed. Hence, clause 8.2.9 has been removed. The following errors are found and corrected: In many test cases, BCCH is stated as being broadcasted on primary CPICH, which is technically wrong. BCCH should be broadcast on primary CCPCH. In clause 8.3.1.X, the specific message contents of some CELL UPDATE CONFIRM messages contain an incorrect IE name - “Downlink DPCH info for one radio link”. The correct name for this IE should be “Downlink information for each radio link”. References for the initial condition in some of the test cases have been updated according to the new clause 7.4 in TS 34.108 version 3.2.0. All instances of “UL data transmission” for IE “Cell update cause” are renamed to “uplink data transmission”. All instances of “Periodic cell update” for IE “Cell update cause” are renamed to “Periodical cell update”. Clause 8.1.2.2 is revised such that two PRACHs are prepared in first step to let the UE randomly choose a PRACH. In the last meeting, it was decided that state 7 defined in clause 7.4 of TS 34.108 should be added in the initial condition of some test cases in RRC Connection Management. Clause 8.2.4.8 is an invalid test-case. PHYSICAL CHANNEL FAILURE can’t be occurred when UE enter into CELL_FACH state. In clause 8.1.1.1, UE is required to send RRC connection setup complete message to SS after step 5. Clause 8.4.1.10 – The condition that triggers the UE to send MEASUREMENT CONTROL FAILURE message is revised. Specifically, an unknown arbitrary 32-bits string is append to MEASUREMENT CONTROL message in step 3. Routing info requires unqiue identity as suggested by ESTI. In clauses 8.1.8.1 and 8.1.8.2, RB identity has been revised. Other corrections (a) Due to Nokia’s comments: "Step xx" is missing from some of the specific message content sections. For the purpose of clarity, they are added. Clause 8.4.1.2 - Expected Sequence: An "arrow" is missing in step 4, RRC CONNECTION SETUP message. Pointed out by Nokia, test procedure in all the “Incompatible simultaneous reconfiguration” test cases should end with RB complete message. Clauses 8.2.1.6, 8.2.1.14, 8.2.2.5, 8.2.2.14, 8.2.3.5, 8.2.3.13, 8.2.4.5, 8.2.4.14, 8.2.6.5, 8.2.6.13 are affected. Following Nokia’s comment, IE “Allowed Transport format combination” in TRANSPORT FORMAT COMBINATION CONTROL message has been revised. Clauses 8.2.5.1 and 8.2.5.2 are corrected. This CR also provides an update to the existing RRC messages in Annex A of TS 34.123-1 version 3.2.0, in accordance to the following CRs to RRC core specification (TS 25.331 version 3.4.1) approved during RAN2 #16 and RAN2#17 meetings. CR-542: “Logical channel max loss” IE is deleted. CR-543r1: The missing IE “NAS Synchronisation Indicator” is added to IE “RAB info”. The value of this IE is set to “Not Present”. CR-544r1: IE “CFN-SFN observed time difference” in IE “Cell measured results” is renamed to “Cell synchronisation information”, while the same IE in IE “Cell reporting quantities” is renamed to “Cell synchronisation information reporting indicator”. At the same time, all IEs in IE “Cell reporting quantities” are appended with “reporting indicator” to explicitly show that these are flags for reporting quantities, rather than the reported quantities themselves. CR-545r1: IE “Timing indication” was previously absent in IE “Downlink DPCH info common for all RL”, it is added and set to “Maintain”. IE “CFN-targetSFN frame offset” is introduced as conditional (but Not Present) IE in IE “Downlink DPCH info common for all RL”. CR-548r1: The enumerated value “SMS” in IE “Paging cause” is changed to “Low Priority Signalling”. CR-554r1: The signalled range for IE “BLER Quality value” is changed. The current BLER quality value (0.00) is replaced by 10-6.3. CR-549: A “CHOICE report criteria” IE is added before “Periodic reporting criteria” IE in MEASUREMENT CONTROL message. CR-587r1: A series of changes are carried out in accordance to the modifications introduced in CR-587r1. They are listed below: IE “Measurement identity number” in MEASUREMENT CONTROL and MEASUREMENT REPORT messages is renamed to “Measurement identity”. “Inter-system measurement” IE is renamed to “Inter-RAT measurement”. Also, “LCS measurment” IE is renamed to “UP measurement”. CR-596: IE “UE Timers and constants in connected mode” is added to UTRAN MOBILITY INFORMATION message. CR-597r5: Several modifications are introduced as described below: IE “DRX Indicator” was changed to IE “RRC State Indicator”, with a set of different enumerated values. Optional IEs “RB information to release list”, “RB information to reconfigure list”, “RB information to be affected list”, “UL Transport channel information common for all transport channels”, “Deleted UL TrCH information list”, “Added or reconfigured TrCH UL information list”, “DL Transport channel information common for all transport channels”, “Deleted DL TrCH information list”, “Added or reconfigured DL TrCH information list” and “Downlink information per radio link list” are added to CELL UPDATE CONFIRM message. “Failure cause” and “RB timer indicator” IEs are added to CELL UPDATE message. RRC connection re-establishment procedure is deleted, hence all related messages are removed from Annex A. CR-598r1: IE “Paging Record” in PAGING TYPE 1 messages is revised. CR-602: The following changes are carried out according to this CR: IE “RRC transaction identifier” is inserted into many messages IE “DRx indicator” is replaced by IE “RRC state indicator” in many messages. The appropriate value for this IE is chosen, depending on the final state the UE will reside on. CR-606: Several measures are approved by RAN2 in order to reduce the size of IEs “RLC info” and “RB mapping info” transmitted in the downlink. As a result of these optimisation efforts, the corresponding changes to the default message contents need to be carried out: IE “Downlink RLC logical channel info” needs to be added to IE “RB mapping info”. RADIO BEARER SETUP, RADIO BEARER RELEASE and RRC CONNECTION SETUP messages are affected. IEs “RLC info” are modified to become IEs “CHOICE RLC info type” in RADIO BEARER SETUP message. CR-609r1: Optional IE “COUNT-C activation time” is added to all uplink radio-bearer related complete messages (e.g. RADIO BEARER RECONFIGURATION COMPLETE, TRANSPORT CHANNEL RECONFIGURATION COMPLETE). The presence of this IE is conditional on whether the UE transits to CELL_DCH state and also existence of RLC-TM RB(s). Also, IE “Activation time for DPCH” in IE “Ciphering mode info” is renamed to “Ciphering activation time info”. CR-615r2: IE “CHOICE RLC size list” is added into IE “RB mapping info”. All instances of this IE are set to “All” so that all the RLC sizes listed in the TFS can be used by the UE. Also, IE “Transport Format Set” is modified to include a list of logical channels so that configuration of RLC size for certain logical channels is made possible. CR-625: An optional IE “RB with PDCP information list” is added into RADIO BEARER SETUP and RADIO BEARER RELEASE messages. These IEs are set to “Not Present” at the moment. CR-629r1: An optional IE “Signalling Connection release indicator” is added into downlink RADIO BEARER RELEASE messages. This IE is set to “Not Present” as it’s not desired to release a RB and a signalling connection simultaneously in the test cases. Other error corrections include: IEs “CN Domain Identity” and “NAS Information” are deleted from MEASUREMENT REPORT message. At the same time, IEs “Additional Measured Results” and “Event results” were mistakenly left out of the default MEASUREMENT REPORT message are now reinstated. IE “CHOICE Measurement type” was mistakenly left out of the default MEASUREMENT CONTROL message. It is now reinserted, with all the sub-IEs set to “Not Present”. Technical error corrections: RRC CONNECTION SETUP (Transition to CELL_FACH state): It was pointed out (by SAS on 10 Jan 01) that only RB#1 to RB#4 can be established by specifying IE “Signalling RB information to setup”. Therefore, IE “Signalling RB information to setup” for SRBs on CCCH, BCCH and PCCH are deleted. The values of Transport channel identity, Logical channel identity and Radio Bearer identity were changed because of the revision of the channel structure as proposed by ETSI in the draft TS 34.123-3 version 1.0.0 (T1S-01001). |
| Consequences if ( not approved: | Test specifications will not be compatible with core specifications. |
| Clauses affected: ( | 8.4.X, 8.4.1.14 (new), 8.4.1.9, 8.4.1.10 |
| Other specs ( |  | Other core specifications ( |  |
| affected: | X | Test specifications | TS 34.108 version 3.2.0 |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

# How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://www.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2000-09 contains the specifications resulting from the September 2000 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

# 8.	Radio Resource Control RRC

## 8.1	RRC Connection Management Procedure

### 8.1.1	Paging

#### 8.1.1.1	Paging for Connection in idle mode

8.1.1.1.1	Definition

8.1.1.1.2	Conformance requirement

In idle mode, UE monitors the paging occasions determined using parameters from SYSTEM INFORMATION BLOCK messages. When the UE receives a PAGING TYPE 1 message transmitted on PCCH during one of its assigned paging occasions, it should attempt to establish an RRC connection.

Reference

3GPP TS 25.331 clause 8.1.2, 3GPP TS 25.211 clause 5.3.3.7, 3GPP TS 25.304 clause 8.

8.1.1.1.3	Test purpose

To confirm that the UE establishes an RRC connection after it receives a PAGING TYPE 1 message which includes IE ”Paging Record”(UE identity) set to the IMSI of the UE.

8.1.1.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 with a CN UE identity (set to IMSI) ,depending on the CN domain(s) supported by the UE.

Test Procedure

The SS transmits a PAGING TYPE 1 message, which includes an unmatched CN UE identity for the UE in the idle state. The UE shall not change its state. The SS transmits a PAGING TYPE 1 message, which includes a matched CN UE identity for the UE in the idle state. During transmission of PAGING TYPE 1 messages, SS selects the correct paging indicator on the PICH in order to allow the UE to respond to paging. Then the UE transmits an RRC CONNECTION REQUEST to the SS, the SS transmits an RRC CONNECTION SETUP to the UE. When the UE receives this message, the UE establishes an RRC connection and transmits an RRC CONNECTION SETUP COMPLETE message on the uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | SYSTEM INFORMATION BLOCK TYPE 13 | Transmit these messages on the BCCH, in addition to the normal BCCH transmissions. See specific message contents. |
| 2 | ( | PAGING TYPE 1 | The SS transmits the message, which includes an unmatched identity (incorrect IMSI), and the UE does not change its state. |
| 3 | ( | PAGING TYPE 1 | The SS transmits the message, which includes a matched identity (test-SIM IMSI). |
| 4 | ( | RRC CONNECTION REQUEST |  |
| 5 | ( | RRC CONNECTION SETUP | SS assigns DPCH resources to allow UE to establish an RRC connection. |
| 6 | ( | RRC CONNECTION SETUP COMPLETE |  |

Specific Message Contents

SYSTEM INFORMATION TYPE 13

| Information Element | Value/remark |
| --- | --- |
| CN domain system information list CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - CN domain specific DRX cycle length coefficient UE Timers and constants in idle mode - T300 - N300 - T312 - N312 | Only 1 entry Supported Domain (PS Domain or CS Domain) Supported CN type Default 6 6000 milliseconds 3 10 sec 200 |

PAGING TYPE 1 (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record CHOICEUsed paging identity - Paging cause - CN domain identity - CHOICE UE Identity - IMSI | Only 1 entry CN identity Terminating Call with one of the supported services Supported Domain (PS Domain or CS Domain) IMSI Set to an arbitrary octet string of length 7 bytes which is different from the IMSI value stored in the USIM card. |

PAGING TYPE 1 (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record CHOICE Used paging identity - Paging cause - CN domain identity - CHOICE UE Identity - IMSI | Only 1 entry CN identity Terminating Call with one of the supported services Supported Domain (PS Domain or CS Domain ) IMSI Set to the same octet string as in the IMSI stored in the USIM card |

RRC CONNECTION REQUEST (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Initial UE identity Establishment Cause Protocol Error Indicator Measured results on RACH | Same as the IMSI stored in the USIM card, or the registered TMSI or P-TMSI Check to see if it is set to the same value as “Paging Cause” IE in the PAGING TYPE 1 message transmitted on step 3. Check to see if it is set to FALSE Not checked. |

8.1.1.1.5		Test requirement

After step 2 the UE shall not transmit on the uplink CCCH in order to establish a RRC connection.

After step 5 the UE shall have an RRC connection based on dedicated physical channel resources and transmit an RRC CONNECTION SETUP COMPLETE message on the uplink DCCH.

#### 8.1.1.2		Paging for Connection in connected mode (CELL_PCH)

8.1.1.2.1		Definition

8.1.1.2.2	Conformance requirement

In CELL_PCH state, a UE can respond to a paging request from UTRAN. In this case, the UTRAN has requested to establish a connection with the UE. The UE should then attempt to perform a cell update procedure and move to CELL_FACH state in order to respond to the paging using uplink CCCH.

Reference

3GPP TS 25.331 clause 8.1.2

8.1.1.2.3	Test purpose

To confirm that the UE enters the CELL_FACH state after it receives a PAGING TYPE 1 message which indicates that the paging has originated from UTRAN. To verify that the UE performs cell update procedure after entering the CELL_FACH state.

8.1.1.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH state (state 6-12) as specified in clause 7.4 of TS 34.108 with a valid U-RNTI already assigned by the SS

Test Procedure

The SS transmits a PAGING TYPE 1 message, which includes an unmatched U-RNTI in CELL_PCH state. The UE does not change its state. Then SS transmits a PAGING TYPE 1 message with a matched identifier but originates from the CN instead of UTRAN. The UE should not change state after receiving this message. The SS transmits a PAGING TYPE 1 message, which includes a matched U-RNTI in the connected state. Then the UE enters the CELL_FACH state and performs the cell updating procedure.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | SYSTEM INFORMATION BLOCK TYPE 13 | Transmit these messages on the BCCH, in addition to the normal BCCH transmissions. See specific message contents |
| 2 | ( | PAGING TYPE 1 | The SS transmits a message including an unmatched identifier. UE shall not respond to the paging. |
| 3 | ( | PAGING TYPE 1 | The SS transmits a message includes a matched identifier but with the originator being the CN, UE shall not respond to the paging. |
| 4 | ( | PAGING TYPE 1 | The SS transmits the message with the UTRAN being the originator and including the UE’s assigned U-RNTI |
| 5 | ( | CELL UPDATE | The UE enters the CELL_FACH state. UE performs cell updating procedure. The CELL UPDATE message shall contain the value “Cell Update Cause” set to “paging response”. |
| 6 | ( | CELL UPDATE CONFIRM | Use the default message specified in Annex A. |

Specific Message Contents

PAGING TYPE 1 (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - U-RNTI - SRNC Identity - S-RNTI | Only 1 entry UTRAN identity Set to an arbitrary 16-bit string which is different from the SRNC identity assigned. Set to an arbitrary 20-bit string which is different from the S-RNTI assigned. |

PAGING TYPE 1 (Step 3)

Same as the PAGING TYPE 1 message as in Clause 8.1.1.1.4, with the exception that the “BCCH modification info” IE should be omitted in the message.

PAGING TYPE 1 (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - U-RNTI - SRNC Identity - S-RNTI | Only 1 entry UTRAN identity Set to the same SRNC identity as previously assigned. Set to the same S-RNTI as previously assigned. |

SYSTEM INFORMATION BLOCK TYPE 13

Use the same SYSTEM INFORMATION BLOCK TYPE 13 message as specified in Clause 8.1.1.1.4.

8.1.1.2.5	Test requirement

After step 2 the UE shall not respond to the PAGING TYPE 1 message sent in step 2.

After step 3 the UE shall not respond to the PAGING TYPE 1 message sent in step 2.

After step 4 the UE shall enter the CELL FACH state and send a CELL UPDATE message with “Cell Update Cause” IE set to “paging response”.

#### 8.1.1.3		Paging for Connection in connected mode(URA_PCH)

8.1.1.3.1	Definition

8.1.1.3.2	Conformance requirement

This procedure is used to transmit a Paging TYPE 1 message from the network to selected UEs in URA_PCH state using the paging control channel (PCCH). The UE listens to it and then enters the CELL_FACH state.

Reference

3GPP TS 25.331 clause 8.1.2

8.1.1.3.3	Test purpose

To confirm that the UE enters the CELL_FACH state after it receives a PAGING TYPE 1 message which includes IE ”Paging Record”(U-RNTI) for the UE and which is set to “UTRAN originator” in IE “paging originator”.

8.1.1.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH state (state 6-13) as specified in clause 7.4 of TS 34.108 with a valid U-RNTI assigned by the SS.

Test Procedure

The SS transmits a PAGING TYPE 1 message, which includes an unmatched U-RNTI in URA_PCH state. The UE does not change its current state. The SS transmits a PAGING TYPE 1 message which includes a matched U-RNTI in the connected state. Then the UE listens to it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PAGING TYPE 1 | The SS transmits the message that includes an unmatched identifier, then the UE does not change its state. |
| 2 | ( | PAGING TYPE 1 | The SS transmits the message that includes a matched identifier. |
| 3 | ( | CELL UPDATE | The UE enters the CELL_FACH state. |

Specific Message Contents

PAGING TYPE 1 (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - U-RNTI - SRNC Identity - S-RNTI | Only 1 entry UTRAN identity Set to an unused SRNC identity which is different from the SRNC identity assigned. Set to an arbitrary 20-bit string which is different from the S-RNTI assigned. |

PAGING TYPE 1 (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - U-RNTI - SRNC Identity - S-RNTI | Only 1 entry UTRAN identity Set to the previously assigned SRNC identity Set to previously assigned S-RNTI |

8.1.1.3.5	Test requirement

After step 1 the UE shall not respond to the paging.

After step 2 the UE shall enter the CELL FACH state, and transmit CELL UPDATE message to initiate the cell updating procedure with the paging cause set to “paging response”.

#### 8.1.1.4	Paging for Notification in idle mode

8.1.1.4.1	Definition

8.1.1.4.2	Conformance requirement

When a system information block on the BCCH is modified, the PAGING TYPE 1 message can be sent on the PCCH to inform the UE about the changes, which are currently taking place in the idle mode. The PAGING TYPE 1 message includes the IE ”BCCH Modification Information”. Upon receiving this notification from the UTRAN, the UE shall read the relevant MIB and/or SIB(s) subsequently during idle mode.

Reference

3GPP TS 25.331 clause 8.1.1.2

8.1.1.4.3	Test purpose

To confirm that the UE checks the new value tag of the master information block and reads the updated SYSTEM INFORMATION BLOCK messages after it receives a PAGING TYPE 1 message which includes the IE ”BCCH Modification Information”.

8.1.1.4.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 with a CN UE identity, depending on the CN domain(s) supported by the UE.

Test Procedure

The UE is in the idle state before it starts to change the SYSTEM INFORMATION BLOCK TYPE 1 or 13 messages, depending on the CN type supported by the UE. The SS transmits a PAGING TYPE 1 message on the paging occasions assigned to the UE. The message shall include the IE “BCCH Modification Information” indicating the time when the first modified master information block is available. Before the starting time, SS continuously broadcast the original MASTER INFORMATION BLOCK and various types of SYSTEM INFORMATION BLOCK on the BCCH mapped to BCH transport channel. SS maintains this status until the SFN which corresponds to the starting time is reached. Then it transmits the new master information block followed by the new SYSTEM INFORMATION BLOCK TYPE 1 or 13 messages. In the new SIB TYPE 1 or 13 messages, the IE “DRX Cycle Length Coefficient” is altered when compared to the original SIB TYPE 1 or 13 messages. At the next paging occasion, SS transmits a new PAGING TYPE 1 message. The message addresses the UE using its IMSI and the “paging cause” IE set to a terminating call type that is supported by the UE. The UE shall react to the PAGING TYPE 1 message and then send a RRC CONNECTION REQUEST message to SS.

Notes: 	For UEs supporting GSM-MAP CN type only, SYSTEM INFORMATION TYPE 1 messages are to be sent by SS in this test case. On the other hand, SS transmits SYSTEM INFORMATION TYPE 13 messages if the UE under test supports only ANSI-41 CN type.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 or SYSTEM INFORMATION BLOCK TYPE 13 | SS transmits information on BCCH in order for UE to listen to one of the S-CCPCH physical channel, which carries PAGING TYPE 1 or 13 messages on PCCH. Relevant paging parameters are also broadcasted. |
| 2 | ( | PAGING TYPE 1 | SS transmits the message includes the IE ”BCCH Modification Information”, with the “Value Tag” changed from the “MIB Value Tag” of the current Master Information Block. Also the modification time is set to 4088 radio frame from the current SFN. SS continuously broadcast the same MASTER INFORMATION BLOCK and various types of SYSTEM INFORMATION BLOCK on BCCH for a period stretching 4087 frames. |
| 3 | ( ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 or SYSTEM INFORMATION BLOCK TYPE 13 | SS starts to transmit the MIB with the “MIB Value Tag” IE different from the original setting. At the same time, SS starts to transmit the affected SIB TYPE 1 or TYPE 13 messages continuously. The value of IE “DRX Cycle Length Coefficient” is changed in this message. SS starts to monitor the uplink RACH after approximately 4087 frames from step 2. |
| 4 | ( | PAGING TYPE 1 | SS starts to transmit this message continuously on the PCCH according to the new value of “DRX Cycle Length Coefficient”, at the next paging occasion immediately following step 3. |
| 5 | ( | RRC CONNECTION REQUEST | UE transmits a request due to answer to the PAGING TYPE 1 received in step 4. The IE “Establishment Cause” should be set to “Terminating Call” supported by the UE and the “Initial UE Identity” set to UE’s IMSI. |
| 6 | ( | RRC CONNECTION REJECT | UE shall return to idle mode after receiving this message |

Specific Message Contents

SYSTEM INFORMATION BLOCK TYPE 1 (Step 1) – for UEs supporting GSM-MAP core networks

| Information Element | Value/remark |
| --- | --- |
| References to other system information blocks CN common GSM-MAP NAS system information CN domain system information list - CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - CN domain specific DRX cycle length coefficient - CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - CN domain specific DRX cycle length coefficient UE Timers and constants in idle mode - T300 - N300 - T312 - N312 UE Timers and constants in connected mode | Not Present Location Area Information (LAI) Supports both CS and PS domains CS domain GSM-MAP Set to the same octet string as in IE ”CN common GSM MAP-NAS system information” 12 PS domain GSM-MAP Set to the same octet string as in IE ”CN common GSM MAP-NAS system information” 12 400 milliseconds 7 10 seconds 200 Not Present |

SYSTEM INFORMATION BLOCK TYPE 13 (Step 1) – for UEs supporting ANSI-41 core networks

| Information Element | Value/remark |
| --- | --- |
| References to other system information blocks CN domain system information list CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - ANSI-41 NAS System Information - ANSI-41 NAS Parameter - CN domain specific DRX cycle length coefficient - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - ANSI-41 NAS System Information - ANSI-41 NAS Parameter - CN domain specific DRX cycle length coefficient UE Capability update requirement | Not Present Supports both CS and PS domains CS ANSI-41 Set to an ANSI-41 user zone information 12 PS ANSI-41 Set to an ANSI-41 user zone information 12 Not Present |

PAGING TYPE 1 (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - Paging Cause - CN Domain Identity - CHOICE UE Identity - IMSI BCCH modification info MIB Value Tag BCCH Modification time | Only 1 entry CN identity Terminating Call with one of the supported services CS Domain IMSI Set to the same octet string as in the IMSI value stored in the USIM card 2 4088 |

MASTER INFORMATION BLOCK (Step 3)

| Information Element | Value/remark |
| --- | --- |
| MIB Value tag | 2 |

SYSTEM INFORMATION BLOCK TYPE 1 (Step 3) – for UEs supporting GSM-MAP core networks

| Information Element | Value/remark |
| --- | --- |
| References to other system information blocks CN common GSM-MAP NAS system information CN domain system information list - CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - CN domain specific DRX cycle length coefficient - CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - CN domain specific DRX cycle length coefficient UE Timers and constants in idle mode - T300 - N300 - T312 - N312 UE Timers and constants in connected mode | Not Present Location Area Information (LAI) Supports both CS and PS domains CS domain GSM-MAP Set to the same octet string as in IE ”CN common GSM MAP-NAS system information” 6 PS domain GSM-MAP Set to the same octet string as in IE ”CN common GSM MAP-NAS system information” 6 400 milliseconds 7 10 seconds 200 Not Present |

SYSTEM INFORMATION BLOCK TYPE 13 (Step 3) – for UEs supporting ANSI-41 core networks

| Information Element | Value/remark |
| --- | --- |
| References to other system information blocks CN domain system information list CN domain system information - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - ANSI-41 NAS system information - ANSI-41 NAS Parameter - CN domain specific DRX cycle length coefficient - CN domain identity - CHOICE CN Type - CN domain specific NAS system information - ANSI-41 NAS system information - ANSI-41 NAS Parameter - CN domain specific DRX cycle length coefficient | Not Present Supports both CS and PS domains CS domain ANSI-41 Set to an ANSI-41 user zone information 6 PS domain ANSI-41 Set to an ANSI-41 user zone information 6 |

PAGING TYPE 1 (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - Paging Cause - CN Domain Identity - CHOICE UE Identity - IMSI | Only 1 entry CN identity Terminating Call with one of the supported service CS Domain IMSI Set to the same octet string as in the IMSI value stored in the USIM card |

RRC CONNECTION REJECT (Step 6)

| Information Element | Value/remark |
| --- | --- |
| Initial UE identity - CHOICE UE id type - IMSI Rejection cause Wait time Redirection info | IMSI Set to the same octet string as in the IMSI value stored in the USIM card Unspecified 0 Not Present |

8.1.1.4.5	Test requirement

After step 5 the UE shall transmit RRC CONNECTION REQUEST message in response to the PAGING TYPE 1 messages sent in step 4.

#### 8.1.1.5		Paging for Notification in connected mode (CELL_PCH)

8.1.1.5.1	Definition

8.1.1.5.2	Conformance requirement

When a system information block on the BCCH is modified, the message PAGING TYPE 1 can be sent on the PCCH to inform the UE about this change in the CELL_PCH state. This message includes the IE “BCCH Modification Information”. Upon receiving this notification from the UTRAN, the UE shall read the relevant MIB and/or SIB(s) subsequently while in CELL_PCH state.

Reference

3GPP TS 25.331 clause 8.1.1.2

8.1.1.5.3	Test purpose

To confirm that the UE enters the CELL_FACH state, checks the new value tag of the master information block, and read the SYSTEM INFORMATION messages after it receives a PAGING TYPE 1 message which includes the IE ”BCCH Modification Information”

8.1.1.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH state (state 6-12) as specified in clause 7.4 of TS 34.108 with valid a U-RNTI assigned to it.

Test Procedure

Identical test steps 1 to 5 in Clause 8.1.1.4 are applied to this test. However, the PAGING TYPE 1 messages used in step 2 and step 4 are altered. The changes are indicated in the specific message content paragraph under this clause. At step 6, UE shall send the CELL UPDATE message indicating the “cell update cause” to be “paging response”. SS then replies with a CELL UPDATE CONFIRM message to allow the UE to transit to CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 or SYSTEM INFORMATION BLOCK TYPE 13 | SS transmits information on BCCH in order for UE to listen to one of the S-CCPCH physical channel, which carries PAGING TYPE 1 or 13 messages on PCCH. Relevant paging parameters are also broadcasted. |
| 2 | ( | PAGING TYPE 1 | SS transmits the paging message which comprises IE “BCCH Modification Information”, with the “Value Tag” changed from the “MIB Value Tag” of the current Master Information Block. Also the modification time is set to 4088 radio frame from the current SFN. SS continuously broadcast the same MASTER INFORMATION BLOCK and various types of SYSTEM INFORMATION BLOCK on BCCH for a period stretching 4087 frames. |
| 3 | ( ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 or SYSTEM INFORMATION BLOCK TYPE 13 | SS starts to transmit the MIB with the “MIB Value Tag” IE different from the original setting. At the same time, SS starts to transmit the affected SIB TYPE 1 or TYPE 13 messages continuously. The value of IE “DRX Cycle Length Coefficient” is changed in this message. SS starts to monitor the uplink RACH after approximately 4087 SFN from step 2. |
| 4 | ( | PAGING TYPE 1 | SS transmits this message continuously on the PCCH according to the new value of “DRX Cycle Length Coefficient”, at the next paging occasion immediately following step 3. This message shall page the UE with its U-RNTI and setting the UTRAN as the paging originator. |
| 5 | ( | CELL UPDATE | The IE “Cell Update Cause” should be set to “Paging Response” and the IE “U-RNTI” shall be similar to the UE’s U-RNTI value. The “Protocol Error Indicator” IE shall be set to FALSE. |
| 6 | ( | CELL UPDATE CONFIRM | UE shall transit to CELL_FACH state after receiving this message. |

Specific Message Contents

SYSTEM INFORMATION BLOCK TYPE 1 or TYPE 13 (Step 1)

The content of this message is the same in the message used in step 1 specified in Clause 8.1.1.4.3.

PAGING TYPE 1 (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - U-RNTI - SRNC Identity - S-RNTI BCCH modification info - MIB Value Tag - BCCH Modification time | Only 1 entry UTRAN identity Equal to the U-RNTI assigned earlier. 2 4088 |

MASTER INFORMATION BLOCK (Step 3) and

SYSTEM INFORMATION BLOCK TYPE 1 or TYPE 13 (Step 3)

The content of these messages is the same in the message used in step 3 specified in Clause 8.1.1.4.4.

PAGING TYPE 1 (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Used paging identity - U-RNTI - SRNC Identity - S-RNTI BCCH modification info | Only 1 entry UTRAN identity Equal to the U-RNTI assigned earlier. Same as the current SRNC allocated Same as the current S-RNTI allocated Not Present |

CELL UPDATE CONFIRM (Step 6)

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_FACH |

8.1.1.5.5	Test requirement

After step 5 the UE shall transmit a CELL UPDATE message with “cell update cause” IE set to “paging response”. Upon receiving CELL UPDATE CONFIRM message, the UE shall enter the CELL_FACH state.

#### 8.1.1.6	Paging for Notification in connected mode (URA_PCH)

8.1.1.6.1	Definition

8.1.1.6.2	Conformance requirement

When a system information block on the BCCH is modified, the UTRAN can send a PAGING TYPE 1 message on the PCCH to inform UE about the changes while the UE is in the URA_PCH state. This message includes the IE ”BCCH Modification Information”. When receiving this message in URA_PCH state, the UE shall read the relevant MIB and/or SIB(s).

Reference

3GPP TS 25.331 clause 8.1.1.2

8.1.1.6.3	Test purpose

To confirm that the UE enters the CELL_FACH state, checks the included new value tag of the master information block and reads the relevant SYSTEM INFORMATION block(s) after it receives a PAGING TYPE 1 message which includes the IE “BCCH Modification Information”.

8.1.1.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH state (state 6-13) as specified in clause 7.4 of TS 34.108 with a valid U-RNTI assigned.

Test Procedure

The UE is in the URA_PCH state before the SS starts changing SYSTEM INFORMATION BLOCK messages. SS modifies its SYSTEM INFORMATION and updates the “value tag” of both the SYSTEM INFORMATION BLOCK TYPE 1 and of the MASTER INFORMATION BLOCK. After a while, the SS transmits a PAGING TYPE 1 message, which includes the IE “BCCH Modification Information”. The UE enters the CELL_FACH state and reads the modified SYSTEM INFORMATION BLOCK. The UE shall act according to the modified message. In this test case, the UE shall adjust it paging occasions and read the new PCCH blocks newly assigned to it under DRX mode.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION | The SS changes the SYSTEM INFORMATION when the UE is in the connected state (URA_PCH). |
| 2 | ( | PAGING TYPE 1 | SS transmits the message includes the IE “BCCH Modification Information”. |
| 3 |  |  | The UE enters the CELL_FACH state and reads the SYSTEM INFORMATION and then the UE follows this message. |

Specific Message Contents

None

8.1.1.6.5	Test requirement

After step 2 the UE shall enter the CELL_FACH state and read the SYSTEM INFORMATION message and follow it.

#### 8.1.1.7		Paging for Connection in connected mode (CELL_DCH)

8.1.1.7.1	Definition

8.1.1.7.2	Conformance requirement

This procedure is used to transmit a Paging TYPE 2 message from the network to selected UEs in CELL_DCH state using the dedicated control channel (DCCH). The UE listens to it and responds to this message accordingly.

Reference

3GPP TS 25.331 clause 8.1.11

8.1.1.7.3	Test purpose

To confirm that the UE responds this message after it receives a PAGING TYPE2 message which includes IE ”Paging Record Type Identifier” for the UE.

8.1.1.7.4	Method of test

Initial Condition

System Simulator: 1 cell.

UE: CELL_DCH state (state 6-9 or state 6-10) as specified in clause 7.4 of TS 34.108, depending on the CN domain(s) supported by the UE, after executing a location registration or attach procedure followed by the release of the TMSI of P-TMSI allocated.

Test Procedure

The SS transmits a PAGING TYPE 2 message which includes an unmatched Paging Record Type Identifier in CELL_DCH state. The UE shall not respond to this message. SS pages the UE again, this time with a matched Paging Record Type Identifier but with the IE “paging cause” set to an invalid value which is not defined. UE shall respond by transmitting a RRC STATUS message on the DCCH using RLC-AM mode. Finally, SS transmits a PAGING TYPE 2 message, which includes a matched Paging Record Type Identifier. Then the UE shall responds to this message by the transmission of an upper layer message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PAGING TYPE 2 | The SS transmits the message includes an unmatched identifier, then the UE does not respond. |
| 2 | ( | PAGING TYPE 2 | The SS transmits the message includes a matched identifier. In the paging message, IE “paging cause” is set to invalid value. |
| 3 | ( | RRC STATUS | The UE shall respond by reporting the protocol error to the SS. |
| 4 | ( | PAGING TYPE 2 | SS pages the UE with a matched identifier and with a valid “paging cause” IE. |
| 5 | ( | UPLINK DIRECT TRANSFER | The UE shall respond to the paging message sent in step 4. |

Specific Message Contents

PAGING TYPE 2 (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Paging cause CN domain identity Paging record type identifier | Terminating Call supported by the UE Domain supported by the UE Set to “TMSI” or “P-TMSI” allocated during the execution of location registration or attach procedure respectively |

PAGING TYPE 2 (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Paging cause | invalid value which is not defined |

RRC STATUS (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Protocol error information | Checked to see if set to “Information element value not comprehended” |

PAGING TYPE 2 (Step 4)

| Information Element | Values/Remarks |
| --- | --- |
| Paging cause CN domain identity Paging record type identifier | Terminating Call supported by the UE Domain supported by the UE Set to “IMSI (GSM-MAP)” for UEs supporting GSM-MAP core network type or “IMSI (DS-41)” for UEs supporting ANSI-41 core network type. |

UPLINK DIRECT TRANSFER (Step 5)

Only the message type IE for this message is checked.

8.1.1.7.5	Test requirement

After step 1 the UE shall not respond to the paging message on the DCCH.

After step 2 the UE shall respond to the paging message by transmitting RRC STATUS on the DCCH, stating the protocol error as “Information element value not comprehended”.

After step 4 the UE shall respond to the paging message by transmitting an UPLINK DIRECT TRANSFER message on the uplink DCCH.

#### 8.1.1.8		Paging for Connection in connected mode (CELL_FACH)

8.1.1.8.1	Definition

8.1.1.8.2	Conformance requirement

This procedure is used to transmit a Paging TYPE 2 message from the network to selected UEs in CELL_FACH state using the dedicated control channel (DCCH). The UE shall listen to it and responds to this message accordingly.

Reference

3GPP TS 25.331 clause 8.1.11

8.1.1.8.3	Test purpose

To confirm that the UE responds to a PAGING TYPE 2 message, which includes a matching value for IE ”Paging Record Type Identifier”.

8.1.1.8.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-11) as specified in clause 7.4 of TS 34.108.

Test Procedure

The SS transmits a PAGING TYPE 2 message, which includes an unmatched Paging Record Type Identifier in CELL_FACH state. The UE shall not respond to this message. The SS transmits a PAGING TYPE 2 message, which includes a matched Paging Record Type Identifier. Then the UE shall respond by transmitting an upper layer message to answer this page.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PAGING TYPE 2 | The SS transmits the message includes an unmatched identifier, then the UE does not respond. |
| 2 | ( | PAGING TYPE 2 | The SS transmits the message includes a matched identifier. |
| 3 | ( | UPLINK DIRECT TRANSFER | The UE responds by sending an upper layer message. |

Specific Message Content

PAGING TYPE 2 (Step 1)

Use the same message content as in step 1 from 8.1.1.7.4

PAGING TYPE 2 (Step 2)

Use the same message content as in step 4 from 8.1.1.7.4

8.1.1.8.5	Test requirement

After step 1 the UE shall not respond.

After step 2 the UE shall respond to the second PAGING TYPE 2 message by transmitting an UPLINK DIRECT TRANSFER message on the uplink DCCH.

### 8.1.2	RRC Connection Establishment

#### 8.1.2.1	RRC Connection Establishment in CELL_DCH state: Success

8.1.2.1.1	Definition

8.1.2.1.2	Conformance requirement

1.	The RRC connection establishment is initiated by the UE, which leaves the idle mode and transmits an RRC Connection Request message. This message shall include the IE “Initial UE identity” and is to be transmitted on the uplink CCCH.

2.	After the UE receives an RRC CONNECTION SETUP message which includes the same value of the IE “initial UE identity”, radio resource parameters (i.e. Signalling link type and multiplexing info) and U-RNTI, UE then configures the layer 2 and layer 1 processing so as to support the DCCH according to the radio resource parameters specified. The procedure successfully ends when the network receives an RRC CONNECTION SETUP COMPLETE message on the uplink DCCH.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.1.3	Test purpose

To confirm that the UE leaves the Idle Mode and correctly establishes a signalling link on the DCCH.

8.1.2.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE transmits an RRC CONNECTION REQUEST message to the SS on the uplink CCCH by attempting to make an outgoing call. After SS receives this message, it assigns the necessary radio resources and U-RNTI to be used by the UE. SS then transmits an RRC CONNECTION SETUP message containing an IE “Initial UE Identity” that does not match the IE “Initial UE Identity” in the most recent RRC CONNECTION REQUEST message sent by the UE. UE receives the RRC CONNECTION SETUP message within timer T300 but discards it due to the IE “Initial UE Identity” mismatch. UE shall wait for timer T300 to time out before re-transmitting a RRC CONNECTION REQUEST message to the SS. SS again assigns the necessary radio resources and U-RNTI. SS then follows by transmitting a RRC CONNECTION SETUP message containing an IE “Initial UE Identity” that matches the IE “Initial UE Identity” in the most recent RRC CONNECTION REQUEST sent by the UE. SS then waits for the UE to transmit an RRC CONNECTION SETUP COMPLETE message on the DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RRC CONNECTION REQUEST | By outgoing call operation |
| 2 | ( | RRC CONNECTION SETUP | This message is not addressed to the UE. |
| 3 | ( | RRC CONNECTION REQUEST | UE shall re-transmit the request message again after a time out of T300 from step 1. |
| 4 | ( | RRC CONNECTION SETUP |  |
| 5 |  |  | The UE configures the layer 2 and layer 1. |
| 6 | ( | RRC CONNECTION SETUP COMPLETE |  |

Specific Message Content

RRC CONNECTION SETUP (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity CHOICE UE id type IMSI | IMSI Set to an arbitrary octet string of length 7 which different from the IMSI value stored in the USIM card. |

8.1.2.1.5	Test requirement

After step 2 the UE shall re-transmit the RRC CONNECTION REQUEST message again in order to continue the RRC connection establishment procedure.

After step 6 the UE shall establish an RRC connection and continue the procedure of the outgoing call on the DCCH.

#### 8.1.2.2	RRC Connection Establishment: Success after T300 timeout

8.1.2.2.1	Definition

8.1.2.2.2 	Conformance requirement

1.	The RRC connection establishment is initiated by the UE, which leaves the idle mode. The UE shall transmit an RRC Connection Request message which includes the IE “Initial UE identity”. This message shall be sent on the uplink CCCH.

When there are more than one PRACHs available, the UE shall select one PRACH randomly and transmit an RRC Connection Request message by use of selected PRACH.

2.	In the case of a failure to establish the RRC connection at the expiry of timer T300 ,the UE retries to establish the RRC connection until V300 is greater than N300

When the UE receives a RRC CONNECTION SETUP message, which contains a protocol error and causing the internal variable PROTOCOL_ERROR_REJECT set to TRUE, it shall perform the appropriate error handling procedure.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.2.3 	Test purpose

To confirm that the UE retries to establish the RRC connection until V300 is greater than N300 after the expiry of timer T300 when the SS transmits no response for an RRC CONNECTION REQUEST message.

8.1.2.2.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

Before the test starts, an internal counter K in SS is initialized to a value = 1. Following this, the UE shall transmit an RRC CONNECTION REQUEST message to the SS on the uplink CCCH by use of selected PRACH from the available PRACH No.1 and PRACH No.2, after the operator attempts to make an outgoing call. SS ignores this message, increments K every time such a message is received and waits for T300 timer to expire. This cycle is repeated until K reaches N300. When K is equal to N300, the SS transmits the RRC CONNECTION SETUP message specified in step 6 to the UE and wait until T300 expires. The UE shall send another RRC CONNECTION REQUEST message on the uplink CCCH. SS verifies that the UE does not access the radio resource allocated in step 6. After confirming this restriction is observed, SS replies with a valid RRC CONNECTION SETUP message. The UE shall then acknowledge the establishment of RRC connection by sending the RRC CONNECTION SETUP COMPLETE message on uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | SYSTEM INFORMATION BLOCK TYPE 5 | Transmit these messages on the BCCH. See specific message contents. |
| 2 |  |  | SS initializes counter K to 1. Operator is asked to make an outgoing call and SS starts to wait for RRC CONNECTION REQUEST on uplink CCCH. |
| 3 | ( | RRC CONNECTION REQUEST |  |
| 4 |  |  | SS checks to see if K is equal to N300. If so, goes to step 6. Else, continues to execute step 5. |
| 5 |  |  | SS increments K. The next step is step 3. |
| 6 | ( | RRC CONNECTION SETUP | The message contains a protocol error, see specific message content. SS waits for T300 to expire again. |
| 7 | ( | RRC CONNECTION REQUEST | UE shall not access the radio resource indicated in RRC CONNECTION SETUP message sent in step 6. |
| 8 | ( | RRC CONNECTION SETUP | This is a legal message. See the clause 9 in TS 34.108 on default message content for RRC. |
| 9 |  |  | The UE configures the layer 1 and layer 2. |
| 10 | ( | RRC CONNECTION SETUP COMPLETE |  |

Specific Message Contents

SYSTEM INFORMATION TYPE 5 (Step 1)

| - PRACH system information | 2PRACHs |
| --- | --- |
| - PRACH info (PRACH No.1) |  |
| - CHOICE mode | FDD |
| - Available Signature | ‘0000 0000 1111 1111’B |
| - Available SF | Reference to clause 6.10 Parameter Set |
| - Preamble scrambling code number | 0 |
| - Puncturing Limit | Reference to clause 6.10 Parameter Set |
| - Available Sub Channel number | ‘1111 1111 1111’B |
| - Transport Channel Identity | 15 |
| - RACH TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to clause 6.10 Parameter Set |
| - Number of TB and TTI List | Reference to clause 6.10 Parameter Set |
| - Number of Tranport blocks | Reference to clause 6.10 Parameter Set |
| - CHOICE Mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to clause 6.10 Parameter Set |
| - Type of channel coding | Reference to clause 6.10 Parameter Set |
| - Coding Rate | Reference to clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to clause 6.10 Parameter Set |
| - CRC size | Reference to clause 6.10 Parameter Set |
| - RACH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - PRACH partitioning |  |
| - Access Service Class |  |
| - ASC Settings |  |
| - Available signature Start Index | 0 (ASC#0) |
| - Available signature End Index | 7 (ASC#0) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#1) |
| - Available signature End Index | 7 (ASC#1) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#2) |
| - Available signature End Index | 7 (ASC#2) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#3) |
| - Available signature End Index | 7 (ASC#3) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#4) |
| - Available signature End Index | 7 (ASC#4) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#5) |
| - Available signature End Index | 7 (ASC#5) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#6) |
| - Available signature End Index | 7 (ASC#6) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#7) |
| - Available signature End Index | 7 (ASC#7) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Persistence scaling factor |  |
| - Persistence scaling factor | 0.9 (for ASC#2) |
| - Persistence scaling factor | 0.9 (for ASC#3) |
| - Persistence scaling factor | 0.9 (for ASC#4) |
| - Persistence scaling factor | 0.9 (for ASC#5) |
| - Persistence scaling factor | 0.9 (for ASC#6) |
| - Persistence scaling factor | 0.9 (for ASC#7) |
| - AC-to-ASC mapping table |  |
| - AC-to-ASC mapping | 6 (AC0-9) |
| - AC-to-ASC mapping | 5 (AC10) |
| - AC-to-ASC mapping | 4 (AC11) |
| - AC-to-ASC mapping | 3 (AC12) |
| - AC-to-ASC mapping | 2 (AC13) |
| - AC-to-ASC mapping | 1 (AC14) |
| - AC-to-ASC mapping | 0 (AC15) |
| - Primary CPICH DL TX power | Reference to clause 6.10 Parameter Set |
| - Constant value | Reference to clause 6.10 Parameter Set |
| - PRACH power offset |  |
| - Power Ramp Step | 3dB |
| - Preamble Retrans Max | 2 |
| - RACH transmission parameters |  |
| - Mmax | 2 |
| - NB01min | 3 slot |
| - NB01max | 10 slot |
| - AICH info |  |
| - Channelisation code | SF-1(SF is reference to clause 6.10 Parameter Set) |
| - STTD indicator | FALSE |
| - AICH transmission timing | 0 |
| - PRACH info (PRACH No.2) |  |
| - CHOICE mode | FDD |
| - Available Signature | ‘0000 0000 1111 1111’B |
| - Available SF | Reference to clause 6.10 Parameter Set |
| - Preamble scrambling code number | 1 |
| - Puncturing Limit | Reference to clause 6.10 Parameter Set |
| - Available Sub Channel number | ‘1111 1111 1111’B |
| - Transport Channel Identity | 16 |
| - RACH TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to clause 6.10 Parameter Set |
| - Number of TB and TTI List | Reference to clause 6.10 Parameter Set |
| - Number of Tranport blocks | Reference to clause 6.10 Parameter Set |
| - CHOICE Mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to clause 6.10 Parameter Set |
| - Type of channel coding | Reference to clause 6.10 Parameter Set |
| - Coding Rate | Reference to clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to clause 6.10 Parameter Set |
| - CRC size | Reference to clause 6.10 Parameter Set |
| - RACH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - PRACH partitioning |  |
| - Access Service Class |  |
| - ASC Settings |  |
| - Available signature Start Index | 0 (ASC#0) |
| - Available signature End Index | 7 (ASC#0) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#1) |
| - Available signature End Index | 7 (ASC#1) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#2) |
| - Available signature End Index | 7 (ASC#2) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#3) |
| - Available signature End Index | 7 (ASC#3) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#4) |
| - Available signature End Index | 7 (ASC#4) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#5) |
| - Available signature End Index | 7 (ASC#5) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#6) |
| - Available signature End Index | 7 (ASC#6) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Available signature Start Index | 0 (ASC#7) |
| - Available signature End Index | 7 (ASC#7) |
| - Assigned Sub-channel Number | ‘1111’B |
| - Persistence scaling factor |  |
| - Persistence scaling factor | 0.9 (for ASC#2) |
| - Persistence scaling factor | 0.9 (for ASC#3) |
| - Persistence scaling factor | 0.9 (for ASC#4) |
| - Persistence scaling factor | 0.9 (for ASC#5) |
| - Persistence scaling factor | 0.9 (for ASC#6) |
| - Persistence scaling factor | 0.9 (for ASC#7) |
| - AC-to-ASC mapping table |  |
| - AC-to-ASC mapping | 6 (AC0-9) |
| - AC-to-ASC mapping | 5 (AC10) |
| - AC-to-ASC mapping | 4 (AC11) |
| - AC-to-ASC mapping | 3 (AC12) |
| - AC-to-ASC mapping | 2 (AC13) |
| - AC-to-ASC mapping | 1 (AC14) |
| - AC-to-ASC mapping | 0 (AC15) |
| - Primary CPICH DL TX power | Reference to clause 6.10 Parameter Set |
| - Constant value | Reference to clause 6.10 Parameter Set |
| - PRACH power offset |  |
| - Power Ramp Step | 3dB |
| - Preamble Retrans Max | 2 |
| - RACH transmission parameters |  |
| - Mmax | 2 |
| - NB01min | 3 slot |
| - NB01max | 10 slot |
| - AICH info |  |
| - Channelisation code | SF-1(SF is reference to clause 6.10 Parameter Set) |
| - STTD indicator | FALSE |
| - AICH transmission timing | 0 |

RRC CONNECTION SETUP (Step 6)

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | Not Present |

8.1.2.2.5	Test requirement

After step 2 the UE shall select either PRACH No.1 or PRACH No.2 and transmit an RRC CONNECTION REQUEST message.

After step 6 the UE shall re-send another RRC CONNECTION REQUEST message and not access any radio resources specified in RRC CONNECTION SETUP message sent in step 6.

After step 9 the UE shall transmit an RRC CONNECTION SETUP COMPLETE message and establish an RRC connection on the DCCH logical channel.

#### 8.1.2.3 	RRC Connection Establishment: Failure (V300 is greater than N300)

8.1.2.3.1	Definition

8.1.2.3.2 	Conformance requirement

1.	The RRC connection establishment is initiated by the UE, which leaves the idle mode and transmits an RRC Connection Request message. This message shall include the IE “Initial UE identity” on the uplink CCCH.

2.	In the case of a failure to establish the RRC connection after (N300+1) attempts, the UE goes back to idle mode.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.3.3 	Test purpose

To confirm that the UE stops retrying to establish the RRC connection if V300 is greater than N300 and goes back to idle mode.

8.1.2.3.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

Before the test starts, SS initializes an internal counter K to 1. The UE transmits an RRC CONNECTION REQUEST message to the SS on the uplink CCCH by an outgoing call operation. SS shall not respond to any RRC CONNECTION REQUEST message, instead the counter K is increased by 1 every time such a message is received. To arrive at the verdict, the SS checks that a total of (N300+1) such messages are received.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | SS initializes counter K to 1and then prompts the operator to make an outgoing call. |
| 2 | ( | RRC CONNECTION REQUEST |  |
| 3 |  |  | SS increments K by 1. |
| 4 |  |  | If K is greater than N300, goes to step 5 else proceed to step 2. |
| 5 |  |  | SS monitor the uplink CCCH for a time period enough for UE to goes back to normal service. The exact amount of time to wait shall be derived from TS related to cell selection. If any uplink transmission is detected, the test fails. |

Specific Message Contents

None

8.1.2.3.5	Test requirement

After step 5, counter K shall be equals to (N300+1) and there shall be no uplink transmission in the monitoring period specified in step 5.

#### 8.1.2.4 	RRC Connection Establishment: Reject (“wait time” is not equal to 0)

8.1.2.4.1	Definition

8.1.2.4.2 	Conformance requirement

1.	The RRC connection establishment is initiated by the UE, which leaves the idle mode and transmits an RRC Connection Request message . This message shall include the IE “Initial UE identity” and is to be sent on the uplink CCCH.

2.	After the UE receives an RRC CONNECTION REJECT message which includes IE “wait time” not set to 0, and neither IE “frequency info” nor IE “system info” is present, the UE shall wait for a period specified in the IE “wait time”. Thereafter re-transmit an RRC CONNECTION REQUEST message to attempt to establish the RRC connection again. However, either IE “frequency info” or IE “system info” is available in the message, the UE shall attempt to perform cell reselection using these information.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.4.3 	Test purpose

To confirm that the UE retries to establish the RRC connection after the “wait time” if the UE receives an RRC CONNECTION REJECT message which includes the IE “wait time” not set to 0.

To confirm that the UE perform a cell reselection when receiving an RRC CONNECTION REJECT message, containing relevant frequency information of the target cell to be re-selected.

8.1.2.4.4 	Method of test

Initial Condition

System Simulator: 2 cells – both cell 1 and cell 2 are active and suitable for camping, but cell 1 is transmitted using a larger power. Cell 1 and cell 2 are being transmitted from different 2 UARFCNs.

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE transmits an RRC CONNECTION REQUEST message to the SS on the uplink CCCH by an outgoing call operation in cell 1. SS rejects the first request by transmitting an RRC CONNECTION REJECT message which indicates a non-zero wait time. In this message, frequency information for cell 2 is available. SS then waits for RRC CONNECTION REQUEST message on the uplink CCCH of cell 2. SS will also monitor the uplink of cell 1 simultaneously to ensure that all transmission activities from cell 1 have ceased. When the UE has successfully camp onto cell 2, it shall send an RRC CONNECTION REQUEST with the same establishment cause as its previous attempt in cell 1. SS responds with an RRC CONNECTION REJECT message, indicating a non-zero “wait time” and omitting the IE “Redirection Info”. The UE shall observe the wait time period indicated. After the wait time has elapsed, the UE shall re-transmit RRC CONNECTION REEQUEST again. Finally, SS transmits an RRC CONNECTION SETUP message to establish an RRC connection with the UE, and the UE replies with an RRC CONNECTION SETUP COMPLETE message and enters CELL_DCH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RRC CONNECTION REQUEST | SS prompts the operator to make an outgoing call in cell 1. |
| 2 | ( | RRC CONNECTION REJECT | This message shall includes the IE “wait time” set to 15 seconds and IE “frequency info” set to the UARFCN of cell 2. |
| 3 |  |  | SS waits for a period of time sufficient for UE to reselect to cell 2. At the same time, it monitors the uplink of cell 1 to make sure that all transmissions have ceased. |
| 4 | ( | RRC CONNECTION REQUEST | UE shall attempt to re-start an RRC connection establishment procedure in cell 2. The establishment cause shall remain unchanged. |
| 5 | ( | RRC CONNECTION REJECT | This message shall includes the IE “wait time” set to 15 seconds, but with IE “Redirection Info” absent. |
| 6 | ( | RRC CONNECTION REQUEST | SS waits until the duration specified in IE “wait time” has elapsed and then listens to the uplink CCCH for a second RRC CONNECTION REQUEST message. |
| 7 | ( | RRC CONNECTION SETUP | SS sends the message to UE, to setup an RRC connection with the UE. |
| 8 |  |  | The UE shall configure the layer 2 and layer 1 in order to access the uplink and downlink DCCH assigned. |
| 9 | ( | RRC CONNECTION SETUP COMPLETE |  |

Specific Message Contents

RRC CONNECTION REQUEST (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity Initial UE Capability Establishment Cause | Must be equal to U-RNTI assigned previously Must be compatible with UE settings in TS25.926 Must be “Originating Call” |

RRC CONNECTION REJECT (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Wait time Redirection Info Frequency Info UARFCN uplink (Nu) UARFCN uplink (Nd) | 15 seconds Set to a different UARFCN from uplink carrier of cell 1 Not present – assuming a duplex distance of 190MHz. |

RRC CONNECTION REQUEST (Step 4 and step 6)

Same requirement as in step 1.

RRC CONNECTION REJECT (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Wait time Redirection Info | 15 seconds Not present |

8.1.2.4.5	Test requirement

After step 3 the UE shall have successfully re-selected to cell 2, using information transmitted in IE “frequency info” of RRC CONNECTION REJECT message. UE shall trigger the start of RRC connection establishment by transmitting RRC CONNECTION REQUEST. The establishment cause shall be similar to the message sent in step 1.

After step 5 the UE shall observe the period specified in IE “wait time” of an RRC CONNECTION REJECT message and not transmit an RRC CONNECTION REQUEST message in this period.

After step 7 the UE shall transmit an RRC CONNECTION SETUP COMPLETE message to SS on uplink DCCH and then establish an RRC connection.

#### 8.1.2.5 	RRC Connection Establishment: Reject (“wait time” is not equal to 0 and V300 is greater than N300)

8.1.2.5.1	Definition

8.1.2.5.2 	Conformance requirement

The RRC connection establishment is initiated by the UE, which leaves the idle mode and transmits an RRC Connection Request message . This message shall include the IE “Initial UE identity” and is to be sent on the uplink CCCH.

After the UE receives an RRC CONNECTION REJECT message which includes IE “wait time” not set to 0, and neither IE “frequency info” nor IE “system info” is present, the UE shall wait for a period specified in the IE “wait time”. Thereafter it re-transmits an RRC CONNECTION REQUEST message to attempt to establish the RRC connection again. In the case of a failure to establish the RRC connection after (N300+1) attempts, the UE goes back to idle mode.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.5.3 	Test purpose

To confirm that the UE retries to establish the RRC connection after the “wait time” if the UE receives an RRC CONNECTION REJECT message which specifies a non-zero IE ”wait time”.

To confirm that the UE stops retrying to establish the RRC connection if V300 is greater than N300 and goes back to idle mode.

8.1.2.5.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

Before the test starts, SS initializes an internal counter K to 0. The UE transmits an RRC CONNECTION REQUEST message to the SS on the uplink CCCH, triggered by an outgoing data call operation. SS rejects all requests by transmitting an RRC CONNECTION REJECT message which indicates a non-zero wait time and the counter K is increased by 1 every time such a message is received. To arrive at the verdict, the SS checks that a total of (N300+1) such messages are received.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | SS initializes counter K to 0 and then prompts the operator to make an outgoing data call. |
| 2 | ( | RRC CONNECTION REQUEST | Shall be sent on CCCH and contain the correct establishment cause. |
| 3 | ( | RRC CONNECTION REJECT | This message includes the IE “wait time” set to 15 seconds. |
| 4 |  |  | SS increments K by 1. |
| 5 |  |  | If K is greater than N300, goes to step 6. Else SS waits for 15 sec before proceeding to step 2. |
| 6 |  |  | SS monitor the uplink CCCH for a time period enough for UE to goes back to normal service. The exact amount of time to wait shall be derived from TS related to cell selection. If any uplink transmission is detected, the test fails. |

Specific Message Contents

RRC CONNECTION REQUEST (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity Initial UE Capability Establishment Cause | Must be equal to U-RNTI assigned previously Must be compatible with UE settings in TR25.926 Must be “Originating Call” |

RRC CONNECTION REJECT (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Wait time | 15 seconds |

8.1.2.5.5	Test requirement

After step 6, counter K shall be equals to (N300+1) and there shall be no uplink transmission in the monitoring period specified in step 6.

#### 8.1.2.6 	RRC Connection Establishment: Reject (“wait time” is set to 0)

8.1.2.6.1	Definition

8.1.2.6.2 	Conformance requirement

1.	The RRC connection establishment is initiated by the UE, which leaves the idle mode and transmits an RRC Connection Request message on the uplink CCCH.

2.	In the case of a failure to establish the RRC connection by the reception of a RRC CONNECTION REJECT message which contains IE “wait time” equals to 0, the UE shall go back to idle mode immediately.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.6.3 	Test purpose

To confirm that the UE goes back to idle mode, if the SS transmits an RRC CONNECTION REJECT message which includes IE “wait time” set to 0. To confirm that the UE ignores an RRC CONNECT REJECT message not addressed to it. To confirm that the UE is capable of handling an erroneous RRC CONNECTION REJECT message correctly.

8.1.2.6.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE transmits an RRC CONNECTION REQUEST message to the SS on the uplink CCCH by making an outgoing call. After the SS receives this message, it transmits an RRC CONNECTION REJECT message which is not addressed to the UE. The UE shall disregard this message and proceed to re-transmit RRC CONNECTION REQUES message upon T300 timer expiry. SS answers the second RRC CONNECTION REQUEST message by transmitting an RRC CONNECTION REJECT message with IE “wait time” set to 15 seconds, but without the mandatory IE “rejection cause”. The UE shall continue to send the third RRC CONNECTION REQUEST message after a 15 second lapse. Next, the SS sends a legal RRC CONNECTION REJECT message which is expected to cause the UE to move to idle mode spontaneously. To confirm that finally the UE goes back to idle mode immediately after receiving the reject message, SS shall monitor the uplink CCCH for the next 60 second and verify that there is no further transmission in the uplink direction.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RRC CONNECTION REQUEST | Test operator is prompted to make an out-going call, |
| 2 | ( | RRC CONNECTION REJECT | IE “Initial UE identity” contains an identity different from any of the UE identities available. |
| 3 | ( | RRC CONNECTION REQUEST | UE shall continue to send this message after T300 time-out. |
| 4 | ( | RRC CONNECTION REJECT | IE “Reject Cause” is omitted, IE “wait time” is set to 15 seconds (maximum). |
| 5 | ( | RRC CONNECTION REQUEST | UE shall continue to send this message after the expiry of “wait time” IE indicated in RRC CONNECTION REJECT message in step 4. |
| 6 | ( | RRC CONNECTION REJECT | IE “wait time” is set to 0. |
| 7 |  |  | The UE goes back to idle mode.. |

Specific Message Contents

RRC CONNECTION REQUEST (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity Initial UE Capability Establishment Cause Protocol Error Indicator Measured Results on RACH | Checked to see if it is set to IMSI stored in the test USIM card. Checked to see if it is compatible to ICS/IXIT statements. Checked to see if set to one of the supported originating call types Checked to see if set to “FALSE” Checked to see if it is absent |

RRC CONNECTION REJECT (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity IMSI Wait time Redirection Info | Set to an arbitrary octet string of length 7 bytes, which is different from the IMSI stored in USIM. 15 seconds Not present |

RRC CONNECTION REQUEST (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity Initial UE Capability Establishment Cause Protocol Error Indicator Measured Results on RACH | Checked to see if it is set to IMSI stored in the test USIM card. Checked to see if it is compatible to ICS/IXIT statements. Checked to see if set to one of the supported originating call types Checked to see if set to “TRUE” Checked to see if it is absent |

RRC CONNECTION REJECT (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity IMSI Reject Cause Wait time Redirection Info | Set to the identical octet string as the IMSI stored in the USIM card. Not Present 15 seconds (Maximum) Not Present |

RRC CONNECTION REQUEST (Step 5)

The contents of this message must be identical to those specified for the message in step 3.

RRC CONNECTION REJECT (Step 6)

| Information Element | Value/remark |
| --- | --- |
| Initial UE Identity IMSI Reject Cause Wait time Redirection Info | Set to the identical octet string as the IMSI stored in the USIM card. Congestion 0 second Not present |

Note: 	T300 is set to 5 seconds and N300 is arbitrarily selected from 4 to 8 in SYSTEM INFORMATION BLOCK TYPE 1 message on BCCH.

8.1.2.6.5	Test requirement

After step 2 the UE shall transmit an RRC CONNECTION REQUEST message on uplink CCCH.

After step 4 the UE shall re-transmit an RRC CONNECTION REQUEST message on the uplink CCCH 15 seconds after the transmission of the second downlink RRC CONNECTION REJECT message. In this message, the “protocol error indicator” IE shall be set to “TRUE”.

After step 6 the UE shall stop sending an RRC CONNECTION REQUEST message, go back to idle mode immediately and not transmit in the uplink direction again.

#### 8.1.2.7	RRC Connection Establishment in CELL_FACH state: Success

8.1.2.7.1	Definition

8.1.2.7.2 	Conformance requirement

During the RRC connection establishment, the UTRAN might assign common physical resource to the UE using an RRC CONNECTION SETUP message. When no information about the physical channels accessible is available from the message, the UE shall utilize the PRACH and S-CCPCH information transmitted on the BCCH and then enter the CELL_FACH. Subsequently, the UE shall establish the required signalling links with the UTRAN using common physical resources.

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.7.3	Test Purpose

To confirm that the UE is able to enter CELL_FACH state and setup signalling links using common physical channels.

8.1.2.7.4		Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE transmits an RRC CONNECTION REQUEST message to the SS on the uplink CCCH by attempting to make an outgoing call. After the SS receives this message, it assigns the necessary radio resources and U-RNTI to be used by the UE, and then transmits an RRC CONNECTION SETUP message to the UE within timer T300. SS then waits for the UE to transmit an RRC CONNECTION SETUP COMPLETE message on the DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RRC CONNECTION REQUEST | Test operator is requested to make an outgoing call. The UE shall transmit this message, indicating the correct establishment cause. |
| 2 | ( | RRC CONNECTION SETUP | SS omits both IE “Uplink DPCH Info” and IE “Downlink DPCH Info” from the message. |
| 3 |  |  | The UE shall configure the layer 2 and layer 1. |
| 4 | ( | RRC CONNECTION SETUP COMPLETE | UE shall send this message on the DCCH, carried by the assigned PRACH resources. |

Specific Message Content

RRC CONNECTION REQUEST

| Information Element | Value/remark |
| --- | --- |
| Establishment Cause | Originating Interactive Call |

RRC CONNECTION SETUP

For this message, the contents of the message to be used are basically identical to the message sub-type entitled “RRC CONNECTION SETUP message (Transition to CELL_FACH)” found in the default message content part. The following exceptions are applicable in this test:

| Information Element | Value/remark |
| --- | --- |
| Uplink DPCH Info | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information per radio link list | Not Present |

RRC CONNECTION SETUP COMPLETE

| Information Element | Value/remark |
| --- | --- |
| UE Radio Access Capability | Checked to see if compatible with the stated capability in PIXIT/PICS statements. |

8.1.2.7.5	Test requirements

After step 3 the UE shall establish the RRC connection, and transmit RRC CONNECTION SETUP COMPLETE message on the DCCH using PRACH physical resource specified in system information block messages.

#### 8.1.2.8 	RRC Connection Establishment: Invalid system information message reception

8.1.2.8.1	Definition

8.1.2.8.2	Conformance requirement

The UE shall ignore the message and shall not select the cell, if the associated a SYSTEM INFORMATION message on the BCCH which includes an invalid value in the mandatory information element which in the master information block is broadcasting.

Reference

3GPP TS 25.331 clause 8.1.1 clause 16

8.1.2.8.3	Test purpose

To confirm that the UE does not select the cell if the transmitted SYSTEM INFORMATION message on the BCCH which includes an invalid value in the information element in the master information block is broadcasting

8.1.2.8.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: Power off (state 1) as specified in clause 7.4 of TS 34.108

Test Procedure

The SS broadcasts the SYSEM INFORMATION message on the BCCH which includes the PLMN Type information element having an invalid value in the master information block. When the UE is supplied the power, it finds that the SYSTEM INFORMATION message on the BCCH includes the unknown value in the mandatory information element and the UE shall ignore this message. When an outgoing call is attempted,  the test operator shall be informed that the UE is in a “No Service” state. The UE shall not transmit an RRC CONNECTION REQUEST message on the uplink CCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | SYSTEM INFORMATION | The SS broadcasts the SYSTEM INFORMATION message on the BCCH which includes an invalid value in the master information block. |
| 2 |  |  | The UE is supplied the power. |
| 3 |  |  | SS waits for 1 minute and then asks the test operator to attempt to make an outgoing call. |
| 4 |  |  | SS checks that no uplink transmission on CCCH is detected. |

Specific Message Contents

SYSTEM INFORMATION (master information block)

The contents of a SYSTEM INFORMATION message in this test case is identical to the corresponding message found in the default contents of layer 3 messages for RRC tests, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Supported PLMN Types | invalid value which is not defined |

8.1.2.8.5	Test requirement

After step 3 the UE shall not transmit an RRC CONNECTION REQUEST message on the uplink CCCH.

#### 8.1.2.9	RRC Connection Establishment: Success after Physical channel failure

8.1.2.9.1	Definition

8.1.2.9.2 	Conformance requirement

1.	The RRC connection establishment is initiated by the UE, which leaves the idle mode. The UE shall transmit an RRC Connection Request message which includes the IE “Initial UE identity”. This message shall be sent on the uplink CCCH.

2.	In the case of a failure to establish the RRC connection at the physical channel failure after the UE receives an RRC CONNECTION SETUP message ,the UE retries to establish the RRC connection until V300 is greater than N300

Reference

3GPP TS 25.331 clause 8.1.3

8.1.2.9.3 	Test purpose

To confirm that the UE retries to establish the RRC connection until V300 is greater than N300 for the physical channel failure as the SS does not configure the physical channel which is specified in the transmitted RRC CONNECTION SETUP message.

8.1.2.9.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: Idle state (state 2 or state 3 or state 7 ) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

Before the test starts, an internal counter K in SS is initialised to a value = 1. Following this, the UE shall transmit an RRC CONNECTION REQUEST message to the SS on the uplink CCCH, after the operator attempts to make an outgoing call. SS transmits an RRC CONNECTION SETUP message to make the UE configure the physical channel in order to communicate on the DCCH but SS does not configure the physical channel. Then the UE detects the physical channel failure and transmits an RRC CONNECTION REQUEST message. SS increments K every time such a message is received. This cycle is repeated until K reaches N300. When K is equal to N300, the SS transmits the RRC CONNECTION SETUP message and configures the physical channel. The UE shall detect “in-sync” from physical layer and then acknowledge the establishment of RRC connection by sending the RRC CONNECTION SETUP COMPLETE message on uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | SS initialises counter K to 1. Operator is asked to make an outgoing call and SS starts to wait for RRC CONNECTION REQUEST on uplink CCCH. |
| 2 | ( | RRC CONNECTION REQUEST |  |
| 3 |  |  | SS checks to see if K is equal to N300+1. If so, goes to step 6. Else, continues to execute step 4. |
| 4 | ( | RRC CONNECTION SETUP | See the clause 9 in TS 34.108 on default message content for RRC. But SS does not configure the physical channel. |
| 5 |  |  | SS increments K. The next step is step 2. |
| 6 | ( | RRC CONNECTION SETUP | See the clause 9 in TS 34.108 on default message content for RRC. SS configures the physical channel. |
| 7 |  |  | The UE configures the layer 1 and layer 2. |
| 8 | ( | RRC CONNECTION SETUP COMPLETE |  |

Specific Message Contents

None

8.1.2.9.5	Test requirement

After step 4 the UE shall re-send RRC CONNECTION REQUEST message.

After step 8 the UE shall transmit an RRC CONNECTION SETUP COMPLETE message and establish an RRC connection.

### 8.1.3	RRC Connection Release

#### 8.1.3.1	RRC Connection Release in CELL_DCH state: Success

8.1.3.1.1	Definition

8.1.3.1.2	Conformance requirement

In case of an RRC connection release from CELL_DCH state, the UTRAN transmits an RRC CONNECTION RELEASE message to the UE using unacknowledged mode on the DCCH. The UE then responds by transmitting an RRC CONNECTION RELEASE COMPLETE message using unacknowledged mode to UTRAN for N308 times, each time at the expiry of T308 timer. Then the UE leaves the RRC connected mode and initiates release of the layer 2 signalling link. The RRC Connection Release procedure ends when all UE dedicated resources (such as radio resources and radio access bearers) associated with the RRC connection are released and the UE returns to idle mode.

Reference

3GPP TS 25.331 clause 8.1.4

8.1.3.1.3	Test purpose

To confirm that the UE releases the L2 signalling link and dedicated resources and goes back to the idle state after it receives an RRC CONNECTION RELEASE message from the SS and transmits an RRC CONNECTON RELEASE COMPLETE message to the SS for N308 times at the interval specified by the value of T308 timer.

8.1.3.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH state (state 6-1 or state 6-3) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to the CELL_DCH state by prompting the operator to initiate an outgoing call. After the DCCH is established, SS transmits an RRC CONNECTION RELEASE message to the UE to disconnect the connection. SS then waits for the UE to transmit an RRC CONNECTION RELEASE COMPLETE message using unacknowledged mode. SS checks to see if P such messages has been received at each expiry of T308 timer. P is equal to the value of IE “Number of RRC Message Transmissions” in an RRC CONNECTION RELEASE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_DCH state after a successful RRC connection establishment by virtue of the operator making an outgoing call. |
| 2 | ( | RRC CONNECTION RELEASE | SS disconnect the connection established. The value in IE “Number of RRC Message Transmissions” is arbitrarily chosen from 4 to 8 and denoted by P. |
| 3 | ( | RRC CONNECTION RELEASE COMPLETE | SS waits for the arrival of N308 such message at the expiry of each T308 timer, using unacknowledged mode. |
| 4 |  |  | The UE releases L2 signalling link and dedicated resources. Then the UE goes to idle mode. |

Specific Message Content

RRC CONNECTION RELEASE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Number of RRC Message Transmission | Arbitrarily chosen between 4 and 8 |

8.1.3.1.5	Test requirement

After step 2 the UE shall start to transmit P times RRC CONNECTION RELEASE COMPLETE messages at the expiry of each T308 timer.

After step 3 the UE shall initiate the release L2 signalling link and dedicated resources, then it shall go to idle mode.

#### 8.1.3.2	RRC Connection Release using on DCCH in CELL_FACH state: Success

8.1.3.2.1	Definition

8.1.3.2.2	Conformance requirement

In CELL_FACH state, the RRC layer entity in the network may issue an RRC CONNECTION RELEASE message using unacknowledged mode on the DCCH. Upon the reception of this message, the UE transmits an RRC CONNECTION RELEASE COMPLETE message using acknowledged mode to UTRAN on the DCCH and goes back to idle mode after it receives an RLC confirmation from the UTRAN.

Reference

3GPP TS 25.331 clause 8.1.4

8.1.3.2.3	Test purpose

To confirm that the UE releases the L2 signalling link and resources and goes back to the idle state after it receives an RRC CONNECTION RELEASE message on downlink DCCH from the SS. It shall transmit an RRC CONNECTON RELEASE COMPLETE message using acknowledged mode on uplink DCCH to the SS.

8.1.3.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to an initial state of CELL_FACH. After the successful establishment of the RRC connection, the SS transmits an RRC CONNECTION RELEASE message to the UE to disconnect the radio link. When the UE receives this message the UE transmits an RRC CONNECTION RELEASE COMPLETE message using acknowledged mode to the SS. Finally, SS checks that the UE performs proper release of all radio resources and then goes back to idle mode.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to the CELL_FACH state. |
| 2 | ( | RRC CONNECTION RELEASE | SS sends this message using unacknowledged mode RLC operations on the uplink DCCH. |
| 3 | ( | RRC CONNECTION RELEASE COMPLETE | The UE transmits this message using acknowledged mode. |
| 4 |  |  | The UE releases L2 signalling link and radio resources. Then the UE goes to idle mode. |

Specific Message Contents

None.

8.1.3.2.5	Test requirement

After step 2 the UE shall transmit an RRC CONNECTION RELEASE COMPLETE message using acknowledged mode then it shall receive a response for this message from the SS-RLC.

After step 3 the UE shall release its L2 signalling link and radio resources, then it shall go back to idle mode.

#### 8.1.3.3	RRC Connection Release using on CCCH in CELL_FACH state: Success

8.1.3.3.1	Definition

8.1.3.3.2	Conformance requirement

In CELL_FACH state, the RRC layer entity in the network may issue an RRC CONNECTION RELEASE message using unacknowledged mode on the CCCH. Upon the reception of this message, the UE shall release the RRC connection immediately, without replying with a RRC CONNECTION RELEASE COMPLETE message on the uplink.

Reference

3GPP TS 25.331 clause 8.1.4

8.1.3.3.3	Test purpose

To confirm that the UE releases all its radio resources upon the reception of a RRC CONNECTION RELEASE message on the downlink CCCH, without transmitting RRC CONNECTION RELEASE COMPLETE message on the uplink.

8.1.3.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to an initial state of CELL_FACH. After the successful establishment of the RRC connection, SS transmits RRC CONNECTION RELEASE message on the downlink CCCH. The UE shall terminate the RRC connection and release all radio resources allocated to it. SS monitors the uplink DCCH and CCCH to verify that no transmission is detected.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to the CELL_FACH state. |
| 2 | ( | RRC CONNECTION RELEASE | SS transmits this message with the contents identical to that found in TS 34.108 clause 9 on downlink CCCH. |
| 3 |  |  | SS waits for a period equivalent to (N308+1) times T308 timer expiry. The UE shall not send any response message on uplink direction during this period. It shall release the radio resources allocated and return to idle mode. |

Specific Message Contents

None.

8.1.3.3.5	Test requirement

After step 2 the UE shall release all its radio resources, return to idle mode, without transmitting RRC CONNECTION RELEASE COMPLETE message on the uplink direction.

#### 8.1.3.4	RRC Connection Release in CELL_FACH state: Failure

8.1.3.4.1	Definition

8.1.3.4.2	Conformance requirement

In case of RRC connection release from CELL_FACH state, the RRC layer entity in the network issues an RRC CONNECTION RELEASE message using unacknowledged mode on the DCCH. When the UE does not succeed to transmit the RRC CONNECTION RELEASE COMPLETE message using acknowledged mode, it shall release all its radio resources, enter idle mode and the procedure ends on the UE side.

Reference

3GPP TS 25.331 clause 8.1.4

8.1.3.4.3	Test purpose

To confirm that the UE releases all its radio resources and enters idle mode when the UE does not succeed in transmitting the RRC CONNECTION RELEASE COMPLETE message using acknowledged mode to the SS (i.e. the UE-RLC cannot receive acknowledgement for the transmission of the RRC CONNECTION RELEASE COMPLETE message from SS.).

8.1.3.4.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

At the start of the test, the UE is brought to CELL_FACH state. When the RRC connection has been established, the SS transmits an RRC CONNECTION RELEASE message to the UE to disconnect the radio link. When the UE receives this message the UE transmits an RRC CONNECTION RELEASE COMPLETE message using acknowledged mode to the SS. The SS ignores the message and does not transmit a STATUS PDU of RLC for this message. SS checks to see that UE continues to release all its radio resources and then enters idle mode.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought into CELL_FACH state by asking the operator to perform an outgoing call attempt. clause |
| 2 | ( | RRC CONNECTION RELEASE | SS ask to disconnect the radio link |
| 3 | ( | RRC CONNECTION RELEASE COMPLETE | The UE transmits this message using acknowledged mode. The SS ignores this message and shall not transmit a STATUS PDU of RLC for this message. |
| 4 |  |  | SS checks to make sure that UE releases its all radio resources and enter idle mode. |

Specific Message Contents

None

8.1.3.4.5	Test requirement

After step 3 the UE shall release its L2 signalling link and radio resources then it shall go to idle mode.

#### 8.1.3.5	RRC Connection Release in CELL_FACH state: Invalid message

8.1.3.5.1	Definition

8.1.3.5.2	Conformance requirement

In CELL_FACH state, the RRC layer entity in UTRAN may issue an RRC CONNECTION RELEASE message using unacknowledged mode on the DCCH. If an invalid RRC CONNECTION RELEASE message is received by the UE, the UE shall activate the appropriate error-handling mechanism and report the error to the UTRAN. After this, the UE shall release the RRC connection.

Reference

3GPP TS 25.331 clause 8.1.4

8.1.3.5.3	Test purpose

When the UE receives an invalid RRC CONNECTION RELEASE message on the downlink DCCH, it shall transmit an RRC CONNECTON RELEASE COMPLETE message that includes the appropriate error cause on the uplink DCCH. Thereafter, it shall release the RRC connection.

8.1.3.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to an initial state of CELL_FACH. SS transmits an RRC CONNECTION RELEASE message on the DCCH to request to disconnect the RRC connection. However, the message contains an invalid value in the IE ”Release cause”. As a result, the UE shall transmit an RRC CONNECTION RELEASE COMPLETE message on the uplink DCCH, which includes the IE “Error indication”. This IE shall contain “Failure cause” IE which is set to “Protocol error” and “Protocol error information” IE which is set to “Information element value not comprehended”. The UE shall release the RRC connection and go back to idle mode after transmitting the RRC CONNECTION RELEASE COMPLETE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to the CELL_FACH state. |
| 2 | ( | RRC CONNECTION RELEASE | See specific message contents for this message |
| 3 | ( | RRC CONNECTION RELEASE COMPLETE | The IE “Protocol error cause” found in IE “Protocol error information” shall be set to “Information element value not comprehended”. |
| 4 |  |  | The UE shall release the signalling link and radio resources, and then return to idle mode. |

Specific Message Contents

RRC CONNECTION RELEASE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Release cause | invalid value |

RRC CONNECTION RELEASE COMPLETE

| Information Element | Value/remark |
| --- | --- |
| Error Indication Failure cause Protocol error information Protocol error cause | Protocol error Information element value not comprehended |

8.1.3.5.5	Test requirement

After step2 the UE shall transmit an RRC CONNECTION RELEASE COMPLETE message which includes the appropriate cause values in IE “Error Indication”.

After step3 the UE shall release its L2 signalling link and radio resources, then it shall go back to idle mode.

| 8.1.4 Void |  |  |  |
| --- | --- | --- | --- |

### 8.1.5	UE capability

#### 8.1.5.1	UE Capability in CELL_DCH state: Success

8.1.5.1.1		Definition

8.1.5.1.2	Conformance requirement

1.	The UE CAPABILITY ENQUIRY message is sent by the UTRAN to request the UE to transmit its capability information related to any radio access network that is supported by the UE or if the UTRAN needs an update of the UE’s UMTS capability information or of its inter-system classmark.

When the UE receives a UE CAPABILITY ENQUIRY message, the UE transmits a UE CAPABILITY INFORMATION message on the uplink DCCH. Then the UTRAN transmits a UE CAPABILITY INFORMATION CONFIRM message.

If during the execution of UE capability update procedure, an invalid UE CAPABILITY INFORMATION CONFIRM is received, the UE shall respond with RRC STATUS message and decide whether to re-transmit UE CAPABILITY INFORMATION message by comparing its internal counter against N304.

Reference

3GPP TS 25.331 clause 8.1.6, 8.1.7

8.1.5.1.3	Test purpose

To confirm that the UE transmits a UE CAPABILITY INFORMATION message after it receives a UE CAPABILITY ENQUIRY message from the SS. To confirm that the UE indicate an invalid message reception when erroneous downlink UE CAPABILITY ENQUIRY and UE CAPABILITY INFORMATION CONFIRM messages are received. The UE shall transmit RRC STATUS message with the correct error cause value to SS.

8.1.5.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH state (state 6-1 or state 6-3) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to the CELL_DCH state after a successful outgoing call attempt. The SS transmits an erroneous UE CAPABILITY ENQUIRY message containing invalid value in the IE “Capability update requirement” as a correct message. After receiving such a message, the UE should report the error using RRC STATUS message with the appropriate error cause specified. Then SS transmits a UE CAPABILITY ENQUIRY message which includes the IE “Capability update requirement”, the UE receives this message and transmits a UE CAPABILITY INFORMATION message on the uplink DCCH which includes the “Inter-system message”IE. The SS transmits a UE CAPABILITY INFORMATION CONFIRM message to the UE to complete the test. Then SS initiates another UE capability update procedure by transmitting the same UE CAPABILITY ENQUIRY using as in step 4. The UE shall reply with a UE CAPABILITY INFORMATION message on the uplink DCCH. When SS receives this message, it transmit an erroneous UE CAPABILITY INFORMATION CONFIRM message. The content of this message is lack of a mandatory IE. The UE shall detect a protocol error and send RRC STATUS message to report this event. After receiving RLC acknowledgement for this message, the UE shall re-transmit UE CAPABILITY INFORMATION message on the uplink DCCH. SS completes this test by an error-free UE CAPABILITY INFORMATION CONFIRM message similar to the message sent in step 6.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_DCH state after an outgoing call has been established successfully. |
| 2 | ( | UE CAPABILITY ENQUIRY | See specific message contents for this message |
| 3 | ( | RRC STATUS | The IE “Protocol error cause” found in IE “Protocol error information” should be set to “Information element value not comprehended” |
| 4 | ( | UE CAPABILITY ENQUIRY | Use default message. |
| 5 | ( | UE CAPABILITY INFORMATION | The message shall includethe IE “Inter-system message”, which carries the GSM classmark information requested. |
| 6 | ( | UE CAPABILITY INFORMATION CONFIRM | Use default message. |
| 7 | ( | UE CAPABILITY ENQUIRY | Same as in step 4. |
| 8 | ( | UE CAPABILITY INFORMATION | Shall be the same message content as in step 5. |
| 9 | ( | UE CAPABILITY INFORMATION CONFIRM | See specific message contents for this message |
| 10 | ( | RRC STATUS | UE shall detect an error and then transmit this message. |
| 11 | ( | UE CAPABILITY INFORMATION | UE shall re-transmit this message after receiving acknowledgement from the SS for RRC STATUS message. |
| 12 | ( | UE CAPABILITY INFORMATION CONFIRM | SS sends an error-free message to acknowledge the receipt of the uplink message. |

Specific Message Contents

UE CAPABILITY ENQUIRY (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Capability update requirement - UE radio access FDD capability update requirement - UE radio access FDD capability update requirement - System specific capability update requirement list - System specific capability update requirement | TRUE FALSE invalid value |

RRC STATUS (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Checked to see if set to “Information element not comprehended” |

UE CAPABILITY INFORMATION CONFIRM (Step 9)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier | Not Present |

RRC STATUS (Step 10)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Checked to see if set to “ASN.1 violation or encoding error” |

8.1.5.1.5	Test requirement

After step 2, the UE shall transmit a RRC STATUS message on the uplink DCCH, reporting the error with protocol error cause set to “Information element value not comprehended”.

After step 4 the UE shall transmit a UE CAPABILITY INFORMATION message on the uplink DCCH to respond to the UE CAPABILITY ENQUIRY message.

After step 9, the UE shall transmit a RRC STATUS message on the uplink DCCH. The protocol error cause shall be set to “ASN.1 violation or encoding error”.

After step 10, the UE shall re-transmit the UE CAPABILITY INFORMATION message with a similar content as in step 8.

#### 8.1.5.2	UE Capability in CELL_DCH state: Success after T304 timeout

8.1.5.2.1	Definition

8.1.5.2.2	Conformance requirement

1.	The UE CAPABILITY ENQUIRY message is sent by the UTRAN to request the UE to transmit its capability information related to any radio access network that is supported by the UE, if the UTRAN needs an update of the UE’s UMTS capability information or of its inter-system classmark.

2. 	After the UE receives a UE CAPABILITY ENQUIRY message, it transmits a UE CAPABILITY INFORMATION message on the uplink DCCH. If it fails to receive a UE CAPABILITY INFORMATION CONFIRM message, the UE re-transmits another UE CAPABILITY INFORMATION message until V304 is greater than N304.

Reference

3GPP TS 25.331 clause 8.1.6, 7

8.1.5.2.3	Test purpose

To confirm that the UE re-transmits a UE CAPABILITY INFORMATION message until V304 is greater than N304, after the expiry of timer T304 when the UE cannot receive a UE CAPABILITY INFORMATION CONFIRM message in response to a UE CAPABILITY INFORMATION message.

8.1.5.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH state (state 6-1 or state 6-3) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to CELL_DCH state. When the SS transmits a UE CACAPABILITY ENQUIRY message which includes the “Capability update requirement” IE, the UE shall reply with a UE CAPABILITY INFORMATION message on the uplink DCCH which includes the “Inter-system message” IE. The SS does not transmits a UE CAPABILITY INFORMATION CONFIRM message to the UE, resulting in the T304 timer to expire. SS shall observe that the UE attempts to transmit a UE CAPABILITY INFORMATION message again. The UE shall re-transmit N304 times, and SS transmits a UE CAPABILITY INFORMATION CONFIRM message to answer the last request and completes this test procedure.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_DCH state. SS sets internal counter K =1 |
| 2 | ( | UE CAPABILITY ENQUIRY | Including the “Capability update requirement”IE. |
| 3 | ( | UE CAPABILITY INFORMATION | Including the “Inter-system message” IE, which indicated the radio access network supported by the UE. |
| 4 |  |  | If K is greater to N304, then proceed to step 6. |
| 5 |  |  | The SS does not transmit a response and wait for T304 timer to expire. K=K+1 and goes to step 3. |
| 6 | ( | UE CAPABILITY INFORMATION CONFIRM | Use default message contents |

Specific Message Contents

None

8.1.5.2.5	Test requirement

After step 3 the UE shall re-transmits a UE CAPABILITY INFORMATION message on the uplink DCCH, after each expiry of timer T304. The UE CAPABILITY INFORMATION message shall contain IE “UE radio access capability” indicating the settings found in PIC/PIXIT statements. IE “UE system specific capability” shall carry relevant GSM classmark information. After (N304+1) re-transmissions, the UE shall receive a UE CAPABILITY INFORMATION CONFIRM message.

#### 8.1.5.3	UE Capability in CELL_DCH state: Failure (After N304 re-transmissions)

8.1.5.3.1		Definition

8.1.5.3.2	Conformance requirement

1.	The UE CAPABILITY ENQUIRY message is sent by the UTRAN to request the UE to transmit its capability information related to any radio access network that is supported by the UE if the UTRAN needs an update of the UE’s UMTS capability information or of its inter-system classmark.

2.	In the case of a failure to transmit a UE CAPABILITY INFORMATION in excess of N304 times, the UE initiates the RRC connection re-establishment procedure.

Reference

3GPP TS 25.331 clause 8.1.6, 8.1.7

8.1.5.3.3	Test purpose

To confirm that the UE stops retrying to transmit a UE CAPABILITY INFORMATION message if V304 is greater than N304. It then initiates the RRC re-establishment procedure.

8.1.5.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH state (state 6-1 or state 6-3) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to CELL_DCH state. When the SS transmits a UE CAPABILITY ENQUIRY message which includes the “Capability update requirement” IE, the UE receives this message and transmits a UE CAPABILITY INFORMATION message on the uplink DCCH which includes the “Inter-system message” IE. The SS does not respond with a UE CAPABILITY INFORMATION CONFIRM message but keeps a count on the number of messages received When the T304 timer expires, the UE shall transmit a UE CAPABILITY INFORMATION message again. After sending (N304+1) messages, the UE shall stop sending UE CAPABILITY INFORMATION messages and initiates the RRC connection re-establishment procedure. This is verified in SS by the reception of RRC CONNECTION RE-ESTABLISHMENT REQUEST. SS allows UE to return to “connected state” by issuing RRC CONNECTION RE-ESTABLISHMENT message on the downlink CCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE starts from CELL_DCH state. SS sets counter K to 1 |
| 2 | ( | UE CAPABILITY ENQUIRY | Including the “Capability update requirement” IE. |
| 3 | ( | UE CAPABILITY INFORMATION | Including the “Inter-system message” IE. |
| 4 |  |  | The SS does not transmit a response and allows T304 timer to expire. SS increments counter K If K is greater than N304, proceeds to step 5 else returns to 3. |
| 5 | ( | RRC CONNECTION RE-ESTABLISHMENT REQUEST | The UE assumes that radio link failure has occurred and transmits this message which includes the IE “U-RNTI” containing the U-RNTI allocated to the UE earlier. |
| 6 | ( | RRC CONNECTION RE-ESTABLISHMENT | Including the new TFCS according to the new transport channel. |
| 7 | ( | RRC CONNECTION RE-ESTABLISHMENT COMPLETE |  |

Specific Message Contents

None

8.1.5.3.5	Test requirement

After step 3 the UE shall transmit a UE CAPABILITY INFORMATION message on the uplink DCCH. The UE shall re-transmit this message for N304 times. Thereafter, the UE shall initiate the RRC re-establishment procedure by sending the message RRC CONNECTION RE-ESTALISHMENT REQUEST.

After step 7 the UE shall have a new RRC connection, using the new transport format dictated in the RRC CONNECTION RE-ESTABLISHMENT message.

#### 8.1.5.4	UE Capability in CELL_FACH state: Success

8.1.5.4.1		Definition

8.1.5.4.2 	Conformance requirement

1.	The UE CAPABILITY ENQUIRY message is sent by the UTRAN to request the UE to transmit its capability information related to any radio access network(s) supported by the UE. UTRAN initiates this procedure when it needs an update of the UE’s UMTS capability information or of its inter-system classmark.

2.	When the UE receives a UE CAPABILITY ENQUIRY message, the UE shall transmit a UE CAPABILITY INFORMATION message on the uplink DCCH.

3.	If during the execution of UE capability update procedure, an invalid UE CAPABILITY INFORMATION CONFIRM is received, the UE shall respond with RRC STATUS message and decide whether to re-transmit UE CAPABILITY INFORMATION message by comparing its internal counter against N304.

Reference

3GPP TS 25.331 clause 8.1.6, 8.1.7

8.1.5.4.3 	Test purpose

To confirm that the UE transmits an UE CAPABILITY INFORMATION message after it receives a UE CAPABILITY ENQUIRY message from the SS. To confirm that the UE indicates an invalid message reception when erroneous downlink UE CAPABILITY ENQUIRY and UE CAPABILITY INFORMATION CONFIRM messages are received. The UE shall transmit RRC STATUS message with the correct error cause value to SS.

8.1.5.4.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to the CELL_FACH state after a successful outgoing call attempt. The SS transmits an erroneous UE CAPABILITY ENQUIRY message containing invalid value in the IE ”Capability update requirement”. After receiving such a message, the UE shall report an error using RRC STATUS message with the appropriate error cause specified. Then SS transmits a UE CAPABILITY ENQUIRY message which includes the IE “Capability update requirement” as a correct message, the UE receives this message and transmits a UE CAPABILITY INFORMATION message on the uplink DCCH, which includes the IE “Inter-system message”. The SS transmits a UE CAPABILITY INFORMATION CONFIRM message to the UE to complete the UE capability enquiry procedure. Then SS initiates another UE capability enquiry procedure by transmitting the same UE CAPABILITY ENQUIRY message as in step 4. The UE shall reply with a UE CAPABILITY INFORMATION message on the uplink DCCH. When SS receives this message, it transmits an erroneous UE CAPABILITY INFORMATION CONFIRM message. The content of this message is lack of a mandatory IE. The UE shall detect a protocol error and send RRC STATUS message to report this event. After receiving the RLC layer acknowledgement PDU for this message, the UE shall re-transmit UE CAPABILITY INFORMATION message on the uplink DCCH. SS completes this test by sending an error-free UE CAPABILITY INFORMATION CONFIRM message similar to the message sent in step 6.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_FACH state after an outgoing call has been established successfully. |
| 2 | ( | UE CAPABILITY ENQUIRY | See specific message contents for this message |
| 3 | ( | RRC STATUS | The IE “Protocol error cause” found in IE “Protocol error information” should be set to “Information element value not comprehended” |
| 4 | ( | UE CAPABILITY ENQUIRY | Use default message. |
| 5 | ( | UE CAPABILITY INFORMATION | The message shall include the IE “Inter-system message”, which carries the GSM classmark information requested. |
| 6 | ( | UE CAPABILITY INFORMATION CONFIRM | Use default message. |
| 7 | ( | UE CAPABILITY ENQUIRY | Same as in step 4. |
| 8 | ( | UE CAPABILITY INFORMATION | The message content shall be the same as in step 5. |
| 9 | ( | UE CAPABILITY INFORMATION CONFIRM | See specific message contents for this message |
| 10 | ( | RRC STATUS | UE shall detect an error and then transmit this message on uplink DCCH. |
| 11 | ( | UE CAPABILITY INFORMATION | UE shall re-transmit this message after receiving the RLC acknowledgement PDU for RRC STATUS message from SS. |
| 12 | ( | UE CAPABILITY INFORMATION CONFIRM | SS sends an error-free message to acknowledge the receipt of the uplink message. |

Specific Message Contents

UE CAPABILITY ENQUIRY (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Capability update requirement - UE radio access FDD capability update requirement - UE radio access FDD capability update requirement - System specific capability update requirement list - System specific capability update requirement | TRUE FALSE invalid value |

RRC STATUS (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Checked to see if set to “Information element not comprehended” |

UE CAPABILITY INFORMATION CONFIRM (Step 9)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier | Not Present |

RRC STATUS (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Checked to see if set to “ASN.1 violation or encoding error” |

8.1.5.4.5	Test requirement

After step 2, the UE shall transmit a RRC STATUS message on the uplink DCCH, reporting the error with protocol error cause set to “Information element value not comprehended”.

After step 4 the UE shall transmit a UE CAPABILITY INFORMATION message on the uplink DCCH to respond to the downlink UE CAPABILITY ENQUIRY message.

After step 9, the UE shall transmit a RRC STATUS message on the uplink DCCH. The protocol error cause shall be set to “ASN.1 violation or encoding error”.

After step 10, the UE shall re-transmit the UE CAPABILITY INFORMATION message with a similar content as in step 8.

#### 8.1.5.5 	UE Capability in CELL_FACH state: Success after T304 timeout

8.1.5.5.1		Definition

8.1.5.5.2 	Conformance requirement

1.	The UE CAPABILITY ENQUIRY message is sent by the UTRAN to request the UE to transmit its capability information related to any radio access network(s) supported by the UE. UTRAN initiates this action when it needs an update of the UE’s UMTS capability information or of its inter-system classmark.

2.	After the UE receives a UE CAPABILITY ENQUIRY message, it transmits a UE CAPABILITY INFORMATION message on the uplink DCCH. If it fails to receive a UE CAPABILITY INFORMATION CONFIRM message, the UE re-transmits another UE CAPABILITY INFORMATION message until its internal counter V304 is greater than N304.

Reference

3GPP TS 25.331 clause 8.1.6, 7

8.1.5.5.3 	Test purpose

To confirm that the UE re-transmits a UE CAPABILITY INFORMATION message until V304 is greater than N304, after the expiry of timer T304 when it fail to receive a downlink UE CAPABILITY INFORMATION CONFIRM message in response to the uplink UE CAPABILITY INFORMATION message sent.

8.1.5.5.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is brought to CELL_FACH state. When the SS transmits a UE CAPABILITY ENQUIRY message which includes the IE “Capability update requirement”, the UE shall reply with a UE CAPABILITY INFORMATION message on the uplink DCCH that contains the IE “Inter-system message”. The SS waits and does not transmit a UE CAPABILITY INFORMATION CONFIRM message to the UE, resulting in the T304 timer to expire. SS shall observe that the UE attempts to transmit a UE CAPABILITY INFORMATION message again. The UE shall re-transmit N304 times, and SS transmits a UE CAPABILITY INFORMATION CONFIRM message to answer the last request and completes this test procedure.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_FACH state. SS sets internal counter K =1 |
| 2 | ( | UE CAPABILITY ENQUIRY | Including the IE “Capability update requirement”. |
| 3 | ( | UE CAPABILITY INFORMATION | Including the IE “Inter-system capability”, which indicated the radio access network supported by the UE. |
| 4 |  |  | If K is greater to N304,then proceeds to step 6. Else, continue with step 5. |
| 5 |  |  | The SS does not transmit a response and wait for T304 timer to expire. K=K+1 and goes to step 3. |
| 6 | ( | UE CAPABILITY INFORMATION CONFIRM | Use default message contents |

Specific Message Contents

None

8.1.5.5.5	Test requirement

After step 3 the UE shall re-transmit a UE CAPABILITY INFORMATION message on the uplink DCCH, after each expiry of timer T304. The UE CAPABILITY INFORMATION message shall contain IE ”UE radio access capability” with the value matching those stated in the ICS/IXIT statements. In the same message, IE ”UE system specific capability” shall be present and it carries relevant GSM classmark information. After (N304+1) re-transmissions, the UE shall receive a UE CAPABILITY INFORMATION CONFIRM message.

### 8.1.6	Direct Transfer

#### 8.1.6.1	Direct Transfer in CELL DCH state (invalid message reception)

8.1.6.1.1	Definition

8.1.6.1.2	Conformance requirement

The UE shall transmit an RRC STATUS message stating the reason “protocol error” in IE “failure cause” and also set value “Information element value not comprehended” in IE “Protocol error cause“ when the UE receives a DOWNLINK DIRECT TRANFER message, which does not include the IE “NAS message”.

Reference

3GPP TS 25.331 clause 8.1.9

8.1.6.1.3	Test purpose

To confirm that the UE transmits an RRC STATUS message on the DCCH using AM RLC if it receives a DOWNLINK DIRECT TRANSFER message which does not include the IE “NAS message”

8.1.6.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH (state 6-1 or state 6-3) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a DOWNLINK DIRECT TRANSFER message to the UE and does not include the IE “NAS message”. The UE shall transmit an RRC STATUS message on the DCCH using AM RLC, setting the value “protocol error” in IE “failure cause”. The error type “Information element value not comprehended” shall also be indicated in IE “Protocol error cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | DOWNLINK DIRECT TRANSFER |  |
| 2 | ( | RRC STATUS |  |

Specific Message Contents

DOWNLINK DIRECT TRANSFER

The contents of DOWNLINK DIRECT TRANSFER message in this test case is identical to those in default contents of layer 3 messages for RRC tests with the following exceptions:.

| Information Element | Value/remark |
| --- | --- |
| NAS message | Not Present |

RRC STATUS

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Protocol error information | Information element value not comprehended |
| Other information element | Not checked |

8.1.6.1.5	Test requirement

After step 1 the UE shall transmit a n RRC STATUS message on the DCCH using AM RLC setting “protocol error” in IE “failure cause” and setting “Information element value not comprehended” in IE “Protocol error cause”.

#### 8.1.6.2	Direct Transfer in CELL FACH state (invalid message reception)

8.1.6.2.1	Definition

8.1.6.2.2	Conformance requirement

The UE shall transmit an RRC STATUS message stating the reason “protocol error” in IE “failure cause” and also set value “Information element value not comprehended” in IE “Protocol error cause” when the UE receives a DOWNLINK DIRECT TRANFER message, which does not include the IE “NAS message”.

Reference

3GPP TS 25.331 clause 8.1.9

8.1.6.2.3	Test purpose

To confirm that the UE transmits an RRC STATUS message on the DCCH using AM RLC if it receives a DOWNLINK DIRECT TRANSFER message which does not include the IE “NAS message”.

8.1.6.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a DOWNLINK DIRECT TRANSFER message to the UE and does not include the IE “NAS message”. The UE shall transmit an RRC STATUS message on the DCCH using AM RLC, setting the value “protocol error” in IE “failure cause”. The error type “Information element value not comprehended” shall also be indicated in IE “Protocol error cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | DOWNLINK DIRECT TRANSFER |  |
| 2 | ( | RRC STATUS |  |

Specific Message Contents

DOWNLINK DIRECT TRANSFER

The contents of DOWNLINK DIRECT TRANSFER message in this test case is identical to those in default contents of layer 3 messages for RRC tests with the following exceptions:.

| Information Element | Value/remark |
| --- | --- |
| NAS message | Not Present |

RRC STATUS

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Protocol error information | Information element value not comprehended |
| Other information element | Not checked |

8.1.6.2.5	Test requirement

After step 1 the UE shall transmit a n RRC STATUS message on the DCCH using AM RLC setting “protocol error” in IE “failure cause” and setting “Information element value not comprehended” in IE “Protocol error cause”.

### 8.1.7	Security mode control

#### 8.1.7.1	Security mode control in CELL_DCH state

8.1.7.1.1	Definition

8.1.7.1.2	Conformance requirement

1.	This procedure is used to trigger the stop or start of ciphering or to command the restart of ciphering with the new ciphering configuration. It is also used to start integrity protection or modify integrity protection configuration, both for the signalling links and any of radio bearers.

2.	When the UE receives a SECURITY MODE COMMAND message from the UTRAN, which indicates the downlink activation time and new integrity protection configuration, the UE shall apply the old ciphering configuration before the stated downlink activation time. It shall start to decipher using the new ciphering configuration at the downlink activation time.

3.	After the UE transmit the SECURITY MODE COMPLETE message using the new integrity protection configuration which includes uplink activation time, it starts to cipher transmission in the uplink using the new configuration at the uplink activation time.

Reference

3GPP TS 25.331 clause 8.1.12

8.1.7.1.3	Test purpose

To confirm that the UE correctly communicates to the UTRAN and activates the new ciphering configurations after the stated activation time. To confirm that after the UE receives a SECURITY MODE COMMAND message, it transmits a SECURITY MODE COMPLETE message to the UTRAN using the old ciphering configuration together with the application of the new integrity protection configuration.

8.1.7.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH (state 6-1 or state 6-3) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is in the RRC connected state CELL_DCH. The SS transmits a SECURITY MODE COMMAND message in which ciphering is requested to be activated, but the IE “Ciphering algorithm capability” is set to an unknown value. The UE shall not trigger any ciphering algorithm and it shall respond by sending SECURITY MODE FAILURE message on the DCCH. Next, SS transmits a valid SECURITY MODE COMMAND message which includes the “Downlink activation time” IE for RB2 and “Integrity check info” IE. Then the UE shall check the integrity check info and shall start to configure ciphering in downlink and transmits a SECURITY MODE COMPLETE message which contains the uplink activation time for RB1,RB2,RB 3 and RB 4 and also “Integrity check info” IE. SS records the uplink ciphering activation time for RB 2. Next, SS transmits COUNTER CHECK message repeated on the downlink DCCH using RLC-AM mode. The UE shall respond to each downlink message with a COUNTER CHECK RESPONSE message on the uplink DCCH using RLC-AM. This cycle repeats itself until both the uplink and downlink ciphering activation time for RB 2 has elapsed. SS checks all uplink COUNTER CHECK RESPONSE messages are integrity-protected by UIA algorithm, and that the messages contain the correct values for “Integrity mode info” IE. After both the uplink and downlink ciphering activation time for RB 2 has passed, the UE shall be able to communicate with the SS. This can be verified in SS through the reception of a correctly ciphering and integrity-protected COUNTER CHECK RESPONSE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | RRC connected state on DCCH |
| 2 | ( | SECURITY MODE COMMAND | IE ”Ciphering Algorithm capability” is set to an invalid value |
| 3 | ( | SECURITY MODE FAILURE | IE “Failure Cause” should be set to “Protocol Error” and IE “Protocol Error Information” should be set to “Information element value not comprehended”. |
| 4 | ( | SECURITY MODE COMMAND | See specific message contents. |
| 5 | ( | SECURITY MODE COMPLETE | SS verifies that this message is sent unciphered. SS records the uplink ciphering activation time for RB 2. |
| 6 | ( | COUNTER CHECK | SS repeats step 6 and step 7 until its internal uplink and downlink RLC SN have both surpassed the uplink and downlink ciphering activation time specified for RB2. This message is sent on the downlink DCCH using RLC-AM. See specific message content. |
| 7 | ( | COUNTER CHECK RESPONSE | UE shall send this message on the uplink DCCH using RLC-AM. See specific message content. |
| 8 |  |  | SS verifies that the last COUNTER CHECK RESPONSE message is both integrity-protected and ciphered correctly. |

Specific Message Contents

SECURITY MODE COMMAND (Step 2)

See notes below for the value of Y.

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info Message authentication code RRC Message sequence number Security Capability Ciphering algorithm capability Integrity protection algorithm capability Ciphering mode info Ciphering mode command Activation time for DPCH Radio bearer downlink ciphering activation time info RB Identity RLC sequence number Integrity protection mode info Integrity protection mode command Downlink integrity protection activation info Integrity protection algorithm Integrity protection initialisation number CN domain identity | 0 Calculated result in SS 0 ”1111111111111111”B ”1111111111111111”B Start Not Present 2 Current RLC SN + Y Start Not Present If integrity is indicated to be active on IXIT statements in TS 34.123-2, use one of the supported integrity algorithms 0000 0000 0000 0000 H (FRESH) Supported domain |

SECURITY MODE COMMAND (Step 4)

See notes below for the value of Y.

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info Message authentication code RRC Message sequence number Security Capability Ciphering algorithm capability Integrity protection algorithm capability Ciphering mode info Ciphering mode command Activation time for DPCH Radio bearer downlink ciphering activation time info RB Identity RLC sequence number Integrity protection mode info Integrity protection mode command Downlink integrity protection activation info Integrity protection algorithm Integrity protection initialisation number CN domain identity | 0 Calculated result in SS 0 If ciphering is indicated to be active on IXIT statements in TS 34.123-2, use one of the supported ciphering algorithms 0000000000000010B(UIA1) Start Not Present 2 Current RLC SN + Y Start Not Present If integrity is indicated to be active on IXIT statements in TS 34.123-2, use one of the supported integrity algorithms 0000 0000 0000 0000 H (FRESH) Supported domain |

SECURITY MODE COMPLETE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info - Message Authentication code - RRC Message sequence number Uplink integrity protection activation info - RRC message sequence number list Radio bearer uplink ciphering activation info - RB Identity - RLC sequence number | 0 Checked to see if present Checked to see if present Check to see if it the RRC SN for RB 0 to RB 4 are present 2 SS records this value. See step 8 in ‘expected sequence’ |

COUNTER CHECK (Step 6)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C MSB information - RB identity - COUNT-C MSB uplink - COUNT-C MSB downlink | 0 Calculated value 2 Current COUNT-C MSB for RB#2 in uplink Current COUNT-C MSB for RB#2 in downlink |

COUNTER CHECK RESPONSE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C information - RB identity - COUNT-C uplink - COUNT-C downlink | 0 Checked to see if the MAC code match Check to if this IE is absent |

Note:	Y = 2 * (size of COUNTER CHECK message, after PER encoding). The unit of Y is the number of RLC-AM PDU.

8.1.7.1.5	Test requirement

After step 2 the UE shall transmit a SECURITY MODE FAILURE message to report the protocol error detected in the first SECURITY MODE COMMAND message. The UE shall be able to communicate normally with the SS, with all control data on the signalling radio bearers unciphered.

After step 4 the UE shall RLC-acknowledge the receipt of the SECRUITY MODE COMMAND message using unciphered mode and which includes calculated integrity check info. SS checks that the SECURITY MODE COMPLETE message is received unciphered and that the calculated “integrity check info” IE is correct.

After step 5 SS verifies that all uplink signalling messages on RB1, RB2, RB3 and RB4 are integrity protected with UIA1 algorithm.

After step 7 SS verifies that the last COUNTER CHECK RESPONSE message received is integrity protected with UIA algorithm and ciphered with the algorithm indicated in the second SECURITY MODE COMMAND (Step 4) message.

#### 8.1.7.2	Security mode control in CELL_FACH state

8.1.7.2.1	Definition

8.1.7.2.2	Conformance requirement

1.	This procedure is used to trigger the stop or start of ciphering, or to command the restart of ciphering with the new ciphering configuration. It is also used to start integrity protection or modify integrity protection configuration, both for signalling link(s) and any radio access bearer(s).

2.	When the UE receives a SECURITY MODE COMMAND message from the UTRAN, which indicates the downlink activation time and new integrity protection configuration, the UE shall apply the old ciphering configuration before the stated downlink activation time. It shall start to decipher using the new ciphering configuration at the downlink activation time.

3.	The UE shall transmit SECURITY MODE COMPLETE message using the new integrity protection configuration stated in the received SECURITY MODE COMMAND message. The SECURITY MODE COMPLETE message shall include the ciphering uplink activation time. The UE shall start to apply the new ciphering configuration on the uplink direction, after the uplink activation time has elapsed.

Reference

3GPP TS 25.331 clause 8.1.12

8.1.7.2.3	Test purpose

To confirm that after the UE receives a SECURITY MODE COMMAND message, it transmits a SECURITY MODE COMPLETE message to the UTRAN using the old ciphering configuration together with the application of the new integrity protection configuration. To confirm that the UE applies the old ciphering configuration in the downlink prior to the activation time; and uses the new ciphering configuration on and after the activation time. To confirm that the UE starts to cipher its uplink transmissions after the uplink activation time stated in SECURITY MODE COMPLETE message is reached.

8.1.7.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH (state 6-2 or state 6-4) as specified in clause 7.4 of TS 34.108 ,depending on the CN domain(s) supported by the UE

Test Procedure

The UE is in the RRC connected state CELL_FACH. The SS transmits a SECURITY MODE COMMAND message in which ciphering is requested to be activated, but the IE ”Ciphering algorithm capability” is set to an unknown value. The UE shall not trigger any ciphering algorithm and it shall respond by sending SECURITY MODE FAILURE message on the DCCH. Next, SS transmits a valid SECURITY MODE COMMAND message which includes IE “Downlink activation time” for RB2 and IE “Integrity check info”. The UE shall check the integrity check info. It shall start to configure ciphering in downlink and transmit a SECURITY MODE COMPLETE message, which contains the uplink activation time for RB2. This message shall contain the IE “Integrity check info”. SS records the uplink ciphering activation time for RB 2. Next, SS transmits COUNTER CHECK message repeated on the downlink DCCH using RLC-AM mode. The UE shall respond to each downlink message with a COUNTER CHECK RESPONSE message on the uplink DCCH using RLC-AM. SS confirms that the uplink COUNTER CHECK RESPONSE messages are not ciphered. SS also checks all uplink messages are integrity-protected by UIA1 algorithm, and that the messages contain the correct values for “Integrity mode info” IE. This cycle repeats itself until both the uplink and downlink ciphering activation time for RB 2 have elapsed. After both the uplink and downlink ciphering activation time for RB 2 have passed, the UE shall be able to communicate with the SS using the new ciphering configurations. This can be verified in SS through the reception of a correctly ciphered and integrity-protected COUNTER CHECK RESPONSE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | UE is initially in CELL_FACH state. |
| 2 | ( | SECURITY MODE COMMAND | IE ”Ciphering Algorithm capability” is set to an invalid value |
| 3 | ( | SECURITY MODE FAILURE | IE “Failure Cause” shall be set to “Protocol Error” and IE “Protocol Error Information” shall be set to “Information element value not comprehended”. |
| 4 | ( | SECURITY MODE COMMAND | See specific message contents. |
| 5 | ( | SECURITY MODE COMPLETE | SS verifies that this message is sent unciphered. SS records the uplink ciphering activation time for RB 2. |
| 6 | ( | COUNTER CHECK | SS repeats step 6 and step 7 until its internal uplink and downlink RLC sequence numbers have both surpassed the uplink and downlink ciphering activation times specified for RB2. This message is sent on the downlink DCCH using RLC-AM. See specific message content. |
| 7 | ( | COUNTER CHECK RESPONSE | UE shall send this message on the uplink DCCH using RLC-AM. See specific message content. |
| 8 |  |  | SS verifies that the last COUNTER CHECK RESPONSE message is both integrity-protected and ciphered correctly. |

Specific Message Contents

SECURITY MODE COMMAND (Step 2)

See notes below for the value of Y.

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info Message authentication code RRC Message sequence number Security Capability Ciphering algorithm capability Integrity protection algorithm capability Ciphering mode info Ciphering mode command Activation time for DPCH Radio bearer downlink ciphering activation time info RB Identity RLC sequence number Integrity protection mode info Integrity protection mode command Downlink integrity protection activation info Integrity protection algorithm Integrity protection initialisation number CN domain identity | 0 Calculated result in SS 0 ”1111111111111111”B ”1111111111111111”B Start Not Present 2 Current RLC SN + Y Start Not Present If integrity is indicated to be active on IXIT statements in TS 34.123-2, use one of the supported integrity algorithms 0000 0000 0000 0000 H (FRESH) Supported domain |

SECURITY MODE COMMAND (Step 4)

See notes below for the value of Y.

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info Message authentication code RRC Message sequence number Security Capability Ciphering algorithm capability Integrity protection algorithm capability Ciphering mode info Ciphering mode command Activation time for DPCH Radio bearer downlink ciphering activation time info RB Identity RLC sequence number Integrity protection mode info Integrity protection mode command Downlink integrity protection activation info Integrity protection algorithm Integrity protection initialisation number CN domain identity | 0 Calculated result in SS 0 If ciphering is indicated to be active on IXIT statements in TS 34.123-2, use one of the supported ciphering algorithms 0000000000000010B(UIA1) Start Not Present 2 Current RLC SN + Y Start Not Present If integrity is indicated to be active on IXIT statements in TS 34.123-2, use one of the supported integrity algorithms 0000 0000 0000 0000 H (FRESH) Supported domain |

SECURITY MODE COMPLETE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info - Message Authentication code - RRC Message sequence number Uplink integrity protection activation info - RRC message sequence number list Radio bearer uplink ciphering activation info - RB Identity - RLC sequence number | 0 Checked to see if present Checked to see if present Check to see if it the RRC SN for RB 0 to RB 4 are present 2 SS records this value. See step 8 in ‘expected sequence’ |

COUNTER CHECK (Step 6)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C MSB information - RB identity - COUNT-C MSB uplink - COUNT-C MSB downlink | 0 Calculated value 2 Current COUNT-C MSB for RB#2 in uplink Current COUNT-C MSB for RB#2 in downlink |

COUNTER CHECK RESPONSE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C information - RB identity - COUNT-C uplink - COUNT-C downlink | 0 Checked to see if the MAC code match Check to if this IE is absent |

Note:	Y = 2 * (size of COUNTER CHECK message, after PER encoding). The unit of Y is the number of RLC-AM PDU.

8.1.7.2.5	Test requirement

After step 2 the UE shall transmit a SECURITY MODE FAILURE message to report the protocol error detected in the first SECURITY MODE COMMAND message. The UE shall be able to communicate normally with the SS, with all control data on the signalling radio bearers unciphered.

After step 4 the UE shall RLC-acknowledge the receipt of the SECRUITY MODE COMMAND message using unciphered mode and which includes calculated integrity check info. SS checks that the SECURITY MODE COMPLETE message is received unciphered and that the calculated MAC-I values in “integrity check info” IE is correct.

After step 5 SS verifies that all uplink signalling messages on RB1, RB2, RB3 and RB4 are integrity protected with UIA1 algorithm.

After step 7 SS verifies that the last COUNTER CHECK RESPONSE message received is integrity protected with UIA1 algorithm and ciphered with the algorithm indicated in the second SECURITY MODE COMMAND (Step 4) message.

### 8.1.8	Counter check

#### 8.1.8.1	Counter check in CELL_DCH state

8.1.8.1.1	Definition

8.1.8.1.2	Conformance requirement

When the UE receives a COUNTER CHECK message that includes matched COUNT-C MSB values, the UE shall transmit a COUNTER CHECK RESPONSE message on the uplink DCCH and omitting “RB COUNT-C information” IE in this message.

When the UE receives a COUNTER CHECK message that includes any mismatched COUNT-C MSB values, the UE shall transmit a COUNTER CHECK RESPONSE message on the uplink DCCH and specifies the current COUNT-C information of the RAB(s) with mismatched values.

Reference

3GPP TS 25.331 clause 8.1.15

8.1.8.1.3	Test purpose

To confirm that the UE transmits a COUNTER CHECK RESPONSE message after it receives a COUNTER CHECK message from the SS. To confirm that the UE responds to the reception of an invalid downlink COUNTER CHECK message by transmitting a RRC STATUS message on the uplink DCCH, stating the correct error cause value in message.

8.1.8.1.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_DCH state (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is brought to the CELL_DCH state after a successful outgoing call attempt. The SS transmits an erroneous COUNTER CHECK message. The content of this message is lack of a mandatory IE. The UE shall detect a protocol error and send RRC STATUS message to report this event. Next, the SS transmits a COUNTER CHECK message that includes the current COUNT-C MSB information in each radio access bearer. The UE shall react by sending a COUNTER CHECK RESPONSE message on the uplink DCCH, which does not include “RB COUNT-C information” IE. The SS transmits a COUNTER CHECK message which includes the current COUNT-C MSB information reversed all the bits in each radio bearer. The UE shall send a COUNTER CHECK RESPONSE message on the uplink DCCH, specifying the current COUNT-C information for each radio access bearer established.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_DCH state after an outgoing call has been established successfully. |
| 2 | ( | COUNTER CHECK | See specific message contents for this message |
| 3 | ( | RRC STATUS | UE shall detect a protocol error and then transmit this message. |
| 4 | ( | COUNTER CHECK | See specific message content. |
| 5 | ( | COUNTER CHECK RESPONSE | The message shall not include the IE “RB COUNT-C information”. |
| 6 | ( | COUNTER CHECK | See specific message content. |
| 7 | ( | COUNTER CHECK RESPONSE | The message shall include the IE “RB COUNT-C information”. |

Specific Message Contents

COUNTER CHECK (Step 2)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier | Not Present |

RRC STATUS (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Checked to see if set to “ASN.1 violation or encoding error” |

COUNTER CHECK (Step 4)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C MSB information - RB identity - COUNT-C MSB uplink - COUNT-C MSB downlink | 0 Calculated value 20 Current COUNT-C MSB for RB#20 in uplink Current COUNT-C MSB for RB#20 in downlink |

COUNTER CHECK RESPONSE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C information - RB identity - COUNT-C uplink - COUNT-C downlink | 0 Not checked Check to if this IE is absent |

COUNTER CHECK (Step 6)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C MSB information - RB identity - COUNT-C MSB uplink - COUNT-C MSB downlink | 0 Calculated value Check to see if set to 20 Toggle all bits of the current COUNT-C MSB in uplink for RB#20 Toggle all bits of the current COUNT-C MSB in downlink for RB#520 |

COUNTER CHECK RESPONSE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C information - RB identity - COUNT-C uplink - COUNT-C downlink | 0 Not checked Check to see if set to 20 Check to see if set to Current COUNT-C for RB#20 in uplink Check to see if set to COUNT-C for RB#20 in downlink |

8.1.8.1.5	Test requirement

After step 2, the UE shall transmit a RRC STATUS message on the uplink DCCH. The protocol error cause shall be set to “ASN.1 violation or encoding error”.

After step 4 the UE shall transmit a COUNTER CHECK RESPONSE message which does not includes the IE “RB COUNT-C information” to indicates that a matched comparison result is obtained.

After step 6, the UE shall transmit a COUNTER CHECK RESPONSE message which includes the IE “RB COUNT-C information” to report that a mismatch in COUNT-C value is detected in RB#20.

#### 8.1.8.2	Counter check in CELL_FACH state

8.1.8.2.1	Definition

8.1.8.2.2 	Conformance requirement

When the UE receives a COUNTER CHECK message that includes matched COUNT-C MSB values, the UE shall transmit a COUNTER CHECK RESPONSE message on the uplink DCCH and omitting “RB COUNT-C information” IE in this message.

When the UE receives a COUNTER CHECK message that includes any mismatched COUNT-C MSB values, the UE shall transmit a COUNTER CHECK RESPONSE message on the uplink DCCH and specifies the current COUNT-C information of the RAB(s) with mismatched values.

Reference

3GPP TS 25.331 clause 8.1.15

8.1.8.2.3 	Test purpose

To confirm that the UE transmits a COUNTER CHECK RESPONSE message after it receives a COUNTER CHECK message from the SS.  To confirm that the UE responds to the reception of an invalid downlink COUNTER CHECK message by transmitting a RRC STATUS message on the uplink DCCH, stating the correct error cause value in message.

8.1.8.2.4 	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_FACH state (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is brought to the CELL_FACH state after a successful outgoing call attempt.  The SS transmits an erroneous COUNTER CHECK message.  The content of this message is lack of a mandatory IE.  The UE shall detect a protocol error and send RRC STATUS message to report this event.  Next, the SS transmits a COUNTER CHECK message that includes the current COUNT-C MSB information in each radio access bearer.  The UE shall react by sending a COUNTER CHECK RESPONSE message on the uplink DCCH, which does not include “RB COUNT-C information” IE.  The SS transmits a COUNTER CHECK message, which includes the current COUNT-C MSB information for each radio bearer but with all the bits reversed.  The UE shall send a COUNTER CHECK RESPONSE message on the uplink DCCH, specifying the current COUNT-C information for each radio access bearer established.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_FACH state after an outgoing call has been established successfully. |
| 2 | ( | COUNTER CHECK | See specific message contents for this message |
| 3 | ( | RRC STATUS | UE shall detect a protocol error and then transmit this message. |
| 4 | ( | COUNTER CHECK | See specific message content. |
| 5 | ( | COUNTER CHECK RESPONSE | The message shall not include the IE “RB COUNT-C information”. |
| 6 | ( | COUNTER CHECK | See specific message content. |
| 7 | ( | COUNTER CHECK RESPONSE | The message shall include the IE ”RB COUNT-C information”. |

Specific Message Contents

COUNTER CHECK (Step 2)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier | Not Present |

RRC STATUS (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Checked to see if set to “ASN.1 violation or encoding” or “conditional information element error” |

COUNTER CHECK (Step 4)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C MSB information - RB identity - COUNT-C MSB uplink - COUNT-C MSB downlink | 0 Calculated value 20 Current COUNT-C MSB for RB#20 in uplink Current COUNT-C MSB for RB#20 in downlink |

COUNTER CHECK RESPONSE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C information - RB identity - COUNT-C uplink - COUNT-C downlink | 0 Not checked Check to if this IE is absent |

COUNTER CHECK (Step 6)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C MSB information - RB identity - COUNT-C MSB uplink - COUNT-C MSB downlink | 0 Calculated value 20 Toggle all bits of the current COUNT-C MSB in uplink for RB#20 Toggle all bits of the current COUNT-C MSB in downlink for RB#20 |

COUNTER CHECK RESPONSE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Integrity check info RB COUNT-C information - RB identity - COUNT-C uplink - COUNT-C downlink | 0 Not checked Check to see if set to 20 Check to see if set to Current COUNT-C for RB#20 in uplink Check to see if set to COUNT-C for RB#20 in downlink |

8.1.8.2.5	Test requirement

After step 2, the UE shall transmit a RRC STATUS message on the uplink DCCH. The protocol error cause shall be set to “ASN.1 violation or encoding error”.

After step 4 the UE shall transmit a COUNTER CHECK RESPONSE message which does not includes the IE ”RB COUNT-C information” to indicates that a matched comparison result is obtained.

After step 6, the UE shall transmit a COUNTER CHECK RESPONSE message which includes the IE ”RB COUNT-C information” to report that a mismatch in COUNT-C value is detected in RB#20.

### 8.1.9	Signalling Connection Release Request

8.1.9.1	Definition

8.1.9.2	Conformance requirement

The UE shall initiate the signalling connection release procedure when the higher layer entities in the UE request to release one or more signalling session (one example of such case is location update failure). In this case, the UE shall transmit a SIGNALLING CONNECTION RELEASE REQUEST message, which includes the CN domain identity of the connection flow to be released.

Reference

3GPP TS 25.331 clause 8.1.14

8.1.9.3	Test purpose

To confirm that the UE transmits a SIGNALLING CONNECTION RELEASE REQUEST message after it fails to receive a response for the LOCATION UPDATING REQUEST message.

8.1.9.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: Switched off (state 1) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is turned on and it shall find a suitable cell to camp on. The UE shall initiate a location updating procedure. The UE shall establish an RRC connection and transmits a LOCATION UPDATING REQUEST message using the INITIAL DIRECT TRANSFER message. The SS does not respond to this message, and the UE shall send a SIGNALLING CONNECTION RELEASE REQUEST message which includes the CN domain identity with the same value as that in the INITIAL DIRECT TRANSFER message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is powered on. |
| 2 | ( | RRC CONNECTION REQUEST | UE shall initiate the location updating procedure. |
| 3 | ( | RRC CONNECTION SETUP |  |
| 4 |  |  | The UE configures the layer 2 and layer 1. |
| 5 | ( | RRC CONNECTION SETUP COMPLETE |  |
| 6 | ( | INITIAL DIRECT TRANSFER (LOCATION UPDATING REQUEST) | LOCATION UPDATE REQUEST is embedded in this message transmission. |
| 7 |  |  | The SS does not respond and waits until the timer for location update procedure expires. |
| 8 | ( | SIGNALLING CONNECTION RELEASE REQUEST |  |

Specific Message Content

SIGNALLING CONNECTION RELEASE REQUEST (Step 8)

| Information Element | Value/remark |
| --- | --- |
| CN domain identity | Check to see if this value is the as same as in the uplink INITIAL DIRECT TRANSFER message. |

8.1.9.5	Test requirement

After step 1 the UE shall initiate the LOCATION UPDATING procedure and establish an RRC connection.

After step 7 the UE shall transmit a SIGNALLING CONNECTION RELEASE REQUEST message which includes the same CN domain identity as that found in the INITIAL DIRECT TRANSFER message.

## 8.2	Radio Bearer control procedure

### 8.2.1	Radio Bearer Establishment

#### 8.2.1.1	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Success (Data integrity protection algorithm is not applied)

8.2.1.1.1	Definition

8.2.1.1.2	Conformance requirement

The UE shall correctly set up a radio bearer according to a RADIO BEARER SETUP message and communicate with the UTRAN for its implementation.

(This is the case where data integrity protection algorithm is not applied.)

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.1.3	Test purpose

To confirm that the UE establishes a new radio bearer according to a RADIO BEARER SETUP message received from the SS.

8.2.1.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state, after the test operator is prompted to make an out-going call. Before step 1, only signalling radio bearers have been established. The SS transmits a RADIO BEARER SETUP message to the UE after it sets up L1 including the start of tx/rx. This message requests the establishment of RABs for carrying the traffic of the speech call. After the UE receives this message, it configures them and establishes a radio bearer. Finally the UE transmits a RADIO BEARER SETUP COMPLETE message using AM RLC. Then the UE and the SS enters the communicating state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | This message do not contain IE “integrity check info” and “integrity protection mode info” |
| 2 | ( | RADIO BEARER SETUP COMPLETE | This message do not contain “integrity check info” and “Uplink integrity activation info |
| 3 |  |  | To confirm the communication. |

Specific Message Contents

For RADIO BEARER SETUP in step 1, using the message sub-type indicated as “Speech in CS” or “Non-speech in CS” found in default message content clause 9 of TS 34.108 and Annex A of TS 34.123-1, respectively.

8.2.1.1.5	Test requirement

After step 2 the UE shall communicate with the SS on the radio bearer for its implementation.

#### 8.2.1.2	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Success (Effected Data integrity protection algorithm)

8.2.1.2.1	Definition

8.2.1.2.2	Conformance requirement

The UE shall correctly set up a radio bearer according to a RADIO BEARER SETUP message, which applies data integrity function, and then communicate with the UTRAN for its implementation.

Reference

3GPP TS 25.331 clause 8.2.1, 8.5.11.

8.2.1.2.3	Test purpose

To confirm that the UE establishes a new radio bearer according to a RADIO BEARER SETUP message which contains IE “Integrity check info” and IE “Integrity protection mode info” received from the SS.

8.2.1.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108 and data integrity algorithm is not applied

Test Procedure

The UE is in the CELL_DCH state, after the test operator is prompted to make an out-going data call. Before step 1, only signalling radio bearers have been established. The SS transmits a RADIO BEARER SETUP message which is including IE “integrity check info” and “integrity protection mode info” to the UE after it sets up L1 including the start of tx/rx. This message requests the establishment of RABs for carrying the traffic of the call. After the UE receives this message, it configures them and establishes a radio bearer. Finally the UE transmits a RADIO BEARER SETUP COMPLETE message which is including IE “integrity check info” using AM RLC. Then the UE and the SS enters the communicating state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | This message contain IE “integrity check info” and “integrity protection mode info” |
| 2 | ( | RADIO BEARER SETUP COMPLETE | This message contain “integrity check info” |
| 3 |  |  | To confirm the communication. |

Specific Message Contents

For RADIO BEARER SETUP in step 1, using the message sub-types indicated as “Speech in CS” or “Non-spech in CS” as found in default message content clause 9 of TS 34.108 and Annex A, respectively.

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is identical with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Integrity check info |  |
| - Message authentication code | Bit string (32) MAC-I See TS 33.102 |
| - RRC Message sequence number | 0 |
| Integrity protection mode info | Present |
| - Integrity protection mode command | “Start” |
| - Downlink integrity protection activation info | Not present (It is needed only when the IE “Integrity protection mode command" has the value “modify”.) |
| - integrity protection algorithm | UIA1 |
| - integrity protection initialisation number | Bit string (32) FRESH See TS 33.102 |

RADIO BEARER SETUP COMPLETE

| Information Element | Value/remark |
| --- | --- |
| Integrity check info |  |
| - Message authentication code | Not checked(MAC-I See TS 33.102) |
| - RRC Message sequence number | Not checked |
| Uplink Integrity protection activation info | Not checked |
| Hyper Frame Number | Not checked |

8.2.1.2.5	Test requirement

After step 2 the UE shall communicate with the SS on the radio bearer for its implementation. This can be verified by the correct reproduction of the u-plane data transmitted and received between the test operator and SS.

#### 8.2.1.3	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Failure (Unsupported configuration)

8.2.1.3.1	Definition

8.2.1.3.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER SETUP message which includes unsupported configuration parameters and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.3.3	Test purpose

To confirm that the UE keeps its configuration and transmits a RADIO BEARER SETUP FAILURE message in case of receiving a RADIO BEARER SETUP message which includes parameters of its unsupported configuration.

8.2.1.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message as the frequency cannot be supported by the UE. After the UE receives this message, it transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | Including the unsupported configuration for the UE. |
| 2 | ( | RADIO BEARER SETUP FAILURE | The UE does not change the configuration. |

Specific Message Contents

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is indicated as “Speech in CS” or “Non-speech in CS“ as found in default message content clause 9 of TS 34.108 and Annex A respectively with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 16383. |
| - UARFCN downlink(Nd) | Not Present. |

RADIO BEARER SETUP FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.1.3.5	Test requirement

After step 1 the UE shall keep its configuration and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause”.

#### 8.2.1.4	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Failure (Physical channel Failure and successful reversion to old configuration)

8.2.1.4.1	Definition

8.2.1.4.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to configure the new radio bearer by the T312 expiry and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.4.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a RADIO BEARER SETUP FAILURE message when the UE fails to configure the new radio bearer following detection of physical channel failure after T312 expiry.

8.2.1.4.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message to the UE and does not configure the new radio bearer. Then after T312 expiry, the UE reverts to the old configuration and transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | The SS does not configure the new radio bearer stated in the message. |
| 2 |  |  | The UE does not configure the new radio bearer and reverts to the old configuration. |
| 3 | ( | RADIO BEARER SETUP FAILURE | UE shall transmit this message using the old RRC signalling bearer operating in RLC-AM mode. |

Specific Message Contents

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is indicated as “Speech in CS” or “Non-speech in CS“ as found in default message content clause 9 of TS 34.108 and Annex A, respectively.

RADIO BEARER SETUP FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.1.4.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

#### 8.2.1.5	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Failure (Physical channel Failure and reversion failure)

8.2.1.5.1	Definition

8.2.1.5.2	Conformance requirement

The UE shall perform a cell update procedure when the UE fails to revert to the old configuration after the detection of physical channel failure in the radio bearer establishment procedure. After the UE complete cell update procedure, the UE transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.5.3	Test purpose

To confirm that UE transmits RADIO BEARER SETUP FAILURE message after it completes a cell update procedure when the UE cannot establish the new radio bearer for the L1 configuration and cannot revert to the old configuration.

8.2.1.5.4	Method of test

Initial Condition

System Simulator: 2 cells- Cell 1 is active, Cell 2 is inactive

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108 in cell No.1

Test Procedure

The UE is in the CELL_DCH state in cell 1. SS transmits a RADIO BEARER SETUP message to the UE. The SS transmits a RADIO BEARER SETUP message to the UE. After transmitting the RADIO BEARER SETUP message, the SS shall not configure L1 in accordance to the settings in the message. At the same time, SS begins to broadcast the BCCH in a cell 2. The UE recognize that it cannot configure the new radio bearer and wants to revert to the old configuration, but the UE cannot revert to the old configuration. The UE shall select Cell 2 by performing cell re-selection and enter CELL FACH state. The UE transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value of IE “failure cause” to ” physical channel failure”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | The SS does not configure the new radio bearer and delete the old configuration. |
| 2 | ( | BCCH | The SS does not configure the new radio bearer and starts to transmit the BCCH in cell 2 |
| 3 |  |  | The UE shall detect a failure to configure the new radio bearers and also subsequently, cannot revert to old configuration. |
| 4 |  |  | The UE select the cell 2 and enter CELL FACH state. |
| 5 | ( | CELL UPDATE | The value “radio link failure” shall be set in IE ”Cell update cause”. |
| 6 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI” |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI” |
| 8 |  | RADIO BEARER SETUP FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO BEARER SETUP message in this test case is indicated as “Speech in CS” or “Non-speech in CS“ as found in default message content clause 9 of TS 34.108 and Annex A

CELL UPDATE (Step 5)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 7)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RECONFIGURATION FAILURE (Step 8)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.1.5.5	Test requirement

After step 3 the UE shall find a new cell 2, enter CELL_FACH state.

After step 8 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 9 the UE shall transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.1.6	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.1.6.1	Definition

8.2.1.6.2	Conformance requirement

If the UE receives a RADIO BEARER SETUP message whilst reconfiguring due to a radio bearer message other than RADIO BEARER SETUP, then it shall keep its configuration as if the RADIO BEARER SETUP message had not been received.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.6.3	Test purpose

To confirm that if the UE receives a RADIO BEARER SETUP message whilst reconfiguring due to a radio bearer message other than RADIO BEARER SETUP, it shall keep its configuration as if the RADIO BEARER SETUP message had not been received and complete the reconfiguration according to the previously received message.

8.2.1.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH+DTCH_DCH (state 6-9) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE. The SS transmits a RADIO BEARER SETUP message before the “activation time” indicated in the RADIO BEARER RECONFIGURATION message expires. When the UE receives the RADIO BEARER SETUP message, the UE shall keep the configuration as if it had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO BEARER SETUP FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message on DCCH using AM RLC.Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Including IE “Uplink DPCH info” |
| 2 | ( | RADIO BEARER SETUP | The SS send this message before the expiry of activation time specified in the message of step 1. |
| 3 | ( | RADIO BEARER SETUP FAILURE | The UE does not change the configuration because of receiving the RADIO BEARER SETUP message. |
| 4 | ( | RADIO BEARER RECONFIGURATION COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

For RADIO BEARER RECONFIGURATION in step 1, use the message sub-type indicated as “Speech in CS” found in Annex A, with the exception of the following Information Elements:

RADIO BEARER RECONFIGURATION (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

RADIO BEARER SETUP (Step 2)

The contents of RADIO BEARER SETUP message in this test case is indicated as “Speech in CS” or “Non-speech in CS” as found in default message content clause 9 of TS 34.108 and Annex A respectively with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Not Present |

RADIO BEARER SETUP FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure case | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.1.6.5	Test requirement

After step 1 The SS transmits a RADIO BEARER SETUP message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER RECONFIGURATION message.

#### 8.2.1.7	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.1.7.1	Definition

8.2.1.7.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER SETUP message, which includes the undefined value in the mandatory IE “UTRAN cycle length coefficient” and criticality is defined as “Reject”. Then it transmits a RADIO BEARER SETUP FAILURE message which is set to “protocol error” in IE “failure cause” and is set to “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a RADIO BEARER SETUP message which includes some IEs set to invalid value, and then the UE shall transmit RADIO BEARER SETUP FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.7.3	Test purpose

To confirm that the UE transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER SETUP message which indicates the undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” whose criticality is defined as “Reject”.

To confirm that the UE transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER SETUP message including some IEs set to invalid value.

8.2.1.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message to the UE which indicates a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” whose criticality is defined as “Reject”. The UE keeps the old configuration and transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “protocol error” in IE “failure cause”, and is set to “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration when SS transmits RADIO BEARER SETUP message including some IEs set to invalid value. The UE transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 | ( | RADIO BEARER SETUP FAILURE | The UE does not change the configuration. |
| 3 | ( | RADIO BEARER SETUP | This message includes IE set to invalid value. |
| 4 |  |  | The UE does not change the configuration. |
| 5 | ( | RADIO BEARER SETUP FAILURE | The IE “failure cause” shall be set to “invalid configuration” |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO BEARER SETUP message in this test case is identical as “Speech in CS” or “Non-speech in CS” as found in default message content clause 9 of TS 34.108 and Annex A respectively with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

RADIO BEARER SETUP FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

RADIO BEARER SETUP (Step 3)

The contents of RADIO BEARER SETUP message in this test case is identical as “Speech in CS” or “Non-speech in CS” as found in default message content clause 9 of TS 34.108 and Annex A respectively with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

RADIO BEARER SETUP FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.1.7.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “protocol error” in IE “failure cause” and set to “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration

After step 4 the UE shall transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

#### 8.2.1.8	Radio Bearer Establishment for transition from CELL_DCH to CELL_FACH: Success

8.2.1.8.1		Definition

8.2.1.8.2	Conformance requirement

The UE shall correctly set up a radio bearer according to a RADIO BEARER SETUP message and communicate with the UTRAN for its implementation.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.8.3	Test purpose

To confirm that the UE establishes a new radio bearer according to a RADIO BEARER SETUP message received from the SS.

8.2.1.8.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH_DCH (state 6-7) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state, after the test operator is asked to initiate a packet-switched data call. The SS transmits a RADIO BEARER SETUP message to the UE after it sets up L1. After the UE receives this message, it configures them and establishes a radio bearer. Finally the UE transmits a RADIO BEARER SETUP COMPLETE message using AM RLC. Then the UE and the SS enters the communicating state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | SS requests test operator to make an outgoing packet-switched data call. |
| 2 |  |  | The UE select PRACH and S-CCPCH using SIB5 or SIB6 after entering CELL FACH state. |
| 3 | ( | RADIO BEARER SETUP COMPLETE |  |
| 4 |  |  | To confirm the communication between UE and SS, based on the exchange of packets. |

Specific Message Contents

For RADIO BEARER SETUP message in step 1, use the message sub-type indicated as “Packet to CELL_FACH from CELL_DCH in PS” found in Annex A.

8.2.1.8.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer for its implementation.

#### 8.2.1.9	Radio Bearer Establishment for transition from CELL_DCH to CELL_FACH: Failure (Cell re-selection)

8.2.1.9.1		Definition

8.2.1.9.2	Conformance requirement

The UE shall initiate the cell update procedure when the UE failed to access the assigned physical channel according to a RADIO BEARER SETUP message when transiting from CELL_DCH state to CELL_FACH state. After the UE completes cell update procedure, the UE transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which sets IE “failure cause” to “cell reselection”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.9.3	Test purpose

To confirm that the UE transmit RADIO BEARER SETUP FAILURE message after it completes a cell update procedure when the UE cannot use the assigned physical channel according to a RADIO BEARER SETUP message as it transits from CELL_DCH to CELL_FACH.

8.2.1.9.4	Method of test

Initial Condition

System Simulator: 2 cells- Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH_DCH (state 6-7) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS transmits a RADIO BEARER SETUP message as the transition occurs from CELL_DCH to CELL_FACH and then broadcast BCCH in cell 2. The UE cannot access the assigned physical channel, as the SS does not transmit any data on the downlink common channel in cell 1. Then the UE shall initiate the cell update procedure in cell 2. The UE transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value of IE “failure cause” to ”cell reselection”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS broadcasts BCCH in cell No. 2. |
| 2 | ( | RADIO BEARER SETUP | Assigned the transition from CELL_DCH to CELL_FACH |
| 3 |  |  | The UE cannot use the assigned the physical channel. |
| 4 | ( | CELL UPDATE | The UE finds a new cell 2 and enter CELL FACH state in cell 2 to begins a cell update procedure. The value “cell reselection” set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. In the CELL_FACH state |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | RADIO BEARER SETUP FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO BEARER SETUP message in this test case is identical  as “Packet to CELL_FACH from CELL_DCH in PS“ as found in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER SETUP FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.1.9.5	Test requirement

After step 3 the UE shall find a new cell No.2 and enter to CELL_FACH state. Then the UE shall initiate a cell update procedure in cell No.2.

After step 5 transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 7 RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value of IE “failure cause” to ”cell reselection”.

#### 8.2.1.10	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Success

8.2.1.10.1		Definition

8.2.1.10.2	Conformance requirement

The UE shall correctly set up a radio bearer according to a RADIO BEARER SETUP message and communicate with the UTRAN for its implementation.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.10.3	Test purpose

To confirm that the UE establishes a new radio bearer according to a RADIO BEARER SETUP message received from the SS.

8.2.1.10.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH_FACH (state 6-8) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state, after SS prompts the test operator to initiate a packet-switched data call. The SS transmits a RADIO BEARER SETUP message to the UE after it sets up L1 including the start of tx/rx. After the UE receives this message, it configures them and establishes the required radio bearers. Finally the UE transmits a RADIO BEARER SETUP COMPLETE message using AM RLC. Then the UE and the SS enters the communicating state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 | ( | RADIO BEARER SETUP COMPLETE |  |
| 3 |  |  | To confirm the communication |

Specific Message Contents

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is identical the message sub-type indicated by “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

8.2.1.10.5	Test requirement

After step2 the UE shall communicate with the SS using the radio bearer indicated in RADIO BEARER SETUP message. Particularly, SS should be able to receive packet data using a terminal equipment (TE) attached to the UE.

#### 8.2.1.11	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Failure (Unsupported configuration)

8.2.1.11.1		Definition

8.2.1.11.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER SETUP message which includes an unsupported configuration and then transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, which sets value “configuration unsupported” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.11.3	Test purpose

To confirm that the UE keeps its configuration and transmits a RADIO BEARER SETUP FAILURE message in case of it receiving a RADIO BEARER SETUP message, which includes parameters of an unsupported configuration.

8.2.1.11.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_FACH (state 6-6) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER SETUP message with a stated frequency that cannot be supported by the UE. After the UE receives this message, it shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC setting value “configuration unsupported” in IE ”failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | This message includes an unsupported configuration for the UE. |
| 2 | ( | RADIO BEARER SETUP FAILURE | The UE shall transmit this message using RLC-AM mode and do not change the current configuration. |

Specific Message Contents

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS” as found in Annex A:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 0 |
| - UARFCN downlink(Nd) | Not Present |

RADIO BEARER SETUP FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.1.11.5	Test requirement

After step 1 the UE shall keep its configuration and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause”.

#### 8.2.1.12	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Failure (Physical channel Failure and successful reversion to old configuration)

8.2.1.12.1	Definition

8.2.1.12.2	Conformance requirement

The UE shall attempt to revert to the old configuration when the UE fails to configure the new radio bearer by the T312 expiry. It shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC containing value “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.12.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a RADIO BEARER SETUP FAILURE message when the UE fails to configure the new radio bearer when it detects physical channel failure, followed by the T312 expiry.

8.2.1.12.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH_FACH (state 6-8) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER SETUP message to the UE and does not configure the new radio bearer. After T312 expiry, the UE shall revert to the old configuration and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC. The content of the message shall indicate “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | The SS does not configure a new radio bearer. |
| 2 |  |  | The UE does not configure a new radio bearer but reverts to the old configuration. |
| 3 | ( | RADIO BEARER SETUP FAILURE |  |

Specific Message Contents

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is identical the message sub-type indicated by “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

RADIO BEARER SETUP FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.1.12.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

#### 8.2.1.13	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Failure (Physical channel Failure and reversion failure)

8.2.1.13.1		Definition

8.2.1.13.2	Conformance requirement

The UE shall perform a cell update procedure when the UE fails to revert to the old configuration after the detection of physical channel failure in the radio bearer establishment procedure. After the UE completes cell update procedure, the UE transmits RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC which set value to IE “failure cause”to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.13.3	Test purpose

To confirm that the UE transmit RADIO BEARER SETUP FAILURE message after it completes a cell update procedure when the UE cannot establish the new radio bearer for the L1 configuration and subsequently fail to revert to the old configuration.

8.2.1.13.4	Method of test

Initial Condition

System Simulator: 2 cells- Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH_FACH(state 6-8) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_FACH state in cell 1.SS transmits a RADIO BEARER SETUP message to the UE. After transmitting the RADIO BEARER SETUP message, the SS shall not configure L1 in accordance to the settings in the message. At the same time, SS begins to broadcast the BCCH in a cell 2. The UE recognize that it cannot configure the new radio bearer and wants to revert to the old configuration, but the UE cannot revert to the old configuration. The UE shall select Cell 2 by performing cell re-selection and enter CELL FACH state. The UE transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value ” physical channel failure” to IE “failure cause”.Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | The SS delete the old configuration. |
| 2 |  | BCCH | The SS does not configure the new radio bearer and starts to transmit the BCCH in cell 2 |
| 3 |  |  | The UE cannot configure a new radio bearer and cannot revert to old configuration. |
| 4 |  |  | The UE select the cell 2. |
| 5 | ( | CELL UPDATE | The value “radio link failure” shall be set in IE ”Cell update cause”. |
| 6 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 8 |  | RADIO BEARER SETUP FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO BEARER SETUP message in this test case is identical to the message sub-type “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A.

CELL UPDATE (Step 5)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 7)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER SETUP FAILURE (Step 8)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.1.13.5	Test requirement

After step 3 the UE shall find the presence of cell 2, which is suitable for camping.

After step 8 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 9 the UE shall transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.1.14	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.1.14.1	Definition

8.2.1.14.2	Conformance requirement

If the UE receives a RADIO BEARER SETUP message whilst reconfiguring due to a radio bearer message other than RADIO BEARER SETUP, it shall keep its configuration as if the RADIO BEARER SETUP message had not been received. Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.14.3	Test purpose

To confirm that if the UE receives a RADIO BEARER SETUP message whilst reconfiguring due to a radio bearer message other than RADIO BEARER SETUP, it shall keep its configuration as if the RADIO BEARER SETUP message had not been received and complete the reconfiguration according to the previously received message.

8.2.1.14.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCT+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE. The SS transmits a RADIO BEARER SETUP message before the “activation time” indicated in the RADIO BEARER RECONFIGURATION message expires. When the UE receives the RADIO BEARER SETUP message, the UE shall keep the configuration as if it had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO BEARER SETUP FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message on DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Including IE “Uplink DPCH info” |
| 2 | ( | RADIO BEARER SETUP | The SS send this message before the expiry of activation time specified in the message of step 1. |
| 3 | ( | RADIO BEAER SETUP FAILURE | The UE does not change the configuration because of receiving the RADIO BEARER SETUP message, and transmit this message on its uplink DCCH using the same RLC-AM mode radio bearer before step 1. |
| 4 | ( | RADIO BEARER RECONFIGURATION COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

The contents of RADIO BEARER RECONFIGURATION message in this test case are identical as “Packet to CELL_DCH from CELL_FACH in PS“ as found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Current CFN-[current CFN mod 8 + 8 ] |

RADIO BEARER SETUP (for Step 2)

For this message, use the message sub-type entitled “Packet to CELL_DCH from CELL_FACH in PS” in the default message content. Information element(s) to be changed are listed below:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Not present |

RADIO BEARER SETUP FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.1.14.5	Test requirement

After step 1 The SS transmits a RADIO BEARER SETUP message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER RECONFIGURATION message.

#### 8.2.1.15	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.1.15.1	Definition

8.2.1.15.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER SETUP message, which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” having criticality defined as “Reject”. It shall transmit a RADIO BEARER SETUP FAILURE message which set value “protocol error” in IE “failure cause” and also value “Information element value not comprehended” in IE “ Protocol error cause”. The UE shall keep existing configuration before reception of a RADIO BEARER SETUP message when the RADIO BEARER SETUP message include some IEs set to invalid value, and then the UE shall transmit RADIO BEARER SETUP FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.15.3	Test purpose

To confirm that the UE transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER SETUP message, with an undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” and having criticality defined as “Reject”.

To confirm that the UE transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER SETUP message including some IEs set to invalid value.

8.2.1.15.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH_FACH (state 6-8) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in CELL_FACH state. The SS transmits a RADIO BEARER SETUP message to the UE which includes an undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” with criticality defined as “Reject”. The UE keeps the old configuration and transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC. This message shall specify “protocol error” in IE “failure cause” and also set the value “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration when SS transmits RADIO BEARER SETUP message including some IEs set to invalid value. The UE transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 | ( | RADIO BEARER SETUP FAILURE | The UE does not change the configuration. |
| 3 | ( | RADIO BEARER SETUP | This message includes IE set to invalid value. |
| 4 |  |  | The UE does not change the configuration. |
| 5 | ( | RADIO BEARER SETUP FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO BEARER SETUP message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

RADIO BEARER SETUP FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

RADIO BEARER SETUP (Step 3)

The contents of RADIO BEARER SETUP message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS“ as found in Annex with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

RADIO BEARER SETUP FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.1.15.5	Test requirement

After step 1 the UE shall keep its old configuration and transmits a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC. The message shall indicate the reason of failure as “protocol error” in IE “failure cause” and set the value“Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration

After step 4 the UE shall transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value of  IE “failure cause” to “invalid configuration”.

#### 8.2.1.16	Radio Bearer Establishment for transition from CELL_FACH to CELL_FACH: Success

8.2.1.16.1	Definition

8.2.1.16.2	Conformance requirement

The UE shall correctly set up a radio bearer according to a RADIO BEARER SETUP message and communicate with the UTRAN for its implementation.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.16.3	Test purpose

To confirm that the UE establishes a new radio bearer according to a RADIO BEARER SETUP message received from the SS.

8.2.1.16.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH_FACH (state 6-8) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state, after the test operator is being prompted to make an outgoing packet-switched call. The SS transmits a RADIO BEARER SETUP message to the UE after it sets up L1 including the start of tx/rx. After the UE receives this message, it configures them and establishes a radio bearer. Finally the UE transmits a RADIO BEARER SETUP COMPLETE message using AM RLC. Then the UE and the SS enters the communicating state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 |  |  | The UE select PRACH and S-CCPCH using SIB5 or SIB6. |
| 3 | ( | RADIO BEARER SETUP COMPLETE |  |
| 4 |  |  | To confirm the proper establishment of the new radio bearer by checking the packet data exchanged between the SS and a TE attached to the UE. |

Specific Message Contents

RADIO BEARER SETUP

For this message, use the message sub-type entitled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A.

8.2.1.16.5	Test requirement

After step 3 the UE shall communicate with the SS using the new radio bearer , this can be confirmed by the exchange of packet data between a terminal equipment (TE) attached to the UE and the SS.

#### 8.2.1.17	Radio Bearer Establishment for transition from CELL_DCH to CELL_DCH: success (Subsequently received)

8.2.1.17.1		Definition

8.2.1.17.2	Conformance requirement

If the UE receives a RADIO BEARER SETUP message before the UE configures the radio bearer according to the previous RADIO BEARER SETUP message, the UE shall ignore the new RADIO BEARER SETUP message and configure according to the previous RADIO BEARER SETUP message. Finally, the UE shall transmit RADIO BEARER SETUP COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.17.3	Test purpose

To confirm that if the UE receives a new RADIO BEARER SETUP message before the UE configures the radio bearer according to a previous RADIO BEARER SETUP message, it ignore the new RADIO BEARER SETUP message and configures according to the previous RADIO BEARER SETUP message received.

8.2.1.17.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH_DCH (state 6-5) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. SS transmits a RADIO BEARER SETUP message to the UE before the UE configures the radio bearer according to the RADIO BEARER SETUP message prior to this new message. The UE ignores the new RADIO BEARER SETUP message and configures according to the former RADIO BEARER SETUP message. On completion of radio bearer configuration, the UE shall transmit RADIO BEARER SETUP COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | Including IE ”Uplink DPCH info” |
| 2 | ( | RADIO BEARER SETUP | SS send this message before the expiry of activation time specified in RADIO BEARER SETUP message of step 1. |
| 3 | ( | RADIO BEARER SETUP COMPLETE | The UE ignores the RADIO BEARER SETUP message in step 2 and confirms configuration according to the RADIO BEARER SETUP message in step 1. |

Specific Message Contents

For RADIO BEARER SETUP in step 1, use the message sub-type indicated as “The other of speech in CS” found in Annex A, with the exception of the following Information Elements:

RADIO BEARER SETUP (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

RADIO BEARER SETUP (Step 2)

For RADIO BEARER SETUP in step 2, use the message sub-type indicated as “The other of speech in CS” found in Annex A, with the exception of the following

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Not Present |

8.2.1.17.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the RADIO BEARER SETUP message in step 1.

#### 8.2.1.18	Radio Bearer Establishment for transition from CELL_FACH to CELL_DCH: Success (Subsequently received)

8.2.1.18.1	Definition

8.2.1.18.2	Conformance requirement

If the UE receives a RADIO BEARER SETUP message before the UE configures the radio bearer according to the previous RADIO BEARER SETUP message, the UE shall ignore the new RADIO BEARER SETUP message and configure according to the previous RADIO BEARER SETUP message. Finally, the UE shall transmit RADIO BEARER SETUP COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.1

8.2.1.18.3	Test purpose

To confirm that if the UE receives a new RADIO BEARER SETUP message before the UE configures the radio bearer according to a previous RADIO BEARER SETUP message, it ignore the new RADIO BEARER SETUP message and configures according to the previous RADIO BEARER SETUP message received.

8.2.1.18.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH_FACH (state 6-8) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER SETUP message, requesting the UE to setup radio bearers using DPCH physical channels. The activation time of this event is specified to be 255 frames from the SS’s current CFN. However, SS sends another RADIO BEARER SETUP message before 255 frames has lapsed. The UE ignores the new RADIO BEARER SETUP message and configures according to the former RADIO BEARER SETUP message. On completion of radio bearer configuration, the UE shall transmit RADIO BEARER SETUP COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | Including IE ”Uplink DPCH info” |
| 2 | ( | RADIO BEARER SETUP | SS send this message before the expiry of activation time specified in RADIO BEARER SETUP message of step 1. |
| 3 | ( | RADIO BEAER SETUP COMPLETE | The UE ignores the RADIO BEARER SETUP message in step 2 and confirms configuration according to the RADIO BEARER SETUP message in step 1. |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

For this message, use the message sub-type entitled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A

RADIO BEARER SETUP (for Step 2)

For this message, use the message sub-type entitled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A. Information element(s) to be changed are listed below:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.1.18.5	Test requirement

After step 2 the UE shall keep its configuration and transmit a RADIO BEARER SETUP COMPLETE message on the DCCH using AM RLC.

After step 3 the UE shall communicate with the SS on the radio bearer specified in the RADIO BEARER SETUP message in step 1.

#### 8.2.1.19	Radio Bearer Establishment from CELL_DCH to CELL_PCH: Success

8.2.1.19.1	Definition

8.2.1.19.2	Conformance requirement

The UE shall configure radio bearers and transition from CELL_DCH state to CELL_PCH state according to the received RADIO BEARER SETUP message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.1.19.3	Test purpose

To conform that the UE transmits a RADIO BEARER SETUP COMPLETE message and enters CELL_PCH state after it received a RADIO BEARER SETUP message from SS and configured new radio bearers.

8.2.1.19.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message. The UE transmits RADIO BEARER SETUP COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message,  causing the UE to enter CELL_FACH state and the UE shall transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to “paging response”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 | ( | RADIO BEARER SETUP COMPLETE |  |
| 3 |  |  | Configuration of Radio Bearer after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity in Initial Condition Previously assigned S-RNTI in Initial Condition |

8.2.1.19.5	Test requirement

After step 1, the UE transmits RADIO BEARER SETUP COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 4, the UE shall transmit CELL UPDATE message on the CCCH.

#### 8.2.1.20	Radio Bearer Establishment from CELL_DCH to URA_PCH: Success

8.2.1.20.1	Definition

8.2.1.20.2	Conformance requirement

The UE shall configure radio bearers and transition from CELL_DCH state to URA_PCH state according to receiving RADIO BEARER SETUP message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.1.20.3	Test purpose

To conform that the UE transmit a RADIO BEARER SETUP COMPLETE message and enters URA_PCH state after it received a RADIO BEARER SETUP message from SS and configured the new radio bearers.

8.2.1.20.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message. The UE transmits RADIO BEARER SETUP COMPLETE message to the UE using AM RLC and enters URA_PCH state. The SS transmits a PAGING TYPE 1 message, causing the UE to enter CELL_FACH state and the UE shall transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to “paging response”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 | ( | RADIO BEARER SETUP COMPLETE |  |
| 3 |  |  | Configuration of Radio Bearer after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity in Initial Condition Previously assigned S-RNTI in Initial Condition |

8.2.1.20.5	Test requirement

After step 1, the UE transmits RADIO BEARER SETUP COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3, the UE shall transmit CELL UPDATE message on the CCCH.

### 8.2.2	Radio Bearer Reconfiguration

#### 8.2.2.1	Radio Bearer Reconfiguration (Hard handover) from CELL_DCH to CELL_DCH: Success

8.2.2.1.1	Definition

8.2.2.1.2	Conformance requirement

The UE shall correctly reconfigure a radio bearer and L1 according to the RADIO BEARER RECONFIGURATION message, which specifies a hard handover to another radio frequency. After executing the reconfiguration, the UE shall be able to communicate with the UTRAN on the newly configured radio bearer.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.1.3	Test purpose

To confirm that the UE reconfigures a new radio bearer by following a RADIO BEARER RECONFIGURATION message, which indicates a hard handover to another radio frequency.

8.2.2.1.4	Method of test

Initial Condition

System Simulator: 2 cells – cell 1 and cell 6 are active. The CPICH_Ec/No and CPICH RSCP of cell 4 are improved to –15dB and –70dBm respectively. The Qrxlevmin and Qrxqualmin.values in SYSTEM INFORMATION BLOCK TYPE 3 and 4 messages of cell 6 is changed to –90dBm and –20dB respectively

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which commands that hard handover to cell 6 be performed. The UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Hard handover to cell 6, |
| 2 |  |  | UE shall stop all uplink transmissions to cell 1 and shall commence the reconfiguration of the affected physical channel parameters to that of cell 6. |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |

Specific Message Contents

RADIO BEARER RECONFIGURATION

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical to the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS“ in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | Same uplink UARFCN as used for cell 6 |
| - UARFCN downlink(Nd) | Same downlink UARFCN as used for cell 6 |
| Downlink information for each radio links | Same downlink UARFCN as used for cell 6 |
| - Primary CPICH info |  |
| - Primary Scrambling Code | 350 |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing Indicator | Initialise |

8.2.2.1.5	Test requirement

After step 1 the UE shall reconfigure the radio links with the SS.

After step 3 the UE shall change its physical channel configuration and communicate with the SS on the DCCH and DTCH of cell 6.

#### 8.2.2.2	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Failure (Unsupported configuration)

8.2.2.2.1	Definition

8.2.2.2.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RECONFIGURATION message which includes unsupported configuration parameters and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE ”failure cause

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.2.3	Test purpose

To confirm that the UE transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if the received RADIO BEARER RECONFIGURATION message includes unsupported configuration parameters.

8.2.2.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which includes unsupported configuration parameters for the UE. The UE shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE ”failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Including unsupported configuration by the UE |
| 2 | ( | RADIO BEARER RECONFIGURATION FAILURE | The UE does not change the radio bearer. |

Specific Message Contents

RADIO BEARER RECONFIGURATION

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 63984. |
| - UARFCN downlink(Nd) | Not Present |

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.2.2.5	Test requirement

After step 2 the UE shall keep its old configuration and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC with the value “configuration unsupported” set in IE “failure cause”.

#### 8.2.2.3	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Failure (Physical channel failure and reversion to old configuration)

8.2.2.3.1	Definition

8.2.2.3.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to reconfigure the new physical channel by received RADIO BEARER RECONFIGURATION message and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.3.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if the UE fails to reconfigure the new radio bearer according to the RADIO BEARER RECONFIGURATION message received previously.

8.2.2.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE which includes the new radio bearer parameters but it does not reconfigure L1 according to the settings found in the message. The UE shall revert to the old configuration. Then the UE shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting value “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | SS does not reconfigure L1 parameters to reflect the radio bearer reconfigurations specified in the message. |
| 3 | ( | RADIO BEARER RECONFIGURATION FAILURE | The UE shall detect a failure to reconfigure the new radio bearer, and send this message using the old radio bearer configuration. |

Specific Message Contents

RADIO BEARER RECONFIGURATION

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS” as found in Annex A.

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.2.3.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC setting value “physical channel failure” in IE “failure cause”.

#### 8.2.2.4	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Failure (Physical channel failure and reversion failure)

8.2.2.4.1	Definition

8.2.2.4.2	Conformance requirement

The UE shall perform acell updatewhen the UE fails to revert to the old configuration after the detection of physical channel failure in the radio bearer reconfiguration procedure. After the UE completes cell update procedure, the UE transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.4.3	Test purpose

To confirm that the UE transmits RADIO BEARER SETUP FAILURE message after it completes an cell update procedure when the UE cannot reconfigure the new radio bearer, and a subsequent failure to revert to the old configuration.

8.2.2.4.4		Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in a cell 1. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which includes the new radio bearer parameters. After transmitting the RADIO BEARER RECONFIGURATION message, the SS shall not reconfigure L1 in accordance to the settings in the message and delete all radio bearer related contexts in cell 1. At the same time, SS begins to broadcast the BCCH in a cell 2. The UE discovers that it cannot reconfigure the new radio bearer and wants to revert to the old configuration, but the UE cannot revert to the old configuration. The UE shall select Cell 2 by performing cell re-selection and enter  CELL FACH state. The UE transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” physical channel failure” to IE “failure cause”. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | The SS does not reconfigure the new radio bearer and delete the old configuration in cell 1. |
| 3 | ( | BCCH | The SS transmit the BCCH in the cell 2. |
| 4 |  |  | The UE fails to reconfigure a new radio bearer. |
| 5 |  |  | The SS shall not revert old configuration. |
| 6 |  |  | The UE select the cell 2 and enter CELL FACH state. |
| 7 | ( | CELL UPDATE | The value “radio link failure” shall be set in IE ”Cell update cause”. |
| 8 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“.. |
| 9 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 10 | ( | RADIO BEARER RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

RADIO BEARER RECONFIGURATION message (Step 1)

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS” as found in Annex.

CELL UPDATE (Step 7)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 8)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RECONFIGURATION FAILURE (Step 9)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.2.4.5	Test requirement

After step 5 the UE shall detect the presence of cell 2, enters CELL_FACH state.

After step 8 the UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 9 the UE shall transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.2.5	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.2.5.1	Definition

8.2.2.5.2	Conformance requirement

If the UE receives a RADIO BEARER RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RECONFIGURATION, it shall keep its configuration as if the RADIO RECONFIGURATION SETUP message had not been received. Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.5.3	Test purpose

To confirm that if the UE receives a RADIO BEARER RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RECONFIGURATION, it shall keep its configuration as if the RADIO BEARER RECONFIGURATION message had not been received and complete the reconfiguration according to the previously received message. 8.2.2.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message to the UE. The SS transmits a RADIO BEARER RECONFIGURATION message before the “activation time” indicated in the RADIO BEARER SETUP message expires. When the UE receives the RADIO BEARER RECONFIGURATION message, the UE shall keep the configuration as if it had not received the RADIO BEARER RECONFIGURATION message and shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO BEARER SETUP FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER SETUP COMPLETE message on DCCH using AM RLC. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | Including IE “Uplink DPCH info” |
| 2 | ( | RADIO BEARER RECONFIGURATION | Sent before the “activation time” in step 1 has elapsed |
| 3 | ( | RADIO BEARER RECONFIGURATION FAILURE | The UE does not change the configuration because of receiving the RADIO BEARER RECONFIGURATION message.. |
| 4 | ( | RADIO BEARER SETUP COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

For RADIO BEARER SETUP in step 1, use the message sub-type indicated as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A.

RADIO BEARER RECONFIGURATION (Step 2)

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical to those in the default contents of layer 3 messages for RRC tests with the following exceptions as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Not Present. |

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | ”RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.2.5.5	Test requirement

After step 1 The SS transmits a RADIO BEARER RECONFIGURATION message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

#### After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters configured as a result of the RADIO BEARER SETUP message 8.2.2.6	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.2.6.1	Definition

8.2.2.6.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RECONFIGURATION message, which includes the undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” having criticality defined as “Reject”. The UE shall transmit a RADIO BEARER RECONFIGURATION FAILURE message which is set to “protocol error” in IE “ failure cause” and is set to “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a RADIO BEARER RECONFIGURATION message when the RADIO BEARER RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit RADIO BEARER RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.6.3	Test purpose

To confirm that the UE transmits a RADIO BEARER RECONFIGRATION FAILURE message on the DCCH using AM RLC, if it receives a RADIO BEARER RECONFIGURATION message containing a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” with criticality defined as “Reject”.

To confirm that the UE transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RECONFIGURATION message including some IEs set to invalid value.

8.2.2.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE which includes the undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” which criticality is defined as “Reject”. The UE keeps the old configuration and transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “protocol error” in IE “failure cause” and is set to “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits RADIO BEARER RECONFIGURATION message including some IEs set to invalid value. The UE transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | The message contains an illegal error in a mandatory IE. |
| 2 | ( | RADIO BEARER RECONFIGRATION FAILURE | The UE does not change the configuration. |
| 3 | ( | RADIO BEARER RECONFIGURATION | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration. |
| 5 | ( | RADIO BEARER RECONFIGRATION FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

The contents of RADIO BEARER RECONFIGRATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with following exceptions, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

RADIO BEARER RECONFIGURATION FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

RADIO BEARER RECONFIGURATION (Step 3)

The contents of RADIO BEARER RECONFIGRATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with following exceptions, with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

RADIO BEARER RECONFIGURATION FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.2.6.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a RADIO BEARER RECONFIGRATION FAILURE message on the DCCH using AM RLC stating the reason “protocol error” in IE “failure cause”. The message shall contain the value “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration

After step 4 the UE shall transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

#### 8.2.2.7	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Success (Continue and stop)

8.2.2.7.1	Definition

8.2.2.7.2	Conformance requirement

The UE shall continue or stop the uplink transmission when the UTRAN indicate stop or continue uplink transmission in radio bearer reconfiguration procedure.Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.7.3	Test purpose

To confirm that the UE reconfigures new radio bearer and have the uplink transmission according to a RADIO BEARER RECONFIGURATIO message which indicates that uplink transmission is continued.

To confirm that the UE reconfigures new radio bearer and don’t transmit data according to a RADIO BEARER RECONFIGURATION message which indicates that uplink transmission is stopped.

8.2.2.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message including IE” RB stop/continue” set to “continue”. The UE reconfigures new radio bearer and transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC. The UE communicate with the SS after transmission the RADIO BEARER RECONFIGURATION COMPLETE message. Then, SS transmit a RADIO BEARER RECONFIGURATION message including IE” RB stop/continue” set to “stop”. The UE reconfigures new radio bearer and transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.  The UE don’t transmit any uplink data without Signalling message after transmission the RADIO BEARER RECONFIGURATION COMPLETE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | This message include IE” RB stop/continue “. |
| 2 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |
| 3 |  |  | The SS Shall communicate with the UE. |
| 4 |  | RADIO BEARER RECONFIGURATION | This message include IE” RB stop/continue “. |
| 5 |  | RADIO BEARER RECONFIGURATION COMPLETE |  |
| 6 |  |  | The SS shall not receive any data from the UE without Signalling message. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RB information to reconfigure list |  |
| RB information to reconfigure -RB identity | 5 |
| -RB stop/continue | “continue” |

RADIO BEARER RECONFIGURATION  (Step 4)

The contents of CELL UPDATE message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RB information to reconfigure list |  |
| RB information to reconfigure -RB identity | 5 |
| -RB stop/continue | “stop” |

8.2.2.7.5	Test requirement

After step 2 the UE shall communicate with the SS using new configuration.

After step 5 the UE shall communicate with the SS using new configuration, but shall not transmit any data to the SS without signalling message.

#### 8.2.2.8	Radio Bearer Reconfiguration from CELL_DCH to CELL_FACH: Success

8.2.2.8.1	Definition

8.2.2.8.2	Conformance requirement

The UE shall correctly reconfigure a radio bearer according to a RADIO BEARER RECONFIGURATION message which is communicate with the UTRAN on the new radio bearer in case of a transition from CELL_DCH to CELL_FACH in the same cell.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.8.3	Test purpose

To confirm that the UE establishes the reconfigured radio bearer(s) using common physical channel, after a RADIO BEARER RECONFIGURATION message has been received from the SS.

8.2.2.8.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE,  which includes the new radio bearer parameters and sets up L1 including the start of tx/rx. The UE reconfigures the new radio bearer and transmits a RADIO BEARER RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | The UE select PRACH and S-CCPCH using SIB5 and SIB6 after entering CELL FACH state. |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

8.2.2.8.5	Test requirement

After step 1 the UE shall reconfigure the radio links with the SS.

After step 3 the UE shall change its radio bearer configuration and communicate with the SS on the DCCH and DTCH, using the common physical channel.

#### 8.2.2.9	Radio Bearer Reconfiguration from CELL_DCH to CELL_FACH: Failure (Cell re-selection)

8.2.2.9.1	Definition

8.2.2.9.2	Conformance requirement

The UE shall initiate cell update procedure when the UE cannot use the assigned physical channel according to a RADIO BEARER CHANNEL RECONFIGURATION message in current cell, during the transition from CELL_DCH to CELL_FACH. After the UE completes cell update procedure, the UE transmits RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “cell reselection”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.9.3	Test purpose

To confirm that the UE transmits RADIO BEARER SETUP FAILURE message after it completes a cell reselection, when the UE cannot use the assigned physical channel according to a RADIO BEARER RECONFIGURATION message as it transits from CELL_DCH to CELL_FACH.

8.2.2.9.4	Method of test

Initial Condition

System Simulator: 2 cells – Cell 1 is active and cell 2 is inactive

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state in cell 1. SS transmit a RADIO BEARER RECONFIGURATION message to the UE, which includes the new radio bearer parameters. After transmitting the RADIO BEARER RECONFIGURATION message, the SS shall not reconfigure L1 in accordance to the settings in the message. At the same time, SS begins to broadcast the BCCH in a cell 2. The UE recognize that it cannot reconfigure the new radio bearer and wants to revert to the old configuration, but the UE cannot revert to the old configuration. The UE shall select cell 2 by performing cell re-selection and enter CELL FACH state. The UE transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” cell reselection” to IE “failure cause”.Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | The SS does not reconfigure the new radio bearer in cell 1. |
| 3 | ( | BCCH | The SS transmit the BCCH in the cell2. |
| 4 |  |  | The UE fails to reconfigure a new radio bearer. |
| 5 |  |  | The SS shall not revert old configuration. |
| 6 |  |  | The UE select the cell 2 and enter CELL FACH state. |
| 7 | ( | CELL UPDATE | The value “cell reselection” shall be set in IE ”Cell update cause”. |
| 8 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 9 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 10 | ( | RADIO BEARER RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

RADIO BEARER RECONFIGURATION

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_FACH from CELL_DCH in PS” found in Annex A:

CELL UPDATE (Step 7)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 9)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RECONFIGURATION FAILURE (Step 10)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.2.9.5	Test requirement

After step 5, the UE shall discover the presence of cell 2, enter CELL_FACH and then perform cell reselection by the transmission of CELL UPDATE using RLC-TM mode on CCCH.

After step 8 UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 9 , the UE shall transmit RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ”cell reselection”.

#### 8.2.2.10	Radio Bearer Reconfiguration: from CELL_FACH to CELL_DCH: Success

8.2.2.10.1	Definition

8.2.2.10.2	Conformance requirement

The UE shall correctly reconfigure a radio bearer according to a RADIO BEARER RECONFIGURATION message which is communicate with the UTRAN on the new radio bearer in case of a transition from CELL_FACH to CELL_DCH in the same cell.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.10.3	Test purpose

To confirm that the UE establishes a new radio bearer by following a RADIO BEARER RECONFIGURATION message received from the SS.

8.2.2.10.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE which includes the new radio bearer parameters and sets up L1 including the start of tx/rx. The UE reconfigures the new radio bearer and transmits a RADIO BEARER RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | This message includes IE “Uplink DPCH Info” |
| 2 |  |  | Reconfiguration of radio bearer |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS“ in Annex A.

8.2.2.10.5	Test requirement

After step 2 the UE shall change its radio bearer configuration and communicate with the SS on the DCCH and DTCH which are being carried by the DPCH physical channel resources.

#### 8.2.2.11	Radio Bearer Reconfiguration from CELL_FACH to CELL_DCH: Failure (Unsupported configuration)

8.2.2.11.1	Definition

8.2.2.11.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RECONFIGURATION message which includes unsupported configuration parameters and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.11.3	Test purpose

To confirm that the UE transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if the RADIO BEARER RECONFIGURATION message received includes unsupported configuration parameters.

8.2.2.15.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE which includes unsupported configuration parameters of the UE. The UE shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC and set “configuration unsupported” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | The message includes an unsupported configuration for the UE |
| 2 | ( | RADIO BEARER RECONFIGURATION FAILURE | The UE does not change the radio bearer. |

Specific Message Contents

RADIO BEARER RECONFIGURATION

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 63984 |
| - UARFCN downlink(Nd) | Not Present |

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.2.11.5	Test requirement

After step1 the UE shall keep its old configuration and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC stating “configuration unsupported” in IE “ failure cause”.

#### 8.2.2.12	Radio Bearer Reconfiguration from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion to old configuration)

8.2.2.12.1	Definition

8.2.2.12.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to reconfigure the new physical channel by received RADIO BEARER RECONFIGURATION message and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “ failure cause”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.12.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if the UE fails to reconfigure the new radio bearer according to a RADIO BEARER RECONFIGURATION message.

8.2.2.12.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which includes the new radio bearer parameters and does not reconfigure L1. Therefore, the UE cannot reconfigure the new radio bearer and shall attempt to revert to the old configuration. Then the UE shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, with the value “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | The SS does not reconfigures L1 including the start of tx/rx |
| 3 | ( | RADIO BEARER RECONFIGURATION FAILURE | The UE fails to reconfigure a new radio bearer. |

Specific Message Contents

RADIO BEARER RECONFIGURATION

Use the same message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.2.12.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting “physical channel failure” in IE “failure cause”.

#### 8.2.2.13	Radio Bearer Reconfiguration from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion failure)

8.2.2.13.1		Definition

8.2.2.13.2	Conformance requirement

The UE shall perform a cell update procedure when the UE fails to revert to the old configuration after the detection of physical channel failure in the radio bearer reconfiguration procedure. After the UE completes cell update procedure, the UE transmits RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.13.3	Test purpose

To confirm that the UE transmits RADIO BEARER RECONFIGURATION FAILURE message after it completesa cell update procedure, when the UE cannot reconfigure the new radio bearer following a failure to configure L1 parameters for the new radio bearer settings and also a reversion failure to the old configuration.

8.2.2.13.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_FACH state in cell 1. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which includes the new radio bearer parameters but SS does not reconfigure L1 such as catered to the new radio bearer settings. The UE cannot reconfigure the new radio bearer and wants to revert to the old configuration. But the SS does not configure the old radio bearer and begins to broadcast the BCCH in a cell 2 and stops broadcasting the BCCH in cell 1. Then the UE finds a new cell 2 and transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” physical channel failure” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | The SS does not reconfigure the new radio bearer and delete the old configuration. |
| 3 |  |  | The UE shall detect a failure to reconfigure a new radio bearer, and start to revert to old configuration. |
| 4 | ( | BCCH | The SS starts to transmit the BCCH in cell 2 and delete the old radio bearer settings in cell 1. |
| 5 |  |  | The SS shall not revert old configuration. |
| 6 |  |  | The UE enter CELL FACH state and select the cell2. |
| 7 | ( | CELL UPDATE | The value “radio link failure” shall be set in IE ”Cell update cause”. |
| 8 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 9 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 10 |  | RADIO BEARER RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

CELL UPDATE (Step 7)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 9)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RECONFIGURATION FAILURE (Step 9)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.2.13.5	Test requirement

After step 5 the UE shall detect the presence of cell 2, enter CELL_FACH state.

After step 8 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 9 the UE shall transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.2.14	Radio Bearer Reconfigure from CELL_FACH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.2.14.1		Definition

8.2.2.14.2	Conformance requirement

If the UE receives a RADIO BEARER RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RECONFIGURATION, it shall keep its configuration as if the RADIO BEARER RECONFIGURATION message had not been received. Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.14.3	Test purpose

To confirm that if the UE receives a RADIO BEARER RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RECONFIGURATION, it shall keep its configuration as if the RADIO BEARER RECONFIGURATION message had not been received and complete the reconfiguration according to the previously received message.

8.2.2.14.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message to the UE. The SS transmits a RADIO BEARER RECONFIGURATION message before the “activation time” indicated in the RADIO BEARER SETUP message expires. When the UE receives the RADIO BEARER RECONFIGUTARION message, the UE shall keep the configuration as if it had not received the RADIO BEARER RECONFIGURATION message and shall transmit a RADIO RECONFIGURATION SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO BEARER SETUP FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER SETUP COMPLETE message on DCCH using AM RLC. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | Including IE “Uplink DPCH info” |
| 2 | ( | RADIO BEARER RECONFIGURATION | Sent before the elapse of the “Activation Time” indicated in the previous message. |
| 3 | ( | RADIO BEARER RECONFIGURATION FAILURE | The UE does not change the configuration because of receiving the RADIO BEARER RECONFIGURATION message. |
| 4 | ( | RADIO BEARER SETUP COMPLETE | This message is on DCCH using AM RLC |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

For RADIO BEARER SETUP in step 1, use the message sub-type indicated as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A.

RADIO BEARER RECONFIGURATION (Step 2)

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Current CFN-[current CFN mod 8 + 8 ] |

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.2.14.5	Test requirement

After step 1, SS transmits a RADIO BEARER RECONFIGURATION message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER SETUP message.

#### 8.2.2.15	Radio Bearer Reconfiguration from CELL_FACH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.2.15.1		Definition

8.2.2.15.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RECONFIGURATION message, which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient” with criticality defined as “Reject”. Then it shall transmit a RADIO BEARER RECONFIGURATION FAILURE message setting “protocol error” in IE “failure cause” and also setting “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a RADIO BEARER RECONFIGURATION message when the RADIO BEARER RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit RADIO BEARER RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.15.3	Test purpose

To confirm that the UE transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RECONFIGURATION message which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”, with criticality defined as “Reject”.

To confirm that the UE transmits a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RECONFIGURATION message including some IEs set to invalid value.

8.2.2.15.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE shall keep the old configuration and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC indicating “protocol error” in IE “failure cause” and also set “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration when SS transmits RADIO BEARER RECONFIGURATION message including some IEs set to invalid value. The UE transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | RADIO BEARER RECONFIGRATION FAILURE | The UE does not change the configuration. |
| 3 | ( | RADIO BEARER RECONFIGURATION | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration |
| 5 | ( | RADIO BEARER RECONFIGRATION FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

The contents of RADIO BEARER RECONFIGRATION message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

RADIO BEARER RECONFIGURATION FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

RADIO BEARER RECONFIGURATION (Step 3)

The contents of RADIO BEARER RECONFIGRATION message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 2 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

RADIO BEARER RECONFIGURATION FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.2.15.5	Test requirement

After step1 the UE shall keep its old configuration and transmit a RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, which contain the cause “protocol error” in IE “failure cause” and “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

#### 8.2.2.16	Radio Bearer Reconfiguration from CELL_FACH to CELL_ FACH: Success (Continue and Stop)

8.2.2.16.1	Definition

8.2.2.16.2	Conformance requirement

The UE shall continue or stop the uplink transmission when the UTRAN indicate stop or continue uplink transmission in radio bearer reconfiguration procedure.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.16.3	Test purpose

To confirm that the UE reconfigures new radio bearer and have the uplink transmission according to a RADIO BEARER RECONFIGURATIO message which indicates that uplink transmission is continued.

To confirm that the UE reconfigures new radio bearer and don’t transmit data according to a RADIO BEARER RECONFIGURATIO message which indicates that uplink transmission is stopped.

8.2.2.16.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which includes IE” RB stop/continue” set to “continue”. The UE reconfigures new radio bearer and transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC. The UE communicates with the SS after transmission the RADIO BEARER RECONFIGURATION COMPLETE message. Then, SS transmits a RADIO BEARER RECONFIGURATION message including IE” RB stop/continue” set to “stop”. The UE reconfigures new radio bearer and transmits RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.  The UE shall not transmit any uplink data without Signalling message after transmission the RADIO BEARER RECONFIGURATION COMPLETE message.Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | The message includes IE “RB stop/continue” for one of the signalling radio bearer. |
| 2 |  |  | The UE select PRACH and S-CCPCH, using SIB5 or SIB6. |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |
| 4 |  |  | The SS Shall communicate with the UE. |
| 5 | ( | RADIO BEARER RECONFIGURATION | This message include IE” RB stop/continue “. |
| 6 |  |  | The UE select PRACH and S-CCPCH, using SIB5 or SIB6. |
| 7 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |
| 8 |  |  | The SS shall not receive any data from the UE without Signalling message. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RB information to reconfigure list |  |
| RB information to reconfigure -RB identity | 5 |
| -RB stop/continue | Set to “continue” |

RADIO BEARER RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| RB information to reconfigure list |  |
| RB information to reconfigure -RB identity | 5 |
| -RB stop/continue | Set to “continue” |

8.2.2.16.5	Test requirement

After step 3 the UE shall communicate with the SS using new configuration.

After step 7 the UE shall communicate with the SS using new configuration, but shall not transmit any data to the SS without signalling message.

#### 8.2.2.17	Radio Bearer Reconfiguration from CELL_FACH to CELL_FACH: Success

8.2.2.17.1		Definition

8.2.2.17.2	Conformance requirement

The UE shall correctly reconfigure a radio bearer according to a RADIO BEARER RECONFIGURATION message which is communicate with the UTRAN on the new radio bearer and a transition from CELL_FACH to CELL_FACH in the another cell.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.17.3	Test purpose

To confirm that the UE establishes a new radio bearer by following a RADIO BEARER RECONFIGURATION message received from the SS.

8.2.2.17.4	Method of test

Initial Condition

System Simulator: 1 cell.

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE which includes the new transport channel parameter reconfigure for transit. The UE reconfigures the new transport cannel and transmits a RADIO BEARER RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 |  |  | The UE select PRACH and S-CCPCH using SIB5 or SIB6. |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE |  |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 2)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS“ in Annex A.

8.2.2.17.5	Test requirement

After step 3 the UE shall change its radio bearer configuration and be in CELL_FACH

After step 4 the UE shall communicate with the SS on the DCCH and DTCH, using the common physical channel.

#### 8.2.2.18	Radio Bearer Reconfiguration from CELL_FACH to CELL_FACH: Failure (Cell re-selection)

8.2.2.18.1	Definition

8.2.2.18.2	Conformance requirement

The UE shall initiate the cell reselection procedure when the UE cannot use the assigned physical channel according to a RADIO BEARER RECONFIGURATION message, during the transition from CELL_FACH to CELL_FACH. After the UE completes cell update procedure, the UE transmits RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “cell reselection” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.18.3	Test purpose

To confirm that the UE initiates a cell update because it cannot access the assigned physical channel in current cell, when attempting to transit from CELL_FACH to CELL_FACH state during the execution of radio bearer reconfiguration procedure.

To confirm that the UE transmit RADIO BEARER SETUP FAILURE message after complete a cell update.

8.2.2.18.4	Method of test

Initial Condition

System Simulator: 2 cells Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state in cell 1. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE, which includes the new radio bearer parameters. After transmitting the RADIO BEARER RECONFIGURATION message, the SS shall not reconfigure L1 in accordance to the settings in the message. At the same time, SS begins to broadcast the BCCH in a cell 2. The UE recognizes that it cannot reconfigure the new radio bearer and wants to revert to the old configuration, but the UE cannot revert to the old configuration. The UE shall select cell 2 by performing cell re-selection. The UE shall move to CELL FACH and transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmit RADIO BEARER RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” cell reselection” to IE “failure cause”. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( |  |  |
| 2 | ( | RADIO BEARER RECONFIGURATION |  |
| 3 |  |  | The SS does not reconfigure the new radio bearer in cell 1. |
| 4 | ( | BCCH | The SS transmit the BCCH in the cell 2. |
| 5 |  |  | The UE shall detect a failure to use the assigned common physical channel and try to perform a cell reselection. |
| 6 | ( | CELL UPDATE | The value “cell reselection” shall be set in IE ”cell update cause”. |
| 7 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 8 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 9 | ( | RADIO BEARER RECONFIGURATION FILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

Use the same message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A:

CELL UPDATE (Step 6)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 8)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RECONFIGURATION FAILURE (Step 9)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.18.5	Test requirement

After step 4the UE shall discover the presence of cell 2, enter CELL_FACH state, and initiate a cell update procedure in that cell.

After step 7 UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 8 UE transmits RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC, setting the value ”cell reselection” to IE “failure cause”.

#### 8.2.2.19	Radio Bearer Reconfiguration from CELL_DCH to CELL_DCH: Success (Subsequently received)

8.2.2.19.1		Definition

8.2.2.19.2	Conformance requirement

If the UE receives a RADIO BEARER RECONFIGURATION message before the UE configures the radio bearer according to the previous RADIO BEARER RECONFIGURATION message, the UE shall ignore the new RADIO BEARER RECONFIGURATION message and configure according to the previous RADIO BEARER RECONFIGURATION message. Finally, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.19.3	Test purpose

If the UE receives another RADIO BEARER RECONFIGURATION message before the UE configures the radio bearer according to a previous RADIO BEARER RECONFIGURATION message, the UE shall ignore the new RADIO BEARER RECONFIGURATION message and configure according to the previous RADIO BEARER RECONFIGURATION message. Finally, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

8.2.2.19.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. SS transmits a RADIO BEARER RECONFIGURATION message to the UE before the UE configures the radio bearer according to the RADIO BEARER RECONFIGURATION message prior to this new message. The UE ignores the new RADIO BEARER RECONFIGURATION message and configures according to the former RADIO BEARER RECONFIGURATION message. On completion of radio bearer configuration, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Including IE ”Uplink DPCH info” |
| 2 | ( | RADIO BEARER RECONFIGURATION | Sent before the “activation time” in step 1 has elapsed |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE | The UE ignores the RADIO BEARER RECONFIGURATION message in step 2 and confirms configuration according to the RADIO BEARER RECONFIGURATION message in step 1. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.2.19.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the RADIO BEARER RECONFIGURATION message in step 1.

#### 8.2.2.20	Radio Bearer Reconfigure from CELL_FACH to CELL_DCH: Success (Subsequently received)

8.2.2.20.1	Definition

8.2.2.20.2	Conformance requirement

If the UE receives a RADIO BEARER RECONFIGURATION message before the UE configures the radio bearer according to the previous RADIO BEARER RECONFIGURATION message, the UE shall ignore the new RADIO BEARER RECONFIGURATION message and configure according to the previous RADIO BEARER RECONFIGURATION message. Finally, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.20.3	Test purpose

To confirm that if the UE receives another RADIO BEARER RECONFIGURATION message before the UE configures the radio bearer according to a previous RADIO BEARER RECONFIGURATION message, the UE shall ignore the new RADIO BEARER RECONFIGURATION message and configure according to the previous RADIO BEARER RECONFIGURATION message. Finally, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

8.2.2.20.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH(state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. SS transmits a RADIO BEARER RECONFIGURATION message to the UE before the UE configures the radio bearer according to the RADIO BEARER RECONFIGURATION message prior to this new message. The UE ignores the new RADIO BEARER RECONFIGURATION message and configures according to the former RADIO BEARER RECONFIGURATION message. On completion of radio bearer configuration, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Including IE ”Uplink DPCH info” |
| 2 | ( | RADIO BEARER RECONFIGURATION | SS send this message before the expiry of activation time specified in RADIO BEARER SETUP message of step 1. |
| 3 | ( | RADIO BEARER RECONFIGURATION COMPLETE | The UE ignores the RADIO BEARER RECONFIGURATION message in step 2 and confirms configuration according to the RADIO BEARER RECONFIGURATION message in step 1. |

Specific Message Contents

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical as “Packet to CELL_FACH from CELL_DCH in PS” found in Annex A with the following exceptions:

RADIO BEARER RECONFIGURATION (step 1)

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.2.20.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the RADIO BEARER RECONFIGURATION message in step 1.

#### 8.2.2.21	Radio Bearer Reconfiguration from CELL_DCH to CELL_PCH: Success

8.2.2.21.1	Definition

8.2.2.21.2	Conformance requirement

The UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message and transit from CELL_DCH to CELL_PCH when receives a RADIO BEARER RECONFIGURATION message. And then, the UE shall reconfigure radio bearers according to the RADIO BEARER RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.21.3	Test purpose

To confirm that the UE transmit RADIO BEARER RECONFIGURATION COMPLETE before entering CELL_PCH state after it received a RADIO BEARER RECONFIGURATION message and reconfigured its radio bearers. The UE is in CELL_PCH state of the same cell.

8.2.2.21.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message. The UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | RADIO BEARER RECONFIGURATION COMPLETE | The UE sends this message before state transition. |
| 3 |  |  | Reconfiguration of Radio Bearer after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.2.21.5	Test requirement

After step 1 the UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_DCH to CELL_PCH.

#### 8.2.2.22	Radio Bearer Reconfiguration from CELL_DCH to URA_PCH: Success

8.2.2.22.1	Definition

8.2.2.22.2	Conformance requirement

The UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message and transit from CELL_DCH to URA_PCH when receives a RADIO BEARER RECONFIGURATION message. And then, the UE shall reconfigure a radio bearer according to the RADIO BEARER RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.22.3	Test purpose

To confirm that the UE transmit RADIO BEARER RECONFIGURATION COMPLETE before entering URA_PCH state after it received a RADIO BEARER RECONFIGURATION message and reconfigured its radio bearers. The UE is in URA_PCH state of the same cell.

8.2.2.22.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the URA_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message. The UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into URA_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | RADIO BEARER RECONFIGURATION COMPLETE | The UE sends this message before state transition. |
| 3 |  |  | Reconfiguration of Radio Bearer after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.2.22.5	Test requirement

After step 1 the UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transits from CELL_DCH to URA_PCH.

#### 8.2.2.23	Radio Bearer Reconfiguration from CELL_FACH to CELL_PCH: Success

8.2.2.23.1	Definition

8.2.2.23.2	Conformance requirement

The UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message and transit from CELL_FACH to CELL_PCH when receive a RADIO BEARER RECONFIGURATION message. And then, the UE shall reconfigure radio bearers according to the RADIO BEARER RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.23.3	Test purpose

To confirm that the UE transmits RADIO BEARER RECONFIGURATION COMPLETE before entering CELL_PCH state after it received a RADIO BEARER RECONFIGURATION message and reconfigured its radio bearers. The UE is in CELL_PCH state of the same cell.

8.2.2.33.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH(state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message. The UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state again.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | RADIO BEARER RECONFIGURATION COMPLETE | The UE sends this message before state transition. |
| 3 |  |  | Reconfiguration of Radio Bearer after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.2.23.5	Test requirement

After step 1 the UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_DCH to CELL_PCH.

#### 8.2.2.24	Radio Bearer Reconfiguration from CELL_FACH to URA_PCH: Success

8.2.2.24.1	Definition

8.2.2.24.2	Conformance requirement

The UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message and transit from CELL_FACH to URA_PCH when receive a RADIO BEARER RECONFIGURATION message. And the UE shall reconfigure radio bearers according to the RADIO BEARER RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.2.24.3	Test purpose

To confirm that the UE transmits RADIO BEARER RECONFIGURATION COMPLETE before entering URA_PCH state after it received a RADIO BEARER RECONFIGURATION message and reconfigured its radio bearers. The UE is in URA_PCH state in the same cell.

8.2.2.24.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH(state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RECONFIGURATION message. The UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into URA_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state again.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | RADIO BEARER RECONFIGURATION COMPLETE | The UE sends this message before state transition. |
| 3 |  |  | Reconfiguration of Radio Bearer after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.2.24.5	Test requirement

After step 1 the UE transmits RADIO BEARER RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_FACH to URA_PCH.

### 8.2.3	Radio Bearer Release

#### 8.2.3.1	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Success

8.2.3.1.1	Definition

8.2.3.1.2	Conformance requirement

The UE shall correctly release a radio bearer according to a RADIO BEARER RELEASE message.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.1.3	Test purpose

To confirm that the UE release the existing radio bearer according to a RADIO BEARER RELEASE message received from the SS.

8.2.3.1.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH+DTCH_DCH (state 6-9) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELEASE message to the UE. The UE release the radio bearer and transmits a RADIO BEARER RELEASE COMPLETE message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 |  |  | Release the radio bearer |
| 3 | ( | RADIO BEARER RELEASE COMPLETE |  |

Specific Message Contents

RADIO BEARER RELEASE

The contents of RADIO BEARER RELEASE message are indicated as “Speech in CS” found in default message content clause 9 of TS 34.108.

8.2.3.1.5	Test requirement

After step 1 the UE shall release its radio bearers.

After step 3 the UE shall stop communicating on the released radio bearers, no uplink transmission shall be observed originating from the released link. The remaining radio bearers shall continue to be operational.

#### 8.2.3.2	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Failure (Unsupported configuration)

8.2.3.2.1	Definition

8.2.3.2.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RELEASE message which includes unsupported configuration parameters and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting value “configuration unsupported” in IE “ failure cause”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.2.3	Test purpose

To confirm that the UE keeps its current configuration and transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, if the received RADIO BEARER RELEASE message indicates an unsupported configuration parameters for the UE.

8.2.3.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH+DTCH_DCH (state 6-9) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELAESE message to the UE specifying a frequency which is not supported by the UE. The UE transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC indicating “configuration unsupported” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE | Including unsupported configuration by the UE |
| 2 | ( | RADIO BEARER RELAESE FAILURE | The UE does not change the radio bearer. |

Specific Message Contents

RADIO BEARER RELEASE

The contents of RADIO BEARER RELEASE message in this test case is identical as “Speech in CS” found in default message content clause 9 of TS 34.108 with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 63984 |
| - UARFCN downlink(Nd) | Not Present |

RADIO BEARER RELEASE FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.3.2.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC with the IE “failure cause” set to “configuration unsupported”. The UE shall able to continue receiving and sending user data.

#### 8.2.3.3	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Failure (Physical channel failure and reversion to old configuration)

8.2.3.3.1	Definition

8.2.3.3.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to configure the new radio bearer by timer T312 expiry and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “ failure cause”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.3.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if the UE fails to release the radio bearer according to a RADIO BEARER RELEASE message by timer T312 expiry.

8.2.3.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH+DTCH_DCH (state 6-9) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELEASE message but it does not configure L1 correspondingly. This causes the UE to fail to release the radio bearer, and after T312 expiry the UE reverts to the old configuration. The UE then transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which specifies “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 |  |  | The SS does not configure L1 to reflect the release of the indicated bearer. |
| 3 | ( | RADIO BEARER RELEASE FAILURE | After T312 expiry, the UE finds that it fails to release a radio bearer and reverts to the old configuration. |

Specific Message Contents

RADIO BEARER RELEASE

The contents of RADIO BEARER RELEASE message in this test case is identical as “Speech in CS” found in default message content clause 9 of TS 34.108

RADIO BEARER RELEASE FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.3.3.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which includes the value “physical channel failure” in IE “failure cause”.

#### 8.2.3.4	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Failure(Physical channel failure and reversion failure)

8.2.3.4.1	Definition

8.2.3.4.2	Conformance requirement

The UE shall perform a cell update procedure when the UE fails to revert to the old configuration after the detection of physical channel failure in the radio bearer release procedure. After the UE completes cell update procedure, the UE transmits RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.4.3	Test purpose

To confirm that the UE transmits RADIO BEARER RELEASE FAILURE message after completes a cell update procedure when the UE cannot revert to the old configuration after encountering a physical channel failure during the execution of a radio bearer release procedure.

8.2.3.4.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, Cell.2 is inactive

UE: CS-DCCH+DTCH_DCH (state 6-9) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS begins to broadcast the BCCH in cell 2 with a lower power level than for cell 1. At the same time, it transmits a RADIO BEARER RELAESE message to the UE but does not configure L1. As a result, the UE fails to release the radio bearer properly and tries to revert to the old configuration. But the SS deletes the old radio bearer so the UE shall find the availability of cell 2 and transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits RADIO RELEASE FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” physical channel failure”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to transmit the BCCH for cell 2 but at a lower power level than cell 1. |
| 2 | ( | RADIO BEARER RELEASE |  |
| 3 |  |  | The SS does not configure L1 and deletes the old configuration. This is expected to cause the UE to fail in the release the radio bearer and can not revert to the old configuration. |
| 4 | ( | CELL UPDATE | The UE shall find cell 2 and enter CELL_FACH state. This message include the value “radio link failure” set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | RADIO BEARER RELEASE FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

RADIO BEARER RELEASE

The contents of RADIO BEARER RELEASE message in this test case are identical as “Speech in CS” found in default message content clause 9 of TS 34.108.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RELEASE FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RELEASE FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.3.4.5	Test requirement

After step 3 the UE shall find the presence of cell 2, enter CELL_FACH state, and transmits CELL UPDATE message on the uplink CCCH.

After step 5 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 6 the UE shall transmit RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.3.5	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.3.5.1	Definition

8.2.3.5.2	Conformance requirement

If the UE receives a RADIO BEARER RELAESE message whilst reconfiguring due to a radio bearer message other than RADIO RELEASE SETUP, it shall keep its configuration as if the RADIO BEARER SETUP message had not been received. Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.5.3	Test purpose

To confirm that if the UE receives a RADIO BEARER RELEASE message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RELEASE, it shall keep its configuration as if the RADIO BEARER RELEASE message had not been received and complete the reconfiguration according to the previously received message. 8.2.3.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message to the UE. The SS transmits a RADIO BEARER SETUP message before the “activation time” indicated in the RADIO BEARER SETUP message expires. When the UE receives the RADIO BEARER SETUP message, the UE shall keep the configuration as if it had not received the RADIO BEARER RELEASE message and shall transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO BEARER RELEASE FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER SETUP COMPLETE message on DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP |  |
| 2 | ( | RADIO BEARER RELEASE | Message sent before the “Activation time” indicated in the message of step 1 has elapsed. |
| 3 | ( | RADIO BEARER RELEASE FAILURE | The UE does not change the configuration due to the reception of RADIO BEARER RELEASE message. |
| 4 | ( | RADIO BEARER SETUP COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO SETUP RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Current CFN-[current CFN mod 8 + 8 ] |

RADIO BEARER RELEASE (Step 2)

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A. Information element(s) to be changed are listed below:

RADIO BEARER RELEASE FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.3.5.5	Test requirement

After step 1,  SS transmits a RADIO BEARER RELEASE message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER RELEASE message and shall transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

#### After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER SETUP message. 8.2.3.6	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.3.6.1	Definition

8.2.3.6.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RELEASE message which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. It shall transmit a RADIO BEARER RELEASE FAILURE message which contains value “protocol error” in IE “ failure cause” and value “Information element value not comprehended” in IE “ Protocol error cause”. The UE shall keep existing configuration before reception of a RADIO BEARER RELEASE message when the RADIO BEARER RELEASE message include some IEs set to invalid value, and then the UE shall transmit RADIO BEARER RELEASE FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.6.3	Test purpose

To confirm that the UE transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RELEASE message, which uses a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”.

To confirm that the UE transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RELEASE message including some IEs set to invalid value.

8.2.3.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-DCCH+DTCH_DCH (state 6-9) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELAESE message to the UE which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE keeps the old configuration and transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC. This message shall indicate “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits RADIO BEARER RELEASE message including some IEs set to invalid value. The UE transmits RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 | ( | RADIO BEARER RELEASE FAILURE | The UE shall not change the configuration. |
| 3 | ( | RADIO BEARER RELEASE | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration |
| 5 | ( | RADIO BEARER RELEASE FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

RADIO BEARER RELEASE (Step1)

The contents of RADIO BEARER RELEASE message in this test case is identical as “Speech in CS” found in default message content clause 9 of TS 34.108 with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

RADIO BEARER RELEASE FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

RADIO BEARER RELEASE (Step 3)

The contents of RADIO BEARER RELEASE message in this test case is identical as “Speech in CS” found in default message content clause 9 of TS 34.108 with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

RADIO BEARER RELEASE FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.3.6.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, which is set to “protocol error” in IE “failure cause” and is set to “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

#### 8.2.3.7	Radio Bearer Release for transition from CELL_DCH to CELL_FACH: Success

8.2.3.7.1	Definition

8.2.3.7.2	Conformance requirement

The UE shall correctly release a radio bearer according to a RADIO BEARER RELEASE message, when the common physical channel are requested to be used for the remaining radio bearers.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.7.3	Test purpose

To confirm that the UE release the existing the radio bearer according to a RADIO BEARER RELEASE message received from the SS.

8.2.3.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DTCH+DCCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELEASE message to the UE. The UE release the radio bearer and transmits a RADIO BEARER RELEASE COMPLETE message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE | SS releases the radio bearer in the fashion specified in the message and allocate common channel resources to carry the remaining radio bearers. |
| 2 |  |  | The UE select PRACH and S-CCPCH using SIB5 and SIB6 after entering CELL FACH state. The UE shall release radio bearers on dedicated transport channels, and reconfigure the remaining radio bearers using the selected common control channel. |
| 3 | ( | RADIO BEARER RELEASE COMPLETE | UE shall be able to continue communication over the remaining radio bearers using the common control channels. |

Specific Message Contents

RADIO BEARER RELEASE (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS” in Annex A.

8.2.3.7.5	Test requirement

After step 3 the UE shall release the specified radio bearer(s) and cease any further uplink transmission from these radio bearer(s)..

#### 8.2.3.8	Radio Bearer Release for transition from CELL_DCH to CELL_FACH: Failure (Cell re-selection)

8.2.3.8.1	Definition

8.2.3.8.2	Conformance requirement

The UE shall initiate the cell update procedure when the UE cannot use the assigned physical channel according to a RADIO BEARER RELEASE message as the transition from CELL_DCH to CELL_FACH. After the UE completes cell update procedure, the UE transmits RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “cell reselection”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.8.3	Test purpose

To confirm that the UE transmits RADIO BEARER RELEASE FAILURE message after the UE completes a cell update procedure when the UE cannot use the assigned physical channel according to a RADIO BEARER RELEASE message as the transition from CELL_DCH to CELL_FACH.

8.2.3.8.4	Method of test

Initial Condition

System Simulator: 2 cells（ No.1 is active, No.2 is inactive）

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state in cell No.1. The SS begins to broadcast the BCCH in cell No.2 and transmits a RADIO BEARER RELEASE message as the transition from CELL_DCH to CELL_FACH. The UE cannot use the assigned physical channel as the SS does not transmit any data on the DL common channel in cell No.1. Then the UE reselects cell 2 and initiates the cell update procedure in cell No.2. The UE transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmits RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” cell reselection”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS broadcasts BCCH in cell No.2. |
| 2 | ( | RADIO BEARER RELEASE | Assigned the transition from CELL_DCH to CELL_FACH |
| 3 |  |  | The UE cannot use the assigned the physical channel. |
| 4 | ( | CELL UPDATE | The UE finds a new cell（No.2） and begins a cell update procedure. The value “cell reselection” shall be set in IE ”cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | RADIO BEARER RELEASE FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

RADIO BEARER RELEASE

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RELEAS FAILURE (Step 6)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.3.8.5	Test requirement

After step 3 the UE shall find a new cell No.2 and enter to CELL_FACH state. Then the UE shall initiate a cell update procedure in cell No.2.

After step 4 UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 5 UE shall transmit RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the value ”cell reselection” to IE “failure cause”.

#### 8.2.3.9	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Success

8.2.3.9.1		Definition

8.2.3.9.2	Conformance requirement

The UE shall correctly release a radio bearer according to a RADIO BEARER RELEASE message.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.9.3	Test purpose

To confirm that an UE, in state CELL_FACH, releases the radio access bearers on RACH and FACH transport channels. After the release, it shall access the affected radio bearers on the newly allocated DCH transport channel.

8.2.3.9.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RELEASE message to the UE. In this message, SS commands the UE to release radio bearers on RACH and FACH. At the same time, SS allocates DCH to support the affected radio bearers. The UE shall release the indicated radio bearer and transmits a RADIO BEARER RELEASE COMPLETE message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 |  |  | UE shall release the radio access bearers carried by RACH and FACH transport channels. |
| 3 | ( | RADIO BEARER RELEASE COMPLETE |  |

Specific Message Contents

RADIO BEARER RELEASE (Step 1)

Use the same message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

8.2.3.9.5	Test requirement

After step3 the UE shall stop communicating on the released radio bearers, and resume all stopped radio bearer using the dedicated physical channel allocated.

#### 8.2.3.10	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Failure (Unsupported configuration)

8.2.3.10.1		Definition

8.2.3.10.2	Conformance requirement

The UE shall keep its old configuration when it receives a RADIO BEARER RELEASE message which specifies unsupported configuration parameters for the UE. Then the UE shall transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which, setting value “configuration unsupported” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.10.3	Test purpose

To confirm that the UE keeps its configuration and transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if the received RADIO BEARER RELEASE message requests for unsupported configuration parameters for the UE.

8.2.3.10.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RELAESE message to the UE, referring to a frequency which cannot be supported by the UE. The UE shall transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC and set “configuration unsupported” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE | The message contains a configuration not supported by the UE |
| 2 | ( | RADIO BEARER RELAESE FAILURE | The UE shall not change the radio bearer configuration. |

Specific Message Contents

RADIO BEARER RELEASE

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 63984 |
| - UARFCN downlink(Nd) | Not Present |

RADIO BEARER RELEASE FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.3.10.5	Test requirement

After step 2 the UE shall keep its old configuration and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, stating the reason “configuration unsupported” in IE “failure cause”.

#### 8.2.3.11	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion to old configuration)

8.2.3.11.1		Definition

8.2.3.11.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to configure the new radio bearer before T312 timer expiry. Then it shall transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the value “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.11.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if the UE fails to release the radio bearer in accordance the specified settings in RADIO BEARER RELEASE message by T312 timer expiry.

8.2.3.11.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RELEASE message and does not configure L1. The UE is expected to encounter a failure while releasing the radio bearer. After T312 timer expiry, the UE shall revert to the old radio bearer configuration, so the UE transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 |  |  | The SS does not configure L1. |
| 3 | ( | RADIO BEARER RELEASE FAILURE | After T312 expiry the UE fails to release a radio bearer and reverts to the old configuration. |

Specific Message Contents

RADIO BEARER RELEASE

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

RADIO BEARER RELEASE FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.3.11.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the value “physical channel failure” in IE “failure cause”.

#### 8.2.3.12	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion failure)

8.2.3.12.1		Definition

8.2.3.12.2	Conformance requirement

The UE shall perform a cell update procedure when the UE fails to revert to the old configuration after the detection of physical channel failure in the radio bearer release procedure. After the UE completes cell update procedure, the UE transmits RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.12.3	Test purpose

To confirm that the UE transmits RADIO BEARER RELEASE FAILURE message after it completes a cell update procedure when the UE cannot revert to the old configuration, following a physical channel failure during the radio bearer release.

8.2.3.12.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell.1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108 in cell No.1

Test Procedure

The UE is in the CELL_FACH state in cell 1. The SS begins to broadcast the BCCH in cell 2 and then transmits a RADIO BEARER RELAESE message to the UE, but it does not configure L1. This is expected to cause the UE to experience a failure to release the radio bearer and it subsequently tries to revert to the old configuration. The SS deletes the old radio bearer, so the UE shall find cell 2 and transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits RADIO RELEASE FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” physical channel failure”. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to transmit the BCCH in a cell 2. |
| 2 | ( | RADIO BEARER RELEASE |  |
| 3 |  |  | The SS does not configure L1 and deletes the old configuration so the UE cannot release the radio bearer and also fails revert to the old configuration. |
| 4 | ( | CELL UPDATE | The UE finds a new cell 2 and enter CELL_FACH state. This message include the value “radio link failure” set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | RADIO BEARER RELEASE FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

RADIO BEARER RELEASE

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

RADIO BEARER RELEASE FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RELEASE FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.3.12.5	Test requirement

After step 3 the UE shall find the presence of cell 2, enter CELL_FACH state, and transmit a CELL UPDATE message on the uplink CCCH.

After step 5 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 6 the UE shall transmit RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.3.13	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.3.13.1		Definition

8.2.3.13.2	Conformance requirement

If the UE receives a RADIO BEARER RELEASE message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RELEASE, it shall keep its configuration as if the RADIO BEARER RELEASE message had not been received.Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.13.3	Test purpose

To confirm that if the UE receives a RADIO BEARER RELEASE message whilst reconfiguring due to a radio bearer message other than RADIO BEARER RELEASE, it shall keep its configuration as if the RADIO BEARER RELEASE message had not been received and complete the reconfiguration according to the previously received message. 8.2.3.13.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER SETUP message to the UE. The SS transmits a RADIO BEARER RELEASE message before the “activation time” indicated in the RADIO BEARER SETUP message expires. When the UE receives the RADIO BEARER SETUP message, the UE shall keep the configuration as if it had not received the RADIO BEARER SETUP message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO BEARER SETUP FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER SETUP COMPLETE message on DCCH using AM RLC. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | The UE receive any message other than RADIO BEARER RELEASE. (e.g. RADIO BEARER SETUP) |
| 2 | ( | RADIO BEARER SETUP | Sent before the expiry stated in IE “Activation Time” of message in step 1. |
| 3 | ( | RADIO BEARER RELEASE FAILURE | The UE does not change the configuration due to the reception of RADIO BEARER SETUP message.. |
| 4 | ( | RADIO BEARER SETUP COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER SETUP (Step 1)

The contents of RADIO BEARER SETUP message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A. Information element(s) to be changed are listed below:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Current CFN-[current CFN mod 8 + 8 ] |

RADIO BEARER RELEASE (Step 2)

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | Current CFN-[current CFN mod 8 + 8 ] |

RADIO BEARER RELEASE FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.3.13.5	Test requirement

After step 1, SS transmits a RADIO BEARER RELEASE message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER RELEASE message and shall transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

#### After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO SETUP message. 8.2.3.14	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.3.14.1	Definition

8.2.3.14.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a RADIO BEARER RELEASE message which uses a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. It shall transmit a RADIO BEARER RELEASE FAILURE message which indicate the value “protocol error” in IE “failure cause” and setting “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a RADIO BEARER RELEASE message when the RADIO BEARER RELEASE message include some IEs set to invalid value, and then the UE shall transmit RADIO BEARER RELEASE FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.14.3	Test purpose

To confirm that the UE transmits RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RELEASE message which uses a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”.

To confirm that the UE transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC if it receives a RADIO BEARER RELEASE message including some IEs set to invalid value.

8.2.3.14.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS_DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RELAESE message to the UE containing a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE keeps the old configuration and transmits a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, which shall indicate the reason “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits RADIO BEARER RELEASE message including some IEs set to invalid value. The UE transmit RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 | ( | RADIO BEARER RELEASE FAILURE | The UE shall not change its current configuration. |
| 3 | ( | RADIO BEARER RELEASE | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration |
| 5 | ( | RADIO BEARER RELEASE FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

RADIO BEARER RELEASE (Step 3)

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX Indicator | Undefined value |

RADIO BEARER RELEASE FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

RADIO BEARER RELEASE (Step 3)

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 4 |

RADIO BEARER RELEASE FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.3.14.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting “protocol error” in IE “failure cause” and also indicating “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit RADIO BEARER RELEASE FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

#### 8.2.3.15	Radio Bearer Release for transition from CELL_FACH to CELL_FACH: Success

8.2.3.15.1	Definition

8.2.3.15.2	Conformance requirement

The UE shall correctly release a radio bearer according to the RADIO BEARER RELEASE message received.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.15.3	Test purpose

To confirm that the UE release the existing the radio bearer(s) according to the RADIO BEARER RELEASE message received from the SS.

8.2.3.15.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a RADIO BEARER RELEASE message to the UE. The UE release the radio bearer and transmits a RADIO BEARER RELEASE COMPLETE message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 |  |  | The UE select PRACH and S-CCPCH using SIB5 and SIB6. The UE shall release the requested radio bearer(s), and stop transmitting using these radio bearer(s). |
| 3 | ( | RADIO BEARER RELEASE COMPLETE |  |

Specific Message Contents

RADIO BEARER RELEASE

Use the same message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A.

8.2.3.15.5	Test requirement

After step 1 the UE shall cease the transmission and reception of the affected radio bearers.

After step 3 the UE shall stop communicating on radio bearers to be released.

#### 8.2.3.16	Radio Bearer Release for transition from CELL_DCH to CELL_DCH: Success (Subsequently received)

8.2.3.16.1		Definition

8.2.3.16.2	Conformance requirement

If the UE receives a RADIO BEARER RELEASE message before the UE releases the radio bearer according to the previous RADIO BEARER RELEASE message, the UE shall ignore the new RADIO BEARER RELEASE message and releases according to the previous RADIO BEARER RELEASE message. Finally, the UE shall transmit RADIO BEARER RELEASE COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.16.3	Test purpose

To confirm that if the UE receives a new RADIO BEARER RELEASE message before the UE releases the radio bearer according to a previous RADIO BEARER RELEASE message it ignore the new RADIO BEARER RELEASE message and configures according to the previous RADIO BEARER RELEASE message received.

8.2.3.16.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. When the SS transmits a RADIO BEARER RELEASE message to the UE before the UE releases the radio bearer, the UE ignores the second RADIO BEARER RELEASE message and releases according to the previous RADIO BEARER RELEASE message received. Finally, the UE shall transmit RADIO BEARER RELEASE COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 | ( | RADIO BEARER RELEASE | Message sent before. the expiry of “activation time” specified in message of step 1. |
| 3 | ( | RADIO BEARER RELEASE COMPLETE | The UE ignores the RADIO BEARER RELEASE message in step 2 and confirms release according to the RADIO BEARER RELEASE message in step 1. |

Specific Message Contents

RADIO BEARER RELEASE (Step 1)

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

RADIO BEARER RELEASE (Step 2)

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A.

8.2.3.16.5	Test requirement

After step 2 the UE shall releases the radio bearer specified in the first RADIO BEARER RELEASE message and transmit an RADIO BEARER RELEASE COMPLETE message on the DCCH using AM RLC.

#### 8.2.3.17	Radio Bearer Release for transition from CELL_FACH to CELL_DCH: Success (Subsequently received)

8.2.3.17.1	Definition

8.2.3.17.2	Conformance requirement

If the UE receives a RADIO BEARER RELEASE message before the UE releases the radio bearer according to the previous RADIO BEARER RELEASE message, the UE shall ignore the new RADIO BEARER RELEASE message and releases according to the previous RADIO BEARER RELEASE message. Finally, the UE shall transmit RADIO BEARER RELEASE COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.3

8.2.3.17.3	Test purpose

To confirm that if the UE receives a new RADIO BEARER RELEASE message before the UE releases the radio bearer according to a previous RADIO BEARER RELEASE message it ignore the new RADIO BEARER RELEASE message and configures according to the previous RADIO BEARER RELEASE message received.

8.2.3.17.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The UE is in the CELL_DCH state. When the SS transmits a RADIO BEARER RELEASE message to the UE before the UE releases the radio bearer, the UE ignores the second RADIO BEARER RELEASE message and releases according to the previous RADIO BEARER RELEASE message received. Finally, the UE shall transmit RADIO BEARER RELEASE COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 | ( | RADIO BEARER RELEASE | Sent before the expiry stated in IE “Activation Time” of RADIO BEARER RELEASE message in step 1. |
| 3 | ( | RADIO BEARER RELEASE COMPLETE | The UE ignores the RADIO BEARER RELEASE message in step 2 and confirms release according to the RADIO BEARER RELEASE message in step 1. |

Specific Message Contents

RADIO BEARER RELEASE

The contents of RADIO BEARER RELEASE message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

(Step 1)

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.3.17.5	Test requirement

After step 2 the UE shall releases the radio bearer specified in the first RADIO BEARER RELEASE message and transmit an RADIO BEARER RELEASE COMPLETE message on the DCCH using AM RLC.

#### 8.2.3.18	Radio Bearer Release from CELL_DCH to CELL_PCH: Success

8.2.3.18.1	Definition

8.2.3.18.2	Conformance requirement

The UE shall transmit RADIO BEARER RELEASE COMPLETE message before completes transition from CELL_DCH to CELL_PCH when receives a RADIO BEARER RELEASE message. And then, the UE shall release radio bearers according to the RADIO BEARER Release message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.3.18.3	Test purpose

To confirm that the UE transmits RADIO BEARER RELEASE COMPLETE before entering CELL_PCH state after it received a RADIO BEARER RELEASE message and released its radio bearers. The UE is in CELL_PCH state of the same cell.

8.2.3.18.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELEASE message. The UE transmits RADIO BEARER RELEASE COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 | ( | RADIO BEARER RELEASE COMPLETE | The UE sends this message before completes state transition. |
| 3 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 4 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER RELEASE (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

PAGING TYPE 1 (Step 3)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.3.18.5	Test requirement

After step 1 the UE transmits RADIO BEARER RELEASE COMPLETE message to the UE on uplink DCCH using AM RLC before completes state transition.

#### 8.2.3.19	Radio Bearer Release from CELL_DCH to URA_PCH: Success

8.2.3.19.1	Definition

8.2.3.19.2	Conformance requirement

The UE shall transmit RADIO BEARER RELEASE COMPLETE message before completes transition from CELL_DCH to CELL_PCH when receives a RADIO BEARER RELEASE message. And then, the UE shall release radio bearers according to the RADIO BEARER Release message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.3.19.3	Test purpose

To confirm that the UE transmits RADIO BEARER RELEASE COMPLETE before entering CELL_PCH state after it received a RADIO BEARER RELEASE message and released its radio bearers. The UE is in CELL_PCH state of the same cell.

8.2.3.19.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RELEASE message. The UE transmit RADIO BEARER RELEASE COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RELEASE |  |
| 2 | ( | RADIO BEARER RELEASE COMPLETE | The UE sends this message before completes state transition. |
| 3 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 4 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

RADIO BEARER RELEASE (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |

PAGING TYPE 1 (Step 3)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.3.19.5	Test requirement

After step 1 the UE transmits RADIO BEARER RELEASE COMPLETE message to the UE on uplink DCCH using AM RLC before completes state transition.

### 8.2.4	Transport channel reconfiguration

#### 8.2.4.1	Transport channel reconfiguration from CELL_DCH to CELL_DCH (Hard handover to same radio frequency): Success with no transport channel type switching

8.2.4.1.1	Definition

8.2.4.1.2	Conformance requirement

The UE shall correctly reconfigure a radio bearer according to the TRANSPORT CHANNEL RECONFIGURATION message, which specifies a hard handover to another cell. After the completion of this procedure, the UE shall be able to communicate with the UTRAN on the new transport channel.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.1.3	Test purpose

To confirm that the UE reconfigures a new transport channel according to a TRANSPORT CHANNEL RECONFIGURATION message,  which also specifies that a hard handover to another cell be performed simultaneously.

8.2.4.1.4	Method of test

Initial Condition

System Simulator: 2 cells – cell 1 and cell 2 are both active

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes new transport channel parameters to be applied in cell 2. The UE shall reconfigure the new transport channel and then transmit a TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH of cell 2 using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONGURATION | Hard handover to cell 2. Including UE information elements(“TFS”I) |
| 2 |  |  | UE shall stop all uplink transmissions and reconfigure itself to use the new transport channel parameters |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS“ in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| TrCH Information Elements |  |
| -Uplink transport Channels |  |
| -Added or Reconfigured TrCH information list | Number of Transport blocks = 2 |
| -Downlink transport Channels |  |
| -Added or Reconfigured TrCH information list | Number of Transport blocks = 2 |
| Downlink information for each radio links | Same downlink UARFCN as used for cell 2 |
| - Primary CPICH info |  |
| - Primary Scrambling Code | 150 |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing Indicator | Initialise |

8.2.4.1.5	Test requirement

After step 1 the UE shall reconfigure the radio links affected by the changes for uplink and downlink DCH. The UE shall stop transmitting on the uplink of cell 1.

After step 3 the UE shall continue to communicate with the SS on the DCCH of cell 2, using the new Transport Format Set (TFS) applicable on the existing transport channel.

#### 8.2.4.2	Transport channel reconfiguration from CELL_DCH to CELL_DCH: Failure (Unsupported configuration)

8.2.4.2.1	Definition

8.2.4.2.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a TRANSPORT CHANNEL RECONFIGURATION message which includes unsupported configuration parameters and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.2.3	Test purpose

To confirm that the UE transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if the received TRANSPORT CHANNEL RECONFIGURATION message specifies unsupported configuration parameters.

8.2.4.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes unsupported configuration parameters of the UE. The UE transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, reporting the event “configuration unsupported” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONGURATION | Including unsupported configuration by the UE |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | The UE shall not change the settings used by the transport channel. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| TrCH Information Elements |  |
| -Uplink transport Channels |  |
| -Added or Reconfigured TrCH information list | Number of Transport blocks = 4096 |
| -Downlink transport Channels |  |
| -Added or Reconfigured TrCH information list | Selected value as the UE can not support. Number of Transport blocks = 4096 |

TRANSPORT CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.4.2.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, indicating “configuration unsupported” in IE “failure cause”.

#### 8.2.4.3	Transport channel reconfiguration from CELL_DCH to CELL_DCH: Failure (Physical channel failure and reversion to old configuration)

8.2.4.3.1	Definition

8.2.4.3.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to reconfigure the new physical channel by received TRANSPORT CHANNEL RECONFIGURATION message and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.3.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, if the UE fails to reconfigure the new transport channel according to a TRANSPORT CHANNEL RECONFIGURATION message.

8.2.4.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes new transport channel parameters but it does not reconfigure the new transport channel. Therefore, the UE cannot reconfigure them and have to revert to the old configuration. Then the UE shall transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting “physical channel failure” in IE “ failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONGURATION | Specifies a change in the TFS of the dedicated transport channel used. |
| 2 |  |  | The SS does not reconfigure the transport channel, leading to the UE unable to reconfigure the new transport channel. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | The UE reverts to the old configuration and transmits this message. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS” in Annex A.

TRANSPORT CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.4.3.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a TRANPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, and it shall set the value “physical channel failure” in IE “failure cause”.

#### 8.2.4.4	Transport channel reconfiguration from CELL_DCH to CELL_DCH: Failure (Physical channel failure and reversion failure)

8.2.4.4.1	Definition

8.2.4.4.2	Conformance requirement

The UE shall perform a cell update upon failure of reconfiguration for a transport channel because of physical channel failure and reversion failure for the transition from CELL_FACH to CELL_FACH in the same cell. After the UE completes cell update procedure, the UE transmits TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.4.3	Test purpose

To confirm that the UE transmits RADIO TRANSPORT CHANNEL RECONFIGURATION FAILURE message after it completes a cell update procedure when the UE cannot reconfigure the new transport channel due to a failure of L1 configuration, and subsequently fail to revert to the old configuration.

8.2.4.4.4	Method of test

Initial Condition

System Simulator: 2 cells – Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. SS begins to broadcast the BCCH of cell 2 using a power level lower than that applied for cell 1. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE. The message specifies a new set of transport channel parameters but the SS does not reconfigure L1 correspondingly. At the same time, SS deletes its current contexts for cell 1. As a result, the UE cannot reconfigure the new transport channel and shall attempt to revert to the old configuration. The UE shall find the presence of cell 2 and then transmit a a CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” physical channel failure”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | SS begins to transmit the BCCH for cell 2. |
| 2 | ( | TRANSPORT CHANNEL RECONGURATION | Specifies the use of a new setting for transport channel. |
| 3 |  |  | The SS does not reconfigure L1 and deletes the old configuration present in cell 1. |
| 4 |  |  | The UE fails to reconfigure a new transport channel. |
| 5 | ( | CELL UPDATE | The UE detects the presence of cell.2, and enters CELL_FACH state. This message includes the value “radio link failure” set in IE ”Cell update cause”. |
| 6 | ( | CELL UPDATE CONFIRM | This message includes IE “new U-RNTI” and IE “new C-RNTI”“. |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 8 | ( | TRANSPORT CHANNEL RECONGURATION FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

Use the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS” in Annex A.

CELL UPDATE (Step 5)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 6)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

TRANSPORT CHANNELRECONGURATION FAILURE (Step 8)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONGURATION” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.4.4.5	Test requirement

After step 4 the UE shall discover cell 2, enter CELL_FACH state, and then transmit a CELL UPDATE message on the uplink CCCH.

After step 6 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 7 the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.4.5	Transport Channel Reconfiguration from CELL_DCH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.4.5.1	Definition

8.2.4.5.2	Conformance requirement

If the UE receives a TRANSPORT CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than TRANSPORT CHANNEL RECONFIGURATION, it shall keep its configuration as if the TRANSPORT CHANNEL RECONFIGURATION message had not been received. Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.5.3	Test purpose

To confirm that if the UE receives a TRANSPORT CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than TRANSPORT CHANNEL RECONFIGURATION, it shall keep its configuration as if the TRANSPORT CHANNEL RECONFIGURATION message had not been received and complete the reconfiguration according to the previously received message. 8.2.4.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message before the “activation time” indicated in the RADIO BEARER RECONFIGURATION message expires. When the UE receives the TRANSPORT CHANNEL RECONFIGURATION message, the UE shall keep the configuration as if it had not received the TRANSPORT CHANNEL RECONFIGURATION message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the TRANSPORT CHANNEL RECONFIGURATION FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message on DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Including IE “Uplink DPCH info” |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION | Sent before the time specified in IE “Activation Time Info” of message in step 1 has elapsed. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | The UE shall not change the configuration due to the reception of TRANSPORT CHANNEL RECONFIGURATION message. |
| 4 | ( | RADIO BEARER RECONFIGURATION COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

For RADIO BEARER RECONFIGURATION in step 1, use the message sub-type indicated as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A.

TRANSPORT CHANNEL RECONFIGURATION (Step 2)

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the corresponding message found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time | Current CFN-[current CFN mod 8 + 8 ] |

TRANSPORT CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.4.5.5	Test requirement

After step 1, SS transmits a TRANSPORT CHANNEL RECONFIGURATION message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER SETUP message and shall transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

#### After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER RECONFIGURATION message. 8.2.4.6	Transport channel reconfiguration from CELL_DCH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.4.6.1	Definition

8.2.4.6.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a TRANSPORT CHANNEL RECONFIGURATION message which makes use of a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. Then it shall transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message with the value “protocol error” set in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a TRANSPORT CHANNEL RECONFIGURATION message when the TRANSPORT CHANNEL RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.6.3	Test purpose

To confirm that the UE transmits TRANSPORT CHANNEL RECONFIGRATION FAILURE message on the DCCH using AM RLC, if the received TRANSPORT CHANNEL RECONFIGURATION message comprises an undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”.

To confirm that the UE transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a TRANSPORT CHANNEL RECONFIGURATION message including some IEs set to invalid value.

8.2.4.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE shall keep the old configuration and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, specifying “protocol error” in IE “failure cause” and also indicating “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits TRANSPORT CHANNEL RECONFIGURATION message including some IEs set to invalid value. The UE transmits TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION | Contains an illegal value for a mandatory IE |
| 2 | ( | TRANSPORT CHANNEL RECONFIGRATION FAILURE | The UE does not change the configuration. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration |
| 5 | ( | TRANSPORT CHANNEL RECONFIGRATION FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical in Annex A for RRC tests with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

TRANSPORT CHANNEL RECONFIGURATION FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “ TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

TRANSPORT CHANNEL RECONFIGURATION (Step 3)

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical in Annex A for RRC tests with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

TRANSPORT CHANNEL RECONFIGURATION FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.4.6.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC. The message shall specify “protocol error” in IE “failure cause” and set value “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

#### 8.2.4.7	Transport channel reconfiguration from CELL_DCH to CELL_FACH: Success

8.2.4.7.1	Definition

8.2.4.7.2	Conformance requirement

The UE shall correctly reconfigure the transport channels according to TRANSPORT CHANNEL RECONFIGURATION message, after it is requested to perform a transition from CELL_DCH to CELL_FACH in the same cell in conjunction with the transport channel reconfiguration.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.7.3	Test purpose

To confirm that the UE reconfigures a new Transport channel according to a TRANSPORT CHANNEL RECONFIGURATION message received from the SS.

8.2.4.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits TRANSPORT CHANNEL RECONFIGURATION message to the UE and the UE performs a state transition from CELL_DCH to CELL_FACH in the same cell. The UE then reconfigures the new transport channel according to this message and reconfigure the new physical channel according to the system information messages. Finally, the UE shall transmit a TRANSPORT CHANNEL RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION | IE “Uplink DPCH Info” and IE “Downlink DPCH Info” are not specified. |
| 2 |  |  | UE shall perform the reconfiguration of transport channel |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS” in Annex A.

8.2.4.7.5	Test requirement

After step 3 the UE shall transit from CELL_DCH to CELL_FACH in the same cell, and then continue to communicate with SS on the new transport channel and common physical channels.

| 8.2.4.8 |  |  |  |
| --- | --- | --- | --- |

Void

#### 8.2.4.9	Transport channel reconfiguration from CELL_DCH to CELL_FACH: Failure (Cell re-selection)

8.2.4.9.1		Definition

8.2.4.9.2	Conformance requirement

The UE shall initiate a cell update procedure when the UE cannot use the assigned physical channel according to a TRANSPORT CHANNEL RECONFIGURATION message as the transition from CELL_DCH to CELL_FACH. After the UE completes cell update procedure, the UE transmits TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “cell reselection” in IE “failure cause”. Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.9.3	Test purpose

To confirm that the UE initiates a cell update procedure when the UE fails successively in the following actions: (a) configure the new transport channel according to TRANSPORT CHANNEL RECONFIGGURATION message received and (b) revert to the old channel configuration after. The UE transmits TRANSPORT CHANNEL RECONFIGURATION FAILURE message after it completes a cell update.

8.2.4.10.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. SS begins to transmit the BCCH for cell 2. The SS then transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which specifies the new transport channel parameters on common physical channel. But the SS does not reconfigure the L1 parameters and the new transport channel to reflect this change. Consequently, the UE discovers that it cannot reconfigure the new transport channel and try to revert to the old configuration. At this time, SS deletes all context related to the old configuration in cell 1. The UE shall select cell 2 by performing cell re-selection and enter CELL FACH state. The UE transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” cell reselection”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to transmit the BCCH cell 2. |
| 2 | ( | TRANSPORT CHANNEL RECONGURATION |  |
| 3 |  |  | The SS does not reconfigure L1. At the same time, it deletes the old channel configuration. |
| 4 |  |  | The UE fails to reconfigure a new transport channel. |
| 5 | ( | CELL UPDATE | The UE shall discover the presence of cell 2 and transmits this message, which includes the IE “U-RNTI”. The value “cell reselection” shall be set in IE ”Cell update cause”. |
| 6 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 8 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

Use the message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS” in Annex A.

CELL UPDATE (Step 5)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 6)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

TRANSPORT CHANNEL RECONFIGURATION FAILURE (Step 8)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.4.9.5	Test requirement

After step 4 the UE shall find cell 2, enter CELL_FACH state and then initiate cell update procedure in cell 2.

After step 6 UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 7 UE shall transmit TRANSPORT CHANNEL FAILURE message on the DCCH using AM RLC, setting the value ”cell reselection” to IE “failure cause”.

#### 8.2.4.10	Transport channel reconfiguration from CELL_FACH to CELL_DCH: Success

8.2.4.10.1		Definition

8.2.4.10.2	Conformance requirement

The UE shall correctly reconfigure the transport channels according to TRANSPORT CHANNEL RECONFIGURATION message, which trigger a state transition from CELL_FACH to CELL_DCH in the same cell.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.10.3	Test purpose

To confirm that the UE reconfigures a new transport channel using dedicated physical channel according to a TRANSPORT CHANNEL RECONFIGURATION message received from the SS.

8.2.4.10.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes IE “Uplink DPCH info” and IE “Downlink DPCH info” leading to a state transition from CELL_FACH to CELL_DCH in the same cell. The UE shall reconfigure the new transport channel according to this message and then reconfigure the new physical channel according to the system information message. Finally, the UE transmits a TRANSPORT CHANNEL RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION | Includes both IE “Uplink DPCH Info” and IE “Downlink DPCH Info” in the message. |
| 2 |  |  | Reconfiguration of transport channel |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

8.2.4.10.5	Test requirement

After step 3 the UE shall transit from CELL_FACH to CELL_DCH in the same cell, and continue to communicate with SS using the new transport channel configuration based on DPCH physical channels.

#### 8.2.4.11	Transport channel reconfiguration from CELL_FACH to CELL_DCH: Failure (Unsupported configuration)

8.2.4.11.1	Definition

8.2.4.11.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a TRANSPORT CHANNEL RECONFIGURATION message which includes unsupported configuration parameters and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE “failure cause

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.11.3	Test purpose

To confirm that the UE transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC when it receives a TRANSPORT CHANNEL RECONFIGURATION message which includes unsupported configuration parameters.

8.2.4.14.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes unsupported configuration parameters for the UE. The UE shall transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting “configuration unsupported” in IE ”failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONGURATION | The message includes unsupported configuration by the UE |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | The UE shall not change the transport channel. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| TrCH Information Elements |  |
| -Uplink transport Channels |  |
| -Added or Reconfigured TrCH information list | Number of transport channels = 4096 |
| -Downlink transport Channels |  |
| -Added or Reconfigured TrCH information list | Number of transport channels = 4096 |

TRANSPORT CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.4.11.5	Test requirement

After step1 the UE shall keep its old configuration and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC. The UE shall set “configuration unsupported” in IE ”failure cause” of the message.

#### 8.2.4.12	Transport channel reconfiguration from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion to old channel)

8.2.4.12.1		Definition

8.2.4.12.2	Conformance requirement

The UE shall revert to the old configuration when the UE has failed to reconfigure the new transport channel requested, and then transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message to UTRAN.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.12.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, if the UE fails to reconfigure the new transport channel according to a TRANSPORT CHANNEL RECONFIGURATION message.

8.2.4.12.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes the new transport channel parameters. However, SS does not reconfigure the new transport channel accordingly. Hence, the UE shall experience a failure in the reconfiguration process. After T312 expiry, the UE shall revert to the old channel configuration. Then the UE transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, stating the reason “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONGURATION | Message includes IE “Downlink DPCH Info” and IE “Uplink DPCH Info” |
| 2 |  |  | SS does not reconfigure the transport channel causing the UE to detect a physical channel failure. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | After T312 expiry the UE shall revert to the old configuration and transmit this message. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

TRANSPORT CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | TRANSPORT CHANNEL RECONFIGURATION FAILURE |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.4.12.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a TRANPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value “physical channel failure” in IE “failure cause”.

#### 8.2.4.13	Transport channel reconfiguration from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion failure)

8.2.4.13.1		Definition

8.2.4.13.2	Conformance requirement

The UE shall initiate a cell update procedure when it fails to revert to the old channel configuration, following a physical channel failure in the transport channel reconfiguration procedure. After the UE completes cell update procedure, the UE transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “physical channel failure” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.13.3	Test purpose

To confirm that the UE transmits RADIO TRANSPORT CHANNEL RECONFIGURATION FAILURE message after it completes a cell update procedure, when the UE cannot reconfigure the new transport channel for the failure of L1 configuration and subsequently fails to revert to the old configuration.

8.2.4.13.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_FACH state in a cell 1. SS begins to broadcast the BCCH of cell 2 at a power level lower than in cell 1, and then it transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE in cell 1. The message includes a new set of transport channel parameters. However, the SS does not reconfigure L1 and the new transport channel accordingly. At the same time, it deletes the current channel configurations in cell 1. As a result, the UE cannot reconfigure the new transport channel and an attempt to revert to the old configuration fails. The UE shall then find that cell 2 is available, camp onto it, and transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” physical channel failure” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to transmit BCCH in cell 2 |
| 2 | ( | TRANSPORT CHANNEL RECONGURATION |  |
| 3 |  |  | The SS does not reconfigure L1 and transport channel, it also deletes its current contexts for cell 1. |
| 4 |  |  | The UE shall experience a failure to reconfigure a new transport channel and also fails to revert to old configuration. |
| 5 | ( | CELL UPDATE | The UE shall find cell 2, camp onto it, and and be in CELL_FACH state. This message include the value “radio link failure” set in IE ”Cell update cause”. |
| 6 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”“. |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 8 | ( | TRANSPORT CHANNEL RECONGURATION FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

CELL UPDATE (Step 5)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 6)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

TRANSPORT CHANNELRECONGURATION FAILURE (Step 8)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONGURATION” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.4.13.5	Test requirement

After step 4 the UE shall find the presence of cell 2, enter CELL_FACH state, and transmit CELL UPDATE message on the uplink CCCH in cell 2.

After step 6 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

#### After step 7 the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ”physical channel failure”.8.2.4.14	Transport Channel Reconfiguration from CELL_FACH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.4.14.1		Definition

8.2.4.14.2	Conformance requirement

If the UE receives a TRANSPORT CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than TRANSPORT CHANNEL RECONFIGURATION, it shall keep its configuration as if the TRANSPORT CHANNEL RECONFIGURATION message had not been received.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.14.3	Test purpose

To confirm that if the UE receives a TRANSPORT CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than TRANSPORT CHANNEL RECONFIGURATION, it shall keep its configuration as if the TRANSPORT CHANNEL RECONFIGURATION message had not been received and complete the reconfiguration according to the previously received message. 8.2.4.14.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message before the “activation time” indicated in the RADIO BEARER RECONFIGURATION message expires. When the UE receives the TRANSPORT CHANNEL RECONFIGURATION message, the UE shall keep the configuration as if it had not received the TRANSPORT CHANNEL RECONFIGURATION message and shall transmit a RADIO BEARER SETUP FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the RADIO TRANSPORT CHANNEL RECONFIGURATION FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message on DCCH using AM RLC. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION | Includes the IE “Uplink DPCH info” |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION | Sent before the elapse of the Activation time specified in step 1. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION FAILURE | The UE does not change the configuration due to the reception of RADIO BEARER SETUP message... |
| 4 | ( | RADIO BEARER RECONFIGURATION FAILURE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

For RADIO BEARER RECONFIGURATION in step 1, use the message sub-type indicated as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A.

TRANSPORT CHANNEL RECONFIGURATION (Step 2)

For TRANSPORT CHANNEL RECONFIGURATION in step 2, use the message sub-type indicated as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A.

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | Current CFN-[current CFN mod 8 + 8 ] |

TRANSPORT CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.4.14.5	Test requirement

After step 1, SS transmits a TRANSPORT CHANNEL RECONFIGURATION message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the RADIO BEARER SETUP message and shall transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

#### After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER RECONFIGURATION message. 8.2.4.15	Transport channel reconfiguration from CELL_FACH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.4.15.1		Definition

8.2.4.15.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a TRANSPORT CHANNEL RECONFIGURATION message which includes a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE shall then transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message, specifying “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a TRANSPORT CHANNEL RECONFIGURATION message when the TRANSPORT CHANNEL RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.15.3	Test purpose

To confirm that the UE transmits TRANSPORT CHANNEL RECONFIGRATION FAILURE message on the DCCH using AM RLC, if it receives a TRANSPORT CHANNEL RECONFIGURATION message which uses a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”.

To confirm that the UE transmits a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a TRANSPORT CHANNEL RECONFIGURATION message including some IEs set to invalid value.

8.2.4.15.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE shall keep the old configuration and then transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC. This message shall contain the value “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits TRANSPORT CHANNEL RECONFIGURATION message including some IEs set to invalid value. The UE transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION | Contains an error in one of the mandatory IE in the message. |
| 2 | ( | TRANSPORT CHANNEL RECONFIGRATION FAILURE | The UE does not change the configuration. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration |
| 5 | ( | TRANSPORT CHANNEL RECONFIGRATION FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

TRANSPORT CHANNEL RECONFIGURATION FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “ TRANSPORT CHANNEL RECONFIGURATION FAILURE” |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

TRANSPORT CHANNEL RECONFIGURATION (Step 3)

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Added or Reconfigured UL TrCH information |  |
| --- | --- |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list |  |
| - Explicit List |  |
| - RB identity | 2 |

TRANSPORT CHANNEL RECONFIGURATION FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.4.15.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC. The content of the message shall specify “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

#### 8.2.4.16	Transport channel reconfiguration from CELL_FACH to CELL_FACH: Success with no transport channel type switching

8.2.4.16.1		Definition

8.2.4.16.2	Conformance requirement

The UE shall remain in CELL_FACH state and transition from CELL_FACH to CELL_FACH in the another cell requested in the received TRANSPORT CHANNEL RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.16.3	Test purpose

To confirm that the UE reconfigures a new transport channel according to a TRANSPORT CHANNEL RECONFIGURATION message received from the SS.

8.2.4.16.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE, which includes new transport channel parameters. The UE reconfigures the new transport channel and the new physical channel according to the system information messages. The UE transmits a TRANSPORT CHANNEL RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONGURATION |  |
| 2 |  |  | Reconfiguration of a new transport channel |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A.

8.2.4.16.5	Test requirement

After step3 the UE shall transit from CELL_FACH to CELL_FACH and continue to communicate with the SS on the DCCH using the existing transport channel.

#### 8.2.4.17	Transport channel reconfiguration from CELL_FACH to CELL_FACH: Failure (Cell re-selection)

8.2.4.17.1		Definition

8.2.4.17.2	Conformance requirement

The UE shall initiate the cell update procedure when the UE cannot use the assigned physical channel according to a TRANSPORT CHANNEL RECONFIGURATION message, during the transition from CELL_FACH to CELL_FACH in the another cell. After the UE complete cell update procedure, the UE transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to ” invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.17.3	Test purpose

To confirm that the UE perform a cell reselection and cell update procedure when the it fail to access the assigned physical channel, according to a TRANSPORT CHANNEL RECONFIGURATION message, during the transition from CELL_FACH to CELL_FACH in the another cell.

To confirm that the UE transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message after UE completes a cell update.

8.2.4.17.4	Method of test

Initial Condition

System Simulator: 2 cells Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state in cell 1. The SS begins to broadcast the BCCH in cell 2 and then transmits a TRANSPORT CHANNEL RECONFIGURATION message, resulting in the UE to attempt to transit from CELL_FACH to CELL_FACH in cell 1. The UE is expected to fail to access the assigned physical channel as the SS ceases downlink transmission in cell 1. After the UE successfully camp onto cell 2, it shall initiate the cell update procedure in cell 2. The UE transmit CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” cell reselection” to IE “failure cause”. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to broadcast the BCCH in cell 2. |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION | The message assigns common resources so that the UE is expected to execute a transition from CELL_FACH in to CELL_FACH in cell 1 |
| 3 |  |  | The UE shall detect a failure to use the assigned common physical channel and try to perform a cell reselection. |
| 4 | ( | CELL UPDATE | The UE discover the presence of cell 2 and triggers a cell update procedure. The value “cell reselection” shall be set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | TRANSPORT CHANNELRECONFIGURATION FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

Use the message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

TRANSPORT CHANNEL RECONFIGURATION FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.4.17.5 	Test requirement

After step 3 the UE shall discover the presence of cell 2, enter CELL_FACH state, and initiate a cell update procedure in that cell.

After step 5 UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 6 UE shall transmit TRANSPORT CHANNEL FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ”cell reselection”.

#### 8.2.4.18	Transport Channel Reconfiguration from CELL_DCH to CELL_DCH: Success (Subsequently received)

8.2.4.18.1		Definition

8.2.4.18.2	Conformance requirement

If the UE receives a TRANSPORT CHANNEL RECONFIGURATION message before the UE configures the radio bearer according to the previous TRANSPORT CHANNEL RECONFIGURATION message, the UE shall ignore the new TRANSPORT CHANNEL RECONFIGURATION message and configure according to the first TRANSPORT CHANNEL RECONFIGURATION message received. Finally, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.18.3	Test purpose

To confirm that if the UE receives a TRANSPORT CHANNEL RECONFIGURATION message before the UE configures the radio bearer according to the previous TRANSPORT CHANNEL RECONFIGURATION message it ignores the second TRANSPORT CHANNEL RECONFIGURATION message and configures according to the previous TRANSPORT CHANNEL RECONFIGURATION message.

8.2.4.18.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. When the SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE before the UE configures the radio bearer, the UE ignores the new TRANSPORT CHANNEL RECONFIGURATION message and configures according to the previous TRANSPORT CHANNEL RECONFIGURATION message. Finally, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION | Including IE ”Uplink DPCH info” |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION | SS send this message before the expiry of “activation time” specified in TRANSPORT CHANNEL SETUP message of step 1. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | The UE ignores the TRANSPORT CHANNEL RECONFIGURATION message in step 2 and confirms configuration according to the TRANSPORT CHANNEL RECONFIGURATION message in step 1. |

Specific Message Contents

The contents of TRANSPORT CHANNEL RECONFIGURATION messages in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

| Information Element | Value/remark |
| --- | --- |
| Activation Time | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.4.18.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the TRANSPORT CHANNEL RECONFIGURATION message in step 1.

#### 8.2.4.19	Transport Channel Reconfiguration from CELL_FACH to CELL_DCH: Success (Subsequently received)

8.2.4.19.1		Definition

8.2.4.19.2	Conformance requirement

If the UE receives a TRANSPORT CHANNEL RECONFIGURATION message before the UE configures the radio bearer according to the previous TRANSPORT CHANNEL RECONFIGURATION message, the UE shall ignore the new TRANSPORT CHANNEL RECONFIGURATION message and configure according to the first TRANSPORT CHANNEL RECONFIGURATION message received. Finally, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.4

8.2.4.19.3	Test purpose

To confirm that if the UE receives a TRANSPORT CHANNEL RECONFIGURATION message before the UE configures the radio bearer according to the previous TRANSPORT CHANNEL RECONFIGURATION message it ignores the second TRANSPORT CHANNEL RECONFIGURATION message and configures according to the previous TRANSPORT CHANNEL RECONFIGURATION message.

8.2.4.19.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. When the SS transmits a TRANSPORT CHANNEL RECONFIGURATION message to the UE before the UE configures the radio bearer, the UE ignores the new TRANSPORT CHANNEL RECONFIGURATION message and configures according to the previous TRANSPORT CHANNEL RECONFIGURATION message. Finally, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION | Includes the IE ”Uplink DPCH info” |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION | Sent before the elapse of the activation time specified in step 1. |
| 3 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | The UE ignores the TRANSPORT CHANNEL RECONFIGURATION message in step 2 and confirms configuration according to the TRANSPORT CHANNEL RECONFIGURATION message in step 1. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.4.19.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the TRANSPORT CHANNEL RECONFIGURATION message in step 1.

#### 8.2.4.20	Transport Channel Reconfiguration from CELL_DCH to CELL_PCH: Success

8.2.4.20.1	Definition

8.2.4.20.2	Conformance requirement

The UE shall transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message using and transits from CELL_DCH to CELL_PCH when receives a TRANSPORT CHANNEL RECONFIGURATION message. And then, the UE shall reconfigure a radio bearer according to the TRANSPORT CHANNEL RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.4.20.3	Test purpose

To confirm that the UE transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message before entering CELL_PCH state after it received a TRANSPORT CHANNEL RECONFIGURATION message and reconfigured its radio bearers. The UE is in CELL_PCH state of the same cell.

8.2.4.20.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message. The UE transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION |  |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | The UE sends this message before start state transition. |
| 3 |  |  | Reconfiguration of Transport channel after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.4.20.5	Test requirement

After step 1 the UE transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_DCH to CELL_PCH.

#### 8.2.4.21	Transport Channel Reconfiguration from CELL_DCH to URA_PCH: Success

8.2.4.21.1	Definition

8.2.4.21.2	Conformance requirement

The UE shall transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message using and transits from CELL_DCH to URA_PCH when receives a TRANSPORT CHANNEL RECONFIGURATION message. And then, the UE shall reconfigure radio bearers according to the TRANSPORT CHANNEL RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.4.21.3	Test purpose

To confirm that the UE transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message before entering URA_PCH state after it received a TRANSPORT CHANNEL RECONFIGURATION message and reconfigured its radio bearers. The UE is in URA_PCH state of the same cell.

8.2.4.21.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message. The UE transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into URA_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | TRANSPORT CHANNEL RECONFIGURATION |  |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | The UE sends this message before start state transition. |
| 3 |  |  | Reconfiguration of Transport channel after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | Cell UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.4.21.5	Test requirement

After step 1 the UE transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_DCH to URA_PCH.

| 8.2.4.22 Void |  |  |  |
| --- | --- | --- | --- |

| 8.2.4.23 |  |  |  |
| --- | --- | --- | --- |

Void

### 8.2.5	Transport format combination control

#### 8.2.5.1	Transport format combination control in CELL_DCH: restriction

8.2.5.1.1	Definition

8.2.5.1.2	Conformance requirement

The UE shall change the subset of allowed transport format combination of uplink when the UE receives TRANSPORT FORMAT COMBINATION CONTROL message.

Reference

3GPP TS 25.331 clause 8.2.5

8.2.5.1.3	Test purpose

To confirm that the UE do not transmit data on the DTCH in the uplink direction, following the reception of TRANSPORT FORMAT COMBINATION CONTROL message sent from the SS, which is set to the valuein IE “Allowed Transport format combination index”.

8.2.5.1.4	Method of test

Initial Condition

System Simulator: 1cell

UE: DCCH+DTCH_DCH (state 6-9 or state 6-10) as specified in clause 7.4 of TS 34.108, depending on the CN domain(s) supported by the UE.

Test Procedure

The UE establishes a radio access bearer on the DCH for a communication. The SS transmits a TRANSPORT FORMAT COMBINATION CONTROL message, which indicates that only TFC0 is allowed on the uplink for DCH transport channel. The UE shall reconfigure the TFCS, stop any transmission on DTCH logical channel and then continues the communication on DCCH only.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | UE s in CELL_DCH state with a DTCH logical channel allocated for communication between UE and SS |
| 2 | ( | TRANSPORT FORMAT COMBINATION CONTROL | The UE shall use the TFC Subset as defined in value IE “ Allowed Transport format combination index”. |
| 3 |  |  | The UE shall not transmit any data on the DTCH. |

Specific Message Contents

TRANSPORT FORMAT COMBINATION CONTROL

| Information Element | Value/remark |
| --- | --- |
| TrCH information elements |  |
| -Allowed Transport format combination list |  |
| - Allowed transport format combination | 0 and 3(If initial state is “state 6-9”) |
| - Allowed transport format combination | 0 and 5(If initial state is “state 6-10”) |

8.2.5.1.5	Test requirement

After step 2 the UE shall stop transmitting data on the DTCH in the uplink.

#### 8.2.5.2	Transport format combination control in CELL_DCH: release a restriction

8.2.5.2.1	Definition

8.2.5.2.2	Conformance requirement

The UE shall change the subset of allowed transport format combination of uplink when it receives TRANSPORT FORMAT COMBINATION CONTROL message, specifying that an existing restriction for the usage of TFCS be removed.

Reference

3GPP TS 25.331 clause 8.2.5

8.2.5.2.3	Test purpose

To confirm that the UE resume transmission of data on the DTCH on the uplink, following the reception of TRANSPORT FORMAT COMBINATION CONTROL message which include IE “Minimum allowed transport format combination set”.

8.2.5.2.4	Method of test

Initial Condition

System Simulator: 1cell

UE: DCCH+DTCH_DCH (state 6-9 or state 6-10) as specified in clause 7.4 of TS 34.108, depending on the CN domain(s) supported by the UE.

Test Procedure

The UE is in CELL_DCH state with DTCH allocated but fully restricted. The UE cannot transmit the data on the DTCH, as a result of the restriction on the transport format combination. Next, the SS transmits a TRANSPORT FORMAT COMBINATION CONTROL message which include “Minimum allowed transport format combination set”

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | No data transmission on the DTCH with a restriction in the uplink direction, following the execution of test 8. 2.5.1. |
| 2 | ( | TRANSPORT FORMAT COMBINATION CONTROL | Use the TFCS according to IE “Minimum allowed Transport format combination index”. |
| 3 |  |  | The UE begins to transmit the data on the DTCH. |

Specific Message Contents

TRANSPORT FORMAT COMBINATION CONTROL

| Information Element | Value/remark |
| --- | --- |
| TrCH information elements |  |
| -Minimum allowed transport format combination set | 5(If initial state is “state 6-9”) |
| -Minimum allowed transport format combination set | 6(If initial state is “state 6-10”) |

8.2.5.2.5	Test requirement

After step 2 the UE shall begin to transmit the data on the DTCH in the uplink.

#### 8.2.5.3	Transport format combination control in CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.5.3.1	Definition

8.2.5.3.2 	Conformance requirement

The UE shall keep its old configuration when the UE receives another TRANSPORT FORMAT COMBINATION CONTROL message before the UE reconfigures the transport channel completely according to a similar message received earlier. The UE shall transmit a TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the DCCH using AM RLC indicating “incompatible simultaneous reconfiguration” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.5

8.2.5.3.3	Test purpose

To confirm that after the UE receives TRANSPORT FORMAT COMBINATION CONTROL message, it transmits TRANSPORT FORMAT COMBINATION CONTROL FAILURE message and keeps the TFC subset as before the TRANSPORT FORMAT COMBINATION CONTROL message is received.

8.2.5.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE establishes a radio access bearer on the DCH for to be used for user-data exchange. SS sends a TRANSPORT CHANNEL RECONFIGURATION message on the downlink DCCH, to request that the channel coding scheme for a DCH be changed. After this message has been acknowledged by the UE RLC-AM entity, the SS transmits a TRANSPORT FORMAT COMBINATION CONTROL message, which includes a full restriction of the TFCS used in the uplink. The UE shall detect a failure to reconfigure the TFCS, then it transmits TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the uplink DCCH. After the activation time specified in the TRANSPORT CHANNEL RECONFIGURATION message has elapsed, the UE shall send TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH. SS verifies that reconfiguration is completed by checking that the user-data exchange is resumed on DTCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | UE is in CELL_DCH connected state, with a DTCH logical channel for user-data communication |
| 2 | ( | TRANSPORT CHANNEL RECONFIGURATION | Requesting for a change in semi-static transport format for DCH carrying the DTCH. The dynamic part remains unchanged. |
| 3 | ( | TRANSPORT FORMAT COMBINATION CONTROL | Requesting for a full restriction on TFCS for the DCH carrying DTCH. |
| 4 | ( | TRANSPORT FORMAT COMBINATION CONTROL FAILURE | The UE shall keep the TFC subset as before the TRANSPORT FORMAT COMBINATION CONTROL message was received |
| 5 |  |  | The UE does not change the configuration of TFC and the UE continues reconfigure the affected transport channel. |
| 6 |  | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | UE shall resume exchange of data over the DTCH logical channel. |

Specific Message Contents

TRANSPORT CHANNEL RECONFIGURATION

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| TrCH Information Elements - Uplink transport channels - Added or reconfigured TrCH information list - Transport channel identity - Semi-Static Transport Format Information - Type of channel coding | 2 Select a different coding scheme from default message content |

TRANSPORT FORMAT COMBINATION CONTROL

| Information Element | Value/remark |
| --- | --- |
| DPCH TFCS in Uplink - Subset Representation - Allowed TFIs | Restricted TrCH information Not Present (All TFCs are restricted) |

TRANSPORT FORMAT COMBINATION CONTROL FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRNSPORT FORMAT COMBINATION CNTROL FAILURE” |
| RRC transaction identifier | 0 |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.5.3.5	Test requirement

After step 3 the UE continue the transport channel reconfiguration as if no TRANSPORT FORMAT COMBINATION CONTROL message was received. Then it shall transmit a TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the DCCH using AM RLC, stating the reason “Incompatible simultaneous reconfiguration” in IE “Failure cause”.

After step 6 the UE shall resume communication with SS on DTCH using the requested channel coding scheme on the transport blocks.

#### 8.2.5.4	Transport format combination control in CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.5.4.1	Definition

8.2.5.4.2	Conformance requirement

The UE shall keep old configuration when it receives a TRANSPORT FORMAT COMBINATION CONTROL message which using a undefined value in the mandatory IE “Minimum allowed Transport format combination index”. It shall then transmits a TRANSPORT FORMAT COMBINATION CONTROL FAILURE message, indicating “protocol error” in IE “failure cause” and “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a TRANSPORT FORMAT COMBINATION CONTROL message when the TRANSPORT CHANNEL RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.5

8.2.5.4.3	Test purpose

To confirm after the UE receives an invalid TRANSPORT FORMAT COMBINATION CONTROL message, it transmits TRANSPORT FORMAT COMBINATION CONTROL FAILURE message and keep the TFC subset as if no TRANSPORT FORMAT COMBINATION CONTROL message has been received.

To confirm that the UE transmits a TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the DCCH using AM RLC if it receives a TRANSPORT FORMAT COMBINATION CONTROL message including some IEs set to invalid value.

8.2.5.4.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: DCCH+DTCH_DCH (state 6-9 or state 6-10) as specified in clause 7.4 of TS 34.108, depending on the CN domain(s) supported by the UE.

Test Procedure

The UE establishes a radio access bearer on the DCH for a communication. The SS transmits a TRANSPORT FORMAT COMBINATION CONTROL message, which uses a undefined value in the mandatory IE “Minimum allowed Transport format combination index”. The UE shall then transmit TRANSPORT FORMAT COMBINATION CONTROL FAILURE message and continues the communication using the radio access bearer. The UE keeps initial configuration and SS transmits TRANSPORT FORMAT COMBINATION CONTROL message including some IEs set to invalid value. The UE transmit TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | RRC connected state on the DTCH for a communication |
| 2 | ( | TRANSPORT FORMAT COMBINATION CONTROL | Contains an error in a mandatory IE. |
| 3 | ( | TRANSPORT FORMAT COMBINATION CONTROL FAILURE | The UE shall not change the configuration |
| 4 | ( | TRANSPORT FORMAT COMBINATION CONTROL | This message includes IE set to invalid value |
| 5 |  |  | The UE does not change the configuration |
| 6 | ( | TRANSPORT FORMAT COMBINATION CONTROL FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

TRANSPORT FORMAT COMBINATION CONTROL (Step 2)

| Information Element | Value/remark |
| --- | --- |
| DPCH TFCS in uplink - Minimum allowed Transport format combination index | Set to the value “MaxTFCValue” |

TRANSPORT FORMAT COMBINATION CONTROL FAILURE (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “TRNSPORT FORMAT COMBINATION CNTROL FAILURE” |
| Failure cause | “protocol error” |
| Protocol error information |  |
| -Protocol error case | Information element value not comprehended |
| Other information element | Not checked |

TRANSPORT FORMAT COMBINATION CONTROL(Step 4)

| Information Element | Value/remark |
| --- | --- |
| TrCH information elements |  |
| - Allowed Transport format combination list |  |
| - Allowed transport format combination | 10 |

TRANSPORT FORMAT COMBINATION CONTROL FAILURE (Step 6)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.5.4.5	Test requirement

After step 3 the UE shall keep its configuration before the TRANSPORT FORMAT COMBINATION CONTROL message was received and transmit a TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the DCCH using AM RLC. The UE shall set the value “protocol error” in IE “Failure cause” and the value “information element not comprehended” in IE “protocol error information”. The UE shall continue communicate with SS using the radio access bearer.

After step 4 the UE shall keep its old configuration.

After step 5 the UE shall transmit TRANSPORT FORMAT COMBINATION CONTROL FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ”invalid configuration”.

### 8.2.6	Physical channel reconfiguration

#### 8.2.6.1	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Success

8.2.6.1.1	Definition

8.2.6.1.2	Conformance requirement

The UE shall correctly reconfigure a physical channel according to the PHYSICAL CHANNEL RECONFIGURATION message received, which is used for hard handover purposes. It shall be able to communicate with the UTRAN on the new frequency subsequently.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.1.3	Test purpose

To confirm that the UE reconfigures the physical channel parameters according to a PHYSICAL CHANNEL RECONFIGURATION message received from the SS. After the reconfiguration, the UE shall resume normal transmission and reception operations.

8.2.6.1.4	Method of test

Initial Condition

System Simulator: 2 cells - cell 1 and cell 6 are active. The Qrxlevmin and Qrxqualmin.values in SYSTEM INFORMATION BLOCK TYPE 3 and 4 messages of cell 6 is changed to –90dBm and –20dB respectively

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE, which includes a new physical channel parameter specified in the “Frequency Info” IE. The UE shall reconfigure itself and tune to the new physical channel and transmits a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH of cell 6 using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION | Including new frequency information. |
| 2 |  |  | UE shall stop uplink activities to cell 1 and begin to reconfigure the physical channel parameters. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS“ in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | Same uplink UARFCN as used for cell 6 |
| - UARFCN downlink(Nd) | Same downlink UARFCN as used for cell 6 |
| Downlink information for each radio links | Same downlink UARFCN as used for cell 6 |
| - Primary CPICH info |  |
| - Primary Scrambling Code | 350 |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing Indicator | Initialise |

8.2.6.1.5	Test requirement

After step 2 the UE shall send PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH of cell 6, and then continue to communicate with SS on the new physical channel.

#### 8.2.6.2	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Failure (Unsupported configuration)

8.2.6.2.1	Definition

8.2.6.2.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a PHYSICAL CHANNEL RECONFIGURATION message which includes an unsupported configuration and transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, with the reason “configuration unsupported” in IE ”failure cause”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.2.3	Test purpose

To confirm that the UE keeps its configuration and transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if the received PHYSICAL CHANNEL RECONFIGURATION message includes unsupported configuration parameters for the UE.

8.2.6.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE which includes unsupported configuration parameters as the frequency cannot be supported by the UE. The UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “configuration unsupported” in IE ”failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION | Includes an unsupported configuration as the frequency cannot be supported by the UE |
| 2 | ( | PHYISICAL CHANNEL RECONFIGURATION FAILURE | The UE shall not change the physical channel and continue to communicate using the old configuration. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 63984 |
| - UARFCN downlink(Nd) | Not Present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.6.2.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC and set “configuration unsupported” in IE ”failure cause”.

#### 8.2.6.3	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Failure (Physical channel failure and reversion to old channel)

8.2.6.3.1	Definition

8.2.6.3.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to reconfigure the new physical channel by the expiry of timer T312, and then transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC indicating  “physical channel failure” in IE “ failure cause”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.3.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if the UE fails to reconfigure the new physical channel according to the received PHYSICAL CHANNEL RECONFIGURATION message by timer T312 expiry.

8.2.6.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE which includes new frequency parameters. However, the SS does not reconfigure the new physical channel. The UE is expected to encounter a failure to reconfigure the new physical channel and after T312 timer expiry the UE shall revert to the old configuration. Finally, the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC specifies “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION | Including a new frequency information |
| 2 |  |  | The SS does not reconfigure the physical channel so that the UE fails to reconfigure to the new physical channel. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | After T312 expiry, the UE shall revert to the old configuration and transmits this message. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS” in Annex A.

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.6.3.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, with the value “physical channel failure” in IE “failure cause”.

#### 8.2.6.4	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Failure (Physical channel failure and reversion failure)

8.2.6.4.1	Definition

8.2.6.4.2	Conformance requirement

The UE shall perform acell update procedure when the UE fails to revert to the old configuration, after the detection of physical channel failure during the course of executing a physical channel reconfiguration procedure. After the UE completes cell update procedure, the UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.4.3	Test purpose

To confirm that the UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message after UE completes a cell update procedure when the UE cannot reconfigure the new physical channel for the failure of L1 configuration and for the failure of the reversion to the old configuration.

8.2.6.4.4	Method of test

Initial Condition

System Simulator: 2 cells- Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS begins to broadcast the BCCH in cell 2 and then transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE, which includes new uplink and downlink frequency parameters and does not reconfigure L1. The UE is expected to fail to reconfigure the new physical channel and tries to revert to the old configuration. The SS then deletes the old physical channel so that the UE would perform cell reselection and finds cell 2. It shall then transmit a CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” physical channel failure” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS transmits the BCCH in cell 2. |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | The message includes new frequency information |
| 3 |  |  | SS does not reconfigure the physical channel to reflect the changes in step 2, at the same time, it deletes the old configuration so the UE cannot reconfigure the new physical channel and cannot revert to the old configuration. |
| 4 | ( | CELL UPDATE | The UE finds a new cell.2 and enters CELL_FACH state. This message includes the value “radio link failure” set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message includes IE “new U-RNTI” and IE “new C-RNTI”“. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | PHYSICAL CHANNEL RECONGURATION FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION (Step 1)

Use the message sub-type titled “Packet to CELL_DCH from CELL_DCH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 4 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

PHYSICAL CHANNEL RECONGURATION FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “PHYSICAL CHANNEL RECONGURATION FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.6.4.5	Test requirement

After step 3 the UE shall find the availability of cell 2, enter CELL_FACH state, and transmits CELL UPDATE message using RLC-TM mode on the uplink CCCH.

After step 6 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 7 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ” physical channel failure”.

#### 8.2.6.5	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Failure (Incompatible simultaneous reconfiguration)

8.2.6.5.1	Definition

8.2.6.5.2	Conformance requirement

If the UE receives a PHYSICAL CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than PHYSICAL CHANNEL RECONFIGURATION SETUP, it shall keep its configuration as if the PHYSICAL CHANNEL RECONFIGURATION SETUP message had not been received. Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.5.3	Test purpose

To confirm that if the UE receives a PHYSICAL CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than PHYSICAL CHANNEL RECONFIGURATION, it shall keep its configuration as if the PHYSICAL CHANNEL RECONFIGURATION message had not been received and complete the reconfiguration according to the previously received message.

8.2.6.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message before the “activation time” indicated in the RADIO BEARER RECONFIGURATION message expires. When the UE receives the PHYSICAL CHANNEL RECONFIGURATION message, the UE shall keep the configuration as if it had not received the PHYSICAL CHANNEL RECONFIGURATION message and shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the PHYSICAL CHANNEL RECONFIGURATION FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message on DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | Sent before the “Activation Time Info” specified in the message in step 1 has elapsed. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The UE does not change the configuration due to the reception of PHYSICAL CHANNEL RECONFIGURATION FAILURE message. |
| 4 | ( | RADIO BEARER RECONFIGURATION COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

For RADIO BEARER RECONFIGURATION in step 1, use the message sub-type indicated as “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A.

PHYSICAL CHANNEL RECONFIGURATION (Step 2)

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | Current CFN-[current CFN mod 8 + 8 ] |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (step 3)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.6.5.5	Test requirement

After step 1, SS transmits a PHYSICAL CHANNEL RECONFIGURATION message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the PHYSICAL CHANNEL RECONFIGURATION message and shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

#### After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER RECONFIGURATION message.8.2.6.6	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Failure (Invalid message reception and Invalid configuration)

8.2.6.6.1	Definition

8.2.6.6.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a PHYSICAL CHANNEL RECONFIGURATION message, which includes undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. It shall then transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message which contains the value “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a TRANSPORT CHANNEL RECONFIGURATION message when the TRANSPORT CHANNEL RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.6.3	Test purpose

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a PHYSICAL CHANNEL RECONFIGURATION message which uses a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”.

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a PHYSICAL CHANNEL RECONFIGURATION message including some IEs set to invalid value.

8.2.6.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE, with a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE keeps the old configuration and transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, with a value “protocol error” in IE “failure cause” and also a value “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits PHYSICAL CHANNEL RECONFIGURATION message including some IEs set to invalid value. The UE transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” invalid configuration” to IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION | This message contains an error in one of the mandatory IEs. |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The UE does not change the configuration. |
| 4 | ( | PHYSICAL CHANNEL RECONFIGURATION | This message includes IE set to invalid value |
| 5 |  |  | The UE does not change the configuration |
| 6 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION (Step 1)

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

PHYSICAL CHANNEL RECONFIGURATION (Step 3)

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_FACH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks - Scheduling information | Not Present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.6.6.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting value “protocol error” in IE “failure cause” and also setting value “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

#### 8.2.6.7	Physical channel reconfiguration for transition from CELL_DCH to CELL_FACH: Success

8.2.6.7.1	Definition

8.2.6.7.2	Conformance requirement

The UE shall correctly reconfigure a physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message when asked to perform a transition from CELL_DCH to CELL_FACH.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.7.3	Test purpose

To confirm that the UE reconfigures a new physical channel according to the PHYSICAL CHANNEL RECONFIGURATION message received from the SS.

8.2.6.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE. The UE shall then reconfigure the new physical channel according to this message and the system information messages. Following this, it shall transmit a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message using AM RLC on the RACH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 |  |  | Reconfiguration of physical channel |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS” in Annex A.

8.2.6.7.5	Test requirement

After step 3 the UE shall transit from CELL_DCH to CELL_FACH and continue to communicate with SS on the common physical channel.

#### 8.2.6.8	Physical channel reconfiguration for transition from CELL_DCH to CELL_FACH: Failure (Cell re-selection)

8.2.6.8.1	Definition

8.2.6.8.2	Conformance requirement

The UE shall initiate the cell update procedure when the UE cannot use the assigned physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message, during the transition from CELL_DCH to CELL_FACH. After the UE completes cell update procedure, the UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which is set to “cell reselection” in IE “failure cause”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.8.3	Test purpose

To confirm that the UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message after the UE completes a cell reselection and cell update procedure when the it fail to access the assigned physical channel, according to a PHYSICAL CHANNEL RECONFIGURATION message, during the transition from CELL_DCH to CELL_FACH.

8.2.6.8.4	Method of test

Initial Condition

System Simulator: 2 cells Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_DCH (state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state in cell 1. The SS begins to broadcast the BCCH in cell 2 and then transmits a PHYSICAL CHANNEL RECONFIGURATION message, resulting in the UE to attempt to transit from CELL_DCH to CELL_FACH. The UE is expected to fail to access the assigned physical channel as the SS ceases downlink transmission in cell 1. After the UE successfully camp onto cell 2, it shall initiate the cell update procedure in cell 2. The UE transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the value ” cell reselection” to IE “failure cause”. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to broadcast the BCCH in cell 2. |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | The message assigns common resources so that the UE is expected to execute a transition from CELL_DCH to CELL_FACH |
| 3 |  |  | The UE shall detect a failure to use the assigned common physical channel and try to perform a cell reselection. |
| 4 | ( | CELL UPDATE | The UE discover the presence of cell 2 and triggers a cell update procedure. The value “cell reselection” shall be set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.6.8.5	Test requirement

After step 3 the UE shall discover the presence of cell 2, enter CELL_FACH state, and initiate a cell update procedure in that cell.

After step 5 UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 6 UE shall transmit PHYSICAL CHANNEL FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ”cell reselection”.

#### 8.2.6.9	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Success

8.2.6.9.1		Definition

8.2.6.9.2	Conformance requirement

The UE shall correctly reconfigure a physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message, which triggers a transition from CELL_FACH to CELL_DCH.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.9.3	Test purpose

To confirm that the UE reconfigures a new physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message received from the UTRAN, in the case of an assignment of dedicated physical resource from the common physical channels used previously by the UE.

8.2.6.9.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE to start a transition from CELL_FACH to CELL_DCH. The UE shall reconfigure the new physical channel correctly according to this message. To complete this procedure, the UE shall transmit a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 |  |  | The UE shall reconfigure the physical channel in order to start using the dedicated channels allocated. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

8.2.6.9.5	Test requirement

After step 3 the UE shall transit from CELL_FACH to CELL_DCH and continue to communicate with SS on the dedicated physical channel.

#### 8.2.6.10	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Failure (Unsupported configuration)

8.2.6.10.1		Definition

8.2.6.10.2	Conformance requirement

The UE shall keep its old configuration when the it receives a PHYSICAL CHANNEL RECONFIGURATION message, which specifies unsupported configuration parameters for the UE. It shall then transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, reporting the cause “configuration unsupported” in IE “ failure cause”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.10.3	Test purpose

To confirm that the UE keeps its configuration and transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, if the received PHYSICAL CHANNEL RECONFIGURATION message includes unsupported configuration parameters.

8.2.6.10.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE, which includes unsupported frequencies for the UE. The PHYSICAL CHANNEL RECONFIGURATION is structured in such a manner as to trigger a transition from CELL_FACH to CELL_DCH in the UE. The UE shall responds with a PHYSICAL CHANNEL RECONFIGURATION FAILURE message sent on the DCCH using AM RLC, setting “configuration unsupported” in IE ”failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION | Includes unsupported frequencies for the UE |
| 2 | ( | PHYISICAL CHANNEL RECONFIGURATION FAILURE | The UE shall not change the physical channel configuration, this message shall be sent using the original allocated physical resource. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Frequency info |  |
| - UARFCN uplink(Nu) | 63984 |
| - UARFCN downlink(Nd) | Not Present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Configuration unsupported |
| Other information element | Not checked |

8.2.6.10.5	Test requirement

After step 1 the UE shall keep its old configuration and transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, the IE “failure cause” shall be set to “configuration unsupported”.

#### 8.2.6.11	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion to old configuration)

8.2.6.11.1		Definition

8.2.6.11.2	Conformance requirement

The UE shall revert to the old configuration when the UE fails to reconfigure the new physical channel by timer T312 expiry. It shall report the failure by transmitting a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, indicating “physical channel failure” in IE “ failure cause”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.11.3	Test purpose

To confirm that the UE reverts to the old configuration and transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if the UE fails to reconfigure the new physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message by the T312 expiry.

8.2.6.11.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE, requesting it to transit from CELL_FACH to CELL_DCH due to a switch in physical resource reallocation. However, it does not reconfigure the new physical channel accordingly but continue to use the old configuration. Consequently, the UE shall fail to reconfigure the new physical channel, and after T312 expiry the UE attempt to revert to the old configuration. Then the UE shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which reports “physical channel failure” in IE “failure cause”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 |  |  | The SS does not reconfigure the physical channel, hence the UE shall detect a failure to reconfigure to the new physical channel. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | After T312 expiry the UE reverts to the old configuration and transmits this message. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Physical channel failure |
| Other information element | Not checked |

8.2.6.11.5	Test requirement

After step 2 the UE shall revert to the old configuration and transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, specifying “physical channel failure” in IE “failure cause”.

#### 8.2.6.12	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Failure (Physical channel failure and reversion failure)

8.2.6.12.1	Definition

8.2.6.12.2	Conformance requirement

The UE shall perform a cell update procedure when the UE fails to revert to the old configuration after the detection of physical channel failure in the physical channel reconfiguration procedure. After the UE completes cell update procedure, the UE transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “physical channel failure”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.12.3	Test purpose

To confirm that the UE initiates a cell update procedure after it fails to reconfigure the new physical channel and experiences a subsequent failure to revert to the old configuration.

To confirm that UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message after UE completes cell update procedure.

8.2.6.12.4	Method of test

Initial Condition

System Simulator: 2 cells- Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108 in cell 1

Test Procedure

The UE is in the CELL_FACH state in cell 1. The SS begins to broadcast the BCCH in cell 2 and transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE, but it does not reconfigure L1 accordingly. This is expected to cause the UE to fail to reconfigure to the new physical channel. As a result, the UE shall try to revert to the old configuration. However, the SS deletes the old physical channel. Therefore, UE shall reselect to cell 2 and sends a CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “radio link failure”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmits UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and subsequently transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” physical channel failure”.

.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS begins to transmit the BCCH in a cell 2. |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 3 |  |  | The SS does not reconfigure the physical channel and deletes the old configuration. As a result, UE should encounter a failure to reconfigure the new physical channel, then attempt to revert to the old configuration. |
| 4 | ( | CELL UPDATE | The UE shall find cell 2 and be in CELL_FACH state. This message includes the value “radio link failure” set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message includes IE “new U-RNTI” and IE “new C-RNTI”“. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE shall send this message in the cell 2. |
| 7 |  | PHYSICAL CHANNEL RECONGURATION FAILURE | The IE “failure cause” shall be set to “physical channel failure” |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION (Step 1)

Use the message sub-type titled “Packet to CELL_DCH from CELL_FACH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 4 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

PHYSICAL CHANNEL RECONGURATION FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “PHYSICAL CHANNEL RECONGURATION FAILURE” |
| Failure cause | “physical channel failure” |
| Other information element | Not checked |

8.2.6.12.5	Test requirement

After step 3 the UE shall detect the presence of cell 2, camp onto it, and transmit a CELL UPDATE message using RLC-TM mode on the uplink CCCH.

After step 6 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 7 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting the IE “failure cause” to ”physical channel failure”.

#### 8.2.6.13	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Failure (Incompatible simultaneous reconfiguration)

8.2.6.13.1		Definition

8.2.6.13.2	Conformance requirement

If the UE receives a PHYSICAL CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than PHYSICAL CHANNEL RECONFIGURATION, it shall keep its configuration as if the PHYSICAL CHANNEL RECONFIGURATION message had not been received. Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.13.3	Test purpose

To confirm that if the UE receives a PHYSICAL CHANNEL RECONFIGURATION message whilst reconfiguring due to a radio bearer message other than PHYSICAL CHANNEL RECONFIGURATION, it shall keep its configuration as if the PHYSICAL CHANNEL RECONFIGURATION message had not been received and complete the reconfiguration according to the previously received message. 8.2.6.13.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a RADIO BEARER RECONFIGURATION message to the UE. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message before the “activation time” indicated in the RADIO BEARER RECONFIGURATION message expires. When the UE receives the PHYSICAL CHANNEL RECONFIGURATION message, the UE shall keep the configuration as if it had not received the PHYSICAL CHANNEL RECONFIGURATION message and shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “incompatible simultaneous reconfiguration”. After the SS receives the PHYSICAL CHANNEL RECONFIGURATION FAILURE message, the UE reconfigures the new physical channel parameters and transmits a RADIO BEARER RECONFIGURATION COMPLETE message on DCCH using AM RLC.Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER RECONFIGURATION |  |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | Sent before the elapse of the frame number specified in IE “Activation time info” of the message dispatched in step 1. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The UE does not change the configuration due to the reception of PHYSICAL CHANNEL RECONFIGURATION message. |
| 4 | ( | RADIO BEARER RECONFIGURATION COMPLETE | This message is on DCCH using AM RLC. |

Specific Message Contents

RADIO BEARER RECONFIGURATION (Step 1)

For RADIO BEARER RECONFIGURATION in step 1, use the message sub-type indicated as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A.

PHYSICAL CHANNEL RECONFIGURATION (Step 2)

For PHYSICAL CHANNEL RECONFIGURATION in step 2, use the message sub-type indicated as “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | Current CFN-[current CFN mod 8 + 8 ] |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Incompatible simultaneous reconfiguration |
| Other information element | Not checked |

8.2.6.13.5	Test requirement

After step 1, SS transmits a PHYSICAL CHANNEL RECONFIGURATION message before the expiry of the activation time specified in the message of step 1.

After step 2 the UE shall keep its configuration as if the UE had not received the PHYSICAL CHANNEL RECONFIGURATION message and shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with IE “failure cause” set to “Incompatible simultaneous reconfiguration”.

After step 4 the UE communicates with the SS on the DCCH and DTCH using the new physical channel parameters reconfigured as a result of the RADIO BEARER RECONFIGURATION message.

#### 8.2.6.14	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Failure (Invalid message reception and Invalid configuration)

8.2.6.14.1		Definition

8.2.6.14.2	Conformance requirement

The UE shall keep its old configuration when the UE receives a PHYSICAL CHANNEL RECONFIGURATION message containing a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”. It shall then transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message, set “protocol error” in IE “failure cause” and also set “Information element value not comprehended” in IE “Protocol error cause”. The UE shall keep existing configuration before reception of a TRANSPORT CHANNEL RECONFIGURATION message when the TRANSPORT CHANNEL RECONFIGURATION message include some IEs set to invalid value, and then the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION FAILURE including IE “failure cause“ set to “invalid configuration”

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.14.3	Test purpose

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if the received message uses a undefined value in the mandatory IE “UTRAN DRX cycle length coefficient”.

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC if it receives a PHYSICAL CHANNEL RECONFIGURATION message including some IEs set to invalid value.

8.2.6.14.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE which comprises a defined value in the mandatory IE “UTRAN DRX cycle length coefficient”. The UE keeps the old configuration and transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting “protocol error” in IE “failure cause” and also setting “Information element value not comprehended” in IE “Protocol error cause”. The UE keeps initial configuration and SS transmits PHYSICAL CHANNEL RECONFIGURATION message including some IEs set to invalid value. The UE transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION | Contains a mandatory error due to illegal use of undefined value |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The UE does not change the configuration. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION | This message includes IE set to invalid value |
| 4 |  |  | The UE does not change the configuration |
| 5 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | The IE “failure cause” shall be set to “invalid configuration |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION (Step 1)

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| UTRAN DRX cycle length coefficient | Undefined value |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause |  |
| - Failure cause | Protocol error |
| - Protocol error information |  |
| - Protocol error cause | Information element value not comprehended |
| Other information element | Not checked |

PHYSICAL CHANNEL RECONFIGURATION (Step 3)

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Uplink DPCH info | Not present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Failure cause | Invalid configuration |
| Other information element | Not checked |

8.2.6.14.5	Test requirement

After step 1 the UE shall keep its old configuration, transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC with “protocol error” in IE “failure cause” and also “Information element value not comprehended” in IE “Protocol error cause”.

After step 3 the UE shall keep its old configuration.

After step 4 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” invalid configuration”.

#### 8.2.6.15	Physical channel reconfiguration for transition from CELL_FACH to CELL_FACH (Hard handover to another frequency): Success

8.2.6.15.1		Definition

8.2.6.15.2	Conformance requirement

The UE shall correctly reconfigure a physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message when asked to perform a transition from CELL_FACH to CELL_FACH.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.15.3	Test purpose

To confirm that the UE reconfigures a new physical channel according to the PHYSICAL CHANNEL RECONFIGURATION message received from the SS.

8.2.6.15.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE. The UE shall then reconfigure the new physical channel according to this message and the system information messages. Following this, it shall transmit a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message using AM RLC on the RACH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 |  |  | Reconfiguration of physical channel |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A.

8.2.6.15.5	Test requirement

After step 3 the UE shall be in CELL_FACH state and continue to communicate with SS on the common physical channel.

#### 8.2.6.16	Physical channel reconfiguration for transition from CELL_FACH to CELL_FACH: Failure (Cell re-selection)

8.2.6.16.1		Definition

8.2.6.16.2	Conformance requirement

The UE shall initiate the cell reselection procedure when the UE cannot use the assigned physical channel according to a PHYSICAL CHANNEL RECONFIGURATION message, during the transition from CELL_FACH to CELL_FACH in the another cell. After the UE completes cell update procedure, the UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC which set IE “failure cause” to “cell reselection”.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.16.3	Test purpose

To confirm that the UE transmits PHYSICAL CHANNEL RECONFIGURATION FAILURE message after the UE completes a cell reselection and cell update procedure when the it fail to access the assigned physical channel, according to a PHYSICAL CHANNEL RECONFIGURATION message, during the transition from CELL_FACH to CELL_FACH.

8.2.6.16.4	Method of test

Initial Condition

System Simulator: 2 cells Cell 1 is active, Cell 2 is inactive

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state in cell 1. The SS begins to broadcast the BCCH in cell 2 and then transmits a PHYSICAL CHANNEL RECONFIGURATION message, resulting in the UE to attempt to transit from CELL_FACH to CELL_FACH. The UE is expected to fail to access the assigned physical channel as the SS ceases downlink transmission in cell 3. After the UE successfully camp onto cell 2, it shall initiate the cell update procedure in cell 2. The UE transmits CELL UPDATE message on uplink CCCH with IE “Cell update cause“ set to  “cell reselection”. The SS shall transmit CELL UPDATE CONFIRM message on downlink CCCH after receiving CELL UPDATE message. The UE transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC and transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ” cell reselection”. Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | BCCH | The SS starts to broadcast the BCCH in cell 2. |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 3 |  |  | The UE shall detect a failure to use the assigned common physical channel and try to perform a cell reselection. |
| 4 | ( | CELL UPDATE | The UE discover the presence of cell 2 and triggers a cell update procedure. The value “cell reselection” shall be set in IE ”Cell update cause”. |
| 5 | ( | CELL UPDATE CONFIRM | This message include IE “new U-RNTI” and IE “new C-RNTI”. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 7 | ( | PHYSICAL CHANNELRECONFIGURATION FAILURE | The IE “failure cause” shall be set to “cell reselection” |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

Use the message sub-type titled “Packet to CELL_FACH from CELL_FACH in PS” in Annex A.

CELL UPDATE (Step 4)

The contents of CELL UPDATE message is identical as “Contents of CELL UPDATE message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI |  |
| - SRNC Identity | Assigned previously in cell 1 |
| - S-RNTI | Assigned previously in cell 1 |
| Cell Update Cause | “radio link failure” |

CELL UPDATE CONFIRM (Step 5)

The contents of CELL UPDATE CONFIRM message is identical as “CELL UPDATE CONFIRM message“ as found in Annex with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Same as CELL UPDATE message in step 7 |
| New U-RNTI |  |
| - SRNC Identity | ‘0000 0000 0000 0001’ |
| - S-RNTI | Different from previous S-RNTI |
| New C-RNTI | Different from previous C-RNTI |

PHYSICAL CHANNEL RECONFIGURATION FAILURE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type | “RADIO BEARER RECONFIGURATION FAILURE” |
| Failure cause | “cell reselection” |
| Other information element | Not checked |

8.2.6.16.5	Test requirement

After step 3 the UE shall discover the presence of cell 2, enter CELL_FACH state, and initiate a cell update procedure in that cell.

After step 5 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

After step 6 the UE shall transmit PHYSICAL CHANNEL FAILURE message on the DCCH using AM RLC, setting IE “failure cause” to ”cell reselection”.

#### 8.2.6.17	Physical channel reconfiguration for transition from CELL_DCH to CELL_DCH (Hard handover to another frequency): Success (Subsequently received)

8.2.6.17.1		Definition

8.2.6.17.2	Conformance requirement

If the UE receives a PHYSICAL CHANNEL RECONFIGURATION message before the UE reconfigures the radio bearer according to the previous PHYSICAL CHANNEL RECONFIGURATION message, the UE shall ignore the new PHYSICAL CHANNEL RECONFIGURATION message and reconfigure according to the previous PHYSICAL CHANNEL RECONFIGURATION message received. Finally, the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.17.3	Test purpose

To confirm that if the UE receives a PHYSICAL CHANNEL RECONFIGURATION message before the UE reconfigures the radio bearer according to the previous PHYSICAL CHANNEL RECONFIGURATION message it ignores the new PHYSICAL CHANNEL RECONFIGURATION message and reconfigures according to the previous PHYSICAL CHANNEL RECONFIGURATION message.

8.2.6.17.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. When the SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE before the UE reconfigures the radio bearer, the UE ignores the new PHYSICAL CHANNEL RECONFIGURATION message and reconfigures according to the previous PHYSICAL CHANNEL RECONFIGURATION message received. Finally, the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS send this message before the expiry of “activation time” specified in PHYSICAL CHANNEL RECONFIGURATION message of step 1. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | The UE ignores the PHYSICAL CHANNEL RECONFIGURATION message in step 2 and confirms configuration according to the PHYSICAL CHANNEL RECONFIGURATION message in step 1. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.6.17.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the PHYSICAL CHANNEL RECONFIGURATION message in step 1.

#### 8.2.6.18	Physical channel reconfiguration for transition from CELL_FACH to CELL_DCH: Success (Subsequently received)

8.2.6.18.1	Definition

8.2.6.18.2	Conformance requirement

If the UE receives a PHYSICAL CHANNEL RECONFIGURATION message before the UE reconfigures the radio bearer according to the previous PHYSICAL CHANNEL RECONFIGURATION message, the UE shall ignore the new PHYSICAL CHANNEL RECONFIGURATION message and reconfigure according to the previous PHYSICAL CHANNEL RECONFIGURATION message received. Finally, the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.2.6

8.2.6.18.3	Test purpose

To confirm that if the UE receives a PHYSICAL CHANNEL RECONFIGURATION message before the UE reconfigures the radio bearer according to the previous PHYSICAL CHANNEL RECONFIGURATION message it ignores the new PHYSICAL CHANNEL RECONFIGURATION message and reconfigures according to the previous PHYSICAL CHANNEL RECONFIGURATION message.

8.2.6.18.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_FACH (state 6-11) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_FACH state. When the SS transmits a PHYSICAL CHANNEL RECONFIGURATION message to the UE before the UE reconfigures the radio bearer, the UE ignores the new PHYSICAL CHANNEL RECONFIGURATION message and reconfigures according to the previous PHYSICAL CHANNEL RECONFIGURATION message received. Finally, the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS send this message before the expiry of “activation time” specified in PHYSICAL CHANNEL RECONFIGURATION message of step 1. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | The UE ignores the PHYSICAL CHANNEL RECONFIGURATION message in step 2 and confirms configuration according to the PHYSICAL CHANNEL RECONFIGURATION message in step 1. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_FACH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Activation Time Info | [256+Current CFN-[current CFN mod 8 + 8 ]]MOD 256 |

8.2.6.18.5	Test requirement

After step 3 the UE shall communicate with the SS on the radio bearer specified in the PHYSICAL CHANNEL RECONFIGURATION message in step 1.

#### 8.2.6.19	Physical Channel Reconfiguration from CELL_DCH to CELL_PCH: Success

8.2.6.19.1	Definition

8.2.6.19.2	Conformance requirement

The UE shall transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message using and transits from CELL_DCH to CELL_PCH when receives a PHYSICAL CHANNEL RECONFIGURATION message. And then, the UE shall reconfigure radio bearers according to the PHYSICAL CHANNEL RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.6.19.3	Test purpose

To confirm that the UE transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message before entering CELL_PCH state after it received a PHYSICAL CHANNEL RECONFIGURATION message and reconfigured its radio bearers. The UE is in CELL_PCH state in the same cell.

8.2.6.19.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message. The UE transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into CELL_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | The UE sends this message before start state transition. |
| 3 |  |  | Reconfiguration of Physical Channel after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.6.19.5	Test requirement

After step 1 the UE transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_DCH to CELL_PCH.

#### 8.2.6.20	Physical Channel Reconfiguration from CELL_DCH to URA_PCH: Success

8.2.6.20.1	Definition

8.2.6.20.2	Conformance requirement

The UE shall transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message using and transits from CELL_DCH to URA_PCH when receives a PHYSICAL CHANNEL RECONFIGURATION message. And then, the UE shall reconfigure radio bearers according to the PHYSICAL CHANNEL RECONFIGURATION message.

Reference

3GPP TS 25.331 clause 8.2.2

8.2.6.20.3	Test purpose

To confirm that the UE transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message before entering URA_PCH state after it received a PHYSICAL CHANNEL RECONFIGURATION message and reconfigured its radio bearers. The UE is in CELL_PCH state.

8.2.6.20.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: PS-DCCH+DTCH_DCH(state 6-10) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message. The UE transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to the UE using AM RLC and enters into URA_PCH state. The SS transmits a PAGING TYPE 1 message and the UE accepts it and enters the CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PHYSICAL CHANNEL RECONFIGURATION |  |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | The UE sends this message before start state transition. |
| 3 |  |  | Reconfiguration of Physical Channel after state transition. |
| 4 | ( | PAGING TYPE 1 | The SS transmits this message included a matched identity. |
| 5 | ( | CELL UPDATE | The UE is in CELL_FACH state. |

Specific Message Contents

PHYSICAL CHANNEL RECONFIGURATION (Step 1)

Use the same message sub-type titled “Packet to CELL_FACH from CELL_DCH in PS“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |

PAGING TYPE 1 (Step 4)

Use the same message sub-type titled “TM (SMS in PS)“ in Annex A with following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Paging record list Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN originator Previously assigned SRNC identity Previously assigned S-RNTI |

8.2.6.20.5	Test requirement

After step 1 the UE transmits PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to the UE on uplink DCCH using AM RLC.

After step 3 the UE shall transit from CELL_DCH to URA_PCH.

| 8.2.6.21 Void |  |  |  |
| --- | --- | --- | --- |

| 8.2.6.22 Void |  |  |  |
| --- | --- | --- | --- |

### 8.2.7	Physical Shared Channel Allocation [TDD only]

[Editor’s note: This message is not included in Release99 so this is FFS.]

### 8.2.8	PUSCH capacity request [TDD only]

[Editor’s note: This message is not included in Release99 so this is FFS.]

| 8.2.9 Void |  |  |  |
| --- | --- | --- | --- |

## 8.3	RRC connection mobility procedure

### 8.3.1 	Cell Update

#### 8.3.1.1	Cell Update: cell reselection in CELL_FACH

8.3.1.1.1	Definition

8.3.1.1.2	Conformance requirement

This procedure is used to update UTRAN with the current cell of the UE after it has performed a cell reselection in CELL_FACH state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.1.3	Test purpose

To confirm that the UE executes a cell update procedure after the successful reselection of another UTRA cell. To confirm that the UE send the correct uplink respond message when executing cell update procedure due to cell reselection.

8.3.1.1.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, with the downlink transmission power shown in column marked “T0” in Table 8.3.1.1-1, while cell 2 is inactive

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

| Parameter | Unit | Cell 1 | Cell 2 |
| --- | --- | --- | --- |
|  |  | T0 | T1 | T2 | T0 | T1 | T2 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 1 |
|  | dB | 7.3 | 1.2 | 7.3 | Cell 2 is switched off | 7.3 | 1.2 |
| CPICH Ec/Io | dB | -10.7 | -17.7 | -11.6 |  | -11.6 | -17.7 |
| CPICH RSCP | dBm | -72.7 | -78.8 | -72.7 |  | -72.7 | -78.8 |

Table 8.3.1.1-1

Table 8.3.1.1-1 illustrates the downlink power to be applied for the 2 cells at various time instants of the test execution.  Columns marked “T0” denote the initial conditions, while columns marked “T1” and “T2” are to be applied subsequently.  SS switches the power settings repeatedly between columns “T1” and “T2”, whenever the description below specifies that the transmission power settings for cell 1 and cell 2 are reversed.

The UE is in the CELL_FACH state, camping onto cell 1. SS configures its downlink transmission power settings according to columns “T1” in Table 8.3.1.1-1. SS starts to broadcast BCCH on the primary CCPCH in cell 2. The UE shall find cell 2 to be more suitable for service and hence perform a cell reselection. After the completion of cell reselection, the UE shall transmits a CELL UPDATE message to the SS on the uplink CCCH of cell 2 and set IE “Cell update cause” to “Cell Reselection”. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message, which includes the IE “RRC State Indicator” set to “CELL_PCH”, to the UE on the downlink DCCH. SS verifies that the UE does not send any response to this message. UE shall move to CELL_PCH state. SS then reverses the transmission power of cell 1 and cell 2. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 1. SS replies with CELL UPDATE CONFIRM message and allocates new C-RNTI and U-RNTI identities to the UE. The IE “RRC State Indicator” is set to “CELL_FACH” in this message. The UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message. Following this, SS reverses the transmission power settings for cell 1 and cell 2 again. The UE shall initiate a cell update procedure by transmitting a CELL UPDATE message and stating the cause as ‘cell re-selection’. SS replies with a CELL UPDATE CONFIRM message which contains IE “Physical channel information elements”. The UE shall send PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to acknowledge the change in physical resources. Then, SS reverses the transmission power settings for cell 1 and cell 2 again. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 1. SS replies with a CELL UPDATE CONFIRM message which contains IE “Transport channel information elements”.  The UE shall send TRANSPORT CHANNEL RECONFIGURATION COMPLETE message. Following this, SS reverses the transmission power settings for cell 1 and cell 2 again. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 2. SS replies with a CELL UPDATE CONFIRM message which contains IE “RB information to be affected list”.  The UE shall send RADIO BEARER RECONFIGURATION COMPLETE message. Finally, SS reverses the transmission power settings for cell 1 and cell 2 once again. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 1. SS replies with a CELL UPDATE CONFIRM message which contains IE “RB information to release list”.  The UE shall send RADIO BEARER RELEASE COMPLETE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_FACH state in cell 1 |
| 2 | ( | BCCH | SS applies the downlink transmission power settings, according to the values in columns “T1” of Table 8.3.1.1-1. The SS starts to broadcast BCCH on the primary CCPCH in cell 2 with a power level that is higher than that in cell 1. The UE shall find that the cell 2 is better for service and perform a reselection. SS waits for the maximum duration required for the UE to camp to cell 2. |
| 3 | ( | CELL UPDATE | Value “cell reselection” should be indicated in IE “ Cell update cause” |
| 4 | ( | CELL UPDATE CONFIRM | IE “RRC State Indicator” is set to “CELL_PCH”. SS set k=0. |
| 5 |  |  | SS checks the uplink PRACH channel to verify that no response is sent by UE. |
| 6 |  |  | SS reverses the transmission power level of cell 1 and cell 2. |
| 7 | ( | CELL UPDATE |  |
| 8 | ( | CELL UPDATE CONFIRM | IE “RRC State Indicator” is set to “CELL_FACH”. If k ( 0, new C-RNTI and U-RNTI identities are assigned to the UE. If k>1, IE ”Physical channel information elements” is included in this message. If k>2, IE ”Transport channel information elements” is included in this message. If k>3, IE ”RB information to be affected list” is included in this message. If k>4, IE ”RB information to release list” is included in this message. Increment k by 1. |
| 9 | ( | UTRAN MOBILITY INFORMATION CONFIRM | If k=1 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 10 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | If k=2 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 11 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | If k=3 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 12 | ( | RADIO BEARER RECONFIGURATION COMPLETE | If k=4 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 13 | ( | RADIO BEARER RELEASE COMPLETE | If k=5 when SS received this message, test ends. Else test fails. If this message is not received, test fails. |

Specific Message Contents

CELL UPDATE (Steps 3 and 7)

The same message found in Annex A shall be transmitted by the UE on the uplink CCCH, with the exception of the following IEs:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0000 0001’ when k<1. Check to see if set to same string in IE “S-RNTI” in IE “New U-RNTI” of CELL UPDATE CONFIRM message in previous step 8 when k<0. Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Cell Re-selection’ |

CELL UPDATE CONFIRM (Step 4)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

CELL UPDATE CONFIRM (Step 8 and k = 0)

Use the same message sub-type found in step 4, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI New C-RNTI | ‘0000 0000 0001’ An arbitrary 20-bits string which is different from original S-RNTI An arbitrary 16-bits string which is different from original C-RNTI assigned in RRC connection establishment procedure. |

CELL UPDATE CONFIRM (Step 8 and k=1)

Use the same message sub-type found in step 8 and k=0, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Maximum allowed uplink TX power | 3 dB below the follow value: Minimum of { 33 dBm, maximum uplink power allowed under the UE power class } |

CELL UPDATE CONFIRM (Step 8 and k=2)

Use the same message sub-type found in step 8 and k=1, with the following exceptions:

| Added or Reconfigured uplink TrCH information -Transport channel identity -TFS -Dynamic Transport format information -Number of Transport blocks -RLC size -Semi-static Transport Format information -Transmission time interval -Type of channel coding -Coding Rate -Rate matching attribute -CRC size | 1 ( This IE is repeated for TFI number) Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set |
| --- | --- |

CELL UPDATE CONFIRM (Step 8 and k=3)

Use the same message sub-type found in step 8 and k=2, with the following exceptions:

| RB information to be affected -RB identity -RB mapping info -Information for each multiplexing option -Number of uplink RLC logical channels -Uplink transport channel type -uplink Transport channel identity -Logical channel identity -CHOICE RLC size list -MAC logical channel priority -Number of downlink RLC logical channels -Downlink transport channel type -DL Transport channel identity -Logical channel identity | (UM DCCH for RRC) 1 1 RACH 1 1 2 1 FACH 1 1 |
| --- | --- |

CELL UPDATE CONFIRM (Step 8 and k=4)

Use the same message sub-type found in step 8 and k=3, with the following exceptions:

| RB information to release -RB identity | 4 |
| --- | --- |

8.3.1.1.5	Test requirement

After step 2 the UE shall reselect to cell 2 and then it shall transmit a CELL UPDATE message which, sets the value  “cell reselection” in IE “Cell update cause”.

After step 4 the UE shall not transmit any uplink message in response to the CELL UPDATE CONFIRMATION message received in step 4.

After step 6 the UE shall sent CELL UPDATE message to cell with stronger transmitting power, in order to indicate that a cell reselection has taken place.

After step 8, if k=1, the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message to acknowledge that it has started to use the new RNTI identities allocated.

If k=2, the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the new physical channel assigned.

If k=3, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to acknowledge that it has reconfigured the transport channels.

If k=4, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message to acknowledge that it has reconfigured the radio bearers.

If k=5, the UE shall transmit RADIO BEARER RELEASE COMPLETE message to acknowledge that it has release its radio bearers.

#### 8.3.1.2	Cell Update: cell reselection in CELL_PCH

8.3.1.2.1	Definition

8.3.1.2.2	Conformance requirement

This procedure is to update UTRAN with information of the current cell, after a cell reselection has occurred in CELL_PCH state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.2.3	Test purpose

To confirm that the UE, in CELL_PCH state, executes a cell update procedure after the successful reselection of another UTRA cell. To confirm that the UE replies with an appropriate uplink message after receiving CELL UPDATE CONFIRM message during the cell update procedure.

8.3.1.2.4	Method of test

Initial Condition

System Simulator: 2 cells – Cell 1 is active with the downlink transmission power shown in column marked “T0” in Table 8.3.1.1-1, while cell  2 is inactive

UE: CELL_PCH (state 6-12) in cell 1 as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is brought to CELL_PCH state and is camped onto cell 1. The SS starts to broadcast system information on the BCCH on the primary CCPCH in cell 2. SS configures its downlink transmission power settings according to columns “T1” in Table 8.3.1.1-1. When the UE detects the presence of cell 2, it moves to CELL_FACH state and transmits a CELL UPDATE message on the uplink CCCH. The value “cell reselection” shall be set in IE “ Cell update cause” in CELL UPDATE message. Upon reception of CELL_UPDATE message, SS replies with a CELL UPDATE CONFIRM message with the IE “RRC State Indicator” set to “CELL_PCH”. After receiving this message, the UE returns to CELL_PCH state without transmitting any uplink message. Next, SS reverses the transmission strengths of cell 1 and cell 2 again. This will cause the UE to send CELL UPDATE message on the uplink CCCH of cell 1. SS then sends CELL UPDATE CONFIRM message with the assignment of new C-RNTI and U-RNTI identities. The UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message as a response. Following this, SS reverses the transmission power settings for cell 1 and cell 2 again.  The UE shall initiate a cell update procedure by transmitting a CELL UPDATE message on the uplink CCCH of cell 2 and stating the cause as ‘cell re-selection’.  SS replies with a CELL UPDATE CONFIRM message which contains “Physical channel information elements”.  The UE shall send PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to acknowledge the change in physical resources.  Then, SS reverses the transmission power settings for cell 1 and cell 2 again. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 1. SS replies with a CELL UPDATE CONFIRM message which contains “Physical channel information elements” and “Transport channel information elements”.  The UE shall send TRANSPORT CHANNEL RECONFIGURATION COMPLETE message. Following this, SS reverses the transmission power settings for cell 1 and cell 2 again. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 2. SS replies with a CELL UPDATE CONFIRM message which contains “Physical channel information elements”, “Transport channel information elements” and IE “RB information to be affected list”.  The UE shall send RADIO BEARER RECONFIGURATION COMPLETE message. Finally, SS reverses the transmission power settings for cell 1 and cell 2 once again. The UE shall send a CELL UPDATE message on the uplink CCCH of cell 1. SS replies with a CELL UPDATE CONFIRM message which contains “Physical channel information elements”, “Transport channel information elements”, IE “RB information to reconfigure list” and IE “RB information to release list”.  The UE shall send RADIO BEARER RELEASE COMPLETE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_PCH state in cell 1 |
| 2 | ( | BCCH | The SS starts to broadcast system information message on BCCH on the primary CCPCH from cell 2. SS reverse the transmission level of cell 2 and cell 1. The UE shall find that the cell 2 is better and attempt to perform a cell reselection. |
| 3 | ( | CELL UPDATE | The UE moves to CELL_FACH state and transmits this message with the IE “ Cell update cause” set to “cell reselection” |
| 4 | ( | CELL UPDATE CONFIRM | IE ”RRC State Indicator” is set to “CELL_PCH”. SS set k=0. |
| 5 |  |  | SS swaps the transmission power of cell 1 and cell 2, making cell 1 the stronger cell. |
| 6 | ( | CELL UPDATE | UE move from CELL_PCH to CELL_FACH to transmit this message. |
| 7 | ( | CELL UPDATE CONFIRM | IE “RRC State Indicator” is set to “CELL_FACH”. If k ( 0, new C-RNTI and U-RNTI identities are assigned to the UE. If k>1, IE ”Physical channel information elements” is included in this message. If k>2, IE ”Transport channel information elements” is included in this message. If k>3, IE ”RB information to be affected list” is included in this message. If k>4, IE ”RB information to release list” is included in this message. Increment k by 1. |
| 8 | ( | UTRAN MOBILITY INFORMATION CONFIRM | If k=1 when SS received this message, go to step 5. Else test fails. If this message is not received, proceed to next step. |
| 9 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | If k=2 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 10 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | If k=3 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 11 | ( | RADIO BEARER RECONFIGURATION COMPLETE | If k=4 when SS received this message, go to step 6. Else test fails. If this message is not received, proceed to next step. |
| 12 | ( | RADIO BEARER RELEASE COMPLETE | If k=5 when SS received this message, test ends. Else test fails. If this message is not received, test fails. |

Specific Message Contents

CELL UPDATE (Steps 3and 6)

Use the same message sub-type found in Annex A, with the following exception.

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0000 0001’ when k<1. Check to see if set to same string in IE “S-RNTI” in IE “New U-RNTI” of CELL UPDATE CONFIRM message in previous step 7 when k<0. Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Cell Re-selection’ |

CELL UPDATE CONFIRM (Step 4)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

CELL UPDATE CONFIRM (Step 7 and k=0)

Use the same message sub-type found in step 4, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI New C-RNTI | ‘0000 0000 0000 0001’ An arbitrary 20-bits string which is different from original S-RNTI An arbitrary 16-bits string which is different from original C-RNTI. |

CELL UPDATE CONFIRM (Step 7 and k=1)

Use the same message sub-type found in step 7 with k=0, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Maximum allowed uplink TX power | 3 dB below the follow value: Minimum of { 33 dBm, maximum uplink power allowed under the UE power class } |

CELL UPDATE CONFIRM (Step 7 and k=2)

Use the same message sub-type found in step 7 with k=1, with the following exceptions:

| Added or Reconfigured uplink TrCH information -Transport channel identity -TFS -Dynamic Transport format information -Number of Transport blocks -RLC size -Semi-static Transport Format information -Transmission time interval -Type of channel coding -Coding Rate -Rate matching attribute -CRC size | 1 ( This IE is repeated for TFI number) Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set |
| --- | --- |

CELL UPDATE CONFIRM (Step 7 and k=3)

Use the same message sub-type found in step 7 with k=2, with the following exceptions:

| RB information to be affected -RB identity -RB mapping info -Information for each multiplexing option -Number of uplink RLC logical channels -Uplink transport channel type -uplink Transport channel identity -Logical channel identity -CHOICE RLC size list -MAC logical channel priority -Number of downlink RLC logical channels -Downlink transport channel type -DL Transport channel identity -Logical channel identity | (UM DCCH for RRC) 1 1 RACH 1 1 2 1 FACH 1 1 |
| --- | --- |

CELL UPDATE CONFIRM (Step 7 and k=4)

Use the same message sub-type found in step 7 with k=3, with the following exceptions:

| RB information to release -RB identity | 4 |
| --- | --- |

8.3.1.2.5	Test requirement

After step 2 the UE shall reselect to cell 2 and transmit a CELL UPDATE message, containing the IE “Cell update cause” set to “cell reselection”.

After step 5 the UE shall reselect to stronger transmitting cell and transmit a CELL UPDATE message, containing the IE ”Cell update cause” set to “cell reselection”.

After step 7, if k=1, the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

If k=2, the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

If k=3, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to acknowledge that it has reconfigured the transport channels.

If k=4, the UE shall transmit RADIO BEARER RECONFIGURATION COMPLETE message to acknowledge that it has reconfigured the radio bearers.

If k=5, the UE shall transmit RADIO BEARER RELEASE COMPLETE message to acknowledge that it has release its radio bearers.

#### 8.3.1.3	Cell Update: periodical cell update in CELL_FACH

8.3.1.3.1	Definition

8.3.1.3.2	Conformance requirement

This procedure is to update UTRAN with the current cell information, after the UE has remained in the service area in the CELL_FACH state for a period exceeding the timer value T305.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.3.3	Test purpose

To confirm that the UE executes a periodic cell update procedure following the expiry of timer T305. To confirm that the UE sends a correct response to the CELL UPDATE CONFIRM message. To confirm that the UE listens to the system information messages and then responds to a change in the setting for timer T305.

8.3.1.3.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

The UE is in CELL_FACH state. When the UE detects the expiry of timer T305 according to the settings in system information, the UE transmits a CELL UPDATE message to the SS on the uplink CCCH with a cause indicating periodic cell updating. SS replies with a CELL UPDATE CONFIRM message, and IE “RRC State Indicator” is set to “CELL_FACH”. SS verifies that the UE does not transmit any uplink message. SS then waits for T305 to expire again. The UE shall send another CELL UPDATE message to report periodic cell updating. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message which includes the IEs ”new C-RNTI”, “new U-RNTI” to the UE on the downlink DCCH. Then the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH to acknowledge the receipt of the new UE identities. Next, the content of the SYSTEM INFORMATION BLOCK TYPE 1 is changed to disable periodic cell updating. SS then monitors the uplink CCCH for a period up to the maximum possible value for timer T305 (720minutes) and verifies that no CELL_UPDATE message is received. After this, the SS changes the timer T305 value to 5 minutes. UE shall resume periodic cell updating procedure and transmit CELL_UPDATE message 5 minutes after this modification.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_FACH state. SS waits until T305 has expired. |
| 2 | ( | CELL UPDATE | IE “Cell update cause” shall be set to “Periodic cell updating” |
| 3 | ( | CELL UPDATE CONFIRM | No RNTI identities are given. No information on PRACH and S-CCPCH are provided. |
| 4 |  |  | SS verifies that no uplink message is received from UE. SS waits for another period to allow T305 to expire. |
| 5 | ( | CELL UPDATE | Which is set to “periodical cell update” in IE “Cell update cause” upon the expiry of timer T305. |
| 6 | ( | CELL UPDATE CONFIRM | Including IEs ”new C-RNTI” , “new U-RNTI” and IE “RRC State Indicator” is set to ”CELL_FACH” |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 8 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 | SS changes the contents of MASTER INFORMATION BLOCK and SYSTEM INFORMATION BLOCK (see specific message contents). It waits for 720 minutes and checks that no CELL UPDATE message is transmitted on uplink PRACH channel. |
| 9 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 2 | SS modified the contents of MASTER INFORMATION BLOCK and SYSTEM INFORMATION BLOCK (see specific message contents) again. |
| 10 | ( | CELL UPDATE | UE shall transmit this message 5 minutes after step 9, with “cell update cause” set to “periodic cell updating” |
| 11 | ( | CELL UPDATE CONFIRM |  |

Specific Message Contents

CELL UPDATE (Step 2 and 5)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ |

CELL UPDATE CONFIRM (Step 3)

Use the same message sub-type found in Annex A.

CELL UPDATE CONFIRM (Step 6 and 11)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI | Set to ‘0000 0000 0001’ Set to an arbitrary string different from ‘0000 0000 0000 0000 0001’ |

CELL UPDATE (Step 14)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0000 0001’ Check to see if set to same bit string as in IE “S-RNTI” in IE “U-RNTI” of the CELL UPDATE CONFIRM message sent in step 6. Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ |

MASTER INFORMATION BLOCK (Step 8)

| Information Element | Value/remark |
| --- | --- |
| MIB Tag | 2 |

SYSTEM INFORMATION BLOCK TYPE 1 (Step 8)

| Information Element | Value/remark |
| --- | --- |
| UE Timers and constants in connected mode T305 | No update Infinity |

MASTER INFORMATION BLOCK (Step 9)

| Information Element | Value/remark |
| --- | --- |
| MIB Tag | 1 |

SYSTEM INFORMATION BLOCK TYPE 1 (Step 9)

| Information Element | Value/remark |
| --- | --- |
| UE Timers and constants in connected mode T305 | 5 minutes |

8.3.1.3.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305 then transmits a CELL UPDATE message setting value “periodical cell update” into IE “Cell update cause”.

After step 3 the UE shall not send any uplink message as a response to CELL UPDATE CONFIRM message sent in step 3.

After step 4 the UE shall send CELL UPDATE message, specifying the cell updating cause to be “periodical cell update”.

After step 6 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

Between step 8 and step 9 the UE shall cease periodic cell updating activity and not transmit any CELL UPDATE messages.

After step 9 the UE shall transmit a CELL UPDATE message stating the cell update cause to be periodic updating, 5 minutes after the SS has modified the BCCH data.

#### 8.3.1.4	Cell Update: periodical cell update in CELL_PCH

8.3.1.4.1	Definition

8.3.1.4.2	Conformance requirement

This procedure is to update UTRAN with the information of the current cell when the UE detects that it is still in the service area, while residing in the CELL_PCH state, after the expiry of timer T305.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.4.3	Test purpose

To confirm that the UE, in CELL_PCH state, executes a cell update procedure after the expiry of timer T305. To confirm that the UE sends an appropriate response message after receiving the CELL UPDATE CONFIRM message.

8.3.1.4.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH (state 6-12) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE starts from CELL_PCH state. When the UE detects the expiry of periodic cell updating timer T305 according to the system information, the UE moves to CELL_FACH state. It shall transmit a CELL UPDATE message on the uplink CCCH and set the value “periodical cell update” into IE “Cell update cause”. SS answers with a CELL UPDATE CONFIRM message, with IE “RRC State Indicator” set to “CELL_FACH”. SS checks to confirm that the UE does not send a response. SS sends a UTRAN MOBILITY INFORMATION message to the UE, stating the new C-RNTI identity to be used and also setting IE “RRC State Indicator” to “CELL_PCH”. The UE shall reply with UTRAN MOBILITY INFORMATION CONFIRM message and transit to CELL_PCH state. Next, SS stays idle until timer T305 is once again expired. The UE shall transmit CELL UPDATE message in order to initiate cell updating procedure. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message which includes the IEs ”new C-RNTI” and “new U-RNTI”. Then the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH and before entering CELL_PCH state. Next, the content of the SYSTEM INFORMATION BLOCK TYPE 1 is changed to disable periodic cell updating.  SS then monitors the uplink CCCH for a period up to the maximum possible value for timer T305 (720minutes) and verifies that no CELL_UPDATE message is received.  After this, the SS changes the timer T305 value to 5 minutes.  UE shall resume periodic cell updating procedure and transmit CELL_UPDATE message 5 minutes after this modification.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_PCH state. SS waits until T305 has expired. |
| 2 | ( | CELL UPDATE | The UE shall move to CELL_FACH state and transmits this message with the IE “ Cell update cause” set to “periodical cell update”. |
| 3 | ( | CELL UPDATE CONFIRM | Does not include IEs “PRACH Info”, “Secondary CCPCH Info”, “new C-RNTI” or “new U-RNTI”. |
| 4 |  |  | SS verifies that no response message is received. |
| 5 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI identity to UE and set IE “RRC State Indicator” to ”CELL_PCH”. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE shall move to CELL_PCH state |
| 7 |  |  | SS remains idle for a period sufficient for T305 timer to expire. |
| 8 | ( | CELL UPDATE | This message shall contain the new U-RNTI identity assigned in step 5. UE moves t o CELL_FACH to transmit this message. |
| 9 | ( | CELL UPDATE CONFIRM | New C-RNTI and U-RNTI identities are assigned. |
| 10 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves back to CELL_PCH after transmitting this message. |
| 11 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 | SS changes the contents of MASTER INFORMATION BLOCK and SYSTEM INFORMATION BLOCK (see specific message contents). It waits for 720 minutes and checks that no CELL UPDATE message is transmitted on uplink PRACH channel. |
| 12 | ( | MASTER INFORMATION BLOCK SYSTEM INFORMATION BLOCK TYPE 1 | SS modified the contents of MASTER INFORMATION BLOCK and SYSTEM INFORMATION BLOCK (see specific message contents) again. |
| 13 | ( | CELL UPDATE | UE shall transmit this message 5 minutes after step 12, with “cell update cause” set to “periodic cell updating” |
| 14 | ( | CELL UPDATE CONFIRM |  |

Specific Message Contents

CELL UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ |

CELL UPDATE CONFIRM (Step 3 and 13)

Use the same message sub-type found in Annex A.

UTRAN MOBILITY INFORMATION (Step 5)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI | Set to ‘0000 0000 0001’ Set to ‘0000 0000 0000 0000 1111’ |
| New C-RNTI | Set to ‘0000 0000 0000 1111’ |
| RRC State Indicator | CELL_PCH |

CELL UPDATE (Step 8)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 1111’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ |

CELL UPDATE CONFIRM (Step 9)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI New C-RNTI | Set to ‘0000 0000 0001’ Set to ‘0000 0000 0000 0000 1010’ Set to ‘0000 0000 0000 0101’ |

MASTER INFORMATION BLOCK (Step 11)

| Information Element | Value/remark |
| --- | --- |
| MIB Tag | 2 |

SYSTEM INFORMATION BLOCK TYPE 1 (Step 11)

| Information Element | Value/remark |
| --- | --- |
| UE Timers and constants in connected mode T305 | No update Infinity |

MASTER INFORMATION BLOCK (Step 12)

| Information Element | Value/remark |
| --- | --- |
| MIB Tag | 1 |

SYSTEM INFORMATION BLOCK TYPE 1 (Step 12)

| Information Element | Value/remark |
| --- | --- |
| UE Timers and constants in connected mode T305 | 5 minutes |

8.3.1.4.5	Test requirement

After step 2 the UE shall detect the expiry of timer T305, it shall then move to CELL_FACH state and transmits a CELL UPDATE message with the IE “Cell update cause” set to “periodical cell update”.

After step 5 the UE shall reply with UTRAN MOBILITY INFORMATION CONFIRM message. It shall subsequently move to CELL_PCH state.

After step 7 the UE shall initiate a cell updating procedure by the transmission of a CELL UPDATE message. In this message, it shall indicate the new U-RNTI value assigned in step 5 and also set IE “Cell Updating Cause” to “Periodical Cell Updating”.

Between step 11 and step 12 the UE shall cease periodic cell updating activity and not transmit any CELL UPDATE messages.

After step 12 the UE shall transmit a CELL UPDATE message stating the cell update cause to be periodic updating, 5 minutes after the SS has modified the BCCH data.

#### 8.3.1.5	Cell Update: UL data transmission in URA_PCH

8.3.1.5.1	Definition

8.3.1.5.2	Conformance requirement

This procedure is to update UTRAN with the current cell information if the UE wants to transmit uplink data while in URA_PCH state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.5.3	Test purpose

To confirm that the UE executes a cell update procedure when the UE transmits uplink data if the UE is in URA_PCH state. To confirm that the UE sends the correct response to CELL UPDATE CONFIRM message, after it has taken into consideration the current TFS and/or TFCS settings.

8.3.1.5.4	Method of test

Initial Condition

System Simulator: 1cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE starts from URA_PCH state, after the operator initiates an outgoing packet data transmission. The UE then moves to CELL_FACH state and transmits a CELL UPDATE message to the SS on the uplink CCCH, with the IE “Cell update cause” set to value “uplink data transmission”. After receiving such a message, SS transmits CELL UPDATE CONFIRM message without specifying IE “new C-RNTI” or IE “new U-RNTI” or “CN information elements” or “ Physical channel information elements” or “Transport channel information elements” or RB information elements”. The UE shall stay in CELL_FACH state and transmit no response message. SS waits until uplink data transmission is completed and sends a UTRAN MOBILITY INFORMATION message. The UE shall reply with UTRAN MOBILITY INFORMATION CONFIRM message. Since the IE “RRC State Indicator” is set to “URA_PCH” in the downlink message, the UE shall move to URA_PCH state. Then SS prompts the test operator to transmit packet data.  The UE shall send CELL UPDATE message once more.  After the SS receives this message, it replies with a CELL UPDATE CONFIRM message including “Physical channel information elements”.  The IE ”RRC State Indicator” is set to “CELL_FACH” in this message.  The UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message.  Then the UE shall enter CELL_FACH state and proceed to transmit packet data. Finally, SS prompts the test operator to transmit packet data once again. The UE shall send CELL UPDATE message and specifies the cause to be “uplink data transmission”. SS replies with CELL UPDATE CONFIRM message including “Transport channel information elements”. After receiving this message, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message and remains in CELL_FACH state. SS again waits for the transmission of user packet data to complete and then sends UTRAN MOBILITY INFORMATION message on the downlink DCCH. The IE “RRC State Indicator” is set to “URA_PCH”. The UE shall move to URA_PCH state after it acknowledges that it starts using the new RNTI identity provided.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to URA_PCH state. SS prompts the test operator to begin a packet data transmission. |
| 2 | ( | CELL UPDATE | The UE shall move to CELL FACH state with the message set to “uplink data transmission” in IE “Cell update cause”. |
| 3 | ( | CELL UPDATE CONFIRM | Use default message content. |
| 4 |  |  | SS check that UE does not send response message. |
| 5 |  |  | SS waits until transmission of uplink data has been completed. |
| 6 | ( | UTRAN MOBILITY INFORMATION | IE “RRC State Indicator” set to “DRX with URA update” |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to URA_PCH state. |
| 8 |  |  | SS prompts test operator to initiate a packet data transmission. |
| 9 | ( | CELL UPDATE | Should be same as in step 2 |
| 10 | ( | CELL UPDATE CONFIRM | Including “Physical channel information elements”. |
| 11 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |
| 12 |  |  | SS waits until transmission of uplink data has been completed. |
| 13 | ( | UTRAN MOBILITY INFORMATION | IE “RRC State Indicator” set to “DRX with URA update” |
| 14 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 15 |  |  | SS prompts test operator to initiate a packet data transmission. |
| 16 | ( | CELL UPDATE | Should be same as in step 2 |
| 17 | ( | CELL UPDATE CONFIRM |  |
| 18 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

CELL UPDATE (Step 2, 9 and 16)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 1111’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘uplink data transmission’ |

CELL UPDATE CONFIRM (Step 3)

Use the same message sub-type found in Annex A.

CELL UPDATE CONFIRM (Step 10)

Use the same message sub-type found in step 3, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Maximum allowed uplink TX power | 3 dB below the follow value: Minimum of { 33 dBm, maximum uplink power allowed under the UE power class } |

CELL UPDATE CONFIRM (Step 17)

Use the same message sub-type found in step 10, with the following exceptions:

| Added or Reconfigured uplink TrCH information -Transport channel identity -TFS -Dynamic Transport format information -Number of Transport blocks -RLC size -Semi-static Transport Format information -Transmission time interval -Type of channel coding -Coding Rate -Rate matching attribute -CRC size | 1 ( This IE is repeated for TFI number) Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set |
| --- | --- |

UTRAN MOBILITY INFORMATION (Step 6)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | ‘0000 0000 0000 1111’ |
| RRC State Indicator | URA_PCH |

UTRAN MOBILITY INFORMATION (Step 13)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | ‘0000 0000 1111 1111’ |
| RRC State Indicator | URA_PCH |

PHYSICAL CHANNEL RECONFIGURATION COMPLETE (Step 11)

Only the message type IE in this message will be checked.

TRANSPORT CHANNEL RECONFIGURATION COMPLETE (Step 18)

Only the message type IE in this message will be checked.

8.3.1.5.5	Test requirement

After step 1 the UE shall move to CELL_FACH state to initiate a cell update procedure and transmits a CELL UPDATE message which is set to “uplink data transmission” in IE “Cell update cause”.

After step 8 the UE shall initiate cell update procedure and transmit CELL UPDATE message on the uplink CCCH. The IE “Cell update cause” shall be set to “uplink data transmission”.

After step 10 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

After step 15 the UE shall initiate cell update procedure and transmit CELL UPDATE message on the uplink CCCH. The IE “Cell update cause” shall be set to “uplink data transmission”.

After step 17 the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

#### 8.3.1.6	Cell Update: UL data transmission in CELL_PCH

8.3.1.6.1	Definition

8.3.1.6.2	Conformance requirement

This procedure is to update UTRAN with the current cell of the UE if the UE wants to transmit uplink data when the UE is in CELL_PCH state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.6.3	Test purpose

To confirm that the UE executes a cell update procedure when the UE transmits uplink data if the UE is in CELL_PCH state. To confirm that the UE sends the correct response to CELL UPDATE CONFIRM message, after it has taken into consideration the current TFS and/or TFCS settings.

8.3.1.6.4	Method of test

Initial Condition

System Simulator: 1cell

UE: CELL_PCH (state 6-12) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_PCH state. SS asks the test operator to send some packet data. The UE moves to CELL_FACH state and transmits a CELL UPDATE message to the SS on the uplink CCCH, which shall indicate “uplink data transmission” in IE “Cell update cause”. After receiving such a message, SS transmits default CELL UPDATE CONFIRM message. The UE shall stay in CELL_FACH state and NOT transmit response message on the DCCH. SS waits until uplink data transmission is completed and sends a UTRAN MOBILITY INFORMATION message. The UE shall reply with UTRAN MOBILITY INFORMATION CONFIRM message. Since the IE “RRC State Indicator” is set to “CELL_PCH” in the downlink message, the UE shall move to CELL_PCH state. SS then prompts the test operator to transmit packet data. The UE shall send CELL UPDATE message and specifies the cause to be “uplink data transmission”. SS replies with a CELL UPDATE CONFIRM message which assigns a new C-RNTI to the UE. After receiving this message, the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message and remains in CELL_FACH state. SS again waits for the transmission of user packet data to complete and then sends UTRAN MOBILITY INFORMATION message on the downlink DCCH. The IE “RRC State Indicator” is set to “CELL_PCH”. The UE shall move to CELL_PCH state and acknowledges that it starts using the new RNTI identity provided. Finally, SS prompts the test operator to transmit packet data. The UE shall send CELL UPDATE message once more. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message which includes the ”Physical channel information elements” and set IE “RRC State Indicator” to “CELL_FACH”. Then the UE shall enter to the CELL_FACH state after sending PHYSICAL CHANNEL RECONFIGURATION COMPLETE message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_PCH state. SS prompts the test operator to initiate a packet data call. |
| 2 | ( | CELL UPDATE | The UE moves to CELL FACH state and transmit this message which is set to “uplink data transmission” in IE “Cell update cause”. |
| 3 | ( | CELL UPDATE CONFIRM | Use default message content. |
| 4 |  |  |  |
| 5 |  |  | SS waits until transmission of uplink data has been completed. |
| 6 | ( | UTRAN MOBILITY INFORMATION | IE “RRC State Indicator” set to “DRX with cell update” |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to CELL_PCH state. |
| 8 |  |  | SS prompts test operator to initiate a packet data transmission. |
| 9 | ( | CELL UPDATE | Should be same as in step 2 |
| 10 | ( | CELL UPDATE CONFIRM | Including the IE “new C-RNTI”. |
| 11 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 12 |  |  | SS waits until transmission of uplink data has been completed. |
| 13 | ( | UTRAN MOBILITY INFORMATION | IE “RRC State Indicator” set to “DRX with cell update” |
| 14 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to CELL_PCH state. |
| 15 |  |  | SS prompts test operator to initiate a packet data transmission. |
| 16 | ( | CELL UPDATE | Should be same as in step 2 |
| 17 | ( | CELL UPDATE CONFIRM | Including the ”Physical channel information elements”. |
| 18 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

CELL UPDATE (Step 2, 9 and 16)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 1111’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘uplink data transmission’ |

CELL UPDATE CONFIRM (Step 3)

Use the same message sub-type found in Annex A.

CELL UPDATE CONFIRM (Step 10)

Use the same message sub-type found in step 3, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | ‘0000 0000 1111 0000’ |

CELL UPDATE CONFIRM (Step 17)

Use the same message sub-type found in step 3, with the following exceptions:

| Maximum allowed uplink TX power | 3 dB below the follow value: Minimum of {33 dBm, maximum uplink power allowed under the UE power class } |
| --- | --- |

UTRAN MOBILITY INFORMATION (Step 6)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | ‘0000 0000 0000 1111’ |
| RRC State Indicator | CELL_PCH |

UTRAN MOBILITY INFORMATION (Step 13)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | ‘0000 0000 1111 1111’ |
| RRC State Indicator | CELL_PCH |

PHYSICAL CHANNEL RECONFIGURATION COMPLETE (Step 18)

Only the message type IE in this message will be checked.

8.3.1.6.5	Test requirement

After step 1 the UE shall move to CELL_FACH state, initiate a cell update procedure for the UL data transmission, and transmit a CELL UPDATE message which is set to “uplink data transmission” in IE “Cell update cause”.

After step 8 the UE shall initiate cell update procedure and transmit CELL UPDATE message on the uplink CCCH. The IE “Cell update cause” shall be set to “uplink data transmission”.

After step 10 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

After step 15 the UE shall initiate cell update procedure and transmit CELL UPDATE message on the uplink CCCH. The IE “Cell update cause” shall be set to “uplink data transmission”.

After step 17 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

#### 8.3.1.7	Cell Update: paging response in URA_PCH

8.3.1.7.1	Definition

8.3.1.7.2	Conformance requirement

This procedure is to update UTRAN with the current cell of the UE after it receives a PAGING TYPE 1 message addressed to itself while it is in URA_PCH state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.7.3	Test purpose

To confirm that the UE executes a cell update procedure when it receives a PAGING TYPE 1 message while operating in URA_PCH state. To confirm that the UE responds with an appropriate uplink message after receiving a CELL UPDATE CONFIRM message during cell updating procedure triggered by paging.

8.3.1.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is brought to URA_PCH state. SS transmits a PAGING TYPE 1 message to page for the UE, setting IE “paging originator” to “UTRAN Originator”. The UE shall move to CELL_FACH state and transmits a CELL UPDATE message to the SS on the uplink CCCH. This message shall set IE “Cell update cause” to “Paging Response”. After the SS receives this message, it transmits the default CELL UPDATE CONFIRM message. The UE shall stay in CELL_FACH state and not transmit response message. SS then sends a UTRAN MOBILITY INFORMATION message. In this message, the IE “RRC State Indicator” is set to “URA_PCH”. As a result, the UE shall reply with UTRAN MOBILITY INFORMATION and move to URA_PCH state. Next SS modifies the contents of SYSTEM INFORMATION BLOCK TYPE 5 and 6 messages. See specific message contents for further details. SS pages the UE again using PAGING TYPE 1 message.  The UE shall send CELL UPDATE message once more.  SS transmits a CELL UPDATE CONFIRM message which includes the IEs ”new C-RNTI”, ”new U-RNTI” on the downlink DCCH.    The UE shall send UTRAN MOBILITY INFORMATION CONFIRM message.  In the next sequence, SS transmits UTRAN MOBILITY INFORMATION message and assigns a new C-RNTI identity to the UE. In this message, the IE ”RRC State Indicator” is set to “URA_PCH”. The UE shall reply with UTRAN MOBILITY INFORMATION CONFIRM message and move to URA_PCH state.  SS then pages the UE once more using PAGING TYPE 1 message.  The UE shall initial the cell update procedure by dispatching a CELL UPDATE message on the uplink CCCH.  SS replies with a CELL UPDATE CONFIRM message which includes “Physical channel information elements”.  The UE shall respond with a PHYSICAL CHANNEL RECONFIGURATION COMPLETE. SS sends another UTRAN MOBILITY INFORMATION message on the downlink DCCH, with the IE”RRC State Indicator” set to “URA_PCH”.  The UE shall move to URA_PCH state and acknowledges that it starts using the new C-RNTI identity provided by transmitting UTRAN MOBILITY INFORMATION CONFIRM message. SS pages the UE again using the U-RNTI identity. The UE shall send CELL UPDATE message and specify the cause to be “Paging Response”. SS replies with CELL UPDATE CONFIRM message which includes “Transport channel information elements”. After receiving this message, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message and remains in CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is first brought to URA_PCH state. |
| 2 | ( | PAGING TYPE 1 | SS transmits a PAGING TYPE 1 message to the UE which includes the UE’s assigned U-RNTI with the IE “paging originator” set to “UTRAN originator”. |
| 3 | ( | CELL UPDATE | The UE shall move to CELL_FACH state and transmits this message with the IE “Cell update cause” set to “paging response”. |
| 4 | ( | CELL UPDATE CONFIRM | Use the default message from TS 34.108 Clause 8. |
| 5 |  |  | The UE shall not transmits response message. |
| 6 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI and set IE “RRC State Indicator” to “URA_PCH”. |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to URA_PCH state. |
| 8 |  |  | SS modifies MASTER INFORMATION BLOCK, SYSTEM INFORMATION BLOCK TYPE 5 and 6 messages. The TFS of the PRACH is changed. |
| 9 | ( | PAGING TYPE 1 | SS pages the UE again |
| 10 | ( | CELL UPDATE | IE “Cell update cause” shall be set to “paging response”. |
| 11 | ( | CELL UPDATE CONFIRM | Includes IE “new C-RNTI” and “new U-RNTI”. |
| 12 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 13 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI and set IE “RRC State Indicator” to “URA_PCH”. |
| 14 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to URA_PCH state. |
| 15 | ( | PAGING TYPE 1 | SS pages the UE again |
| 16 | ( | CELL UPDATE | IE “Cell update cause” shall be set to “paging response”. |
| 17 | ( | CELL UPDATE CONFIRM | ”Physical channel information elements” is included in this message |
| 18 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE |  |
| 19 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI and set IE “RRC State Indicator” to “URA_PCH”. |
| 20 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to URA_PCH state. |
| 21 | ( | PAGING TYPE 1 | UE paged using U-RNTI identity. |
| 22 | ( | CELL UPDATE | IE “Cell Update Cause” shall be set to “Paging Response” |
| 23 | ( | CELL UPDATE CONFIRM | “Transport channel information elements” is included. |
| 24 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE | This message shall be sent on the PRACH resource allocated in step 23. |

Specific Message Contents

PAGING TYPE 1 (Step 2 and 9)

| Information Element | Value/remark |
| --- | --- |
| CHOICE Paging Originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN Originator ‘0000 0000 0001’ ‘0000 0000 0000 0000 0001’ |

PAGING TYPE 1 (Step 15 and 21)

| Information Element | Value/remark |
| --- | --- |
| CHOICE Paging Originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN Originator ‘0000 0000 0001’ Check to see if set to value provided in step 11 |

CELL UPDATE (Step 3  and 10)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ |

CELL UPDATE (Step 16 and 22)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to value provided in step 11 Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ |

CELL UPDATE CONFIRM (Step 4)

Use the same message sub-type found in Annex A.

CELL UPDATE CONFIRM (Step 11)

Use the same message sub-type found in step 4, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI New C-RNTI | ‘0000 0000 0000 0001’ An arbitrary 20-bits string which is different from original S-RNTI An arbitrary 16-bits string which is different from original C-RNTI. |

PHYSICAL CHANNEL RECONFIGURATION (Step 18)

Only the message type for this message is checked.

MASTER INFORMATION BLOCK (Step 8)

Use the same message sub-type found in Clause 6.1 of TS 34.108, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| MIB Tag | 2 |

SYSTEM INFORMATION BLOCK TYPE 5 and TYPE 6 (Step 8)

Use the same message sub-type found in Clause 6.1 of TS 34.108, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| PRACH system information - RACH TFS - CHOICE Transport channel type - Dynamic Transport Format Information - Number of Transport blocks - RLC Size - Semi-static Transport Format - Transmission time interval - Type of channel coding - Coding Rate - Rate matching attribute - CRC Size | Common transport channels 1 296 bits 80 msec No coding No Present 1 16 bits |

UTRAN MOBILITY INFORMATION (Step 6, 13 and 19)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | Selects any arbitrary unused 16-bits string |
| RRC State Indicator | URA_PCH |

TRANSPORT CHANNEL RECONFIGURATION COMPLETE(Step 24)

Only the message type for this message is checked.

CELL UPDATE CONFIRM (Step 17)

Use the same message sub-type found in step 11, with the following exceptions:

| Maximum allowed uplink TX power | 3 dB below the follow value: Minimum of {33 dBm, maximum uplink power allowed under the UE power class } |
| --- | --- |

CELL UPDATE CONFIRM (Step 23)

Use the same message sub-type found in step 17, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Added or Reconfigured UL TrCH information -Transport channel identity -TFS -Dynamic Transport format information -Number of Transport blocks -RLC size -Semi-static Transport Format information -Transmission time interval -Type of channel coding -Coding Rate -Rate matching attribute -CRC size | 1 ( This IE is repeated for TFI number) Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set |

8.3.1.7.5	Test requirement

After step 2 the UE shall answer to the paging message then moves to CELL_FACH state and transmit a CELL UPDATE message. This message shall set the value “paging response” into IE “Cell update cause”.

After step 9 the UE shall respond the paging by replying with a CELL UPDATE message. IE “Cell Update Cause” shall be set to “Paging Response” in this message.

After step 11 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

After step 15 the UE shall answer the PAGING TYPE 1 message by sending a CELL UPDATE message. The IE “Cell Update Cause” shall have a value equals to “Paging Response”.

After step 17 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

After step 21 the UE shall respond to the PAGING TYPE 1 message addressed to itself and initiate a cell update procedure. It shall transmit CELL UPDATE message with the IE “Cell Update Cause” set to “Paging Response” in this message.

After step 23 the UE shall send TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

#### 8.3.1.8	Cell Update: paging response in CELL_PCH

8.3.1.8.1	Definition

8.3.1.8.2	Conformance requirement

This procedure is to update UTRAN with the current cell when the UE receives a PAGING TYPE 1 message addressed to it while in CELL_PCH state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.8.3	Test purpose

To confirm that the UE executes a cell update procedure when the UE receives a PAGING TYPE 1 message while in CELL_PCH state. To confirm that the UE sends an appropriate uplink message after receiving a CELL UPDATE CONFIRM message during cell updating procedure due to paging.

8.3.1.8.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH (state 6-12) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the CELL_PCH state. The SS transmits a PAGING TYPE 1 message to the UE on the downlink PCCH which includes the connected mode identity of the UE and set value “UTRAN originator” into IE “paging originator”. The UE shall respond to this message. Then the UE shall move to CELL_FACH state and transmits a CELL UPDATE message to the SS on the uplink CCCH which and set the value “Paging Response” into IE “Cell update cause”. After the SS receives this message, it transmits the default CELL UPDATE CONFIRM message. The UE shall stay in CELL_FACH state and not transmit response message on the DCCH. Next SS modifies the contents of SYSTEM INFORMATION BLOCK TYPE 5 and 6 messages. See specific message contents for further details. SS then sends a UTRAN MOBILITY INFORMATION message on the downlink DCCH, with the IE “RRC State Indicator” set to “CELL_PCH”. The UE acknowledges that it starts using the new C-RNTI identity provided by transmitting UTRAN MOBILITY INFORMATION CONFIRM message and moves to CELL_PCH state. SS pages the UE again using PAGING TYPE 1 message. The UE shall send CELL UPDATE message once more. SS replies with a CELL UPDATE CONFIRM message which includes the IE “new C-RNTI” to the UE on the downlink DCCH. Then the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH and enters the CELL_FACH state. In the final sequence, SS transmits UTRAN MOBILITY INFORMATION message and assigns a new C-RNTI identity to the UE. The UE shall reply with UTRAN MOBILITY INFORMATION CONFIRM message and move to CELL_PCH state. SS then pages the UE once more using PAGING TYPE 1 message. The UE shall initial the cell update procedure by dispatching a CELL UPDATE message on the uplink CCCH. SS replies with a CELL UPDATE CONFIRM message which includes the “Physical channel information elements”. The UE shall respond with a PHYSICAL CHANNEL RECONFIGURATION COMPLETE, sent on the DCCH. Next, SS sends UTRAN MOBILITY INFORMATION message to UE with the “RRC State Indicator” IE set to “CELL_PCH”. The UE shall respond by transmitting UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH and then move to CELL_PCH state. SS pages the UE again using connected mode identity at the paging occasions assigned to the UE. The UE shall answer to the page and sent CELL UPDATE message on the uplink CCCH. SS responds to the reception of this message by transmitting a CELL UPDATE CONFIRM message on the downlink DCCH. In this message, ”Transport channel information elements”is assigned. The UE shall acknowledge the receipt of this message and send TRANSPORT CHANNEL RECONFIGURATION COMPLETE on the uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_PCH state. |
| 2 | ( | PAGING TYPE 1 | The SS transmits a PAGING TYPE 1 message addressing the UE with its connected mode identity and set IE “paging originator” to “UTRAN originator”. |
| 3 | ( | CELL UPDATE | The UE shall move to CELL_FACH state and transmits this message with the IE “Cell update cause” set to “paging response”. |
| 4 | ( | CELL UPDATE CONFIRM | Use the default message from TS 34.108 Clause 8. |
| 5 |  |  | The UE shall transmits response message. |
| 6 |  |  | SS modifies the contents of MASTER INFORMATION BLOCK, SYSTEM INFORMATION BLOCK TYPE 5 and 6 messages. |
| 7 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI and set IE “RRC State Indicator” to “CELL_PCH” |
| 8 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to CELL_PCH state |
| 9 | ( | PAGING TYPE 1 | SS pages the UE again |
| 10 | ( | CELL UPDATE | IE “ Cell update cause” shall be set to “paging response” |
| 11 | ( | CELL UPDATE CONFIRM | Contains the IE “new C-RNTI” |
| 12 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 13 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI and set IE “RRC State Indicator” to “CELL_PCH”. |
| 14 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to CELL_PCH state. |
| 15 | ( | PAGING TYPE 1 | SS pages the UE again |
| 16 | ( | CELL UPDATE | IE “Cell update cause” shall be set to “paging response”. |
| 17 | ( | CELL UPDATE CONFIRM | Including ”Physical channel information elements” in this message. |
| 18 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | To be sent on the new PRACH channel. |
| 19 | ( | UTRAN MOBILITY INFORMATION | Allocates a new C-RNTI and set IE “RRC State Indicator” to “CELL_PCH”. |
| 20 | ( | UTRAN MOBILITY INFORMATION CONFIRM | UE moves to CELL_PCH state. |
| 21 | ( | PAGING TYPE 1 | UE paged using U-RNTI identity. |
| 22 | ( | CELL UPDATE | IE “Cell Update Cause” shall be set to “Paging Response” |
| 23 | ( | CELL UPDATE CONFIRM | ”Transport channel information elements” is included. |
| 24 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

PAGING TYPE 1

| Information Element | Value/remark |
| --- | --- |
| CHOICE Paging Originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN Originator ‘0000 0000 0001’ ‘0000 0000 0000 0000 0001’ |

CELL UPDATE (Step 3, 10 and 16)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ |

CELL UPDATE CONFIRM (Step 4)

Use the same message sub-type found Annex A.

CELL UPDATE CONFIRM (Step 11)

Use the same message sub-type found in step 4, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | An arbitrary 16-bits string which is different from original C-RNTI. |

PHYSICAL CHANNEL RECONFIGURATION COMPLETE (Step 18)

Only the message type for this message is checked.

MASTER INFORMATION BLOCK (Step 6)

Use the same message sub-type found in Clause 6.1 of TS 34.108, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| MIB Tag | 2 |

SYSTEM INFORMATION BLOCK TYPE 5 and TYPE 6 (Step 6)

Use the same message sub-type found in Clause 6.1 of TS34.108, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| PRACH system information - RACH TFS - CHOICE Transport channel type - Dynamic Transport Format Information - Number of Transport blocks - RLC Size - Semi-static Transport Format - Transmission time interval - Type of channel coding - Coding Rate - Rate matching attribute - CRC Size | Common transport channels 1 296 bits 80 msec No coding No Present 1 16 bits |

UTRAN MOBILITY INFORMATION (Step 7 ,13 and 19)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | Selects any arbitrary unused 16-bits string |
| RRC State Indicator | CELL_PCH |

TRANSPORT CHANNEL RECONFIGURATION COMPLETE (Step 24)

Only the message type for this message is checked.

CELL UPDATE CONFIRM (Step 17)

Use the same message sub-type found in step 11, with the following exceptions:

| Maximum allowed uplink TX power | 3 dB below the follow value: Minimum of {33 dBm, maximum uplink power allowed under the UE power class } |
| --- | --- |

CELL UPDATE CONFIRM (Step 23)

Use the same message sub-type found in step 17, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Added or Reconfigured UL TrCH information -Transport channel identity -TFS -Dynamic Transport format information -Number of Transport blocks -RLC size -Semi-static Transport Format information -Transmission time interval -Type of channel coding -Coding Rate -Rate matching attribute -CRC size | 1 ( This IE is repeated for TFI number) Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set Reference to TS34.108 clause 6.10 Parameter Set |

8.3.1.8.5	Test requirement

After step 2 the UE shall answer to the paging message, moves to CELL_FACH state, and then transmits a CELL UPDATE message setting “paging response” into IE “Cell update cause”.

After step 9 the UE shall respond to the paging again by sending CELL UPDATE message, with the IE “Cell update cause” set to “Paging response”.

After step 11 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message to end the cell updating procedure.

After step 15 the UE shall answers the paging message by sending a CELL UPDATE message, with the IE “Cell update cause” set to “Paging response”.

After step 17 the UE shall transmit PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

After step 21 the UE shall respond to the paging and initiate a cell update procedure. It shall transmit CELL UPDATE message with the IE “Cell Update Cause” set to “Paging Response” in this message.

After step 23 the UE shall send TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.

#### 8.3.1.9	Cell Update: re-entering of service area after T305 expiry and being out of service area

8.3.1.9.1		Definition

8.3.1.9.2	Conformance requirement

When a UE detects that it’s out of service area after experiencing a T305 timer expiry, it shall try to search for a suitable cell to camp on. At the same time, it shall start timer T307. If the UE subsequently re-enters the service area of a cell before T307 expires, it shall perform a cell update procedure.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.9.3	Test purpose

To confirm that the UE performs a cell search after experiencing an “out of service area” condition following the expiry of timer T305. To confirm that the UE initiates cell updating procedure if it manages to re-enter the service area.

8.3.1.9.4	Method of test

Initial Condition

System Simulator: 1 cell.

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

The UE is in the CELL_FACH state. SS decreases the transmission power of cell 1 until the cell selection parameter S<0 (decrease transmission power of cell 1’s CPICH by 15 dBm). Following the expiry of periodic cell updating timer T305 according to the system information, the UE shall detect that it is out of service area. Within the time interval equivalent to T307 timer value, the SS restores the transmission power of cell 1. The UE shall find that it is back in service area, and transmits a CELL UPDATE message to the SS on the uplink CCCH. In this message, the IE “Cell update cause” shall be set to “re-entered service area”. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message with the IE “RRC State Indicator” set “CELL_PCH” on the downlink DCCH. The UE shall enter CELL_PCH state. SS decreases the transmission power of cell 1 until the cell selection parameter S<0.  Following the expiry of periodic cell updating timer T305 according to the system information, the UE shall detect that it is out of service area.  Within the time interval equivalent to T307 timer value, the SS restores the transmission power of cell 1.  The UE shall find that it is back in service area, move to CELL_FACH and transmits a CELL UPDATE message to the SS on the uplink CCCH.  In this message, the IE ”Cell update cause” shall be set to “re-entered service area”.  After the SS receives this message, it transmits a CELL UPDATE CONFIRM message on the downlink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_FACH state of cell 1. |
| 2 |  |  | SS decreases the transmission power of cell 1 so that its S value falls below 0. |
| 3 |  |  | The UE shall detect a “out of service” condition upon expiry of timer T305 and it shall search for other cells to camp on. (T307 timer starts) |
| 4 |  |  | SS restores cell 1’s original power level before T307 timer expires. |
| 5 | ( | CELL UPDATE | The value “re-entered service area” should be found in IE “Cell update cause” in this message |
| 6 | ( | CELL UPDATE CONFIRM | ”RRC State Indicator” is set to “CELL_PCH” |
| 7 |  |  | SS decreases the transmission power of cell 1 so that its S value falls below 0and wait until T305 has expired. |
| 8 |  |  | SS restores cell 1’s original power level before T307 timer expires. |
| 9 | ( | CELL UPDATE | UE shall move to CELL_FACH. It shall transmit this message with cause set to “re-entered service area” |
| 10 | ( | CELL UPDATE CONFIRM |  |

Specific Message Contents

CELL UPDATE (Step 5 and 9)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 1111’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘re-entered service area’ |

CELL UPDATE CONFIRM (Step 6 and 10)

Use the same message sub-type found in Annex A, with the following exception.

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | CELL_PCH |

8.3.1.9.5	Test requirement

After step 4 the UE shall transmit a CELL UPDATE message in which the IE “Cell update cause” is set to the value “re-entered service area”.

After step 8 the UE shall move to CELL_FACH and then transmit a CELL UPDATE message, with the IE “Cell Update Cause” set to “re-entered service area”.

#### 8.3.1.10 	Cell Update: expiry of T307 after T305 expiry and being out of service area

8.3.1.10.1		Definition

8.3.1.10.2	Conformance requirement

This procedure is required to cater for the case of a failure to update UTRAN with the current cell, after the expiry of T307. In this case, the UE shall return to idle mode and perform cell reselection if possible.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.10.3	Test purpose

To confirm that the UE moves to idle mode after the expiry of T307, indicating that it is out of service area when attempting to perform a periodic cell updating procedure.

8.3.1.10.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH (state 6-12) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in CELL_PCH state at the start of the test. Before the expiry of periodic cell updating timer T305, SS starts to decrease the downlink transmission power such that the UE discovers that the cell is no longer suitable for camping and this results in a “out of service area” condition. The SS continues to listen to the uplink channel to detect possible attempts to perform a cell updating procedure. The UE shall not send CELL UPDATE message on the uplink DCCH, instead it triggers timer T307. After the expiry of timer T307 the UE shall enter idle state. This is confirmed by the SS, when it sends a PAGING TYPE 1 message to the UE using its U-RNTI identity, and the UE does not respond to the page. SS then attempts to page for the UE again, this time using PAGING TYPE 2 message sent on downlink DCCH. Likewise, the UE shall not respond to this page.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_PCH state. |
| 2 |  |  | SS starts to decrease the transmission power until the cell is no longer suitable for camping. The UE shall detect that it is out of service area and refrains from transmitting CELL UPDATE message due to periodic cell updating. |
| 3 |  |  | The UE detects the expiry of timer T305 and it searches for other cells to camp on. After the expiry of timer T307, the UE shall enter idle mode. |
| 4 | ( | PAGING TYPE 1 | SS pages the UE at its assigned paging occasion using the allocated U-RNTI value. The UE shall not respond to this page as it has already entered the idle mode. |
| 5 | ( | PAGING TYPE 2 | SS pages the UE on the downlink DCCH. The UE shall not respond to this page. |

Specific Message Contents

PAGING TYPE 1 (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Page record list - Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN Originator Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 1111’ |

PAGING TYPE 2 (Step 5)

| Information Element | Value/remark |
| --- | --- |
| Paging cause CN domain identity Paging Record Type Identifier | Set to a cause corresponding to one radio access bearer services supported by the UE. CS-Domain IMSI |

8.3.1.10.5	Test requirement

After step 4 the UE shall remain in the idle mode and not respond to the paging message sent on PCCH.

After step 5 the UE shall remain in the idle mode and not respond to the paging message addressed to it on the DCCH.

#### 8.3.1.11 	Cell Update: Success after T302 time-out

8.3.1.11.1		Definition

8.3.1.11.2	Conformance requirement

The UE transmits a CELL UPDATE message to the UTRAN when it needs to update the UTRAN with the current cell of the UE. When the UE does not receive a CELL UPDATE CONFIRM message upon expiry of timer T302, the UE transmits a CELL UPDATE message repeatedly until its internal counter V302 counter is greater than N302.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.11.3	Test purpose

To confirm that the UE repeats the transmission of CELL UPDATE message upon the expiry of timer T302, after failing to receive any response from the SS during T302 timer period.

8.3.1.11.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

At the start of the test, the UE is brought to CELL_FACH state. When the UE detects the expiry of periodic cell updating timer T305 according to the system information, the UE transmits a CELL UPDATE message to the SS on the uplink CCCH. The IE “Cell update cause” in this message shall be set to “periodical cell update”. SS ignores this message, and the UE shall then re-transmit a CELL UPDATE message after the expiry of timer T302. When the SS has received (N302+1) such messages, it transmits a CELL UPDATE CONFIRM message with new values for “C-RNTI” to the UE. Finally, the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE starts from CELL_FACH state. SS initializes its internal counter K to 0 and wait until the expiry of T302 timer. |
| 2 | ( | CELL UPDATE | The value “periodical cell update” shall be set in IE “Cell update cause” after the expiry of timer T305. |
| 3 |  |  | If K is equal to N302+2 then proceeds to step 5. |
| 4 |  |  | SS increments counter K, transmits no response to the UE and waits for an additional period equals to the value of timer T302. The next step is step 2. |
| 5 | ( | CELL UPDATE CONFIRM | The message includes IEs ”new C-RNTI”. The IE “RRC State Indicator” is set to “CELL_FACH”. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |

Specific Message Contents

CELL UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ |

CELL UPDATE CONFIRM (Step 5)

Use the same message sub-type found in Annex A, with the following exception:

| Information Element | Value/remark |
| --- | --- |
| New C-RNTI | Set to an arbitrary string different from ‘0000 0000 0000 0001’ |

8.3.1.11.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305 then transmit a CELL UPDATE message on the uplink CCCH, setting “periodical cell update” into IE “Cell update cause”.

After step 2 the UE shall re-transmits a CELL UPDATE message after the expiry of timer T302. A total of (N302+2) transmissions shall be detected in SS.

After step 5 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH and stays at CELL_FACH state.

#### 8.3.1.12 	Cell Update: Failure (After Maximum Re-transmissions)

8.3.1.12.1		Definition

8.3.1.12.2	Conformance requirement

The UE transmits a CELL UPDATE message to the UTRAN when it needs to update UTRAN with information on the current cell of the UE. If the UE fails to receive a CELL UPDATE CONFIRM message, it re-transmits a CELL UPDATE message repeatedly upon the expiry of timer T302 until the value of V302 counter is greater than N302. If V302 is greater than N302, the UE stop the re-transmission and enters idle state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.12.3	Test purpose

To confirm that the UE repeats the cell update procedure at the expiry of timer T302 and moves to idle state when its internal counter V302 is greater than N302.

8.3.1.12.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

The UE is initially in CELL_FACH state. When the UE detects the expiry of periodic cell updating timer T305, the UE transmits a CELL UPDATE message to the SS on the uplink CCCH to perform a periodic cell updating procedure. The SS ignores this message, and the UE shall attempt to re-transmit a CELL UPDATE message up to a maximum of (N302+1) times after the expiry of timer T302. After (N302+1) attempts of retransmission, the UE shall return to idle state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_FACH state. SS sets its internal counter K=0 and waits for a period equals to timer value T302. If CELL UPDATE message is received upon timer expiry, proceeds to step 2. Else goes to step 4. |
| 2 | ( | CELL UPDATE | The value “periodical cell update” should be set in IE “Cell update cause” and this message should be sent for each expiry of timer T302. |
| 3 |  |  | SS transmits no response to the UE and increments counter K. SS waits for an additional period equals to T302 timer. |
| 4 |  |  | SS waits for an additional period equals to T302 timer. If CELL UPDATE message is received, proceed to step 2. Otherwise, terminates the test. If K is not equal to N302+2, the test should be considered as a failure. |

Specific Message Contents

CELL UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ |

8.3.1.12.5	Test requirement

After step 1 the UE shall transmit a CELL UPDATE message on the uplink CCCH and set value “periodical cell update” into IE “Cell update cause”.

After step 4 the counter K in SS shall be equal to N302+2.

#### 8.3.1.13	Cell Update: Reception of Invalid CELL UPDATE CONFIRM Message

8.3.1.13.1		Definition

8.3.1.13.2	Conformance Requirement

If the UE encounters an invalid CELL UPDATE CONFIRM message while executing a cell update procedure, it shall check the current value of its internal counter V302. If V302 is not greater than N302, the UE shall set contexts pertaining to protocol error, re-transmits CELL UPDATE message on uplink CCCH, restart T302 timer and increments V302. It shall use the same “Cell Update Cause” as before receiving the invalid downlink message. On the other hand, if V302 is greater than N302, the UE shall abandon cell update procedure and enters idle mode.

8.3.1.13.3	Test Purpose

To confirm that the UE retransmits CELL UPDATE message when it receives an erroneous CELL UPDATE CONFIRM message, if the number of retransmissions is not the maximum allowed value. To confirm that the UE returns to idle mode after sending maximum allowed number of CELL UPDATE messages without receiving a valid CELL UPDATE CONFIRM message.

8.3.1.13.4	Method of Test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH (state 6-12) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is brought to CELL_PCH state at the beginning of the test. SS pages the UE by sending PAGING TYPE 1 message using the U-RNTI identity assigned during RRC connection establishment procedure. The UE shall transmit CELL UPDATE message on the uplink CCCH. Upon receiving such a message, the SS replies with a CELL UPDATE CONFIRM message containing a protocol error in IE “RRC transaction identifier”. The UE shall detect the protocol error and re-transmit CELL UPDATE message up to a maximum of N302+1 times. The time interval between the transmissions shall be approximately equal to T302. SS verifies that it receives a total of (N302+2) identical CELL UPDATE messages. The UE shall return to idle mode after all uplink transmissions have finished. SS verifies this by paging the UE using the U-RNTI identity. The UE shall not respond to this page.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PAGING TYPE 1 | The UE is in the CELL_PCH state. SS sets its internal counter K=0. SS pages for the UE using the allocated connected mode identity (U-RNTI). |
| 2 | ( | CELL UPDATE | If CELL UPDATE message is received, check that the value “paging response” is set in IE “Cell update cause”. Else goes to step 6. |
| 3 | ( | CELL UPDATE CONFIRM | SS transmits an invalid message. SS increments K. |
| 4 | ( | CELL UPDATE | SS waits for T302 timer to expire. The UE shall send CELL UPDATE message. |
| 5 |  |  | If a CELL UPDATE message is received in step 4, SS increments K and returns to step 3. Else, SS proceeds to step 6. |
| 6 |  |  | SS verifies that K = (N302+2) and proceeds to the next step. Else, the test fails. |
| 7 | ( | PAGING TYPE 1 | SS pages the UE. |
| 8 |  |  | UE shall not respond. |

Specific Message Content

CELL UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ |

CELL UPDATE CONFIRM (Step 3)

Use the same message sub-type found in Annex A, with the following exception:

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier | Invalid values. |

CELL UPDATE (Step 4)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause Failure cause -Protocol error information | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ Check to see if it is set to ‘protocol error’ Check to see if it is set to ‘Information element value not comprehended’ |

PAGING TYPE 1 (Step 1 and 7)

| Information Element | Value/remark |
| --- | --- |
| Page record list - Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN Originator ‘0000 0000 0001’ ‘0000 0000 0000 0000 0001’ |

8.3.1.13.5	Test Requirement

After step 3 the UE shall continue to transmit CELL UPDATE message for N302+1 times.

At step 6 the counter K should be equal to (N302+2).

After step 7 the UE shall return to idle mode and not respond the PAGING TYPE 1 message sent by the SS.

| 8.3.1.14 |  |  |  |
| --- | --- | --- | --- |

Void

#### 8.3.1.15	Cell Update: Acknowledged Mode RLC Reset

8.3.1.15.1	Definition

8.3.1.15.2		Conformance Requirement

In CELL_FACH, the UE shall ensure that all AM RLC entities (both signalling and u-plane links) are operational. In the event that an unrecoverable error has occurred, the UE shall trigger cell update procedure to report this event. The UE shall send CELL UPDATE message on the uplink CCCH and set the appropriate AM_RLC error indicator IE(s) to TRUE. After receiving the CELL UPDATE CONFIRM message, the UE shall reset the affected AM RLC entities and then resume transmission and reception activities.

8.3.1.15.3	Test Purpose

To confirm that the UE reports the occurrence of an unrecoverable error in a C-plane AM RLC entity by initiating cell update procedure. To confirm that the UE is able to resume normal C-plane data transmission and reception after the completion of cell update procedure.

8.3.1.15.4	Method of Test

Initial Condition

System Simulator: 1 cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

The UE is initially in CELL_FACH state. SS sends RADIO BEARER SETUP message on the DCCH using AM mode to establish a DTCH logical channel for u-plane packet data transfer. The UE shall reply with a RADIO BEARER SETUP COMPLETE message, sent using AM RLC on the DCCH. Then it activates the associated DTCH logical channel for user data transmission and reception. SS does not acknowledge the RADIO BEARER SETUP COMPLETE message. The UE shall continue to transmit the AM PDU carrying RADIO BEARER COMPLETE message until the maximum re-transmission count is reached. Thereafter, the UE shall start sending RESET PDUs to request that the AM RLC entity for RRC signalling be re-initialized. SS ignores the requests and wait for a duration equivalent to (MAX_RST+1) times expiry of Timer_RST. This figure is specified in IE “RLC info” of RADIO BEARER SETUP message in step 6. At this point, the UE shall initiate a cell update procedure by transmitting CELL UPDATE message on the uplink CCCH. The CELL UPDATE message shall specify the value “TRUE” in IE “AM_RLC error indicator (for C-plane)”. SS replies with CELL UPDATE CONFIRM message using the default message content. SS then attempts to perform a local authentication by transmitting a COUNTER CHECK message using AM RLC on DCCH. The UE shall respond by sending a COUNTER CHECK RESPONSE message on the uplink DCCH, verifying that the AM RLC entity for RRC signalling was successfully reset.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is initially in CELL_FACH state. |
| 2 | ( | RADIO BEARER SETUP | Establishes a DTCH logical channel operating in AM mode. |
| 3 | ( | RADIO BEARER SETUP COMPLETE | UE shall stay in CELL_FACH state. SS does not acknowledge this AM PDU. The UE shall re-transmit this AM PDU until the maximum number has been reached. |
| 4 |  |  | UE shall start to transmit RESET PDU using AM RLC on the DCCH. SS does not respond to any PDU frames originating from the UE, and it waits for a period equivalent to (MAX_RST+1) times expiry of Timer_RST. This figure is specified in IE “RLC info” of RADIO BEARER SETUP message in step 6. |
| 5 | ( | CELL UPDATE | UE shall send this message on CCCH. IE “AM_RLC Error Indication (for C-plane)” shall be set to ‘TRUE’ |
| 6 | ( | CELL UPDATE CONFIRM | “RRC State Indicator” set to “CELL_FACH”. UE shall transit to CELL_FACH state. |
| 7 | ( | COUNTER CHECK | SS requests for a local authentication of the amount of data sent/received during the lifetime of the RRC connection. |
| 8 | ( | COUNTER CHECK RESPONSE | This message shall be transmitted using AM RLC for RRC signalling on the uplink DCCH. |

Specific Message Contents

RADIO BEARER SETUP (Step 2)

Use the same message sub-type entitled “Packet to CELL_FACH from CELL_FACH in PS” found in Annex A.

RADIO BEARER SETUP COMPLETE (Step 3)

Only the message type IE is checked for this message.

CELL UPDATE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI AM_RLC error indicator (for U-plane) START List | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘TRUE’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE |

CELL UPDATE CONFIRM (Step 6)

Use the same message sub-type found in Annex A.

COUNTER CHECK (Step 7)

| Information Element | Values/Remarks |
| --- | --- |
| Integrity check info RB COUNT-C MSB Information - RB Identity - COUNT-C-MSB-uplink - COUNT-C-MSB-downlink | Not present 5 Set to an arbitrary integer equals to the 25 MSBs from COUNT-C for RB#5 Set to an arbitrary integer equals to the 25 MSBs from COUNT-C for RB#5 |

COUNTER CHECK RESPONSE (Step 8)

| Information Element | Values/Remarks |
| --- | --- |
| Integrity check info RB COUNT-C Information - RB Identity - COUNT-C-uplink - COUNT-C-downlink | Not checked Not checked |

8.3.1.15.5	Test Requirement

After step 4 the UE shall transmit a CELL UPDATE message on the uplink CCCH to report the occurrence of an unrecoverable error in AM RLC entity for C-plane data.

After step 7 the UE shall send a COUNTER CHECK RESPONSE message on the uplink DCCH. This message shall be sent using the AM RLC entity for RRC signalling.

#### 8.3.1.16	Cell Update: cell reselection in CELL_FACH

8.3.1.16.1	Definition

8.3.1.16.2	Conformance requirement

This procedure is used to update UTRAN with the current cell of the UE after it has perform a cell reselection in CELL_FACH state. UE shall receive acknowledgement from UTRAN on downlink CCCH.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.16.3	Test purpose

To confirm that the UE executes a cell update procedure after the successful reselection of another UTRA cell. To confirm that the UE send the correct uplink respond message when executing cell update procedure due to cell reselection. To confirm cell update procedure completes after UE receives CELL UPDATE CONFIRM on downlink CCCH from UTRAN.

8.3.1.16.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, with the downlink transmission power shown in column marked “T0” in Table 8.3.1.1-1, while cell 2 is inactive

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE, ciphering in both UL and DL are disabled during RRC connection establishment.

Test Procedure

The UE is in the CELL_FACH state, camping onto cell 1. SS configures its downlink transmission power settings according to columns “T1” in Table 8.3.1.1-1. The UE shall find cell 2 to be more suitable for service and hence perform a cell reselection. After the completion of cell reselection, the UE shall transmits a CELL UPDATE message to the SS on the uplink CCCH of cell 2 and set IE “ Cell update cause” to “Cell Reselection”. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message, which includes the IE “RRC State Indicator” set to “CELL_PCH”, IE “U-RNTI” and an IE “New U-RNTI” to the UE on the downlink CCCH. UE shall response with UTRAN MOBILITY INFORMATION CONFIRM message.. UE shall move to CELL_PCH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_FACH state in cell 1 |
| 2 | ( | BCCH | SS applies the downlink transmission power settings, according to the values in columns “T1” of Table 8.3.1.1-1. The UE shall find that the cell 2 is better for service and perform a reselection. SS waits for the maximum duration required for the UE to camp to cell 2. |
| 3 | ( | CELL UPDATE | Value “cell reselection” should be indicated in IE “ Cell update cause” |
| 4 | ( | CELL UPDATE CONFIRM | IE “RRC State Indicator” is set to “CELL_PCH”. IE “U-RNTI” and IE “new U-RNTI” are also included. This message is sent without ciphering on downlink CCCH. |
| 5 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |

Specific Message Contents

CELL UPDATE (Steps 3)

Use the same message sub-type found in Clause 9 of TS34.108.

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘Cell Re-selection’ |

CELL UPDATE CONFIRM (Step 4)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI RRC State Indicator New U-RNTI - SRNC Identity - S-RNTI | ‘0000 0000 0001’ ‘0000 0000 0000 0000 0001’ CELL_PCH ‘0000 0000 0000 0001’ An arbitrary 20-bits string which is different from original S-RNTI |

8.3.1.16.5	Test requirement

After step 2 the UE shall reselect to cell 2 and then it shall transmit a CELL UPDATE message which, sets the value  “cell reselection” in IE “ Cell update cause”.

After step 4 the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM message.

#### 8.3.1.17 	Cell Update: Failure (UTRAN initiate an RRC connection release procedure on DCCH)

8.3.1.17.1	Definition

8.3.1.17.2	Conformance requirement

The UE transmits a CELL UPDATE message to the UTRAN when it needs to update UTRAN with information on the current cell of the UE. If the UE receives a RRC CONNECTION RELEASE message on DCCH, it shall transmit an RRC CONNECTION RELEASE COMPLETE message using AM RLC on the DCCH to the UTRAN.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.17.3	Test purpose

To confirm that the UE moves to idle state after sending RRC CONNECTION RELEASE COMPLETE message to UTRAN upon the reception of RRC CONNECTION RELEASE message on DCCH.

8.3.1.17.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

The UE is initially in CELL_FACH state. When the UE detects the expiry of periodic cell updating timer T305, the UE transmits a CELL UPDATE message to the SS on the uplink CCCH to perform a periodic cell updating procedure. The SS transmits RRC CONNECTION RELEASE message on downlink DCCH. The UE shall transmit RRC CONNECTION RELEASE COMPLETE message using AM RLC on the DCCH and return to idle mode after release of all current signalling flows and radio access bearers.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | CELL UPDATE | The value “periodical cell update” should be set in IE “ Cell update cause” and this message should be sent upon expiry of timer T302. |
| 2 | ( | RRC CONNECTION RELEASE | SS transmits RRC CONNECTION RELEASE message to the UE. |
| 3 | ( | RRC CONNECTION RELEASE COMPLETE | The UE transmits this message using acknowledged mode. The UE releases L2 signalling link and radio resources then the UE goes to idle mode. |

Specific Message Contents

CELL UPDATE (Step 1)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘Periodic cell updating’ |

RRC CONNECTION RELEASE (Step 2)

Only the message type is checked for this message.

RRC CONNECTION RELEASE COMPLETE (Step 3)

Only the message type is checked for this message.

8.3.1.17.5	Test requirement

After step 1 the UE shall transmit a CELL UPDATE message on the uplink CCCH and set value “periodical cell update” into IE “ Cell update cause”.

After step 2 the UE shall transmit a RRC CONNECTION RELEASE COMPLETE message on the uplink DCCH and return to idle mode.

#### 8.3.1.18 	Cell Update: Radio Link Failure (T314>0, T315=0)

8.3.1.18.1	Definition

8.3.1.18.2 	Conformance requirement

When a UE loses the radio connection due to e.g. radio link failure in CELL_DCH state. UE must release the radio bearer which is associated with T315 if T315 is set to 0. After a successful cell re-selection and subsequent transition to CELL_FACH state, the UE transmits CELL UPDATE message on the uplink CCCH.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.1.18.3 	Test purpose

To confirm that the UE shall indicate to the non-access stratum the release of radio access bearer which is associated with T315 and try to find a new cell after detecting that a radio link failure has occurred.

8.3.1.18.4 	Method of test

Initial Condition

System Simulator:  2 cells（ Cell 1 is active, Cell 2 is inactive）

UE: CS_DCCH_DCH (state 6-5) or PS_DCCH_DCH (state 6.7) in cell 1, depending on the CN domain(s) supported by the UE.

Test Procedure

The UE is brought to CELL_DCH state in a cell 1 after making an successful outgoing call attempt.  After the call has been established, SS begins to broadcast the BCCH in cell 2, and then stops transmitting and receiving in cell 1. The UE shall detect a radio link failure in cell 1 and indicate to the non-access stratum the release of the radio bearer which is associated with T315. Then it shall attempt to re-select to cell 2. After that, it should then enter CELL_FACH state and transmits CELL UPDATE on the uplink CCCH to SS. The SS transmits CELL UPDATE CONFIRM message which includes IE “new C-RNTI”. UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | RADIO BEARER SETUP | T315=0 |
| 2 | ( | RADIO BEARER SETUP COMPLETE |  |
| 3 |  |  | The UE is brought to CELL_DCH state in a cell 1, after making a successful outgoing call. |
| 4 | ( | BCCH | The SS starts transmitting the BCCH in a cell 2 using the same contents (except for cell identity which is set to “0000 0000 0000 0010”) for system information sent on cell 1. SS starts to listen to the uplink CCCH of cell 2. |
| 5 |  |  | The SS stops transmitting and receiving in a cell .1. |
| 6 |  |  | The UE detects the radio link failure which is associated with T315. The UE indicates to the non-access stratum the release of the radio bearer . |
| 7 | ( | CELL UPDATE | The UE should find a new cell 2 and the value “radio link failure” should be set in IE ”Cell update cause”. |
| 8 | ( | CELL UPDATE CONFIRM | Including IE “new U-RNTI” and IE “new C-RNTI” |
| 9 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |

Specific Message Contents

RADIO BEARER SETUP

The contents of RADIO BEARER SETUP message in this test case is identical to those in default contents of layer 3 messages for RRC tests with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RAB information to setup list |  |
| - RAB information to setup |  |
| - RAB info |  |
| - T315 | 0 |

CELL UPDATE (Step 7)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI -SRNC Identity - S-RNTI Cell Update Cause | Check to see if set to value assigned previously in cell 1. Check to see if set to value assigned previously in cell 1. Check to see if set to ‘radio link failure’ |

CELL UPDATE CONFIRM (Step 8)

Use the same message sub-type found in step 4, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI New C-RNTI | ‘0000 0000 0000 0001’ An arbitrary 20-bits string which is different from original S-RNTI An arbitrary 16-bits string which is different from original C-RNTI. |

8.3.1.18.5	Test requirement

After step 5, the UE shall indicate to the non-access stratum the release of the radio bearer which is associated with T315.

After step 6, the UE shall detect the presence of cell 2, perform cell re-selection and transmit CELL UPDATE message.

After step 8, the UE shall transmit UTRAN MOBILITY INFORMATION CONFIRM to SS.

#### 8.3.1.19 	Cell Update: Unrecoverble error in RLC

8.3.1.19.1	Definition

8.3.1.19.2 	Conformance requirement

When a UE loses the radio connection due to e.g. detection of RLC unrecoverble error ( amount of the retransmission of RESET_PDU reaches the value of Max_DAT and receives no ACK ) in CELL_DCH state. After a successful cell re-selection and transition to CELL_FACH state, the UE shall transmit CELL UPDATE message which includes the value “RLC unrecoverable error” in the IE “cell update cause” on the uplink CCCH.

Reference

3GPP TS 25.331  clause 8.3.1

8.3.1.19.3 	Test purpose

To confirm that the UE tries to find a new cell, after detecting that a RLC unrecoverble error has occurred.  The UE shall move to CELL_FACH state and transmit CELL UPDATE message to SS.

8.3.1.19.4 	Method of test

Initial Condition

System Simulator :  2 cells（ Cell 1 is active, with the downlink transmission power shown in column marked “T0” in Table 8.3.1.1-1, while cell 2 is inactive）

UE: CS_DCCH_DCH (state 6-5) or PS_DCCH_DCH (state 6-7) as defined in clause 7.4 of TS 34.108 in cell 1, depending on the CN domain(s) supported by the UE.

Test Procedure

The UE is brought to CELL_DCH state in a cell 1 after a successful outgoing call attempt.  After the call has been established, the SS transmits a PAGING TYPE 2 message on the downlink DCCH. Then the UE transmits an UPLINK DIRECT TRANSFER message on the uplink using AM-RLC for the response and the SS does not transmit a STATUS PDU for the response to AM-RLC PDU and begins to broadcast the BCCH in cell 2. The UE should detect an unrecoverble error in cell 1 and attempts to re-select to cell 2. It should then enter CELL_FACH state and transmits CELL UPDATE message which includes the value “RLC unrecoverable error” in IE ”cell update cause” on the uplink CCCH to SS. The SS transmits CELL UPDATE CONFIRM message which includes “TRUE” in RLC reset indicator( for C-plane) IE and a new TFCS setting according to the new transport channel. After this, UE shall reconfigure the RLC and the new radio connection and transmits TRANSPORT CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_DCH state in a cell 1, after making a successful outgoing call. |
| 2 | ( | PAGING TYPE2 | The SS transmits a PAGING TYPE 2 message to the UE on the downlink DCCH in cell 1. |
| 3 | ( | UPLINK DIRECT TRANSFER | The UE responds to the PAGING TYPE 2 message using AM-RLC but the SS does not transmit a STATUS PDU as an acknowledgement. |
| 4 | ( | BCCH | The SS starts transmitting the BCCH in a cell 2 using the same contents (except for cell identity which is set to “0000 0000 0000 0010”) for system information sent on cell 1. SS starts to listen to the uplink CCCH of cell 2. |
| 5 |  |  | The UE detects an unrecoverble error in the RLC level. |
| 6 | ( | CELL UPDATE | The UE should find a new cell 2 and then transmits this message which includes the value “RLC unrecoverable error” in the IE ”cell update cause”. |
| 7 | ( | CELL UPDATE CONFIRM | Including the new configuration information. |
| 8 | ( | TRANSPORT CHANNEL RECONFIGURATION COMPLETE |  |

Specific Message Contents

Cell 1: SYSTEM INFORMATION TYPE 1

| Information Element | Value/remark |
| --- | --- |
| UE Timers and constants in connected mode T301 T313 T314 T315 N313 | 8 seconds 15 seconds 20 seconds 30 seconds 200 |

CELL UPDATE (Step 6)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI -SRNC Identity - S-RNTI Cell Update Cause | Check to see if set to value assigned previously in cell 1. Check to see if set to value assigned previously in cell 1. Check to see if set to ‘RLC unrecoverable error’ |

8.3.1.19.5	Test requirement

After step 5, the UE shall detect the presence of cell 2 and move to CELL_FACH in cell 2 to transmit CELL UPDATE message to SS.

After step 7, the UE shall transmit TRANSPORT CHANNEL RECONFIGURATION COMPLETE message to SS.

#### 8.3.1.20	Cell Update: Reception of CELL UPDATE CONFIRM Message that causes invalid configuration

8.3.1.20.1		Definition

8.3.1.20.2	Conformance Requirement

If the UE encounters a CELL UPDATE CONFIRM message that set the variable INVALID_CONFIGURATION to TRUE while executing a cell update procedure, it shall check the current value of its internal counter V302. If V302 is not greater than N302, the UE shall set IE “failure cause” to “invalid configuration”, re-transmits CELL UPDATE message on uplink CCCH, restart T302 timer and increments V302. It shall use the same “Cell Update Cause” as before receiving the invalid downlink message. On the other hand, if V302 is greater than N302, the UE shall abandon cell update procedure and enters idle mode.

8.3.1.20.3	Test Purpose

To confirm that the UE retransmits CELL UPDATE message when it receives a CELL UPDATE CONFIRM message that will trigger an invalid configuration in the UE, if the number of retransmissions has not reached the maximum allowed value. To confirm that the UE returns to idle mode after sending maximum allowed number of CELL UPDATE messages without receiving a valid CELL UPDATE CONFIRM message.

8.3.1.20.4	Method of Test

Initial Condition

System Simulator: 1 cell

UE: CELL_PCH (state 6-12) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is brought to CELL_PCH state at the beginning of the test. SS pages the UE by sending PAGING TYPE 1 message using the U-RNTI identity assigned during RRC connection establishment procedure. The UE shall transmit CELL UPDATE message on the uplink CCCH. Upon receiving such a message, the SS replies with a CELL UPDATE CONFIRM message with IE “RRC State Indicator” set to “CELL_DCH”. The UE shall detect its variable “invalid configuration” is set and re-transmit CELL UPDATE message up to a maximum of N302+1 times. SS verifies that it receives a total of (N302+2) identical CELL UPDATE messages. The UE shall return to idle mode after all uplink transmissions have finished. SS verifies this by paging the UE using the U-RNTI identity. The UE shall not respond to this page.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | PAGING TYPE 1 | The UE is in the CELL_PCH state. SS sets its internal counter K=0. SS pages for the UE using the allocated connected mode identity (U-RNTI). |
| 2 | ( | CELL UPDATE | If CELL UPDATE message is received, check that the value “paging response” is set in IE “Cell update cause”. Else goes to step 6. |
| 3 | ( | CELL UPDATE CONFIRM | SS transmits an invalid message. SS increments K. |
| 4 | ( | CELL UPDATE |  |
| 5 |  |  | If a CELL UPDATE message is received in step 4, SS increments K and returns to step 3. Else, SS proceeds to step 6. |
| 6 |  |  | SS verifies that K = (N302+2) and proceeds to the next step. Else, the test fails. |
| 7 | ( | PAGING TYPE 1 | SS pages the UE. |
| 8 |  |  | UE shall not respond. |

Specific Message Content

CELL UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ |

CELL UPDATE CONFIRM (Step 3)

Use the same message sub-type found in Annex A, with the following exception:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator Uplink DPCH info | CELL_DCH Not Present |

CELL UPDATE (Step 4)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause Failure cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ Check to see if it is set to ‘invalid configuration’ |

PAGING TYPE 1 (Step 1 and 7)

| Information Element | Value/remark |
| --- | --- |
| Page record list - Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI | UTRAN Originator ‘0000 0000 0001’ ‘0000 0000 0000 0000 0001’ |

8.3.1.20.5	Test Requirement

After step 3 the UE shall continue to transmit CELL UPDATE message for N302+1 times.

At step 6 the counter K should be equal to (N302+2).

After step 7 the UE shall return to idle mode and not respond the PAGING TYPE 1 message sent by the SS.

### 8.3.2	URA Update

#### 8.3.2.1	URA Update: URA reselection

8.3.2.1.1	Definition

8.3.2.1.2	Conformance requirement

This procedure is to update UTRAN with the current URA of the UE after a URA reselection has occurred in URA_PCH state. It may also be used for supervision of the RRC connection, even if no URA reselection takes place.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.1.3	Test purpose

To confirm that the UE executes an URA update procedure after the successful URA reselection.

8.3.2.1.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active with URA-ID 1 and the downlink transmission power shown in column marked “T0” in Table 8.3.1.1-1, while cell 2 is inactive with URA-ID 2

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108, with URA-ID 1 from the list of URA-ID in cell 1

Test Procedure

The UE is in the URA_PCH state and assigned with only 1 URA identity in cell 1: URA-ID 1. The SS starts to broadcast BCCH in cell 2 with URA-ID 2 and stop transmitting BCCH in cell 1. This is expected to cause the UE to perform a cell reselection to cell 2. When the UE finds that its current URA-ID 1 is not in the new broadcasted list of URA-IDs, it moves to CELL_FACH state and transmits a URA UPDATE message on the uplink CCCH. After the SS receives this message, it transmits URA UPDATE CONFIRM message which includes the IEs “RRC State Indicator” and “URA-ID” to the UE on the downlink DCCH. The “RRC State Indicator” is set to “URA_PCH”. Finally, the UE returns to URA_PCH state in cell 2 without sending a uplink response message.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is updated with only 1 URA identity carried currently by cell 1. The starting state of the UE is URA_PCH |
| 2 | ( | BCCH | SS starts sending BCCH for cell 2 with URA-ID 2 and ceases to transmit BCCH with URA-ID 1 carried by cell 1. |
| 3 | ( | URA UPDATE | The UE shall perform a cell reselection first and when it finds that its current URA-ID 1 is not in the new broadcasted list of URA-IDs, it shall then transmit this message and set value “URA reselection” into IE “URA update cause”. |
| 4 | ( | URA UPDATE CONFIRM | Message comprises IE “RRC State Indicator” set “URA_PCH”, and also IE “URA Identity” equals to “URA-ID 2”. |

Specific Message Contents

URA UPDATE (Step 3)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI URA Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘URA reselection’ |

URA UPDATE CONFIRM (Step 4)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |

8.3.2.1.5	Test requirement

After step 2 the UE shall find that URA-ID 2 is not in its maintained list of URA-IDs. After cell reselection, the UE shall move to CELL_FACH state and transmit URA UPDATE message setting value “URA reselection” into IE “URA update cause”.

#### 8.3.2.2 	URA Update: periodical URA update

8.3.2.2.1	Definition

8.3.2.2.2	Conformance requirement

This procedure is to update UTRAN with the current URA of the UE when the UE detects that it is still within the service area after the expiry of periodic URA updating timer T305.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.2.3	Test purpose

To confirm that the UE executes a URA update procedure after the expiry of timer T305. To verify that the UE handles an invalid URA UPDATE CONFIRM message correctly when executing the URA update procedure.

8.3.2.2.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the URA_PCH state. When the UE detects the expiry of timer T305, set according to the value specified in system information, the UE moves to CELL_FACH state and transmits a URA UPDATE message to the SS on the uplink CCCH. The message shall indicate the cause to be “periodic URA update” in IE “URA update cause”. SS replies with an illegal URA UPDATE CONFIRM message sent on downlink CCCH, and check to see if the UE handles this event properly. The UE shall attempt to retransmit the identical URA UPDATE message. After the SS receives the second URA UPDATE message, it transmits a correct URA UPDATE CONFIRM message, which includes the IE “ new U-RNTI”, to the UE on the downlink DCCH. Then the UE shall then transmits an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH. The UE returns to CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the URA_PCH state. SS wait until T305 timer has expired. |
| 2 | ( | URA UPDATE | UE shall transmit this message and set value “periodic URA update” into IE “URA update cause”. |
| 3 | ( | URA UPDATE CONFIRM | SS sends an illegal message. |
| 4 | ( | URA UPDATE | UE shall not return to idle mode immediately, but attempts to re-transmit this message. |
| 5 | ( | URA UPDATE CONFIRM | Including IE “new U-RNTI” |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |

Specific Message Contents

URA UPDATE (Step 2 and 4)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI URA Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘Periodic URA update’ |

URA UPDATE CONFIRM (Step 3)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| U-RNTI | Not Present |

URA UPDATE CONFIRM (Step 5)

Use the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI SRNC Identity S-RNTI | ’0000 0000 0001’ ‘0000 0000 0000 0000 1111’ |

UTRAN MOBILITY INFORMATION CONFIRM (Step 6)

Only the message type IE of this message is checked.

8.3.2.2.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305, move to CELL_FACH state, and transmit a URA UPDATE message which is set the value “periodical cell update” into IE “URA update cause”.

After step 3 the UE shall re-transmit URA UPDATE message.

After step 5 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH and returns to the CELL_FACH state.

#### 8.3.2.3 	URA Update: re-entering of service area after T305 expiry

8.3.2.3.1	Definition

8.3.2.3.2	Conformance requirement

This procedure is to update UTRAN with the current URA of the UE if the UE detects that it is out of service area after the expiry of timer T305, and then subsequently re-enters the service area before the expiry of T307.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.3.3	Test purpose

To confirm that the UE executes a URA update procedure when the UE re-enters the service area before the expiry of timer T307, after being out of service area at the expiry of timer T305.

8.3.2.3.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active with URA-ID 1 and the downlink transmission power shown in column marked “T0” in Table 8.3.1.1-1, while cell 2 is inactive with URA-ID 2

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108, with URA-ID 1 in the list of URA-ID from cell 1

Test Procedure

The UE is initially in URA_PCH state. SS decrease the transmission power of cell such that cell selection figure of merit S<0. When the UE detects the expiry of timer T305 according to the system information, the UE moves to CELL_FACH state and finds that it is out of service area. The UE is expected to search for cell to camp. Then SS increases the transmission power so that the UE detects that it returns to normal service within T307. The UE shall move to CELL_FACH state and starts transmitting a URA UPDATE message which contains the value “re-entered service area” in IE “URA update cause” to the SS on the uplink CCCH. After the SS receives this message, it transmits a URA UPDATE CONFIRM message which includes the IE “new C-RNTI”, and “new U-RNTI” to the UE on the downlink DCCH. Then the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH. Next, cell 1 is switched off. SS waits until T305 timer has expired and then turns on cell 2. The UE shall discover that cell 1 is no longer suitable for camping and initiate a cell search. It shall detect the presence of cell 2 and reselects to this cell. . When the UE finds that URA-ID 2 is not in its current list of URA-IDs, it moves to CELL_FACH state and transmits a URA UPDATE message on the uplink CCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE starts operating from URA_PCH state. |
| 2 |  |  | SS decreases the transmission power such that the cell 1 is no longer suitable for camping i.e. S<0. |
| 3 |  |  | The UE shall attempt to perform a URA update upon the expiry of timer T305. It shall discover that it is out of service and starts searching for cell to camp.(T307 timer starts) |
| 4 |  |  | SS increases the transmission power to the original level before T307 expires. |
| 5 | ( | URA UPDATE | Value “re-entered service area” shall be set in IE “URA update cause” |
| 6 | ( | URA UPDATE CONFIRM | The message includes IEs ”new C-RNTI” , and “new U-RNTI” |
| 7 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 8 |  |  | SS ceases to transmit BCCH with URA-ID 1 carried by cell 1and wait until T305 expires. |
| 9 |  |  | SS starts sending BCCH for cell 2 with URA-ID 2 and. |
| 10 | ( | URA UPDATE | UE shall detect the presence of cell 2 and re-select to it. It shall transmit this message with cause set to “URA reselection” |

Specific Message Contents

Use the same message sub-type found in Annex A, with the following exceptions:

URA UPDATE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI URA Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘re-entered service area’ |

URA UPDATE CONFIRM (Step 6)

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI | ‘0000 0000 0001’ ‘0000 0000 0000 1111 1111’ |
| New C-RNTI | Arbitrary 16-bit string which is different the assigned C-RNTI in RRC CONNECTION SETUP message. |

URA UPDATE (Step 10)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI URA Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 1111 1111’ Check to see if set to ‘URA reselection’ |

8.3.2.3.5	Test requirement

After step 2 the UE shall detect that it is out of service area and shall not send a URA UPDATE on the uplink CCCH channel.

After step 4 the UE shall transmit a URA UPDATE message which sets value “re-entered service area” into IE “URA update cause”, before the expiry of timer T307.

After step 6 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

After step 9 the UE shall transmit a URA UPDATE message which sets value “URA reselection” into IE “URA update cause”.

#### 8.3.2.4 	URA Update: loss of service after expiry of timers T307 and T305

8.3.2.4.1	Definition

8.3.2.4.2	Conformance requirement

This procedure is required to handle the case when the UE fails to update UTRAN with the current URA of after expiry of timers T307 and T305 consecutively. The UE shall move to idle mode subsequently.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.4.3	Test purpose

To confirm that the UE moves to idle mode after the expiry of timer T307, following an expiry of timer T305 when it discovers that it is out of service area.

8.3.2.4.4	Method of test

Initial Condition

System Simulator: 1cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in URA_PCH state. SS stops the downlink transmissions of cell 1. When the UE detects the expiry of periodic URA updating timer T305 according to the system information, the UE moves to CELL_FACH state and detects that it is out of service area. After the expiry of timer T307, the UE moves to the idle state and start to perform cell reselection.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | Initially, the UE is in the URA_PCH state. |
| 2 |  |  | SS switched off the downlink transmission of cell 1 so that the UE detects that it is out of service area. |
| 3 |  |  | Upon the expiry of timer T305, the UE shall search for cell to camp and triggers T307 timer. SS listens to the uplink CCCH to verify that URA UPDATE message is not transmitted. |
| 4 |  |  | After the expiry of timer T307, the UE enters idle state. |

Specific Message Contents

None

8.3.2.4.5	Test requirement

After step 2 the UE shall detect the expiry of timer T305, not transmit URA UPDATE message on the uplink CCCH, move to CELL_FACH state, and start timer T307.

#### 8.3.2.5 	URA Update: Success after Confirmation error of URA-ID list

8.3.2.5.1	Definition

8.3.2.5.2	Conformance requirement

UE transmits a URA UPDATE message to the UTRAN when it needs to update UTRAN with the current URA of the UE. UTRAN should respond to the URA UPDATE message by sending a URA UPDATE CONFIRM message. When the indicated URA-ID in the received URA UPDATE CONFIRM message is not found in the list of URA-IDs that is broadcasted in system information block type 2, the UE transmits a URA UPDATE message repeatedly until its internal counter V302 is greater than N302.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.5.3	Test purpose

To confirm that the UE retries to perform the URA update procedure following a confirmation error of URA-ID list.

8.3.2.5.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

At the start of this test, the UE is brought to URA_PCH state and assigned a URA with URA-ID 1. When the UE detects the expiry of timer T305 according to the system information, the UE moves to CELL_FACH state and transmits a URA UPDATE message to the SS on the uplink CCCH. The reason for performing URA updating shall be set to “periodic URA update” in IE “URA update cause”. After the SS receives this message, it transmits a URA UPDATE CONFIRM message which includes the IE “new C-RNTI”, “new U-RNTI” and “URA-ID 2” to the UE on the downlink DCCH. The UE finds that the indicated URA-ID is not included in the list of URA-IDs broadcasted in system information block type 2, then the UE shall retry to transmit a URA UPDATE message for a confirmation error of URA-ID list. SS continue to send the same URA UPDATE CONFIRM message until N302+1 URA UPDATE messages have been received. Then SS transmits a URA UPDATE CONFIRM message to the UE which includes IE “URA Identity” set to ”URA-ID 1”. The UE shall find this URA-ID in its URA-ID list and transmits an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is URA_PCH state. SS initializes counter K to 0 |
| 2 | ( | URA UPDATE | This message shall contain value “periodic URA update” set in IE URA update cause” after expiry of timer T305. |
| 3 |  |  | SS increments K by 1. |
| 4 | ( | URA UPDATE CONFIRM | SS transmits this message, setting the value “URA-ID 2” to IE “URA Identity”. If K is not greater than N302+1, SS waits for T302 to expires and then returns to step 2. If K is greater than N302+1, SS proceeds to step 5. |
| 5 | ( | URA UPDATE CONFIRM | SS transmits this message, setting IE “URA Identity” to “URA-ID 1”. This message also comprises IE “New U-RNTI”. |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |

Specific Message Contents

URA UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI URA Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘Periodic URA update’ |

URA UPDATE CONFIRM (Step 4)

Use the same message sub-type as specified in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC State Indicator | URA_PCH |
| URA Identity | 2 |

URA UPDATE CONFIRM (Step 5)

Use the same message sub-type as specified in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI -SRNC Identity -S-RNTI | ‘0000 0000 0001’ ‘0000 0000 0000 0101 0101’ |
| URA Identity | 1 |

UTRAN MOBILITY INFORMATION CONFIRM (Step 6)

Only the message type IE in this message is checked.

8.3.2.5.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305, move to CELL_FACH state, transmit a URA UPDATE message on the uplink CCCH and set value “periodic URA update” into IE “URA update cause”.

After step 2 the UE shall repeatedly re-transmit a URA UPDATE message after it detects a confirmation error of URA-ID list for the URA-ID indicated in the URA UPDATE CONFIRM message. A total of (N302+2) URA UPDATE messages shall be received by the SS.

After step 5 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

#### 8.3.2.6 	URA Update: Failure (V302 is greater than N302: Confirmation error of URA-ID list)

8.3.2.6.1	Definition

8.3.2.6.2	Conformance requirement

UE transmits a URA UPDATE message to the UTRAN when it needs to update UTRAN with the current URA of the UE. When the indicated URA-ID in the received URA UPDATE CONFIRM message is not in the list of URA-IDs that is broadcasted in system information block type 2, the UE transmits URA UPDATE messages repeatedly until its internal counter V302 is greater than N302. If V302 is greater than N302 then the UE enters idle state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.6.3	Test purpose

To confirm that the UE make repeated attempts to perform the URA update procedure following a detection of a confirmation error of URA-ID list. It then moves to idle state when internal counter V302 is greater than N302.

8.3.2.6.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is originally in the URA_PCH state updated with URA-ID 1. When the UE detects the expiry of timer T305 according to the system information, the UE shall move to CELL_FACH state and transmit a URA UPDATE message to the SS on the uplink CCCH. In this message, the value “periodic URA update” shall be set in IE “URA update cause”. After the SS receives this message, it transmits a URA UPDATE CONFIRM message which includes the IE “new C-RNTI”, “new U-RNTI” and indicating the IE “URA Identity” to be “URA-ID 2” to the UE on the downlink DCCH. The UE finds that the indicated URA-ID is not included in the list of URA-IDs broadcasted, the UE shall retry to transmit a URA UPDATE message for N302+1 times. After that, the UE shall enter idle state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in URA_PCH state at the start of the test. SS sets internal counter K to 0. |
| 2 | ( | URA UPDATE | The message shall indicate “periodic URA update” in IE “URA update cause”. This message is sent following the expiry of timer T305. SS increments counter K by 1. |
| 3 | ( | URA UPDATE CONFIRM | The SS transmit this message and set IE “URA Identity” to “URA-ID 2”. When K greater than N302+2 proceeds to step 4, else SS waits for T302 to expires and executes step 2. |
| 4 |  |  | SS waits for a T305 to verify that no further URA UPDATE messages are transmitted by UE. The counter K shall be equal to (N302+2). The UE shall enter idle state. |

Specific Message Contents

URA UPDATE CONFIRM (Step 4)

Use the same message sub-type defined in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| URA Identity | 2 |

8.3.2.6.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305, then it shall move to CELL_FACH state and transmit a URA UPDATE message on the uplink CCCH, setting value “periodic URA update” into IE “URA update cause”.

After step 2 the UE shall retry to transmit a URA UPDATE message after it detects the confirmation error of URA-ID list for the URA-ID included in the URA UPDATE CONFIRM message.

After step 3 the UE shall stop transmitting URA UPDATE message and then enters idle state. The counter K shall be equal to (N302+2).

#### 8.3.2.7 	URA Update: Success after T302 timeout

8.3.2.7.1	Definition

8.3.2.7.2	Conformance requirement

The UE transmits an URA UPDATE message to the UTRAN when it needs to update UTRAN with the current URA identity stored the UE. When the UE fails to receive any URA UPDATE CONFIRM message after T302 timer expiry, it transmits a URA UPDATE message repeatedly at an interval of T302 timer value until its internal counter V302 is greater than N302.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.7.3	Test purpose

To confirm that the UE attempts to repeat the URA update procedure upon the expiry of timer T302. To confirm that a maximum of N302+1 re-transmission is performed.

8.3.2.7.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the URA_PCH. When the UE detects the expiry of timer T305 according to the system information, the UE moves to CELL_FACH state and transmits a URA UPDATE message to the SS on the uplink CCCH, setting value “periodic URA update” into IE “URA update cause”. The SS ignores this message, the UE shall then retry to transmit a URA UPDATE message after the expiry of timer T302. SS continues to ignore further URA UPDATE message until it receives (N302+1) such messages. Then it transmits a URA UPDATE CONFIRM message to the UE which includes IEs ”new C-RNTI”, ”new U-RNTI”. The UE shall then transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in URA_PCH state at the beginning of test. SS sets counter K to 0. SS waits for T305 to expire. |
| 2 | ( | URA UPDATE | This message shall contain value “periodic URA update” in IE “URA update cause” sent upon the expiry of timer T305. |
| 3 |  |  | SS increments K by 1. |
| 4 |  |  | If K is not greater than N302+1, SS transmits no response to the UE, waits for an additional period equals to T302 timer and returns to step 2. Else, SS executes step 5. |
| 5 | ( | URA UPDATE CONFIRM | This message includes IEs” new C-RNTI” , “new U-RNTI” |
| 6 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |

Specific Message Contents

URA UPDATE CONFIRM (Step 5)

Use the same message sub-type as in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI SRNC Identity S-RNTI | ‘0000 0000 0001’ Arbitrary 20-bit string which is different from S-RNTI field in IE “U-RNTI” |
| New C-RNTI | Arbitrary 16-bit string which is different the assigned C-RNTI in RRC CONNECTION SETUP message. |

8.3.2.7.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305, then it shall move to CELL_FACH state and transmit a URA UPDATE message on the uplink CCCH. The updating cause shall be set to “periodic URA update” in IE “URA update cause”.

After step 2 the UE shall retry to transmit a URA UPDATE message at each expiry of timer T302. UE shall attempt to re-transmit N302+1 URA UPDATE messages.

After step 5 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH.

#### 8.3.2.8 	URA Update: Failure (V302 is greater than N302:T302 timeout)

8.3.2.8.1	Definition

8.3.2.8.2	Conformance requirement

The UE transmits a URA UPDATE message to the UTRAN when it needs to update the UTRAN with the current URA of the UE. When the UE fails to receive the URA UPDATE CONFIRM message, the UE transmits a URA UPDATE message repeatedly after every expiry of T302 until its internal counter V302 is greater than N302. If V302 is greater than N302, UE stops sending URA UPDATE message and then enters idle state.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.8.3	Test purpose

To confirm that the UE retries to perform the URA update procedure upon expiry of timer T302 and moves to idle state after retrying for N302+1 times.

8.3.2.8.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the URA_PCH state. When the UE detects the expiry of timer T305 according to the system information, the UE moves to CELL_FACH state and transmits a URA UPDATE message to the SS on the uplink CCCH. This message shall contain value “periodical URA update” in IE “URA update cause”. SS ignores this message, the UE shall continue to transmit URA UPDATE messages for N302+1 times after the expiry of timer T302. After N302+1 re-transmissions, the UE shall enter idle state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in URA_PCH state and SS sets counter K=0. SS wait until T303 expires. |
| 2 | ( | URA UPDATE | The value “periodic URA update” shall be set in IE “URA update cause”. |
| 3 |  |  | SS ignores the message, waits for T302 timer to expire and increments K by 1. If a message is received after T303 expiry, return to step 2. Else, go to step 4. |
| 4 |  |  | SS checks that K is equal to (N302+2). |
| 5 |  |  | The UE shall enter idle state. |

Specific Message Contents

None

8.3.2.8.5	Test requirement

After step 1 the UE shall detect the expiry of timer T305, then it shall move to CELL_FACH state and transmit a URA UPDATE message on the uplink CCCH, setting “periodical URA update” into IE “URA update cause”.

After step 2 the UE shall retry to transmit a URA UPDATE message after the expiry of timer T302. SS shall receive (N302+2) CELL UPDATE message. After this, the UE shall enter idle state.

#### 8.3.2.9 	URA Update: Failure (UTRAN initiate an RRC connection release procedure on DCCH)

8.3.2.9.1	Definition

8.3.2.9.2	Conformance requirement

The UE transmits a URA UPDATE message to the UTRAN when it needs to update UTRAN with information on the current URA of the UE. If the UE receives a RRC CONNECTION RELEASE message on downlink DCCH, it shall enter idle state after sending a RRC CONNECTION RELEASE COMPLETE message to UTRAN.

Reference

3GPP TS 25.331 clause 8.3.1

8.3.2.9.3	Test purpose

To confirm that the UE moves to idle state after sending RRC CONNECTION RELEASE COMPLETE message to UTRAN upon the reception of RRC CONNECTION RELEASE message on downlink DCCH.

8.3.2.9.4	Method of test

Initial Condition

System Simulator: 1 cell

UE: URA_PCH (state 6-13) as specified in clause 7.4 of TS 34.108

Test Procedure

The UE is in the URA_PCH state. When the UE detects the expiry of periodic URA updating timer T305, the UE moves to CELL_FACH state and transmits a URA UPDATE message to the SS on the uplink CCCH. The message shall indicate the cause to be “periodic URA update” in IE “ URA update cause”. The SS transmits RRC CONNECTION RELEASE message on downlink DCCH. The UE shall transmit RRC CONNECTION RELEASE COMPLETE message using AM RLC on the DCCH and return to idle mode after release of all current signalling flows and radio access bearers.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the URA_PCH state. SS wait until T305 timer has expired. |
| 2 | ( | URA UPDATE | UE shall transmit this message and set value “periodic URA update” into IE “ URA update cause”. |
| 3 | ( | RRC CONNECTION RELEASE | SS transmits RRC CONNECTION RELEASE message to the UE on the downlink CCCH. |
| 4 | ( | RRC CONNECTION RELEASE COMPLETE | The UE transmits this message using acknowledged mode. The UE releases L2 signalling link and radio resources then the UE goes to idle mode. |

Specific Message Contents

URA UPDATE (Step 2)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI URA Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0001’ Check to see if set to ‘Periodic URA update’ |

RRC CONNECTION RELEASE (Step 3)

Only the message type is checked for this message.

RRC CONNECTION RELEASE COMPLETE (Step 4)

Only the message type is checked for this message.

8.3.2.9.5	Test requirement

After step 1 the UE shall transmit a URA UPDATE message on the uplink CCCH and set value “periodic URA update” into IE “ Cell update cause”.

After step 3 the UE shall transmit a RRC CONNECTION RELEASE COMPLETE message on the uplink DCCH and return to idle mode.

### 8.3.3.	UTRAN Mobility Information

#### 8.3.3.1 	UTRAN Mobility Information: Success

8.3.3.1.1	Definition

8.3.3.1.2	Conformance requirement

This procedure is used by the network to assign a new RNTI identity to the UE. It is initiated by the UTRAN when it sends an UTRAN MOBILITY INFORMATION message, which includes a new C-RNTI and/or U-RNTI on the downlink DCCH. The UE starts to use the new identities and transmits an UTRAN MOBILITY INFORMATION CONFIRM message to the UTRAN on the uplink DCCH.

Reference

3GPP TS 25.331 clause 8.3.3

8.3.3.1.3	Test purpose

To confirm that the UE starts to use the new identities after it receives an UTRAN MOBILITY INFORMATION message from the SS. To confirm that the UE use the new U-RNTI identity to calculate the applicable paging occasions.

[Editor’s note] In this test case, it is assumed that the paging occasion during connected states is determined using U-RNTI. From TS 25.304 Clause 8, this assumption cannot be confirmed. Further clarification is required regarding this issue.

8.3.3.1.4	Method of test

Initial Condition

System Simulator: 1cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

Initially, the UE is in the CELL_FACH state and it has been assigned a C-RNTI and U-RNTI. The SS transmits an UTRAN MOBILITY INFORMATION message which includes new C-RNTI and U-RNTI to the UE. Then the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message as confirmation and transits to CELL_PCH state. SS pages the UE by sending a PAGING TYPE 1 message and specifying the newly assigned U-RNTI identity in this message. The UE shall transmit a CELL UPDATE message to the SS on the uplink CCCH which includes the U-RNTI identical to that found in UTRAN MOBILITY INFORMATION message received in step 2. The CELL UPDATE message shall also contain IE “Cell update cause” with this IE set to “paging response”. After the SS receives this message, it transmits a CELL UPDATE CONFIRM message which includes IE “RRC State Indicator” set to value “CELL_FACH” to the UE on the downlink DCCH. The UE shall return to CELL_FACH state.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The initial state of the UE is CELL_FACH state. UE has been allocated both C-RNTI and U-RNTI during RRC connection establishment phase. |
| 2 | ( | UTRAN MOBILITY INFORMATION | Contains new C-RNTI and U-RNTI identities. |
| 3 | ( | UTRAN MOBILITY INFORMATION CONFIRM |  |
| 4 | ( | PAGING TYPE 1 | SS pages the UE using the new U-RNTI allocated in step 2. |
| 5 | ( | CELL UPDATE | UE shall trigger cell updating. The message shall indicate the same U-RNTI assigned in the UTRAN MOBILITY INFORMATION message in step 2. |
| 6 | ( | CELL UPDATE CONFIRM | IE “RRC State Indicator” is set to “CELL_FACH”. |

Specific Message Content

UTRAN MOBILITY INFORMATION (Step 2)

Use the same message sub-type as in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI New C-RNTI RRC State Indicator | ‘0000 0000 0001’ ‘0101 0101 0101 0101 0101’ ‘1010 1010 1010 1010’ CELL_PCH |

UTRAN MOBILITY INFORMATION CONFIRM (Step 3)

Only the message type IE is checked in this message.

PAGING TYPE 1 (Step 4)

Use the same message sub-type as in TS 34.108 Clause 9, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Page Record List - Paging record - CHOICE Paging originator - U-RNTI - SRNC Identity - S-RNTI BCCH modification info | UTRAN originator ‘0000 0000 0001’ ‘0101 0101 0101 0101 0101’ Not Present |

CELL UPDATE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell Update Cause | Check to see if set to ‘0000 0000 0001’ Check to see if set to ‘0101 0101 0101 0101 0101’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Paging Response’ |

CELL UPDATE CONFIRM (Step 6)

Use the same message sub-type as in Annex A.

8.3.3.1.5	Test requirement

After step 2 the UE shall transmit an UTRAN MOBILITY INFORMATION CONFIRM message on the uplink DCCH. The MAC PDU carrying this message shall comprise either the new C-RNTI or U-RNTI allocated in the “UE-id” field of the MAC header.

After step 4 the UE shall transmit a CELL UPDATE message on the uplink CCCH with IE “Cell update cause” set to “paging response”. The IE “U-RNTI” shall be identical to the IE “New RNTI” found in UTRAN MOBILITY INFORMATION message sent by the SS in step 2.

#### 8.3.3.2 	UTRAN Mobility Information: Failure (Invalid message reception)

8.3.3.2.1	Definition

8.3.3.2.2	Conformance Requirements

When the UE receives an UTRAN MOBILITY INFORMATION message, which contains an error in one of the mandatory IE, it shall transmit a UTRAN MOBILITY INFORMATION FAILURE message on the DCCH using AM RLC and set the value "protocol error" in the IE “failure cause”. The IE “protocol error information” in this message shall also be set to an appropriate value. The UE shall not utilize any identities relayed in the erroneous message, and it shall resume normal operations.

8.3.3.2.3	Test Purpose

To confirm that the UE ignore the new connected mode identities conveyed in an erroneous UTRAN MOBILITY INFORMATION message. To confirm that the UE report this event to the UTRAN by sending UTRAN MOBILITY INFORMATION FAILURE message, stating the appropriate failure cause and information.

8.3.3.2.4	Method of test

Initial Conditions

System Simulator: 1 cell

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

The UE is brought to CELL_FACH state. SS transmits a UTRAN MOBILITY INFORMATION message to the UE on the DCCH using UM-RLC mode. In this message, the IE “RRC State Indicator” is set to one of the spare values. A new U-RNTI identity is also present in this message. The UE shall respond by transmitting the UTRAN MOBILITY INFORMATION FAILURE message, indicating “protocol error” in IE “failure cause” and also “Information element not comprehended” in IE “Protocol error information”. After receiving the UTRAN MOBILITY INFORMATION FAILURE message, SS waits for a duration to allow T305 to expire. The UE shall transmit CELL UPDATE message with the original U-RNTI identity assigned. SS complete this test by sending CELL UPDATE CONFIRM message to the UE on the downlink DCCH.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The initial state of the UE is CELL_FACH state. |
| 2 | ( | UTRAN MOBILITY INFORMATION | Contains a new U-RNTI identity, but a spare value is used in the IE “RRC State Indicator” |
| 3 | ( | UTRAN MOBILITY INFORMATION FAILURE | UE shall transmit this message to report the error in UTRAN MOBILITY INFORMATION message. It shall include the appropriate cause in the message. |
| 4 |  |  | SS waits for a period up to timer T305 to allow the UE to start performing a cell updating procedure. |
| 5 | ( | CELL UPDATE | UE shall trigger periodic cell updating. The message shall not contain the U-RNTI given in the UTRAN MOBILITY INFORMATION message in step 2. |
| 6 | ( | CELL UPDATE CONFIRM |  |

Specific Message Content

UTRAN MOBILITY INFORMATION (Step 2)

Use the same message sub-type as in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI - SRNC Identity - S-RNTI RRC State Indicator | 0000 0000 0001B 0000 0000 0000 0000 00011B Set to one of the spare value |

UTRAN MOBILITY INFORMATION FAILURE (Step 3)

| Information Element | Value/remark |
| --- | --- |
| Failure Cause Protocol Error Information | Check to see if set to ‘Protocol error’ Check to see if set to ‘Information Element not comprehended’ |

CELL UPDATE (Step 5)

| Information Element | Value/remark |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI START List Cell update cause | Shall be the same as the original U-RNTI allocated Check to see if set to ‘0000 0000 0001’B Check to see if set to ‘0000 0000 0000 0000 0001’B \ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic Cell Updating’ |

CELL UPDATE CONFIRM (Step 6)

Use the same message sub-type as in Annex A.

8.3.3.2.5	Test Requirement

After step 2 the UE shall transmit UTRAN MOBILITY INFORMATION FAILURE message, indicating the value “protocol error” in IE “failure cause” and also “information element not comprehended” in IE “protocol error information”.

After step 4 the UE shall initiate a periodic cell updating procedure by transmitting CELL UPDATE message on the CCCH. In this message, the U-RNTI identity shall be set to the same value as assigned during the RRC connection establishment procedure.

### 8.3.4 	Active set update in soft handover

#### 8.3.4.1 	Active set update in soft handover: Radio Link addition

8.3.4.1.1	Definition

8.3.4.1.2	Conformance requirement

Radio link addition is triggered in the network’s RRC layer. The RRC entity in the network first configures the new radio link. Transmission and reception then begin immediately. This procedure is to update the active set of the connection between the UE and UTRAN. The UTRAN then transmits an ACTIVE SET UPDATE message to the UE. The UE configures layer 1 to begin reception for the additional radio link. After the UE receives confirmation from the physical layer in the UE, an ACTIVE SET UPDATE COMPLETE message is sent to the UTRAN.

Reference

3GPP TS 25.331 clause 8.3.4

8.3.4.1.3	Test purpose

To confirm that the UE continues to communicate with the SS on both the additional radio link and an already existing radio link after the radio link addition.

8.3.4.1.4	Method of test

Initial Condition

System Simulator: 2cells - Cell 1 is active, Cell 2 is active

UE: CS-CELL_DCH_Initial (state 6-1) or PS-CELL_DCH_Initial (state 6-3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

Initially, the UE establishes a radio access bearer in the CELL_DCH state in cell 1. The SS begins to configure the new radio link to be added from cell 2. Then the SS transmits to the UE an ACTIVE SET UPDATE message in cell 1 on DCCH using AM RLC which includes the IE “Radio Link Addition Information” (e.g. Downlink DPCH information and other optional parameters relevant for the additional radio links with Primary CPICH info used for the reference ID). When the UE receives this message, the UE shall configure layer 1 to begin reception without affecting the current uplink and downlink activities of existing radio links. After the UE confirms the synchronization with the new radio link from cell 2, the UE shall transmit an ACTIVE SET UPDATE COMPLETE message to the SS on the uplink DCCH using AM RLC. The UE continues to communicate with the SS on the both radio links. To test this condition, SS ceases the operations of all uplink and downlink DPCH from cell 1. SS shall observe that the data communication for both DCCH and DTCH channels continue as per normal using cell 2, as if cell 1 is still operational.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is brought to CELL_DCH state in cell 1, after the successful establishment of a radio access bearer service. |
| 2 |  |  | The SS configures an additional radio link in the downlink direction from cell 2. |
| 3 | ( | ACTIVE SET UPDATE | SS transmits this message in cell 1 on downlink DCCH using AM RLC. The message includes IE “Radio Link Addition Information”. (e.g. Downlink DPCH information and other optional parameters relevant for the additional radio links with Primary CPICH info used for the reference ID in cell 2) |
| 4 | ( | ACTIVE SET UPDATE COMPLETE | The UE shall configure a new radio link to cell 2, without interfering with existing connections on the radio link in cell 1. SS ceases all Tx and Rx activities in cell 1. But it shall be able to communicate with UE through cell 2. |

Specific Message Content

ACTIVE SET UPDATE

The message to be used in this test is defined in the default message content clause, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Radio link addition information - Primary CPICH Info - Primary Scrambling Code - Downlink DPCH info for each RL - Primary CPICH usage for channel estimation - DPCH frame offset - Secondary CPICH info - DL channelisation code - Secondary scrambling code - CHOICE Spreading factor - Code Number - Scrambling code change - TPC Combination Index - SSDT Cell Identity - Close loop timing adjustment mode - TFCI Combining Indicator - SCCPCH information for FACH Radio link removal information | Set to same code as assigned for cell 2 P-CPICH can be used. 0 chips Not Present This IE is repeated for all existing downlink DPCHs allocated to the UE Not Present 512 For each DPCH, assign the same code number in the current code given in cell 1. Not Present Not Present Not Present Not Present Not Present Not Present Not Present |

8.3.4.1.5	Test requirement

After step 3 the UE shall configures a new radio link to cell.2, with the connection on the old radio link in cell 1 remaining operational and unaffected. It shall transmit an ACTIVE SET UPDATE COMPLETE message on the uplink DCCH using AM RLC to acknowledge the completion of the active set additional procedure.

After step 4 the SS shall continue to communicate with the UE using the radio links added to the UE from cell 2.

#### 8.3.4.2 	Active set update in soft handover: Radio Link removal

8.3.4.2.1	Definition

8.3.4.2.2	Conformance requirement

This procedure is to update the active set of the connection between the UE and the UTRAN after the UTRAN has commanded a removal of a radio link from the current active set. The UTRAN RRC transmits an ACTIVE SET UPDATE message to the UE RRC. The UE RRC requests UE L1 to terminate transmission and reception of the radio link to be removed. The UE shall continue to communicate normally with the UTRAN using the new active set, without losing the connection link. After this the UE acknowledges the radio link removal by sending an ACTIVE SET UPDATE COMPLETE message to the UTRAN on DCCH using AM RLC.

Reference

3GPP TS 25.331 clause 8.3.4

8.3.4.2.3	Test purpose

To confirm that the UE continues to communicate with the SS on the remaining radio link after radio link removal on the active set.

8.3.4.2.4	Method of test

Initial Condition

System Simulator: 2 cells - both Cell 1 and Cell 2 are active

UE: CS-CELL_DCH_Initial (state 6-1) or PS-CELL_DCH_Initial (state 6-3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

At the start of the test, the UE establishes a radio access bearer service in the CELL_DCH state in cell 1. This is followed by a radio link addition procedure in cell 2. SS then transmits an ACTIVE SET UPDATE message, which includes IE “Radio Link Removal Information” and specifying the P-CPICH information of the cell to be removed. When the UE receives this message, the UE RRC entity shall request UE L1 entity to terminate transmission and reception of the radio link from cell 1. Then the UE transmits an ACTIVE SET UPDATE COMPLETE message to the SS on the uplink DCCH using AM RLC. The UE shall continue to communicate with the SS on the remained radio link in cell 2.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL DCH state in cell 1. SS executes test 8. 3.4.1, and the UE shall update the active set to contain cell 1 and cell 2 after the radio link addition procedure. |
| 2 | ( | ACTIVE SET UPDATE | The SS transmits this message on downlink DCCH using AM RLC which includes IE “Radio Link Removal Information”. |
| 3 | ( | ACTIVE SET UPDATE COMPLETE | The UE shall remove the radio link associated with cell 1. |
| 4 |  |  | The SS stops transmission on the downlink direction from cell 1 and the UE shall continue to communicate on the remaining radio link in cell 2. |

Specific Message Contents

ACTIVE SET UPDATE

The message to be used in this test is the same as the message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Radio link addition information Radio link removal information - Primary CPICH info - Primary scrambling code | Not Present 1 radio link to be removed Set to the same P-CPICH scrambling code assigned for cell 1 |

8.3.4.2.5	Test requirement

After step 2 the UE shall remove the radio link from cell 1 and it shall transmit an ACTIVE SET UPDATE COMPLETE message on the uplink DCCH using AM RLC.

After step 3 the UE shall continue to communicate on the remaining radio link from cell 2.

#### 8.3.4.3	Active set update in soft handover: Combined radio link addition and removal (active set is not full)

8.3.4.3.1	Definition

8.3.4.3.2	Conformance requirement

When radio links are to be replaced, the UTRAN RRC first configures the UTRAN L1 to activate the radio link(s) that are being added. The UTRAN RRC then transmits an ACTIVE SET UPDATE message to the UE RRC, which shall configure the UE L1 to terminate transmission and reception on the removed radio link(s) and begin transmission and reception on the added radio link(s). At the completion of the reconfiguration of radio links, the UE shall acknowledge the replacement with an ACTIVE SET UPDATE COMPLETE message.

Reference

3GPP TS 25.331 clause 8.3.4

8.3.4.3.3	Test purpose

To confirm that the UE continues to communicate with the SS on the added radio link and removes radio link which exists prior to the execution of active set update procedure.

8.3.4.3.4	Method of test

Initial Condition

System Simulator: 2 cells- Both Cell 1 and Cell 2 are active

UE: CS-CELL_DCH_Initial (state 6-1) or PS-CELL_DCH_Initial (state 6-3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE [Active set is not full.]

Test Procedure

The UE establishes a radio access bearer in the CELL_DCH state in cell 1. SS begin to configure the new radio link in cell 2. Then the SS transmits to the UE an ACTIVE SET UPDATE message in cell 1 on DCCH using AM RLC. The message includes IE “Radio Link Addition Information” and IE “Radio Link Removal Information”, indicating the removal of cell 1 and addition of cell 2 into the active set. When the UE receives this message, the UE RRC shall terminate the transmission and reception of the removed radio link in cell 1 and then configures layer 1 to begin transmission and reception in cell 2. After the UE received confirmations from the physical layer regarding the update of active set, it transmits an ACTIVE SET UPDATE COMPLETE message on the uplink DCCH to the SS. The UE shall continue to communicate with the SS on the added radio link in cell 2. When SS receives ACTIVE SET UPDATE COMPLETE message, it verifies that the UE has ceased any uplink transmission in cell 1.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_DCH state in cell 1 |
| 2 |  |  | The SS configures an additional radio link in cell 2, starting the transmission and reception of data in cell 2. clause |
| 3 | ( | ACTIVE SET UPDATE | The SS transmit this message on downlink DCCH using AM RLC which includes IE “Radio Link Addition Information” for cell 2 and IE “Radio Link Removal Information” for cell 1. |
| 4 | ( | ACTIVE SET UPDATE COMPLETE | The UE shall configure a new radio link in cell 2 and removes the old radio link in cell 1. |
| 5 |  |  | The SS removes the radio link from cell 1 and the UE shall continue to communicate on the added radio link in cell 2, and not transmit any data in cell 1. |

Specific Message Content

ACTIVE SET UPDATE

The message to be used in this test is defined in the default message content clause, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Radio link addition information - Primary CPICH Info - Primary Scrambling Code - Downlink DPCH info for each RL - Primary CPICH usage for channel estimation - DPCH frame offset - Secondary CPICH info - DL channelisation code - Secondary scrambling code - CHOICE Spreading factor - Code Number - Scrambling code change - TPC Combination Index - SSDT Cell Identity - Close loop timing adjustment mode - TFCI Combining Indicator - SCCPCH information for FACH Radio link removal information - Primary CPICH Info - Primary Scrambling Code | Set to same code as assigned for cell 2 P-CPICH can be used. 0 chips Not Present This IE is repeated for all existing downlink DPCHs allocated to the UE Not Present 512 For each DPCH, assign the same code number in the current code given in cell 2. Not Present Not Present Not Present Not Present Not Present Not Present Set to same code assigned as for cell 1 |

8.3.4.3.5	Test requirement

After step 3 the UE shall remove the radio link in cell 1 and add the radio link in cell 2. Then the UE shall transmit an ACTIVE SET UPDATE COMPLETE message the uplink DCCH.

After step 4 the UE shall continue to communicate on the added radio link in cell 2. SS monitors the uplink direction to confirm that no data are designated for reception in cell 1.

#### 8.3.4.4	Active set update in soft handover: Invalid Configuration

8.3.4.4.1	Definition

8.3.4.4.2	Conformance requirement

If the UTRAN attempts to remove a radio link that is not currently present in the UE’s active set, the UE transmits an ACTIVE SET UPDATE FAILURE message on the DCCH using AM RLC and maintain its current communication status with the radio links.

Reference

3GPP TS 25.331 clause 8.3.4

8.3.4.4.3	Test purpose

To confirm that the UE transmits an ACTIVE SET UPDATE FAILURE message on the DCCH using AM RLC, following the reception of a message specifying the removal of a radio link unknown to the UE.

8.3.4.4.4	Method of test

Initial Condition

System Simulator: 2 cells - Cell 1 is active, Cell 2 is active.

UE: CS-CELL_DCH_Initial (state 6-1) or PS-CELL_DCH_Initial (state 6-3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

The UE establishes a radio access bearer in the CELL_DCH state in cell 1. SS requests for a radio link addition by executing the steps described in test case 8.3.4.1. The UE shall then include cell 2 into its active set and establish the transmission and reception capabilities related to cell 2. SS then transmits an ACTIVE SET UPDATE message in cell 1 on DCCH using AM RLC which includes IE “Radio Link Removal Information” This IE indicates that a cell with unknown P-CPICH scrambling code be removed from the active set. When the UE receives this message, it transmits an ACTIVE SET UPDATE FAILURE message which is set to “Invalid configuration” in IE “failure cause” on the uplink DCCH using AM RLC to the SS, and continues to communicate on the existing radio links in cell 1 and cell 2.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_DCH state in cell 1. |
| 2 |  |  | SS commands the UE to perform a radio link addition procedure by executing the steps in test case 8.3.4.1. The UE shall respond accordingly. Both cell 1 and cell 2 should be found in the active set maintained by the UE. |
| 3 | ( | ACTIVE SET UPDATE | The SS transmits this message on downlink DCCH using AM RLC which includes IE “Radio Link Removal Information”. This content of this IE indicates an unknown cell. |
| 4 | ( | ACTIVE SET UPDATE FAILURE | The message shall state “Invalid configuration” in IE “failure cause”. UE shall continue to communicate normally with both cells |

Specific Message Contents

ACTIVE SET UPDATE (Step 3)

The message to be used in this test is defined in the default message content clause, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Radio link addition information Radio link removal information - Primary CPICH info - Primary scrambling code | Not Present 1 radio link to be removed Set to an unknown scrambling code not assigned to any cells. |

ACTIVE SET UPDATE FAILURE (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Integrity check info Failure cause | Not Checked Check to see if it’s set to ‘Invalid configuration’ |

8.3.4.4.5	Test requirement

After step 3 the UE shall transmit an ACTIVE SET UPDATE FAILURE message, setting “Invalid configuration” in IE “failure cause” and sent on the uplink DCCH using AM RLC.

After step 4 the UE shall continue to communicate on the radio links for both cell 1 and cell 2.

#### 8.3.4.5	Active set update in soft handover: Combined radio link addition and removal (active set is full)

8.3.4.5.1	Definition

8.3.4.5.2	Conformance requirement

When the UE active set is full, the UE shall first remove the old radio link and then add the new radio link, after it receives an ACTIVE SET UPDATE message for the combined radio link addition and removal.

Reference

3GPP TS 25.331 clause 8.3.4

8.3.4.5.3	Test purpose

To confirm that the UE removes one of existing radio links, which is indicated in an ACTIVE SET UPDATE message and continues to communicate on the added radio link.

8.3.4.5.4	Method of test

Initial Condition

System Simulator: 3 cells - Cell 1, Cell 2, and Cell 3 are all active

UE: CS-CELL_DCH_Initial (state 6-1) or PS-CELL_DCH_Initial (state 6-3) in cell 1 and cell 2 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE (The assumed maximum number for active set is 2.)

[Editor’s Note] The maximum number of radio link (i.e. MaxRL) specified in CR328 of TS 25.331 is 8. However, if the UE capability is more inferior in this aspect, can the assumption above still stands?

Test Procedure

The UE establishes a radio access bearer in the CELL_DCH state in cell 1 and cell 2. The SS configures the new radio link in cell 3 and sends an ACTIVE SET UPDATE message on DCCH using AM. This message includes IE “Radio Link Addition Information” indicating cell 3 to be added into the active set, and IE “Radio Link Removal Information” indicating the removal of cell 1 from the active set. When the UE receives this message, it shall not report a failure but firstly removes the indicated radio link and then adds the new radio link. Then the UE transmits an ACTIVE SET UPDATE COMPLETE message on the DCCH using AM RLC to the SS and continues to communicate with the SS on the added radio link and the remaining old radio link.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_DCH state in cell 1 and cell 2. |
| 2 |  |  | The SS configures an additional radio link in for cell 3, and starts reception and transmission using cell 3. |
| 3 | ( | ACTIVE SET UPDATE | The SS transmit this message on downlink DCCH using AM RLC which includes IE “Radio Link Addition Information” and IE “Radio Link Removal Information”. The contents of the IE dictate the addition of cell 3 into the active set and removal of cell 1 from it. |
| 4 | ( | ACTIVE SET UPDATE COMPLETE | The UE shall configure a new radio link in cell 3 and removes the old radio link in cell 1. |
| 5 |  |  | The SS removes the radio link in cell 1. The UE shall continue to communicate on the added radio link in cell 3 and also the existing radio link in cell 2. |

Specific Message Content

ACTIVE SET UPDATE

The message to be used in this test case isidentical to the same message sub-type found in Annex A, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Radio link addition information - Primary CPICH Info - Primary Scrambling Code - Downlink DPCH info for each RL - Primary CPICH usage for channel estimation - DPCH frame offset - Secondary CPICH info - DL channelisation code - Secondary scrambling code - CHOICE Spreading factor - Code Number - Scrambling code change - TPC Combination Index - SSDT Cell Identity - Close loop timing adjustment mode - TFCI Combining Indicator - SCCPCH information for FACH Radio link removal information - Primary CPICH Info - Primary Scrambling Code | Set to same code as assigned for cell 3 P-CPICH can be used. 0 chips Not Present This IE is repeated for all existing downlink DPCHs allocated to the UE Not Present 512 For each DPCH, assign the same code number in the current code given in cell3. Not Present Not Present Not Present Not Present Not Present Not Present Set to same code assigned as for cell 1 |

8.3.4.5.5	Test requirement

After step 3 the UE shall remove the radio link in cell 1 and add the radio link in cell 3. Then the UE shall transmit an ACTIVE SET UPDATE COMPLETE message on the uplink DCCH.

After step 4 the UE shall continue to communicate on the added radio link in cell 3 and on the existing old radio link in cell 2. It shall cease all transmission to cell 1.

Void

#### 8.3.4.7	Active set update in soft handover: Invalid Message Reception

8.3.4.7.1	Definition

8.3.4.7.2	Conformance Requirement

The UE shall keep its old configuration when the UE receives an ACTIVE SET UPDATE message, which omits a conditional IE. It shall transmit a ACTIVE SET UPDATE FAILURE message which set value “protocol error” in IE “failure cause” and also value “Conditional information element error” in IE “Protocol error cause”.

Reference

3GPP TS 25.331 clause 8.3.4

8.3.4.7.3	Test Purpose

To confirm that the UE retains its active set list when it receives an ACTIVE SET UPDATE message, with a conditional IE missing in the message.

8.3.4.7.4	Method of test

Initial Condition

System Simulator: 2 cells – both cell 1 and cell 2 are active.

UE: CS-CELL_DCH_Initial (state 6-1) or PS-CELL_DCH_Initial (state 6-3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE (Integrity protection algorithm is not applied at the start of test)

Test Procedure

The UE establishes a radio access bearer in CELL_DCH in cell 1. SS requests that cell 2 be added into the active set by performing the steps described in test cases 8.3.4.1. The UE shall react accordingly and incorporate cell 2 into its active set. SS transmits an ACTIVE SET UPDATE message , with both IE “Integrity check info” and IE “Integrity protection mode info” present in the message. This message also commands the starting of integrity mode protection. However, the IE “integrity protection initialisation number” is omitted. The UE shall detect that it has received an invalid message. It shall then send an ACTIVE SET UPDATE FAILURE message, stating the reason “Conditional information element error” in the IE “Protocol error information”. The UE shall not remove cell 1 from its current active set.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is CELL_DCH state in cell 1. |
| 2 |  |  | SS executes the steps in test case 8.3.4.1. The UE shall add cell 2 into its active set. |
| 3 | ( | ACTIVE SET UPDATE | The SS transmits this message on downlink DCCH using AM RLC which includes IE “Integrity check info” and IE “Integrity protection mode info”. This message indicates that integrity mode protection be started but omit the IE “integrity protection initialisation number”. The message also specifies that cell 1 be removed from the active set. |
| 4 | ( | ACTIVE SET UPDATE FAILURE | The message shall state “conditional information element error” in IE “protocol error information”. UE shall continue to communicate normally with both cells. |

Specific Message Contents

ACTIVE SET UPDATE (Step 3)

The message to be used in this test is defined in the default message content clause, with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| Integrity Check Info - Message authentication code - RRC Message sequence number Integrity Protection Mode Info - Integrity protection mode command - Downlink integration protection activation info - Integrity protection algorithm - Integrity protection initialisation number Radio link addition information Radio link removal information - Primary CPICH info - Primary scrambling code | Set to an arbitrary 32-bits string Set to an arbitrary integer between 0 and 15 Start Not Present Standard UMTS Integrity Algorithm UIA1 Not Present Not Present Set to the P-CPICH scrambling code assigned to cell 1. |

ACTIVE SET UPDATE FAILURE (Step 4)

| Information Element | Value/remark |
| --- | --- |
| Protocol Error Information - Protocol Error Cause | Check to see if it’s set to ‘Conditional information element error’ |

8.3.4.7.5	Test Requirement

After step 3 the UE shall report a protocol error by transmitting the ACTIVE SET UPDATE FAILURE message on the DCCH. In this message, the value “Conditional information element error” shall be set in IE “Protocol Error Information”. The UE shall continue to communicate normally with the SS using cell 1 and cell 2.

### 8.3.5	Hard Handover

[Editor’s note: This test is included in the “Physical channel reconfiguration”, ”Radio bearer establishment”, “Radio bearer reconfiguration”, “Radio bearer release” and “Transport channel reconfiguration”.]

### 8.3.6	Inter-system hard handover from GSM to UTRAN

Clauses 8.3.6 contains test procedures to be used for executing Inter-system Handover from GSM to UTRAN tests. Table 8.3.6-1 contains a summary of the different combinations of parameters being tested, together with a reference to the appropriate generic test procedure. If a test uses a parameter which the UE under test does not support, the test shall be skipped. Test cases in this clause are applicable only to the UE supporting both UTRAN and GSM. The test USIM shall support service 27 to carry out these test cases.

Table 8.3.6-1

| From | To | State of call | Ref. clause | Exec counter | Remark |
| --- | --- | --- | --- | --- | --- |
| GSM FR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U10 | 8.3.6.1 | 1 | call active state |
| GSM EFR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U10 | 8.3.6.1 | 2 | call active state |
| GSM AMR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U10 | 8.3.6.1 | 3 | call active state |
| GSM HR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U10 | 8.3.6.1 | 4 | call active state |
| GSM 14.4 kbps CS data | UTRAN (Streaming/unknown/ uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | U10 | 8.3.6.2 | 1 | same data rate |
| GSM 28.8 kbps CS data | UTRAN (Streaming/unknown/ uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | U10 | 8.3.6.2 | 2 | same data rate |
| GSM 57.6 kbps CS data | UTRAN (Streaming/unknown/ uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | U10 | 8.3.6.2 | 3 | same data rate |
| GSM 14.4 kbps CS data | UTRAN (Streaming/unknown/ uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | U10 | 8.3.6.3 | 1 | data rate upgrading |
| GSM 14.4 kbps CS data | UTRAN (Streaming/unknown/ uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | U10 | 8.3.6.3 | 2 | data rate upgrading |
| GSM 28.8 kbps CS data | UTRAN (Streaming/unknown/ uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | U10 | 8.3.6.3 | 3 | data rate upgrading |
| GSM FR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U1 | 8.3.6.4 | 1 | during call establishment |
| GSM FR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U10 | 8.3.6.5 | 1 | blind handover |
| GSM FR | UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | U10 | 8.3.6.6 | 1 | failure case |

#### 8.3.6.1	Inter system handover to UTRAN/From GSM/Speech/Success

8.3.6.1.1	Definition

8.3.6.1.2	Conformance requirement

The UE shall be able to receive a HANDOVER TO UTRAN COMMAND message from GSM and perform an inter-system handover, even if no prior UE measurements have been performed on the target UTRAN cell and/or frequency.

If the UE succeeds to establish the connection to UTRAN, it shall transmit a HANDOVER TO UTRAN COMPLETE message on the uplink DCCH.

Reference(s)

TS 25.331 Clause 8.3.6.

TS 04.18 Clause 3.4.4a.

8.3.6.1.3	Test purpose

To test that UE supporting both GSM and UTRAN handovers to the indicated channel in the UTRAN target cell when it is in the speech call active state in the GSM serving cell and receives a HANDOVER TO UTRAN COMMAND.

8.3.6.1.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is GSM,  Cell 2 is UTRAN. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 1.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN AMR,

UE supports GSM ARM,

UE supports GSM EFR,

UE supports GSM HR,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the GSM cell and UTRAN cell with cell selection conditions in favour of GSM cell, the UE selects the GSM cell for camping on. In UTRAN cell SIB16 is broadcast and contains the pre-configuration for conversationa/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS. After UE received and stored the SIB16,  the SS brings the UE into the call active state (CC state U10) with FR speech call (for execution counter M = 1). The SS configures the dedicated channel corresponding to the pre-configuration in UTRAN cell, then sends HANDOVER TO UTRAN COMMAND indicating the dedicated channel of the target cell to the UE through the GSM serving cell. After the UE receives the command it shall configure itself accordingly and switch to the dedicated channel of UTRAN cell. The SS checks whether the handover is performed by checking that the UE transmits HANDOVER TO UTRAN COMPLETE to the SS through DCCH of the UTRAN cell.

Depending on the PIXIT parameters, the above procedure is executed maximum four times, each time for different initial conditions:

-	If the UE supports GSM FR, the procedure is executed for execution counter M = 1;

-	If the UE supports GSM EFR, the procedure is executed for execution counter M = 2;

-	If the UE supports GSM AMR, the procedure is executed for execution counter M = 3;

-	If the UE supports GSM HR, the procedure is executed for execution counter M = 4.

Expected sequence

This sequence is performed for a maximum execution counter M = 1, 2, 3, 4, depending on the PIXIT parameters.

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | SS |  | The SS configures GSM and UTRAN cells, UE camps on GSM cell and received SIB16 from UTRAN cell. |
| 2 | UE |  | The SS bring the UE into GSM U10 state in cell 1 and for M = 1: the UE is in GSM FR speech call; for M = 2: the UE is in GSM EFR speech call; for M = 3: the UE is in GSM AMR speech call; for M = 4: the UE is in GSM HR speech call. |
| 3 | SS |  | The SS configures the dedicated channel with the configuration: conversational/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs in UTRAN cell. |
| 4 | ( | HANDOVER TO UTRAN COMMAND | Send on cell 1 (GSM cell) |
| 5 | UE |  | The UE accepts the handover command and configures its lower layers using the parameters contained in the HANDOVER TO UTRAN COMMAND |
| 6 | SS |  | The SS waits for uplink physical channel in synchronization |
| 7 | ( | HANDOVER TO UTRAN COMPLETE | The SS receives this message on DCCH of cell 2 (UTRAN cell). It implies that the down link physical channel has synchronised with UTRAN. |

Specific message contents

Content of “SysInfoType16”

| Information Element | Value/remark |
| --- | --- |
| re-EstablishmentTimer T315 | 30 s |
| PredefinedRB_Configuration |  |
| - SRB information list |  |
| - RB identity | 1 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | UM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - CHOICE DL RLC mode | UM RLC mode |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 1 |
| - RB identity | 2 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - MAC logical channel priority | 2 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - RB identity | 3 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 3 |
| - MAC logical channel priority | 3 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 3 |
| - RB identity | 4 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 4 |
| - MAC logical channel priority | 4 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 4 |
| - RB information list |  |
| - RB information to setup |  |
| - RB identity | 10 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 2 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 2 |
| - Logical channel identity | 1 |
| - RB information to setup |  |
| - RB identity | 11 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 3 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 3 |
| - Logical channel identity | 1 |
| - RB information to setup |  |
| - RB identity | 12 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 4 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 4 |
| - Logical channel identity | 1 |
| preDefTransChConfiguration |  |
| - uplink Common Transport channel Info |  |
| - TFC subset |  |
| - Allowed Transport Format combination | 0, 1, 2, 3, 4, 5 |
| - CHOICE Mode specific info | FDD |
| - CHOICE uplink DCH TFCS | Normal signalling |
| - CHOICE Normal signalling | Addition |
| - CHOICE CTFC Size | 6 bits |
| - CTFC information | 0 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 1 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 11 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 12 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 13 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 23 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - uplink Add or reconfigured transport channel info list |  |
| - Transport channel identity | 2 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 81 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 39 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 81 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 20 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 180-220 |
| - CRC size | 12 bits |
| - Transport channel identity | 3 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 103 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 103 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 20 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 170-210 |
| - CRC size | N/A |
| - Transport channel identity | 4 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 60 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 60 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 20 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/2 |
| - Rate matching attribute | 215-256 |
| - CRC size | N/A |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 148 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 148 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 40 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 155-165 |
| - CRC size | 16 bits |
| - DL Common transport channel info |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE Mode specific info | FDD |
| - CHOICE TFCS Signalling mode | Same as uplink |
| - Added or reconfigured DL TrCH info list |  |
| - Transport channel identity | 2 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 2 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| - Addide or reconfigured DL TrCH info list |  |
| - Transport channel identity | 3 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 3 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| - Added or reconfigured DL TrCH info list |  |
| - Transport channel identity | 4 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 4 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| PreDefPhyChConfiguration |  |
| -uplink_DPCH_InfoPredef |  |
| - uplink DPCH Info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 15 slots |
| - CHOICE Mode specific info | FDD |
| - TFCI existence | TRUE |
| - Puncturing Limit | 0.88 |
| - DL_ CommonInformationPredef |  |
| - DL_DPCH_InfoCommon |  |
| - Timing indication | initialize |
| - CHOICE Mode specific info | FDD |
| - Spreading factor and pilot | 128 |
| - Number of bits for Pilot bits | 4 bits |
| - Fixed or Flexible Position | Fixed |
| - TFCI existence | FALSE |
| - Downlink DPCH Offset Value | 0 |

HANDOVER TO UTRAN COMMAND

| Information Element | Value/remark |
| --- | --- |
| RR management Protocol Discriminator | ‘0110’B |
| Skip Indicator | ‘0000’B |
| Inter System to UTRAN Handover Command Message Type | ‘01100011’B |
| Handover to UTRAN Command IEI | TBD |
| Length of Handover to UTRAN Command contents | Octet length of the “Handover to UTRAN Command value part” |
| Handover to UTRAN Command value part | PER encoded ASN.1 value of type “HandoverToUTRANCommand-v1-IEs”, the content is presented in the next table. |

Content of “HandoverToUTRANCommand-v1-IEs”

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI |  |
| - SRNC Identiy | ‘000000000001’B |
| - S-RNTI-2 | 1 |
| Activation time | now |
| Ciphering algorithm | Standard UMTS Encryption Algorithm UEA1 |
| RAB Info |  |
| - RAB identity |  |
| - GSM-MAP RAB identity | ‘00000001’B |
| - CN domain identity | CS domain |
| CHOICE Specification mode | Preconfiguration |
| - Predefined configuration identity | 1 |
| - CHOICE Mode specific info | FDD |
| - uplink DPCH info |  |
| - uplink DPCH power control info |  |
| - Power control algorithm1 | 1 |
| - Scrambling code type | long |
| - Reduced scrambling code number | 0 |
| - Spreading factor | 128 |
| - DL common information post |  |
| - DL DPCH info common |  |
| - Timing indication | initialize |
| - CFN target SFN frame offset | Not present |
| - DL DPCH power control info |  |
| - CHOICE Mode specific info | FDD |
| - DPC mode | Single TPC |
| - DL information perRL list |  |
| - Premary CPICH info |  |
| - Primary scrambling code | 100 |
| - DL DPCH info perRL |  |
| - pCPICH usage for channelEst | May be used |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - SF and code number | SF = 128, code number = 127 |
| - Scrambling code change | No code change |
| - TPC combination index | 0 |
| - Frequency info |  |
| - UARFCN uplink(Nu) | See PIXIT |
| - UARFCN downlink(Nd) | See PIXIT |
| Maximum allowed uplink TX power | 33dBm |

8.3.6.1.5	Test requirement

After step 7 the ongoing call shall be continued on UTRAN cell.

#### 8.3.6.2	Inter system handover to UTRAN/From GSM/Data/Same data rate/Success

8.3.6.2.1	Definition

8.3.6.2.2	Conformance requirement

The UE shall be able to receive a HANDOVER TO UTRAN COMMAND message from GSM and perform an inter-system handover, even if no prior UE measurements have been performed on the target UTRAN cell and/or frequency.

If the UE succeeds to establish the connection to UTRAN, it shall transmit a HANDOVER TO UTRAN COMPLETE message on the uplink DCCH.

Reference(s)

TS 25.331 Clause 8.3.6.

TS 04.18 Clause 3.4.4a.

8.3.6.2.3	Test purpose

To test that the UE handovers to the indicated UTRAN target cell and the data rate of the target channel is the same as the old channel when it is in the data call active state in the GSM serving cell and receives a HANDOVER TO UTRAN COMMAND.

8.3.6.2.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is GSM,  Cell 2 is UTRAN. GSM 11.10-1 section 26.6.5.1 or section 26.13.1.3 (for HSCSD) shall be referenced for the default parameters of cell 1.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN Streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports UTRAN Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports UTRAN Streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports GSM 14.4 kbps data (HSCSD or full rate traffic channel for 14.4 kbit/s user data (TCH/F14.4)),

UE supports GSM 28.8 kbps data (HSCSD or full rate traffic channel for 28.8 kbit/s user data (E-TCH/F28.8)),

UE supports GSM 57.6 kbps data,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the GSM cell and the UTRAN cell, the cell selection conditions of these two cells are in favour of GSM cell. The UE selects the GSM cell for camping on. After the UE receives and stores pre-configuration information from SIB16 broadcast in the UTRAN cell, the SS brings the UE into the call active state (CC state U10) with 14.4 kbps CS data call (for execution counter M = 1). The SS configures a dedicated channel corresponding to the pre-configuration (streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS for M = 1) in UTRAN cell, then sends HANDOVER TO UTRAN COMMAND indicating the dedicated channel of the target cell to the UE through the GSM serving cell. After the UE receives the command it shall configure itself accordingly and switch to the dedicated channel of the UTRAN cell. The SS checks whether the handover is performed by checking that the UE transmits HANDOVER TO UTRAN COMPLETE to the SS through DCCH of the UTRAN cell.

Depending on the PIXIT parameters, the above procedure is executed maximum three times, each time for different initial conditions:

-	If the UE supports GSM 14.4 kbps CS data and UTRAN streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs, the procedure is executed for execution counter M = 1;

-	If the UE supports GSM 28.8 kbps CS data and UTRAN streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs, the procedure is executed for execution counter M = 2;

-	If the UE supports GSM 57.6 kbps CS data and UTRAN streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs, the procedure is executed for execution counter M = 3;

Expected sequence

This sequence is performed for a maximum execution counter M = 1, 2, 3, depending on the PIXIT parameters.

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | SS |  | The SS configures GSM and UTRAN cells, the UTRAN cell broadcasts SIB16 containing pre-configuration information: For M = 1: (streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 2: (streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 3: (streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs). UE camps on GSM cell and received SIB16 from UTRAN cell. |
| 2 | UE |  | The SS bring the UE into GSM U10 state in cell 1 and for M = 1: the UE is in GSM 14.4 kbps CS data call; for M = 2: the UE is in GSM 28.8 kbps CS data call; for M = 3: the UE is in GSM 57.6 kbps CS data call; |
| 3 | SS |  | The SS configures a dedicated channel in the UTRAN cell with the configuration: For M = 1: (streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 2: (streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 3: (streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs) |
| 4 | ( | HANDOVER TO UTRAN COMMAND | Send on cell 1 (GSM cell) |
| 5 | UE |  | The UE accepts the handover command and configures its lower layers using the parameters contained in the HANDOVER TO UTRAN COMMAND |
| 6 | SS |  | The SS waits for uplink physical channel in synchronization |
| 7 | ( | HANDOVER TO UTRAN COMPLETE | The SS receives this message on DCCH of cell 2 (UTRAN cell). It implies that the down link physical channel has synchronised with UTRAN. |

Specific message contents

For execution1 (M = 1):

Content of “SysInfoType16”

| Information Element | Value/remark |
| --- | --- |
| re-EstablishmentTimer T315 | 30 s |
| PredefinedRB_Configuration |  |
| - SRB information list |  |
| - RB identity | 1 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | UM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - CHOICE DL RLC mode | UM RLC mode |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 1 |
| - RB identity | 2 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - MAC logical channel priority | 2 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - RB identity | 3 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 3 |
| - MAC logical channel priority | 3 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 3 |
| - RB identity | 4 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 4 |
| - MAC logical channel priority | 4 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 4 |
| - RB information list |  |
| - RB information to setup |  |
| - RB identity | 10 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 2 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 2 |
| - Logical channel identity | 1 |
| preDefTransChConfiguration |  |
| - uplink Common Transport channel Info |  |
| - TFC subset |  |
| - Allowed Transport Format combination | 0, 1, 2, 3 |
| - CHOICE Mode specific info | FDD |
| - CHOICE uplink DCH TFCS | Normal signalling |
| - CHOICE Normal signalling | Addition |
| - CHOICE CTFC Size | 2 bits |
| - CTFC information | 0 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 1 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 2 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 3 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - uplink Add or reconfigured transport channel info list |  |
| - Transport channel identity | 2 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 576 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 40 ms |
| - Type of channel coding | Turbo coding |
| - Rate matching attribute | 145-185 |
| - CRC size | 16 bits |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 148 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 148 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 40 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 155-165 |
| - CRC size | 16 bits |
| - DL Common transport channel info |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE Mode specific info | FDD |
| - CHOICE TFCS Signalling mode | Same as uplink |
| - Added or reconfigured DL TrCH info list |  |
| - Transport channel identity | 2 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 2 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| PreDefPhyChConfiguration |  |
| -uplink_DPCH_InfoPredef |  |
| - uplink DPCH Info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 15 slots |
| - CHOICE Mode specific info | FDD |
| - TFCI existence | TRUE |
| - Puncturing Limit | 1 |
| - DL_ CommonInformationPredef |  |
| - DL_DPCH_InfoCommon |  |
| - Timing indication | initialize |
| - CHOICE Mode specific info | FDD |
| - Spreading factor and pilot | 128 |
| - Number of bits for Pilot bits | 8 bits |
| - Fixed or Flexible Position | Fixed |
| - TFCI existence | FALSE |
| - Downlink DPCH Offset Value | 0 |

HANDOVER TO UTRAN COMMAND

| Information Element | Value/remark |
| --- | --- |
| RR management Protocol Discriminator | ‘0110’B |
| Skip Indicator | ‘0000’B |
| Inter System to UTRAN Handover Command Message Type | ‘01100011’B |
| Handover to UTRAN Command IEI | TBD |
| Length of Handover to UTRAN Command contents | Octet length of the “Handover to UTRAN Command value part” |
| Handover to UTRAN Command value part | PER encoded ASN.1 value of type “HandoverToUTRANCommand-v1-IEs”, the content is presented in the next table. |

Content of “HandoverToUTRANCommand-v1-IEs”

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI |  |
| - SRNC Identiy | ‘000000000001’B |
| - S-RNTI-2 | 1 |
| Activation time | now |
| Ciphering algorithm | Standard UMTS Encryption Algorithm UEA1 |
| RAB Info |  |
| - RAB identity |  |
| - GSM-MAP RAB identity | ‘00000001’B |
| - CN domain identity | CS domain |
| CHOICE Specification mode | Preconfiguration |
| - Predefined configuration identity | 1 |
| - CHOICE Mode specific info | FDD |
| - uplink DPCH info |  |
| - uplink DPCH power control info |  |
| - Power control algorithm1 | 1 |
| - Scrambling code type | long |
| - Reduced scrambling code number | 0 |
| - Spreading factor | 64 |
| - DL common information post |  |
| - DL DPCH info common |  |
| - Timing indication | initialize |
| - CFN target SFN frame offset | Not present |
| - DL DPCH power control info |  |
| - CHOICE Mode specific info | FDD |
| - DPC mode | Single TPC |
| - DL information perRL list |  |
| - Premary CPICH info |  |
| - Primary scrambling code | 100 |
| - DL DPCH info perRL |  |
| - pCPICH usage for channelEst | May be used |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - SF and code number | SF = 128, code number = 127 |
| - Scrambling code change | No code change |
| - TPC combination index | 0 |
| - Frequency info |  |
| - UARFCN uplink(Nu) | See PIXIT |
| - UARFCN downlink(Nd) | See PIXIT |
| Maximum allowed uplink TX power | 33dBm |

For execution2 (M = 2):

Content of “SysInfoType16” same as for M=1 except:

| Information Element | Value/remark |
| --- | --- |
| preDefTransChConfiguration |  |
| - uplink Common Transport channel Info |  |
| - TFC subset |  |
| - Allowed Transport Format combination | 0, 1, 2, 3, 4, 5 |
| - CHOICE Mode specific info | FDD |
| - CHOICE uplink DCH TFCS | Normal signalling |
| - CHOICE Normal signalling | Addition |
| - CHOICE CTFC Size | 4 bits |
| - CTFC information | 0 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 1 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 2 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 3 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 4 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 5 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - uplink Add or reconfigured transport channel info list |  |
| - Transport channel identity | 2 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 2 |
| - RLC size | 576 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 40 ms |
| - Type of channel coding | Turbo coding |
| - Rate matching attribute | 135-175 |
| - CRC size | 16 bits |
| PreDefPhyChConfiguration |  |
| -uplink_DPCH_InfoPredef |  |
| - uplink DPCH Info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 15 slots |
| - CHOICE Mode specific info | FDD |
| - TFCI existence | TRUE |
| - Puncturing Limit | 1 |
| - DL_ CommonInformationPredef |  |
| - DL_DPCH_InfoCommon |  |
| - Timing indication | initialize |
| - CHOICE Mode specific info | FDD |
| - Spreading factor and pilot | 64 |
| - Number of bits for Pilot bits | 8 bits |
| - Fixed or Flexible Position | Fixed |
| - TFCI existence | FALSE |
| - Downlink DPCH Offset Value | 0 |

HANDOVER TO UTRAN COMMAND

| Information Element | Value/remark |
| --- | --- |
| RR management Protocol Discriminator | ‘0110’B |
| Skip Indicator | ‘0000’B |
| Inter System to UTRAN Handover Command Message Type | ‘01100011’B |
| Handover to UTRAN Command IEI | TBD |
| Length of Handover to UTRAN Command contents | Octet length of the “Handover to UTRAN Command value part” |
| Handover to UTRAN Command value part | PER encoded ASN.1 value of type “HandoverToUTRANCommand-v1-IEs”, the content is presented in the next table. |

Content of “HandoverToUtranCommand-v1-IEs”

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI |  |
| - SRNC Identiy | ‘000000000001’B |
| - S-RNTI-2 | 1 |
| Activation time | now |
| Ciphering algorithm | Standard UMTS Encryption Algorithm UEA1 |
| RAB Info |  |
| - RAB identity |  |
| - GSM-MAP RAB identity | ‘00000001’B |
| - CN domain identity | CS domain |
| CHOICE Specification mode | Preconfiguration |
| - Predefined configuration identity | 1 |
| - CHOICE Mode specific info | FDD |
| - uplink DPCH info |  |
| - uplink DPCH power control info |  |
| - Power control algorithm1 | 1 |
| - Scrambling code type | long |
| - Reduced scrambling code number | 0 |
| - Spreading factor | 32 |
| - DL common information post |  |
| - DL DPCH info common |  |
| - Timing indication | initialize |
| - CFN target SFN frame offset | Not present |
| - DL DPCH power control info |  |
| - CHOICE Mode specific info | FDD |
| - DPC mode | Single TPC |
| - DL information perRL list |  |
| - Premary CPICH info |  |
| - Primary scrambling code | 100 |
| - DL DPCH info perRL |  |
| - pCPICH usage for channelEst | May be used |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - SF and code number | SF = 64, code number = 63 |
| - Scrambling code change | No code change |
| - TPC combination index | 0 |
| - Frequency info |  |
| - UARFCN uplink(Nu) | See PIXIT |
| - UARFCN downlink(Nd) | See PIXIT |
| Maximum allowed uplink TX power | 33dBm |

For execution3 (M = 3):

Content of “SysInfoType16” same as for M=1 except:

| Information Element | Value/remark |
| --- | --- |
| preDefTransChConfiguration |  |
| - uplink Common Transport channel Info |  |
| - TFC subset |  |
| - Allowed Transport Format combination | 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 |
| - CHOICE Mode specific info | FDD |
| - CHOICE uplink DCH TFCS | Normal signalling |
| - CHOICE Normal signalling | Addition |
| - CHOICE CTFC Size | 4 bits |
| - CTFC information | 0 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 1 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 2 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 3 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 4 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 5 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 6 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 7 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 8 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 9 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - uplink Add or reconfigured transport channel info list |  |
| - Transport channel identity | 2 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 2 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 3 |
| - RLC size | 576 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 4 |
| - RLC size | 576 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 40 ms |
| - Type of channel coding | Turbo coding |
| - Rate matching attribute | 125-165 |
| - CRC size | 16 bits |
| PreDefPhyChConfiguration |  |
| -uplink_DPCH_InfoPredef |  |
| - uplink DPCH Info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 15 slots |
| - CHOICE Mode specific info | FDD |
| - TFCI existence | TRUE |
| - Puncturing Limit | 1 |
| - DL_ CommonInformationPredef |  |
| - DL_DPCH_InfoCommon |  |
| - Timing indication | initialize |
| - CHOICE Mode specific info | FDD |
| - Spreading factor and pilot | 32 |
| - Number of bits for Pilot bits | 8 bits |
| - Fixed or Flexible Position | Fixed |
| - TFCI existence | FALSE |
| - Downlink DPCH Offset Value | 0 |

HANDOVER TO UTRAN COMMAND

| Information Element | Value/remark |
| --- | --- |
| RR management Protocol Discriminator | ‘0110’B |
| Skip Indicator | ‘0000’B |
| Inter System to UTRAN Handover Command Message Type | ‘01100011’B |
| Handover to UTRAN Command IEI | TBD |
| Length of Handover to UTRAN Command contents | Octet length of the “Handover to UTRAN Command value part” |
| Handover to UTRAN Command value part | PER encoded ASN.1 value of type “HandoverToUTRANCommand-v1-IEs”, the content is presented in the next table. |

Content of “HandoverToUTRANCommand-v1-IEs”

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI |  |
| - SRNC Identiy | ‘000000000001’B |
| - S-RNTI-2 | 1 |
| Activation time | now |
| Ciphering algorithm | Standard UMTS Encryption Algorithm UEA1 |
| RAB Info |  |
| - RAB identity |  |
| - GSM-MAP RAB identity | ‘00000001’B |
| - CN domain identity | CS domain |
| CHOICE Specification mode | Preconfiguration |
| - Predefined configuration identity | 1 |
| - CHOICE Mode specific info | FDD |
| - uplink DPCH info |  |
| - uplink DPCH power control info |  |
| - Power control algorithm1 | 1 |
| - Scrambling code type | long |
| - Reduced scrambling code number | 0 |
| - Spreading factor | 16 |
| - DL common information post |  |
| - DL DPCH info common |  |
| - Timing indication | initialize |
| - CFN target SFN frame offset | Not present |
| - DL DPCH power control info |  |
| - CHOICE Mode specific info | FDD |
| - DPC mode | Single TPC |
| - DL information perRL list |  |
| - Premary CPICH info |  |
| - Primary scrambling code | 100 |
| - DL DPCH info perRL |  |
| - pCPICH usage for channelEst | May be used |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - SF and code number | SF = 32, code number = 31 |
| - Scrambling code change | No code change |
| - TPC combination index | 0 |
| - Frequency info |  |
| - UARFCN uplink(Nu) | See PIXIT |
| - UARFCN downlink(Nd) | See PIXIT |
| Maximum allowed uplink TX power | 33dBm |

8.3.6.2.5	Test requirement

After step 7 the ongoing call shall be continued on UTRAN cell.

#### 8.3.6.3	Inter system handover to UTRAN/From GSM/Data/Data rate upgrading/Success

8.3.6.3.1	Definition

8.3.6.3.2	Conformance requirement

The UE shall be able to receive a HANDOVER TO UTRAN COMMAND message from GSM and perform an inter-system handover, even if no prior UE measurements have been performed on the target UTRAN cell and/or frequency.

If the UE succeeds to establish the connection to UTRAN, it shall transmit a HANDOVER TO UTRAN COMPLETE message on the uplink DCCH.

Reference(s)

TS 25.331 Clause 8.3.6.

TS 04.18 Clause 3.4.4a.

8.3.6.3.3	Test purpose

To test that the UE being in the data call active state handovers from the GSM serving cell to the indicated channel of  a higher data rate in the UTRAN target cell after it receives a HANDOVER TO UTRAN COMMAND.

8.3.6.3.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is GSM,  Cell 2 is UTRAN. GSM 11.10-1 section 26.6.5.1 or section 26.13.1.3(for HSCSD) shall be referenced for the default parameters of cell 1.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports UTRAN Streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports GSM 14.4 kbps data (HSCSD or full rate traffic channel for 14.4 kbit/s user data (TCH/F14.4)),

UE supports GSM 28.8 kbps data (HSCSD or full rate traffic channel for 28.8 kbit/s user data (E-TCH/F28.8)),

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the GSM cell and the UTRAN cell with cell selection conditions in favour of GSM cell. In UTRAN cell SIB16 is broadcast. The UE selects the GSM cell and received the pre-configuration information from SIB16. Then the SS brings the UE into the call active state (CC state U10) with 14.4 kbps CS data call (for execution counter M = 1). The SS configures a dedicated channel corresponding to the pre-configuration (streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS for M = 1), then sends HANDOVER TO UTRAN COMMAND indicating the dedicated channel of the target cell to the UE through the GSM serving cell. After the UE receives the command it shall configure itself accordingly and switch to the new channel of the UTRAN cell. The SS checks whether the handover is performed by checking that the UE transmits HANDOVER TO UTRAN COMPLETE to the SS through DCCH of the UTRAN cell.

Depending on the PIXIT parameters, the above procedure is executed maximum three times, each time for different  conditions:

-	If the UE supports GSM 14.4 kbps CS data and UTRAN streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs, the procedure is executed for execution counter M = 1;

-	If the UE supports GSM 14.4 kbps CS data and UTRAN streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs, the procedure is executed for execution counter M = 2;

-	If the UE supports GSM 28.8 kbps CS data and UTRAN streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs, the procedure is executed for execution counter M = 3;

Expected sequence

This sequence is performed for a maximum execution counter M = 1, 2, 3, depending on the PIXIT parameters.

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | SS |  | The SS configures GSM and UTRAN cells, the UTRAN cell broadcasts SIB16 containing pre-configuration information: For M = 1: (streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 2: (streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 3: (streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs). UE camps on GSM cell and received SIB16 from UTRAN cell. |
| 2 | UE |  | The SS bring the UE into GSM U10 state in cell 1 and for M = 1: the UE is in GSM 14.4 kbps CS data call; for M = 2: the UE is in GSM 14.4 kbps CS data call; for M = 3: the UE is in GSM 28.8 kbps CS data call; |
| 3 | SS |  | The SS configures a dedicated channel in the UTRAN cell with the configuration: For M = 1: (streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 2: (streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs); For M = 3: (streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs) |
| 4 | ( | HANDOVER TO UTRAN COMMAND | Send on cell 1 (GSM cell) |
| 5 | UE |  | The UE accepts the handover command and configures its lower layers using the parameters contained in the HANDOVER TO UTRAN COMMAND |
| 6 | SS |  | The SS waits for uplink physical channel in synchronization |
| 7 | ( | HANDOVER TO UTRAN COMPLETE | The SS receives this message on DCCH of cell 2 (UTRAN cell). It implies that the down link physical channel has synchronised with UTRAN. |

Specific message contents

For execution1 (M = 1):

Same as the default message contents in clause 8.3.6.2 for M = 2.

For execution2 (M = 2):

Same as the default message contents in clause 8.3.6.2 for M = 3.

For execution3 (M = 3):

Same as the default message contents in clause 8.3.6.2 for M = 3.

8.3.6.3.5	Test requirement

After step 7 the ongoing call shall be continued on UTRAN cell.

#### 8.3.6.4	Inter system handover to UTRAN/From GSM/Speech/Establishment/Success

8.3.6.4.1	Definition

8.3.6.4.2	Conformance requirement

The UE shall be able to receive a HANDOVER TO UTRAN COMMAND message from GSM and perform an inter-system handover, even if no prior UE measurements have been performed on the target UTRAN cell and/or frequency.

If the UE succeeds to establish the connection to UTRAN, it shall transmit a HANDOVER TO UTRAN COMPLETE message on the uplink DCCH.

Reference(s)

TS 25.331 Clause 8.3.6.

TS 04.18 Clause 3.4.4a.

8.3.6.4.3	Test purpose

To test that the UE supporting both GSM and UTRAN handovers from the GSM serving cell to the indicated channel in UTRAN target cell when the UE is in the call establishment phase and receives a HANDOVER TO UTRAN COMMAND.

8.3.6.4.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is GSM,  Cell 2 is UTRAN. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 1.

UE : CC State U1 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN AMR,

UE supports GSM FR,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U1 on cell 2.

Test Procedure

The SS starts GSM cell and UTRAN cell with the cell selection conditions in favour of GSM cell. The UE selects the GSM cell. After the UE camps on the GSM cell and received SIB16 broadcast in the UTRAN cell, the UE is triggered to make an MO speech call. After the SS received SETUP message it configures a dedicated channel corresponding to the predefined configuration (conversationa/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) described by SIB16, then the SS sends HANDOVER TO UTRAN COMMAND indicating the dedicated channel to the UE through the GSM serving cell. After the UE receives the command and it shall configure itself accordingly and switch to the new channel of UTRAN cell. The SS checks whether the handover is performed by checking that the UE transmits HANDOVER TO UTRAN COMPLETE to the SS through DCCH of the UTRAN cell.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | SS |  | The SS configures GSM and UTRAN cells, UE camps on GSM cell and received SIB16 from UTRAN cell. |
| 2 | UE |  | To trigger UE to make an MO call |
| 3 | ( | CHANNEL REQUEST | initiate outgoing call |
| 4 | ( | IMMEDIATE ASSIGNMENT | SDCCH, U0 |
| 5 | ( | CM SERVICE REQUEST | U0.1 |
| 6 | ( | SETUP | U1 |
| 7 | SS |  | The SS configures a dedicated channel with the configuration: conversational/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs in UTRAN cell. |
| 8 | ( | HANDOVER TO UTRAN COMMAND | Send on cell 1 (GSM cell) |
| 9 | UE |  | The UE accepts the handover command and configures its lower layers using the parameters contained in the HANDOVER TO UTRAN COMMAND |
| 10 | SS |  | The SS waits for uplink physical channel in synchronization |
| 11 | ( | HANDOVER TO UTRAN COMPLETE | The SS receives this message on DCCH of cell 2 (UTRAN cell). It implies that the down link physical channel has synchronised with UTRAN. |

Specific message contents

Same as the default message contents in clause 8.3.6.1 for M = 1.

8.3.6.4.5	Test requirement

After step 11 the ongoing call shall be continued on UTRAN cell.

#### 8.3.6.5	Inter system handover to UTRAN/From GSM/Speech/Blind HO/Success

8.3.6.5.1	Definition

8.3.6.5.2	Conformance requirement

The UE shall be able to receive a HANDOVER TO UTRAN COMMAND message from GSM and perform an inter-system handover, even if no prior UE measurements have been performed on the target UTRAN cell and/or frequency.

If the UE succeeds to establish the connection to UTRAN, it shall transmit a HANDOVER TO UTRAN COMPLETE message on the uplink DCCH.

Reference(s)

TS 25.331 Clause 8.3.6.

TS 04.18 Clause 3.4.4a.

8.3.6.5.3	Test purpose

To test that the UE handovers from the GSM serving cell to the indicated channel of UTRAN target cell when it is in the speech call active state without any knowledge of  the target system (blind handover) and receives a HANDOVER TO UTRAN COMMAND.

8.3.6.5.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is GSM,  Cell 2 is UTRAN. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 1.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN AMR,

UE supports GSM FR,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the GSM cell and the UTRAN cell with cell selection conditions in favour of GSM cell, SIB16 is not broadcast in the UTRAN cell and the UE has no any predefined configuration stored. The UE selects the GSM cell. Then the SS brings the UE into the call active state (CC state U10) with FR speech. The SS configures a dedicated channel (conversationa/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS), then sends HANDOVER TO UTRAN COMMAND indicating the dedicated channel of the target cell to the UE through the GSM serving cell. After the UE receives the command it shall configure itself accordingly and switch to the dedicated channel of UTRAN cell. The SS checks whether the handover is performed by checking that the UE transmits HANDOVER TO UTRAN COMPLETE to the SS through DCCH of the UTRAN cell.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | UE |  | The SS bring the UE into GSM U10 state in cell 1 and the UE has no any pre-configuration information stored |
| 2 | SS |  | The SS configures dedicated channel with the configuration: conversational/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs in UTRAN cell. |
| 3 | ( | HANDOVER TO UTRAN COMMAND | Send on cell 1 (GSM cell) |
| 4 | UE |  | The UE accepts the handover command and configures its lower layers using the parameters contained in the HANDOVER TO UTRAN COMMAND |
| 5 | SS |  | The SS waits for uplink physical channel in synchronization |
| 6 | ( | HANDOVER TO UTRAN COMPLETE | The SS receives this message on DCCH of cell 2 (UTRAN cell). It implies that the down link physical channel has synchronised with UTRAN. |

Specific message contents

HANDOVER TO UTRAN COMMAND

| Information Element | Value/remark |
| --- | --- |
| RR management Protocol Discriminator | ‘0110’B |
| Skip Indicator | ‘0000’B |
| Inter System to UTRAN Handover Command Message Type | ‘01100011’B |
| Handover to UTRAN Command IEI | TBD |
| Length of Handover to UTRAN Command contents | Octet length of the “Handover to UTRAN Command value part” |
| Handover to UTRAN Command value part | PER encoded ASN.1 value of type “HandoverToUTRANCommand-v1-IEs”, content is presented in the next table. |

Content of “HandoverToUTRANCommand-v1-IEs”

| Information Element | Value/remark |
| --- | --- |
| New U-RNTI |  |
| - SRNC Identiy | ‘000000000001’B |
| - S-RNTI-2 | 1 |
| Activation time | now |
| Ciphering algorithm | Standard UMTS Encryption Algorithm UEA1 |
| RAB Info |  |
| - RAB identity |  |
| - GSM-MAP RAB identity | ‘00000001’B |
| - CN domain identity | CS domain |
| CHOICE Specification mode | complete |
| - re-Establishment timer | 1800 seconds |
| - SRB information setup list |  |
| - RB identity | 1 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | UM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - CHOICE DL RLC mode | UM RLC mode |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 1 |
| - RB identity | 2 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - MAC logical channel priority | 2 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - RB identity | 3 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 3 |
| - MAC logical channel priority | 3 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 3 |
| - RB identity | 4 |
| - CHOICE RLC info choice | RLC info |
| - CHOICE uplink RLC mode | AM RLC mode |
| - Transmission RLC discard | MaxDAT retransmissions |
| - Max_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - transmission window size | 8 |
| - Timer_RST | 500 |
| - MAX_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll windows | 99 |
| - CHOICE DL RLC mode | AM RLC mode |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 4 |
| - MAC logical channel priority | 4 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping |  |
| - DL transport channel type | DCH |
| - Transport channel identity | 1 |
| - Logical channel identity | 4 |
| - RB information setup list |  |
| - RB information to setup |  |
| - RB identity | 10 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 2 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 2 |
| - Logical channel identity | 1 |
| - RB information to setup |  |
| - RB identity | 11 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 3 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 3 |
| - Logical channel identity | 1 |
| - RB information to setup |  |
| - RB identity | 12 |
| - PDCP info | Not Present |
| - RLC info |  |
| - CHOICE Uplink RLC mode | TM RLC mode |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC mode |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - CHOICE uplink logical channel mappings | One logical channel |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 4 |
| - Logical channel identity | 1 |
| - MAC logical channel priority | 1 |
| - Logical channel max loss | 0 |
| - DL logical channel mapping | 1 |
| - Downlink transport channel type | DCH |
| - Transport channel identity | 4 |
| - Logical channel identity | 1 |
| - uplink Common Transport channel Info |  |
| - TFC subset |  |
| - Allowed Transport Format combination | 0, 1, 2, 3, 4, 5 |
| - CHOICE Mode specific info | FDD |
| - CHOICE uplink DCH TFCS | Normal signalling |
| - CHOICE Normal signalling | Addition |
| - CHOICE CTFC Size | 6 bits |
| - CTFC information | 0 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 1 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 11 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 12 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 13 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - CTFC information | 23 |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor ßc | 0 |
| - Gain factor ßd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| - uplink Add or reconfigured transport channel info list |  |
| - Transport channel identity | 2 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 81 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 39 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 81 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 20 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 180-220 |
| - CRC size | 12 bits |
| - Transport channel identity | 3 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 103 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 103 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 20 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 170-210 |
| - CRC size | N/A |
| - Transport channel identity | 4 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 60 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 60 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 20 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/2 |
| - Rate matching attribute | 215-256 |
| - CRC size | N/A |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 0 |
| - RLC size | 148 |
| - Dynamic Transport format information |  |
| - Number of Transport blocks | 1 |
| - RLC size | 148 |
| - Semi-static Transport Format information |  |
| - Transmission time interval | 40 ms |
| - Type of channel coding | convolutional |
| - Coding Rate | 1/3 |
| - Rate matching attribute | 155-165 |
| - CRC size | 16 bits |
| - DL Common transport channel info |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE Mode specific info | FDD |
| - CHOICE TFCS Signalling mode | Same as uplink |
| - Added or reconfigured DL TrCH info list |  |
| - Transport channel identity | 2 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 2 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| - Addide or reconfigured DL TrCH info list |  |
| - Transport channel identity | 3 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 3 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| - Added or reconfigured DL TrCH info list |  |
| - Transport channel identity | 4 |
| - CHOICE TFS signalling mode | SameAsUL |
| - uplink TrCH Identity | 4 |
| - DCH quality target |  |
| - BLER Quality value | 0 |
| - Transparent mode signalling info | Not Present |
| - uplink DPCH Info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 15 slots |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - CHOICE Mode specific info | FDD |
| - Scrambling code type | Long |
| - Scrambling code number | 0 |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | 64 |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | 0.88 |
| - CHOICE Mode specific info | FDD |
| - DL PDSCH information | Not present |
| - CPCH SET info | Not present |
| - Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indication | initialize |
| - CFN target SFN frame offset | Not present |
| - CHOICE Mode specific info | FDD |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - Spreading factor and pilot | 128 |
| - Number of bits for Pilot bits | 4 bits |
| - Fixed or Flexible Position | Fixed |
| - TFCI existence | FALSE |
| - Downlink DPCH Offset Value | 0 |
| - DPCH compressed mode info |  |
| -TGPSI | 1 |
| -TGPS Status Flag | Inactive |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - uplink/DL Mode | DL |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - S field |  |
| - DL information perRL list |  |
| - Premary CPICH info |  |
| - Primary scrambling code | 100 |
| - DL DPCH info perRL |  |
| - pCPICH usage for channelEst | May be used |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - SF and code number | SF = 128, code number = 127 |
| - Scrambling code change | No code change |
| - TPC combination index | 0 |
| - Frequency info |  |
| - UARFCN uplink | See PIXIT |
| - UARFCN downlink | See PIXIT |
| - Maximum allowed uplink transmission power | 33 dbm |

8.3.6.5.5	Test requirement

At step 6 the HANDOVER TO UTRAN COMPLETE shall be received on UTRAN cell.

#### 8.3.6.6	Inter system handover to UTRAN/From GSM/Speech/Failure

8.3.6.6.1	Definition

8.3.6.6.2	Conformance requirement

The UE shall be able to receive a HANDOVER TO UTRAN COMMAND message from GSM and perform an inter-system handover, even if no prior UE measurements have been performed on the target UTRAN cell and/or frequency.

If the UE can not establish the connection to UTRAN, it shall reactivate the old channel and transmit a HANDOVER FAILURE message on the old channel.

Reference(s)

TS 25.331 Clause 8.3.6.

TS 04.18 Clause 3.4.4a.

8.3.6.6.3	Test purpose

To test that the UE reactivates the old channel and transmits HANDOVER FAILURE message to the network on the old channel in the GSM cell when it received HANDOVER TO UTRAN COMMAND and the handover to UTRAN failed.

8.3.6.6.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is GSM,  Cell 2 is UTRAN. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 1.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN AMR,

UE supports GSM RF,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 1.

Test Procedure

The SS starts the GSM cell and the UTRAN cell with cell selection conditions in favour of GSM cell. SIB16 is broadcast in UTRAN cell. The UE selects the GSM cell, and received the SIB16. Then the SS brings the UE into the call active state (CC state U10) with FR speech call. The SS does not configure the dedicated channel corresponding to the predefined configuration described in SIB16 (conversationa/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS), then sends HANDOVER TO UTRAN COMMAND indicating the dedicated channel of the target cell to the UE through the GSM serving cell. The UE will not be able to establish the connection to UTRAN. The SS checks that the handover is failed by checking that the UE returns to the old channel and transmits HANDOVER FAILURE to the SS through the old channel.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | SS |  | The SS starts GSM and UTRAN cells, SIB16 is broadcast in the UTRAN cell. The UE camps on GSM cell and received SIB16. |
| 2 | UE |  | The SS bring the UE into GSM U10 state in cell 1 |
| 3 | SS |  | There is no dedicated channel with the configuration: conversational/speech/uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBs in UTRAN cell. |
| 4 | ( | HANDOVER TO UTRAN COMMAND | Send on cell 1 (GSM cell) |
| 5 | UE |  | The UE accepts the handover command and configures its lower layers using the parameters contained in the HANDOVER TO UTRAN COMMAND |
| 6 | UE |  | The UE fails to establish a connection to UTRAN cell |
| 7 | ( | HANDOVER FAILURE | The SS receives this message on DCCH of cell 1 (old channel in GSM cell) |

Specific message contents

Same as the specific message contents in clause 8.3.6.1 for M = 1.

8.3.6.6.5	Test requirement

At step 7 the HANDOVER FAILURE shall be received on GSM cell.

### 8.3.7	Inter-system hard handover from UTRAN to GSM

Clauses 8.3.7 contains test procedures to be used for executing Inter-system Handover from UTRAN to GSM tests. Table 8.3.7-1 contains a summary of the different combinations of parameters being tested, together with a reference to the appropriate generic test procedure. If a test uses a parameter which the UE under test does not support, the test shall be skipped. Test cases in this clause are applicable only to the UE supporting both UTRAN and GSM. The test USIM shall support service 27 to carry out these test cases.

Table 8.3.7-1

| From | To | State of call | Ref. clause | Exec counter | Remark |
| --- | --- | --- | --- | --- | --- |
| UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | GSM AMR | U10 | 8.3.7.1 | 1 | call active state |
| UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | GSM EFR | U10 | 8.3.7.1 | 2 | call active state |
| UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | GSM FR | U10 | 8.3.7.1 | 3 | call active state |
| UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | GSM HR | U10 | 8.3.7.1 | 4 | call active state |
| UTRAN (Streaming/unknown/ uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | GSM 14.4 kbps CS data | U10 | 8.3.7.2 | 1 | Same data rate |
| UTRAN (Streaming/unknown/ uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | GSM 28.8 kbps CS data | U10 | 8.3.7.2 | 2 | Same data rate |
| UTRAN (Streaming/unknown/ uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | GSM 57.6 kbps CS data | U10 | 8.3.7.2 | 3 | Same data rate |
| UTRAN (Streaming/unknown/ uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | GSM 14.4 kbps CS data | U10 | 8.3.7.3 | 1 | Data rate down grading |
| UTRAN (Streaming/unknown/ uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | GSM 14.4 kbps CS data | U10 | 8.3.7.3 | 2 | Data rate down grading |
| UTRAN (Streaming/unknown/ uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBS) | GSM 28.8 kbps CS data | U10 | 8.3.7.3 | 3 | Data rate down grading |
| UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | GSM FR | U1 | 8.3.7.4 | 1 | During call establishment |
| UTRAN AMR (conversational/speech/ uplink:12.2 DL:12.2 kbps/CS RAB + uplink:3.4 DL3.4 kbps SRBS) | GSM FR | U10 | 8.3.7.5 | 1 | failure case |

#### 8.3.7.1	Inter system handover from UTRAN/To GSM/Speech/Success

8.3.7.1.1	Definition

8.3.7.1.2	Conformance requirement

When the UE receives an INTER-SYSTEM HANDOVER COMMAND message from UTRAN the UE shall take the following actions:

-	Establish the connection to the other radio access system, by using the contents of the IE "Inter system message". This IE contains candidate/ target cell identifier(s) and radio parameters relevant for the other radio access system.

-	For each IE "Remaining radio access bearer", associate the radio access bearer given by the IE "RAB info" to the radio resources in the target system given by the IE "Inter system message". Other information for making the association may be included in the IE "Inter system message" and requirements may be stated in the specifications relevant for the target system [FFS].

-	Switch the current connection to the other radio access system.

NOTE 1:	Requirements concerning the establishment of the radio connection towards the other radio access system and the signalling procedure are outside the scope of this specification.

NOTE 2:	The release of the UMTS radio resources is initiated by the other system.

NOTE 3:	Currently only one radio access bearer can be associated with the IE "Inter-system message", and this association is limited to the radio access bearers in the CS domain. It is assumed that all the radio access bearers in the PS domain, if any, remain after the handover.

Reference(s)

TS 25.331 Clause 8.3.7.3.

8.3.7.1.3	Test purpose

To test that the UE supporting both GSM and UTRAN handovers from a UTRAN serving cell to the indicated channel of GSM target cell when the UE is in the speech call active state and receives an INTER-SYSTEM HANDOVER COMMAND.

8.3.7.1.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is UTRAN,  Cell 2 is GSM. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 2.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports GSM ARM,

UE supports GSM EFR,

UE supports GSM HR,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the UTRAN cell and brings the UE into call active state (CC state U10) with AMR. The SS starts GSM cell and configures a traffic channel, then sends INTER-SYSTEM HANDOVER COMMAND indicating the traffic channel of the target GSM cell to the UE through DCCH of the serving UTRAN cell. After the UE receives the command it shall configure itself accordingly and switch to the new channel of the UTRAN cell. The SS checks whether the handover is performed by checking that the UE transmits the HANDOVER COMPLETE message to the SS through GSM cell.

Depending on the PIXIT parameters the above procedure is executed maximum four times, each time with different target channel in the GSM cell.

Expected sequence

This sequence is performed for a maximum execution counter M = 1, 2, 3, 4, depending on the PIXIT parameters.

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | UE |  | The SS bring the UE into UTRAN U10 state in cell 1 |
| 2 | SS |  | The SS configures cell 2 as a GSM cell with a traffic channel: for GSM AMR (M = 1); or for GSM EFR (M = 2); or for GSM FR (M = 3); or for GSM HR (M = 4). |
| 3 | ( | InterSystemHandoverCommand-GSM | Send on cell 1 (UTRAN cell) and the message indicates: the target channel for GSM AMR (M = 1); or the target channel for GSM EFR (M = 2); or the target channel for GSM FR (M = 3); or the target channel for GSM HR (M = 4). |
| 4 | UE |  | The UE accepts the handover command and switches to the GSM traffic channel specified in the InterSystemHandoverCommand-GSM |
| 5 | ( | HANDOVER ACCESS | The SS receives this burst on the traffic channel of cell 2 (GSM cell) It implies that the UE has switched to GSM cell. |
| 6 | ( | HANDOVER ACCESS |  |
| 7 | ( | HANDOVER ACCESS |  |
| 8 | ( | HANDOVER ACCESS |  |
| 9 | ( | PHYSICAL INFORMATION |  |
| 10 | ( | SABM |  |
| 11 | ( | UA |  |
| 12 | ( | HANDOVER COMPLETE | The SS receives the message on the traffic channel of GSM cell. |

Specific message contents

For execution:

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 2 in clause 26.6.5.1 of GSM 11.10-1, Release 1999, except that the CHANNEL MODE IE is included with value = speech full rate or half rate version 3

For execution 2:

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 2 in clause 26.6.5.1 of GSM 11.10-1, Release 1999, except that the CHANNEL MODE IE is included with value = speech full rate or half rate version 2

For execution 3:

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 2 in clause 26.6.5.1 of GSM 11.10-1, Release 1999, except that the CHANNEL MODE IE is included with value = speech full rate or half rate version 1

For execution 4:

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 4 in clause 26.6.5.1 of GSM 11.10-1 version 8.2.0 Release 1999, except that the CHANNEL MODE IE is included with value = speech full rate or half rate version 1

8.3.7.1.5	Test requirement

After step 12 the ongoing call shall be continued on the GSM cell.

#### 8.3.7.2	Inter system handover from UTRAN/To GSM/Data/Same data rate/Success

8.3.7.2.1	Definition

8.3.7.2.2	Conformance requirement

When the UE receives an INTER-SYSTEM HANDOVER COMMAND message from UTRAN the UE shall take the following actions:

-	Establish the connection to the other radio access system, by using the contents of the IE "Inter system message". This IE contains candidate/ target cell identifier(s) and radio parameters relevant for the other radio access system.

-	For each IE "Remaining radio access bearer", associate the radio access bearer given by the IE "RAB info" to the radio resources in the target system given by the IE "Inter system message". Other information for making the association may be included in the IE "Inter system message" and requirements may be stated in the specifications relevant for the target system [FFS].

-	Switch the current connection to the other radio access system.

NOTE 1:	Requirements concerning the establishment of the radio connection towards the other radio access system and the signalling procedure are outside the scope of this specification.

NOTE 2:	The release of the UMTS radio resources is initiated by the other system.

NOTE 3:	Currently only one radio access bearer can be associated with the IE "Inter-system message", and this association is limited to the radio access bearers in the CS domain. It is assumed that all the radio access bearers in the PS domain, if any, remain after the handover.

Reference(s)

TS 25.331 Clause 8.3.7.3.

8.3.7.2.3	Test purpose

To test that the UE handovers to the indicated channel of same data rate in the GSM target cell when it is in the data call active state in the UTRAN serving cell and receives an INTER-SYSTEM HANDOVER COMMAND.

8.3.7.2.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is UTRAN,  Cell 2 is GSM. GSM 11.10-1 section 26.6.5.1 or section 26.13.1.3 (for HSCSD) shall be referenced for the default parameters of cell 2.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN Streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports UTRAN Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports UTRAN Streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports GSM 14.4 kbps data (HSCSD or full rate traffic channel for 14.4 kbit/s user data (TCH/F14.4)),

UE supports GSM 28.8 kbps data (HSCSD or enhanced circuit switched full rate traffic channel for 28.8 kbit/s user date (E-TCH/F28.8)),

UE supports GSM 57.6 kbps data,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the UTRAN cell and brings the UE into data call active state (CC state U10) with a suitable configuration (e.g. Streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs for M = 1). The SS starts GSM cell and configures a traffic channel (e.g. 14.4 kbps data channel for M = 1), then sends INTER-SYSTEM HANDOVER COMMAND indicating the traffic channel of the target GSM cell to the UE through DCCH of the serving UTRAN cell. After the UE receives the command it shall configure itself accordingly and switch to the new channel of the GSM cell. The SS checks whether the handover is performed by checking that the UE transmits the HANDOVER COMPLETE message to the SS in GSM cell.

Depending on the PIXIT parameters the above procedure is executed maximum three times, each time with different target channel in the GSM cell.

Expected sequence

This sequence is performed for a maximum execution counter M = 1, 2, 3, depending on the PIXIT parameters.

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | UE |  | The SS bring the UE into UTRAN U10 state in cell 1, the configuration is: Streaming/unknown/uplink:14.4 DL:14.4 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs (for M = 1); Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs (for M = 2); Streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs (for M = 3). |
| 2 | SS |  | The SS configures cell 2 as a GSM cell with a traffic channel: for GSM 14.4 kbps data (M = 1); or for GSM 28.8 kbps data (M = 2); or for GSM 57.6 kbps data (M = 3). |
| 3 | ( | InterSystemHandoverCommand-GSM | Send on cell 1 (UTRAN cell) and the message indicates: the target channel for GSM 14.4 kbps data (M = 1); or for GSM 28.8 kbps data (M = 2); or for GSM 57.6 kbps data (M = 3). |
| 4 | UE |  | The UE accepts the handover command and switches to the GSM traffic channel specified in the InterSystemHandoverCommand-GSM |
| 5 | ( | HANDOVER ACCESS | The SS receives this burst on the traffic channel of cell 2 (GSM cell) It implies that the UE has switched to GSM cell. |
| 6 | ( | HANDOVER ACCESS |  |
| 7 | ( | HANDOVER ACCESS |  |
| 8 | ( | HANDOVER ACCESS |  |
| 9 | ( | PHYSICAL INFORMATION |  |
| 10 | ( | SABM |  |
| 11 | ( | UA |  |
| 12 | ( | HANDOVER COMPLETE | The SS receives the message on the traffic channel of GSM cell. |

Specific message contents

For execution :

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

If the UE supports 14.4 kbps single slot:

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 2 in clause 26.6.5.1 of GSM 11.10-1, Release 1999, except that the CHANNEL MODE IE is included with value = data, 14.5 kbit/s radio interface rate (14.4 kbit/s user data (TCH/F14.4))

If the UE supports HSCSD:

HANDOVER COMMAND

Same as the HANDOVER COMMAND in clause 26.13.3.1 of GSM 11.10-1, Release 1999, except that the Description of a multislot configuration supporting 14.4 kbps user data.

For execution 2:

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

If the UE supports enhanced circuit switched full rate traffic channel for 28.8 kbps user data:

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 2 in clause 26.6.5.1 of GSM 11.10-1, Release 1999, except that the CHANNEL MODE IE is included with value = data, 29.0 kbit/s radio interface rate (28.8 kbit/s user data (E-TCH/F28.8))

If the UE supports HSCSD:

HANDOVER COMMAND

Same as the HANDOVER COMMAND in clause 26.13.3.1 of GSM 11.10-1, Release 1999, except that the Description of a multislot configuration supporting 28.8 kbps user data.

For execution 3:

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

HANDOVER COMMAND

Same as the HANDOVER COMMAND in clause 26.13.3.1 of GSM 11.10-1, Release 1999, except that the Description of a multislot configuration supporting 57.6 kbps user data.

8.3.7.2.5	Test requirement

After step 12 the ongoing call shall be continued on the GSM cell.

#### 8.3.7.3	Inter system handover from UTRAN/To GSM/Data/Data rate down grading/Success

8.3.7.3.1	Definition

8.3.7.3.2	Conformance requirement

When the UE receives an INTER-SYSTEM HANDOVER COMMAND message from UTRAN the UE shall take the following actions:

-	Establish the connection to the other radio access system, by using the contents of the IE "Inter system message". This IE contains candidate/ target cell identifier(s) and radio parameters relevant for the other radio access system.

-	For each IE "Remaining radio access bearer", associate the radio access bearer given by the IE "RAB info" to the radio resources in the target system given by the IE "Inter system message". Other information for making the association may be included in the IE "Inter system message" and requirements may be stated in the specifications relevant for the target system [FFS].

-	Switch the current connection to the other radio access system.

NOTE 1:	Requirements concerning the establishment of the radio connection towards the other radio access system and the signalling procedure are outside the scope of this specification.

NOTE 2:	The release of the UMTS radio resources is initiated by the other system.

NOTE 3:	Currently only one radio access bearer can be associated with the IE "Inter-system message", and this association is limited to the radio access bearers in the CS domain. It is assumed that all the radio access bearers in the PS domain, if any, remain after the handover.

Reference(s)

TS 25.331 Clause 8.3.7.3.

8.3.7.3.3	Test purpose

To test that the UE handovers to the indicated channel of lower data rate in the GSM target cell when it is in the data call active state in the UTRAN serving cell and receives an INTER-SYSTEM HANDOVER COMMAND.

8.3.7.3.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is UTRAN,  Cell 2 is GSM. GSM 11.10-1 section 26.6.5.1 or section 26.13.1.3 (for HSCSD) shall be referenced for the default parameters of cell 2.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports UTRAN Streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs,

UE supports GSM 14.4 kbps data (HSCSD or full rate traffic channel for 14.4 kbit/s user data (TCH/F14.4)),

UE supports GSM 28.8 kbps data (HSCSD or enhanced circuit switched full rate traffic channel for 28.8 kbit/s user date (E-TCH/F28.8)),

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 2.

Test Procedure

The SS starts the UTRAN cell and brings the UE into data call active state (CC state U10) with a suitable configuration (e.g. Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs for M = 1). The SS starts GSM cell and configures a traffic channel (e.g. 14.4 kbps data channel for M = 1), then sends INTER-SYSTEM HANDOVER COMMAND indicating the traffic channel of the target GSM cell to the UE through DCCH of the serving UTRAN cell. After the UE receives the command it shall configure itself accordingly and switch to the new channel of the GSM cell. The SS checks whether the handover is performed by checking that the UE transmits the HANDOVER COMPLETE message to the SS in GSM cell.

Depending on the PIXIT parameters the above procedure is executed maximum three times, each time with different target channel in the GSM cell.

Expected sequence

This sequence is performed for a maximum execution counter M = 1, 2, 3, depending on the PIXIT parameters.

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | UE |  | The SS bring the UE into UTRAN U10 state in cell 1, the configuration is: Streaming/unknown/uplink:28.8 DL:28.8 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs (for M = 1); Streaming/unknown/uplink:57.6 DL:57.6 kbps/CS RAB + uplink:3.4 DL:3.4 kbps SRBs (for M = 2 and 3). |
| 2 | SS |  | The SS configures cell 2 as a GSM cell with a traffic channel: for GSM 14.4 kbps data (M = 1 and 2); or for GSM 28.8 kbps data (M = 3). |
| 3 | ( | InterSystemHandoverCommand-GSM | Send on cell 1 (UTRAN cell) and the message indicates: the target channel for GSM 14.4 kbps data (M = 1 and 2); or for GSM 28.8 kbps data (M = 3). |
| 4 | UE |  | The UE accepts the handover command and switches to the GSM traffic channel specified in the InterSystemHandoverCommand-GSM |
| 5 | ( | HANDOVER ACCESS | The SS receives this burst on the traffic channel of cell 2 (GSM cell) It implies that the UE has switched to GSM cell. |
| 6 | ( | HANDOVER ACCESS |  |
| 7 | ( | HANDOVER ACCESS |  |
| 8 | ( | HANDOVER ACCESS |  |
| 9 | ( | PHYSICAL INFORMATION |  |
| 10 | ( | SABM |  |
| 11 | ( | UA |  |
| 12 | ( | HANDOVER COMPLETE | The SS receives the message on the traffic channel of GSM cell. |

Specific message contents

For execution 1:

Same as the message contents of clause 8.3.7.2 for M = 1.

For execution 2:

Same as the message contents of clause 8.3.7.2 for M = 1.

For execution 3:

Same as the message contents of clause 8.3.7.2 for M = 2.

8.3.7.3.5	Test requirement

After step 12 the ongoing call shall be continued on the GSM cell.

#### 8.3.7.4	Inter system handover from UTRAN/To GSM/Speech/Establishment/Success

8.3.7.4.1	Definition

8.3.7.4.2	Conformance requirement

When the UE receives an INTER-SYSTEM HANDOVER COMMAND message from UTRAN the UE shall take the following actions:

-	Establish the connection to the other radio access system, by using the contents of the IE "Inter system message". This IE contains candidate/ target cell identifier(s) and radio parameters relevant for the other radio access system.

-	For each IE "Remaining radio access bearer", associate the radio access bearer given by the IE "RAB info" to the radio resources in the target system given by the IE "Inter system message". Other information for making the association may be included in the IE "Inter system message" and requirements may be stated in the specifications relevant for the target system [FFS].

-	Switch the current connection to the other radio access system.

NOTE 1:	Requirements concerning the establishment of the radio connection towards the other radio access system and the signalling procedure are outside the scope of this specification.

NOTE 2:	The release of the UMTS radio resources is initiated by the other system.

NOTE 3:	Currently only one radio access bearer can be associated with the IE "Inter-system message", and this association is limited to the radio access bearers in the CS domain. It is assumed that all the radio access bearers in the PS domain, if any, remain after the handover.

Reference(s)

TS 25.331 Clause 8.3.7.3.

8.3.7.4.3	Test purpose

To test that the UE handovers to the indicated channel in the GSM target cell when it is in the call establishment phase in the UTRAN serving cell and receives an INTER-SYSTEM HANDOVER COMMAND.

8.3.7.4.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is UTRAN, Cell 2 is GSM. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 2.

UE : CC State U1 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports UTRAN AMR,

UE supports GSM FR,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U1 on cell 2.

Test Procedure

The SS starts the UTRAN cell and the UE is triggered to initialise an MO speech call. During the call establishment phase, after the SS receives SETUP message the SS starts GSM cell and configures a dedicated channel, then sends the UE an INTER-SYSTEM HANDOVER COMMAND indicating the dedicated channel in the target GSM cell. After the UE receives the command it shall configure itself accordingly and switch to the new channel of the GSM cell. The SS checks whether the handover is performed by checking that the UE transmits the HANDOVER COMPLETE message to the SS in GSM cell.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | UE |  | To trigger the UE to initialise an MO call |
| 2 | ( | SETUP | U1 |
| 3 | SS |  | The SS starts the GSM cell and configure a dedicated channel SDCCH. |
| 4 | ( | InterSystemHandoverCommand-GSM | Send on cell 1 (UTRAN cell) and the message indicates: the dedicated channel SDCCH. |
| 5 | UE |  | The UE accepts the handover command and switches to the GSM dedicated channel specified in the InterSystemHandoverCommand-GSM |
| 6 | ( | HANDOVER ACCESS | The SS receives this burst on the dedicated channel of cell 2 (GSM cell) It implies that the UE has switched to GSM cell. |
| 7 | ( | HANDOVER ACCESS |  |
| 8 | ( | HANDOVER ACCESS |  |
| 9 | ( | HANDOVER ACCESS |  |
| 10 | ( | PHYSICAL INFORMATION |  |
| 11 | ( | SABM |  |
| 12 | ( | UA |  |
| 13 | ( | HANDOVER COMPLETE | The SS receives the message on the dedicated channel of GSM cell. |

Specific message contents

InterSystemHandoverCommand-GSM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info |  |
| - Message authentication code |  |
| - Message sequence number |  |
| Activation time | now |
| RAB Info | Not present |
| Inter-system message |  |
| - System type | GSM |
| - CHOICE system | GSM |
| - Message | GSM HANDOVER COMMAND formatted as BIT STRING(1..512). The contents of the HANDOVER COMMAND see next table. |

HANDOVER COMMAND

Same as the HANDOVER COMMAND for M = 4 in clause 26.6.5.2 of GSM 11.10-1 version 8.2.0 Release 1999

8.3.7.4.5	Test requirement

At step 13 the SS shall receive HANDOVER COMPLETE message on the dedicated channel of the GSM cell.

#### 8.3.7.5	Inter system handover from UTRAN/To GSM/Speech/Failure

8.3.7.5.1	Definition

8.3.7.5.2	Conformance requirement

If the UE does not succeed to establish the connection to the other radio access technology, it shall

-	resume the connection to UTRAN using the resources used before receiving the INTER-SYSTEM HANDOVER COMMAND message; and

-	transmit the INTER-SYSTEM HANDOVER FAILURE message on uplink DCCH using AM RLC. When the successful delivery of the INTER-SYSTEM FAILURE message has been confirmed by RLC, the procedure ends.

Reference(s)

TS 25.331 Clause 8.3.7.5.

8.3.7.5.3	Test purpose

To test that the UE reactivates the old channel and transmits INTER-SYSTEM HANDOVER FAILURE message to the network on the old channel in UTRAN cell when it receives an INTER-SYSTEM HANDOVER COMMAND and the connection to GSM for handover can not be established.

8.3.7.5.4	Method of test

Initial conditions

System Simulator : 2 cells - Cell 1 is UTRAN,  Cell 2 is GSM. GSM 11.10-1 section 26.6.5.1 shall be referenced for the default parameters of cell 2.

UE : CC State U10 in cell 1

Related ICS/IXIT statement(s)

UE supports both GSM and UTRAN Radio Access Technologies,

UE supports GSM FR,

UE supports UTRAN AMR,

UE supports GSM-P, GSM-E, GSM-DCS, GSM-450, GSM-480.

Foreseen final state of the UE

The UE is in CC state U10 on cell 1.

Test Procedure

The SS starts the UTRAN cell and brings the UE into call active state (CC state U10) with AMR. The SS starts GSM cell without activating any dedicated channel in the cell, then sends INTER-SYSTEM HANDOVER COMMAND indicating a dedicated channel of the target GSM cell to the UE through DCCH of the serving UTRAN cell. The UE receives the command and configures itself accordingly but can not complete the handover. The SS checks that the handover is failed by checking that the UE transmits the INTER-SYSTEM HANDOVER FAILURE message to the SS in UTRAN cell.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | UE |  | The SS bring the UE into UTRAN U10 state in cell 1 |
| 2 | SS |  | The SS configures cell 2 as a GSM cell but without any traffic channel. |
| 3 | ( | InterSystemHandoverCommand-GSM | Send on cell 1 (UTRAN cell) and the message indicates: the target channel for GSM FR which does not exist in the GSM cell. |
| 4 | UE |  | The UE accepts the handover command and switches to the GSM traffic channel specified in the InterSystemHandoverCommand-GSM |
| 5 | ( | HANDOVER ACCESS | The SS receives this burst on the traffic channel of cell 2 (GSM cell) It implies that the UE has switched to GSM cell. |
| 6 | ( | HANDOVER ACCESS |  |
| 7 | ( | HANDOVER ACCESS |  |
| 8 | ( | HANDOVER ACCESS |  |
| n | ( | HANDOVER ACCESS | The last handover access burst before T3124 times out. |
| n+1 | ( | InterSystemHandoverFailure | The SS receives the message on the old channel of UTRAN cell. |

Specific message contents

Same as the message contents of clause 8.3.7.1 for M = 3.

8.3.7.5.5	Test requirement

After step n+1 the SS shall receive INTER-SYSTEM HANDOVER FAILURE message on the old channel of the UTRAN cell.

### 8.3.8	Inter system cell reselection to UTRAN

[Editor’s note: This test is FFS until R2000 core specification will be defined.]

### 8.3.9	Inter system cell reselection from UTRAN

[Editor’s note: This test is FFS until R2000 core specification will be defined.]

## 8.4	Measurement procedure

### 8.4.1	Measurement Control and Report

#### 8.4.1.1   	Measurement Control and Report: Intra-frequency measurement for transition from idle mode to CELL_DCH state

8.4.1.1.1		Definition

8.4.1.1.2	Conformance requirement

After a state transition from idle mode to CELL_DCH state, the UE shall continue to monitor the list of neighbouring cells which is specified in System Information Block type 11 or 12 messages on BCCH.  When entering CELL_DCH state, the UE shall send a MEASUREMENT REPORT message when reporting criteria are satisfied.  During CELL_DCH state, if the UE receives a MEASUREMENT CONTROL message, it shall terminate existing monitoring activities for the neighbouring cells previously known from System Information Block type 11 or 12 messages.  It shall perform the measurement and reporting tasks based on the latest MEASUREMENT CONTROL message received.

Reference

3GPP TS 25.331 clause 8.4.1.8.1

8.4.1.1.3	Test Purpose

To confirm that the UE continue to monitor intra-frequency measurement quantity of the neighbour cells listed in System Information Block type 11 or 12 messages, after it has entered the CELL_DCH state from idle mode.  When the reporting criteria specified in System Information Block type 11 or 12 messages have been met, it shall report the measurements t using MEASUREMENT REPORT messages.  To confirm that the UE terminates monitoring activities for the neighbour cells found in System Information Block type 11 or 12 messages, after it has received a MEASUREMENT CONTROL message that specifies the measurement type to be “intra-frequency measurement”.  To confirm that the UE reconfigures the monitoring and reporting activities based on the last MEASUREMENT CONTROL message received.

8.4.1.1.4	Method of test

Initial Condition

System Simulator: 2 cells –  The initial configurations of the 2 cells in the SS should follow the values indicated in the column marked “T0” in table 8.4.1.1-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-registered idle mode (state 2) or PS-registered idle mode (state 3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE

Test Procedure

Table 8.4.1.1-1 illustrates the downlink power to be applied for the 2 cells at various time instants of the test execution.  Column marked “T0” denotes the initial conditions, while columns marked “T1 are to be applied subsequently.  The exact instants on which these values shall be applied are described in the texts in this sub-clause.

Table 8.4.1.1-1

| Parameter | Unit | Cell 1 | Cell 2 |
| --- | --- | --- | --- |
|  |  | T0 | T1 | T0 | T1 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 1 |
|  | dB | 14.3 | 5.3 | -11.3 | -1.3 |
| CPICH Ec/Io | dB | -11.9 | -11.8 | -14.9 | -18.4 |
| CPICH RSCP | dBm | -65.7 | -74.4 | -68.7 | -81.3 |

The UE is initially at idle mode and has selected cell 1 for camping.  The System Information Block type 11 messages are modified with respect to the default settings to prevent reporting of CFN-SFN difference and also to include cell 2 into the monitored neighbour cell list. The key measurement parameters are as follow: measurement type = “intra-frequency measurement”, measurement quantity = “CPICH RSCP”, report criteria = “periodic reporting criteria”, reporting interval = “12 seconds”.

SS prompts the operator to make an outgoing call of a supported traffic class.  The UE shall transmit a RRC CONNECTION REQUEST message on the CCCH, SS replies with RRC CONNECTION SETUP message and allocates uplink and downlink DPCH physical resources to the UE.  UE shall then transmit RRC CONNECTION SETUP COMPLETE message and move to CELL_DCH state.  After approximately 12 seconds, the UE shall transmit a MEASUREMENT REPORT message with measurement readings from cell 2.  SS waits for 25 seconds after the sending of RRC CONNECTION SETUP message to verify that 2 consecutive MEASUREMENT REPORT messages are received.

SS sends a MEASUREMENT CONTROL message on the downlink DCCH.  In this message, SS assigns an intra-frequency measurement type with the measurement quantity based on cell 2’s CPICH RSCP value.  Parameters used in this message are: measurement identity = “2”, report criteria = “event-trigger”, event identity = “1f”, reporting threshold = “-75 dBm”.  After receiving this message, the UE shall delete the existing measurement and reporting contexts captured from System Information Block type 11 messages.  SS checks to see that no MEASUREMENT REPORT messages are sent within the next 12 seconds (which is due to periodic reporting).  SS reconfigures the downlink transmission power settings according to values in column “T1” in Table 8.4.1.1-1.  The UE shall transmit MEASUREMENT REPORT messages when it detects that the CPICH RSCP of cell 2 has reached the threshold value specified.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 11 | The UE is idle mode and camped onto cell 1. The System Information Block type 11 messages to be transmitted are different from the default settings (see specific message contents) |
| 2 |  |  | SS prompts the operator to make an outgoing call. |
| 3 | ( | RRC CONNECTION REQUEST |  |
| 4 | ( | RRC CONNECTION SETUP | SS allocates DPCH physical channels to UE |
| 5 | ( | RRC CONNECTION COMPLETE | UE transmits this message to acknowledge the RRC CONNECTION SETUP message and moves to CELL_DCH state. |
| 6 | ( | MEASUREMENT REPORT | SS waits for 25 seconds. It shall receive 2 consecutive MEASUREMENT REPORT messages |
| 7 | ( | MEASUREMENT CONTROL | A new measurement identity is assigned, with the reporting quantity changed to cell 2’s P-CPICH RSCP. See specific message content for the rest of the message. |
| 8 |  |  | SS waits for approximately 15 seconds and verifies that no further MEASUREMENT REPORT messages are detected on the uplink DCCH. |
| 9 |  |  | SS re-adjusts the downlink transmission power settings according to columns “T1” in Table 8.4.1.1-1. |
| 10 | ( | MEASUREMENT REPORT | SS verifies that UE transmits 2 MEASUREMENT REPORT messages at 500 msec interval to report the P-CPICH RSCP value of cell 2. |

Specific Message Contents

All messages indicated below shall use the same content as described in default message content, with the following exceptions:

System Information Block type 11 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| SIB12 indicator FACH measurement occasion info Measurement control system information - Intra-frequency measurement system information - Intra-frequency measurement identity - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection - Qoffsets,n - Maximum allowed UL TX power - HCS neighbouring cell information - Qqualmin - Qrxlevmin - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency measurement for RACH reporting - SFN-SFN observed time difference - Reporting quantity - Maximum number of reported cells on RACH - Reporting information for state CELL_DCH - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - CHOICE report criteria - Amount of reporting - Reporting interval - Inter-frequency measurement system information - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | FALSE Not Present 1 Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE 0dB 0dBm Not Present -115dB -20dB 0 CPICH RSCP No report No report No report No report FALSE FALSE FALSE FALSE FALSE No report FALSE TRUE FALSE TRUE FALSE Not present Periodic reporting criteria Infinity 12 seconds Not present Not Present Not Present Not Present |

RRC CONNECTION REQUEST (Step 3)

| Information Element | Value/Remarks |
| --- | --- |
| Establishment cause Measured results on RACH | Check to see if set to originating call of a supported traffic class Check to see if this IE is absent |

RRC CONNECTION SETUP (Step 4)

Use the message sub-type in clause 9 of TS 34.108, which is marked as “Transition to CELL_DCH”.

MEASUREMENT REPORT (Step 6)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to 1 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is absent Check value to see if within acceptable range Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |

MEASUREMENT CONTROL (Step 7)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - CHOICE report criteria - Parameters required for each events - Intra-frequency event identity - Triggering condition 1 - Triggering condition 2 - Reporting range - Cells forbidden to affect reporting range - W - Hysteresis - Threshold used frequency - Reporting deactivation threshold - Replacement activation threshold - Time to trigger - Amount of reporting - Reporting interval - Reporting cell status DPCH compressed mode status info | 2 Setup Not Present Not Present Intra-frequency measurement Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE 0 CPICH RSCP Same as in default message content No report FALSE FALSE FALSE FALSE FALSE No report FALSE TRUE FALSE TRUE FALSE Not present Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Intra-frequency measurement reporting criteria 1f Monitored set cells Not Present Not Present Not Present Not Present 1 dB -75 dBm Not Present Not Present 0 msec 2 500 msec Not Present Not Present |

MEASUREMENT REPORT (Step 10)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to 2 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is absent Check to see if this IE is present Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |

8.4.1.1.5	Test Requirement

After step 5 the UE shall start to transmit MEASUREMENT REPORT message.  The measurement quantity “CPICH RSCP” of cell 2 shall be reported to the SS at 12 seconds interval.

After step 7 the UE shall not transmit any MEASUREMENT REPORT messages within 15 seconds after SS has transmitted the MEASUREMENT CONTROL message.

After step 9 the UE shall transmit 2 MEASUREMENT REPORT messages on the uplink DCCH, to report that the CPICH RSCP value for cell 2 has dropped below the threshold stated in the MEASUREMENT CONTROL message transmitted by the SS in step 7.

#### 8.4.1.2  	Measurement Control and Report: Inter-frequency measurement for transition from idle mode to CELL_DCH state

8.4.1.2.1		Definition

8.4.1.2.2	Conformance requirement

After entering CELL_DCH state from idle mode, the UE shall discontinue the monitoring of the list of neighbouring cells assigned in System Information Block 11 or 12 messages.  In CELL_DCH state, when the UE receives a MESUREMENT CONTROL message requesting for inter-frequency measurement to be setup, it shall start inter-frequency measurement and the associated reporting activities if “DPCH compressed mode status info” IE in the message simultaneously activates at least one compressed mode pattern sequence.  When the UE receives a MEASUREMENT CONTROL message with “Reporting cell status” IE omitted, it shall not include “Cell measured results” IE for any cells in MEASUREMENT REPORT messages sent on uplink DCCH.

Reference

3GPP TS 25.331 clause 8.4.1.8.2, 8.6.7.9

8.4.1.2.3	Test Purpose

To confirm that the UE stops monitoring the list of neighbouring cell assigned in the IE “inter-frequency cell info” in System Information Block type 11 messages, after it enters CELL_DCH state from idle mode.  To confirm that the UE starts to perform inter-frequency measurement and related reporting activities, when it receives a MEASUREMENT CONTROL message with the “DPCH compress mode status info” IE indicating that a stored compressed mode pattern sequence be simultaneously activated.  To confirm that the UE exclude the IE “cell measured results” for any cells in the MEASUREMENT REPORT messages, after it receives a MEASUREMENT CONTROL message with “Reporting cell status” IE omitted.

8.4.1.2.4	Method of test

Initial Condition

System Simulator: 2 cells – The initial configurations of the 2 cells in the SS should follow the values indicated in table 8.4.1.2-1.  The table is found in “Test Procedure” sub-clause. UE:CS-registered idle mode (state 2) or PS-registered idle mode (state 3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.2-1 illustrates the downlink power to be applied for the 2 cells.

Table 8.4.1.2-1

| Parameter | Unit | Cell 1 | Cell 4 |
| --- | --- | --- | --- |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 2 |
|  | dB | 5.7 | 2.3 |
| CPICH Ec/Io | dB | -12.4 | -15.8 |
| CPICH RSCP | dBm | -74.3 | -77.7 |

The UE is initially at idle mode and has selected cell 1 for camping.  The System Information Block type 11 messages are modified with respect to the default settings to prevent reporting of CFN-SFN difference, and also to include cell 4 into the monitored neighbour cells list.

SS prompts the operator to make an outgoing call for one of the traffic classes supported by the UE.  The UE shall transmit a RRC CONNECTION REQUEST message on the CCCH, SS replies with RRC CONNECTION SETUP message and allocates uplink and downlink dedicated physical resources to the UE.  The RRC CONNECTION SETUP message contains IE “DPCH compressed mode info”, signifying the establishment of a transmission pattern gap sequence with TGPSI=1.  UE shall send RRC CONNECTION SETUP COMPLETE on the uplink DCCH and then moves to CELL_DCH state.  The UE shall not transmit any MEASUREMENT REPORT messages, which pertain to measurement readings from cells belonging to the monitored set.

SS sends PHYSICAL CHANNEL RECONFIGURATION message on the downlink DCCH, specifying that compressed mode sequence pattern with TGPSI=1 be deactivated.  The UE shall reply with PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on the uplink DCCH.  It shall stop compressed mode operations at the activation time stated in PHYSICAL CHANNEL RECONFIGURATION message.  After the designated activation time has elapsed, SS sends MEASUREMENT CONTROL message on the downlink DCCH.  In this message, SS requests UE to perform inter-frequency measurement with periodic reporting of CPICH RSCP values for cell 4.  The “DPCH compressed status info” IE in this message activates the transmission gap pattern sequence with TGPSI = 1.  The UE shall start inter-frequency measurement for cell 4’s CPICH RSCP values.  It shall report this measurement result by transmitting MEASUREMENT REPORT messages on uplink DCCH periodically at 16 seconds interval.

In the next sequence, SS sends another MEASUREMENT CONTROL message on the downlink DCCH.  In this message, the IE “Reporting cell status” is not included.  The UE shall send MEASUREMENT REPORT messages on the uplink DCCH, with the IE “Cell measured results” excluded from these messages.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 11 | The UE is idle mode and camped onto cell 1.System Information Block Type 11 to be transmitted is different from the default settings (see specific message contents) |
| 2 |  |  | SS prompts the operator to make an outgoing call. |
| 3 | ( | RRC CONNECTION REQUEST |  |
| 4 | ( | RRC CONNECTION SETUP | SS allocates dedicated physical channels to UE, as well as specifying the activation of compressed mode behaviour with TGCPSI = 1. |
| 5 | ( | RRC CONNECTION SETUP COMPLETE | UE transmits this message to acknowledge the RRC CONNECTION SETUP message and moves to CELL_DCH state. |
| 6 |  |  | SS checks to see that no MEASUREMENT REPORT messages are sent from UE to cell 1. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION | Existing compressed mode sequence pattern is de-activated in this message. |
| 8 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall remain in CELL_DCH state. |
| 9 | ( | MEASUREMENT CONTROL | SS requests UE to start inter-frequency measurement for cell 4 and performing periodic reporting for cell 4 CPICH RSCP. “DPCH compressed mode status info” IE is set to simultaneously activate compressed mode pattern. |
| 10 | ( | MEASUREMENT REPORT | UE shall report cell 4’s CPICH RSCP reading periodically. |
| 11 | ( | MEASUREMENT CONTROL | SS changes the reporting criteria of cell 4 to ‘event 2c’. “Reporting cell status” IE in this message is omitted. |
| 12 | ( | MEASUREMENT REPORT | SS monitors the uplink DCCH to make sure that only 1 such message is received 32 seconds after step 11. This message shall not contain IE “Cell measured results” |

Specific Message Content

All messages indicated below shall use the same content as described in default message content, with the following exceptions:

System Information Block type 11 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| SIB12 indicator FACH measurement occasion info Measurement control system information - Intra-frequency measurement system information - Inter-frequency measurement system information - Inter-frequency measurement identity - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and re-selection info - Qoffsets,n - Maximum allowed UL TX power - HCS neighbouring cell information - Qqualmin, Qrxlevmin - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | FALSE Not Present Not Present 1 No inter-frequency cells removed Set to id of cell 2 Set to the uplink UARFCN of cell 2 Set to the downlink UARFCN of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE 0 dB 0 dBm Not Present -20 dB, -115dBm Not Present Not Present Not Present |

RRC CONNECTION REQUEST (Step 3)

| Information Element | Value/Remarks |
| --- | --- |
| Establishment cause Measured results on RACH | Check to see if set to originating call of a supported traffic class Check to see if this IE is absent |

RRC CONNECTION SETUP (Step 4)

Use the message sub-type found in TS 34.108 clause 9 which is marked as “Transition to CELL_DCH”, with the following exceptions:

| Information Element | Value/Remarks |
| --- | --- |
| Downlink information common for all radio links - Downlink DPCH info common for all RL - CHOICE Mode - Downlink DPCH power control information - DPC mode - DL rate matching restriction information - Spreading factor - Fixed or flexible position - TFCI existence - Number of bits for Pilot bits (SF=128, 256) - DPCH compressed mode info - TGPSI - TGPS Status Flag - TGCFN - Transmission gap pattern sequence configuration parameters - TGMP - TGPRC - TGCFN - TGSN - TGL1 - TGL2 - TGD - TGPL1 - TGPL2 - RPP - ITP - UL/DL Mode - Downlink compressed mode method - Uplink compressed mode method - Downlink frame type - DeltaSIR1 - DeltaSIRAfter1 - DeltaSIR2 - DeltaSIR2After2 - TX Diversity Mode - SSDT information - S field - Code Word Set - Default DPCH Offset Value | FDD 0 (Single) Refer to the parameter set in TS 34.108 Not Present Flexible FALSE Not Present 1 Active 255 FDD Measurement 62 (Current CFN + (256 – TTI/10msec)) mod 256 8 10 5 15 35 35 Mode 1 Mode 1 DL SF/2 Not Present A 2.0 1.0 Not Present Not Present None Not Present 0 |

PHYSICAL CHANNEL RECONFIGURATION (Step 7)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info | Not Present |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN - (CFN MOD 8 + 8 ))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present –use default |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info | Not Present – use default |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Uplink DPCH info |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 |
| - Number of DPDCH | Not Present (Use default value of 1) |
| - Spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present (Use default value of 0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - CHOICE mode | FDD |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits (SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - Transmission gap pattern sequence |  |
| - TGPSI | 1 |
| - TPGS status Flag | Inactive |
| - TGCFN - Transmission gap pattern sequence configuration parameters | 255 Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - S field |  |
| - Code Word Set |  |
| - Default DPCH Offset Value | 0 |
| Downlink information per radio link list | Not Present |

MEASUREMENT CONTROL (Step 9)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 1 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downlink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH RSCP FALSE TRUE No report FALSE FALSE FALSE TRUE FALSE Report cell within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 1 Active 255 |

MEASUREMENT REPORT (Step 10)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to 1 Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 4 Check to see if set to the UARFCN of the downlink frequency for cell 4 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 4 Check to see if it is absent Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent |

MEASUREMENT CONTROL (Step 11)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - Measurement validity - Inter-frequency set update - CHOICE report criteria - Parameters required for each event - Inter-frequency event identity - Threshold used frequency - W used frequency - Hysteresis - Time to trigger - Reporting cell status - Parameters required for each non-used frequency - Threshold non used frequency - W non used frequency DPCH compressed mode status info | 1 Modify Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH RSCP FALSE TRUE No report FALSE FALSE FALSE TRUE FALSE Not Present Not present Not present Inter-frequency measurement reporting criteria Event 2c Not Present Not Present 0.5 dB 0 milliseconds Not Present -85 dBm 0 Not Present |

MEASUREMENT REPORT (Step 12)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results Measured Results on RACH Event Results | Check to see if set to 1 Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 4 Check to see if set to the UARFCN of the downlink frequency for cell 4 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent |

8.4.1.2.5	Test Requirement

After step 5 the UE shall not transmit any MEASUREMENT REPORT messages pertaining to the measurement of CPICH RSCP quantity of cell 4.

After step 9 the UE shall transmit MEASUREMENT REPORT messages on uplink DCCH, reporting cell 4’s CPICH RSCP value at periodic time interval of 16 seconds.

After step 11 the UE shall transmit only 1 MEASUREMENT REPORT message on the uplink DCCH.  In this message, IE “inter-frequency cell measured results”  should be absent.

#### 8.4.1.3  	Measurement Control and Report: Intra-frequency measurement for transition from idle mode to CELL_FACH state

8.4.1.3.1		Definition

8.4.1.3.2	Conformance requirement

During a transition from idle mode to CELL_FACH state, the UE shall start to monitor neighbouring cells listed in the IE ”Intra-frequency cell info” received in System Information Block type 11 or  12 messages.  If an “intra-frequency measurement reporting criteria” is also specified in these messages, the UE shall store this information and apply the reporting rules when deciding to transmit MEASUREMENT REPORT messages following a subsequent transition to CELL_DCH state.  If reporting during RACH transmissions is dictated by the UTRAN, the UE shall append the measurement information when sending messages on RACH.

Reference

3GPP TS 25.331, clause 8.4.1.9

8.4.1.3.3	Test Purpose

To confirm that the UE begins to monitor the neighbouring cells listed in IE “intra-frequency cell info” of System Information Block type 11 or 12 messages, after it has entered the CELL_FACH state.  If information regarding the intra-frequency measurement reporting criteria is also broadcasted, the UE shall store this information and apply the reporting criteria after a subsequent transition to CELL_DCH state.  If RACH measurement reporting is dictated in System Information Block type 11 or 12 messages, the UE shall include these measurements when transmitting on the RACH channel.

8.4.1.3.4	Method of test

Initial Condition

System Simulator: 2 cells – both cell 1 and cell 2 are active.See Table 8.4.1.3-1 for the power settings.

UE: CS-registered idle mode (state 2) or PS-registered idle mode (state 3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.3-1 illustrates the downlink power to be applied for the 2 cells in this test case.

Table 8.4.1.3-1

| Parameter | Unit | Cell 1 | Cell 2 |
| --- | --- | --- | --- |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 2 |
|  | dB | 5.7 | 2.3 |
| CPICH Ec/Io | dB | -12.4 | -15.8 |
| CPICH RSCP | dBm | -74.3 | -77.7 |

The UE is initially at idle mode and has selected cell 1 for camping.  The System Information Block type 11 messages are modified with respect to the default settings to prevent reporting of CFN-SFN difference and also to include cell 2 into the monitored neighbour cell list. The key measurement parameters are as follow: measurement type = “intra-frequency measurement”, measurement quantity = “CPICH Ec/No”, report criteria = “periodic reporting criteria”, reporting interval = “12 seconds”.  In the System Information type 11 messages, reporting of CPICH Ec/No is also required for intra-frequency reporting when transmitting RACH messages to cell 1.

SS prompts the operator to make an outgoing call of one of the traffic classes supported by the UE.  The UE shall transmit a RRC CONNECTION REQUEST message on the uplink CCCH, SS replies with RRC CONNECTION SETUP message and allocates PRACH and S-CCPCH physical channels for uplink and downlink usage.  UE shall then enter CELL_FACH state.  SS starts timer T305 and waits until timer T305 expires, the UE shall send a CELL UPDATE message which includes the measurement reading of cell 2’s CPICH Ec/No values.  SS then reply with CELL UPDATE CONFIRM message on the downlink DCCH, without changing the physical channel resources.

In the next sequence, SS transmits PHYSICAL CHANNEL RECONFIGURATION message, and allocates DPCH channels to the UE.  The UE shall transit to CELL_DCH state and then send a MEASUREMENT REPORT message, correctly stating the measurement identity.  The measurement identity indicated shall match the value that was previously broadcasted on System Information Block type 11 messages when the UE was still in idle mode.  The IE “Measured results” in the MEASUREMENT REPORT messages shall contain measured values of cell 2’s CPICH Ec/No.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 2, System Information Block type 11 | The UE is idle mode and camped onto cell 1. System Information Block type 2 and 11 to be transmitted are different from the default settings (see specific message contents) |
| 2 |  |  | SS prompts the test operator to make an outgoing call. |
| 3 | ( | RRC CONNECTION REQUEST | The Ec/No value of P-CPICH of Cell 1 should be reported. |
| 4 | ( | RRC CONNECTION SETUP | SS allocates common physical channels to UE. |
| 5 | ( | RRC CONNECTION COMPLETE | UE shall enter CELL_FACH state, and transmit this message to acknowledge the RRC CONNECTION SETUP message. |
| 6 |  |  | SS monitors the uplink DCCH to confirm that no MEASURENENT REPORT messages are detected. SS waits for 5 minutes (for the expiry of T305 timer). |
| 7 | ( | CELL UPDATE | This message shall contain measurement readings of CPICH Ec/No for cell 1. |
| 8 | ( | CELL UPDATE CONFIRM | SS does not change the physical channel configurations. |
| 9 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS assigns DPCH physical resources to the UE, but keeps the parameters for transport channels and RBs unchanged. |
| 10 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall transit to CELL_DCH state after sending this message. |
| 11 | ( | MEASUREMENT REPORT | UE shall begin to report cell 2’s CPICH Ec/No value periodically at 12 seconds interval. The measurement identity shall match measurement contexts transmitted on BCCH in step 1 |

Specific Message Content

System Information Block type 2 (Step 1)

| Information Element | Value/Remarks |
| --- | --- |
| UE Timers and constants in connected mode - T305 | 5 minutes. |

System Information Block type 11 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| SIB12 indicator FACH measurement occasion info - FACH Measurement occasion cycle length coefficient - Inter-frequency FDD measurement indicator - Inter-frequency TDD measurement indicator - Inter-RAT measurement indicators Measurement control system information - Intra-frequency measurement system information - Intra-frequency measurement identity - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Qoffsets,n - Maximum allowed UL TX power - HCS neighbouring cell information - Qqualmin, Qrxlevmin - Intra-frequency Measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency measurement for RACH reporting - SFN-SFN observed time difference - Reporting quantity - Maximum number of reported cells on RACH - Reporting information for state CELL_DCH - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected set cells - Measurement Reporting Mode - Measurement Reporting Transfer Mode - Periodic Reporting/Event Trigger Reporting Mode - CHOICE report criteria - Amount of reporting - Reporting interval - Reporting Cell Status - CHOICE reported cell - Maximum number of reported cells - Inter-frequency measurement system information - Traffic volume measurement system information - UE internal measurement system information | FALSE 2 FALSE FALSE Not Present 5 Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE 0 dB 0 dBm Not Present -20dB, -115dBm 0 CPICH Ec/No No report CPICH Ec/No Current cell No report FALSE FALSE FALSE FALSE FALSE No report FALSE TRUE TRUE FALSE FALSE Not present Acknowledged mode RLC Periodic Reporting Periodical reporting criteria Infinity 12 seconds Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not Present Not Present Not Present |

RRC CONNECTION REQUEST (Step 3)

| Information Element | Value/Remarks |
| --- | --- |
| Initial UE Identity Establishment cause Measured results on RACH - Measured result for current cell - CHOICE measurement quantity - CPICH Ec/No - Measured results for monitored cells | Check to see if it is the same as the IMSI in USIM card, TMSI or P-TMSI previously allocated. Check to see if set to originating call of the compatible traffic classes supported by the UE Check to see if value is present Check to see if this IE is absent |

RRC CONNECTION SETUP (Step 4)

Use the same message sub-type found in Annex A, which is entitled “Transition to CELL_FACH”.

CELL UPDATE (Step 7)

| Information Element | Value/Remarks |
| --- | --- |
| U-RNTI Integrity check info AM_RLC error indicator (for C-plane) AM_RLC error indicator (for U-plane) START List Cell update cause Protocol error indicator Measured results on RACH - Measurement result for current cell - CHOICE measurement quantity - CPICH Ec/No - Measurement results for monitored cells Protocol error information | Check to see if set to same U-RNTI value assigned in RRC CONNECTION SETUP message. Not checked Check to see if set to ‘FALSE’ Check to see if set to ‘FALSE’ Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘Periodic cell updating’ Check to see if set to ‘FALSE’ CPICH Ec/No Checked to see if set to within an acceptable range. Checked to see if this IE is not present. Check to see if set to ‘FALSE’ |

PHYSICAL CHANNEL RECONFIGURATION (Step 9)

Use the same message sub-type found in Annex A, which is entitled “Packet to CELL_DCH from CELL_FACH”.

MEASUREMENT REPORT (Step 11)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to 5 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is within acceptable range Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |

8.4.1.3.5	Test Requirement

After step 3 the UE shall send RRC CONNECTION REQUEST message, which includes measured value of cell 1’s CPICH Ec/No value.

After step 5 the UE shall not transmit any MEASUREMENT REPORT messages on the uplink DCCH.

After step 6 the UE shall initiate cell update procedure by transmitting CELL UPDATE message.  In this message, the cause shall be set to “periodic cell updating”.  It shall include measured value for cell 1’s CPICH Ec/No measurement quantity.

After step 10 the UE shall move to CELL_DCH state and transmit MEASUREMENT REPORT messages at 12 seconds interval.  In these messages, neighbouring cell 2’s CPICH Ec/No value shall be reported.  The IE ”measurement identity” in this message shall match the IE ”Intra-frequency measurement identity” found in System Information Block type 11 messages transmitted in step 1.

#### 8.4.1.4  	Measurement Control and Report: Inter-frequency measurement for transition from idle mode to CELL_FACH state

8.4.1.4.1		Definition

8.4.1.4.2	Conformance requirement

After entering CELL_FACH state from idle mode, the UE shall start to monitor the list of “inter-frequency” neighbouring cells assigned in the System Information Block type 11 or 12 messages on transmitted on the BCCH.

Reference

3GPP TS 25.331, clause 8.4.1.9.2

8.4.1.4.3	Test Purpose

To confirm that the UE begins to monitor the list of neighbouring cell assigned in the IE “inter-frequency cell info” in System Information Block type 11 or 12 messages, after it enters CELL_FACH state from idle mode.  However, it shall not transmit any MEASUREMENT REPORT messages to report measured results for inter-frequency cells.

8.4.1.4.3	Method of test

Initial Condition

System Simulator: 2 cells – The initial configurations of the 2 cells in the SS should follow the values indicated in the columns marked “T0” in table 8.4.1.4-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-registered idle mode (state 2) or PS-registered idle mode (state 3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.4-1 illustrates the downlink power to be applied for the 2 cells at various time instants of the test execution.  Columns marked “T0” denote the initial conditions, while columns marked “T1 are to be applied subsequently.  The exact instants on which these values shall be applied are described in the texts in this sub-clause.

Table 8.4.1.4-1

| Parameter | Unit | Cell 1 | Cell 4 |
| --- | --- | --- | --- |
|  |  | T0 | T1 | T0 | T1 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 2 |
|  | dB | 9.7 | 0.5 | 0.5 | 9.7 |
| CPICH Ec/Io | dB | -10.4 | -12.8 | -12.8 | -10.4 |
| CPICH RSCP | dBm | -70.3 | -79.5 | -79.5 | -70.3 |

The UE is initially at idle mode and has selected cell 1 for camping.  The System Information Block type 12 messages are modified with respect to the default settings to prevent reporting of CFN-SFN difference and also to include cell 2 into the monitored neighbour cell list for inter-frequency measurement type. The key measurement parameters are as follow: measurement type = “inter-frequency measurement”, measurement quantity = “CPICH Ec/No”.

SS prompts the operator to make an outgoing call of a supported traffic class.  The UE shall transmit a RRC CONNECTION REQUEST message on the CCCH, SS replies with RRC CONNECTION SETUP message and allocates PRACH channel on the uplink and S-CCPCH channel on the downlink to the UE.  UE then moves to CELL_FACH state.  The UE shall not transmit any MEASUREMENT REPORT messages, which pertain to measurement readings from inter-frequency cells belonging to the monitored set.  SS re-adjusts its downlink power settings according to columns marked “T1” in Table 8.4.1.4-1.  This is expected to trigger a cell reselection in the UE.  The UE shall send CELL UPDATE message to cell 4 in order to report this event.  Upon receiving this message, SS replies with the default CELL UPDATE CONFIRM message on the downlink DCCH.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 11 | The UE is idle mode and camped onto cell 1. System Information Block type 11 to be transmitted is different from the default settings (see specific message contents) |
| 2 |  |  | SS prompts the test operator to make an outgoing call. |
| 3 | ( | RRC CONNECTION REQUEST |  |
| 4 | ( | RRC CONNECTION SETUP | SS allocates PRACH and S-CCPCH resources to UE |
| 5 | ( | RRC CONNECTION COMPLETE | UE transmits this message to acknowledge the SETUP message and moves to CELL_FACH state. |
| 6 |  |  | SS checks to see that no MEASUREMENT REPORT messages are sent from UE to cell 1. |
| 7 |  |  | SS reconfigures the downlink transmission power, according to columns “T1” of Table 8.4.1.4-1. |
| 8 | ( | CELL UPDATE | UE shall detect that cell 4 has become stronger than cell 1. It sends this message after re-selecting to cell 4 |
| 9 | ( | CELL UPDATE CONFIRM | Use default message. |

Specific Message Content

All messages indicated below shall use the same content as described in default message content, with the following exceptions:

System Information Block type 11 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| SIB12 Indicator FACH measurement occasion info - FACH Measurement occasion cycle length coefficient - Inter-frequency FDD measurement indicator - Inter-frequency TDD measurement indicator - Inter-RAT measurement indicators Measurement control system information - Intra-frequency measurement system information - Inter-frequency measurement system information - Inter-frequency measurement identity - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and re-selection info - Qoffsets,n - Maximum allowed UL TX power - HCS neighbouring cell information - Qqualmin, Qrxlevmin - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | FALSE 2 TRUE FALSE Not Present Not Present 1 No inter-frequency cells removed Set to id of cell 4 Set to uplink UARFCN of cell 4 Set to the downlink UARFCN of cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE 0 dB 0 dBm Not Present -20dB, -115dBm Not Present Not Present Not Present |

RRC CONNECTION REQUEST (Step 3)

| Information Element | Value/Remarks |
| --- | --- |
| Establishment cause Measured results on RACH | Check to see if set to originating call of the compatible traffic class supported by the UE Check to see if this IE is absent |

RRC CONNECTION SETUP (Step 4)

Use the message sub-type in default message content defined in Annex A, which is marked as “Transition to CELL_FACH”.

CELL UPDATE (Step 8)

| Information Element | Value/Remarks |
| --- | --- |
| U-RNTI Integrity check info AM_RLC error indication (for C-plane) AM_RLC error indication (for U-plane) START List Cell update cause Protocol error info Measured results on RACH Protocol error information | Check to see if same to value as in RRC CONNECTION SETUP message Check to see if it is absent Check to see if it is set to FALSE Check to see if it is set to FALSE Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if it is set to “Cell Reselection” Check to see if it is absent or set to FALSE Check to see if it is absent Check to see if it is absent |

CELL UPDATE CONFIRM (Step 9)

Use the message sub-type in default message content defined in Annex A.

8.4.1.4.5	Test Requirement

After step 5 the UE shall not transmit any MEASUREMENT REPORT messages pertaining to the measurement of CPICH Ec/No quantity for cell 4.

After step 7 the UE shall reselect to cell 4 and transmit a CELL UPDATE message on the uplink CCCH of cell 4.

#### 8.4.1.5  	Measurement Control and Report: Intra-frequency measurement for transition from CELL_DCH to CELL_FACH state

8.4.1.5.1		Definition

8.4.1.5.2	Conformance requirement

After entering CELL_FACH state from CELL_DCH state, the UE shall stop intra-frequency type measurement reporting assigned in a previous MEASUREMENT CONTROL message.  After transition to CELL_FACH state, the UE shall start to monitor neighbouring cells listed in the “intra-frequency cell info” received in System Information Block type 11 or 12.  The UE shall apply the reporting criteria specified in System Information Block type 11 or 12 messages, after a subsequent return to CELL_DCH state.  If requested to perform measurement reporting on RACH channels, the UE shall append the measured results when transmitting uplink RACH messages.

Reference

3GPP TS 25.331, clause 8.4.1.6.1

8.4.1.5.3	Test Purpose

To confirm that the UE stops to perform intra-frequency measurement reporting specified in a previously received MEASUREMENT CONTROL message, when it moves from CELL_DCH state to CELL_FACH state.  To confirm that the UE read the System Information Block type 11 or 12 messages when in CELL_FACH state and starts to monitor the neighbouring cells as indicated in these messages.  To confirm that the UE performs measurements on uplink RACH channel and appends the measured results in RACH messages, when requested in the system information messages.

8.4.1.5.4	Method of test

Initial Condition

System Simulator: 3 cells –  The initial configurations of the 3 cells in the SS should follow the values indicated in the column marked “T0” in table 8.4.1.14-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-registered idle mode (state 2) or PS-registered idle mode (state 3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.5-1 illustrates the downlink power to be applied for the 3 cells at various time instants of the test execution.  Column marked “T0” denotes the initial conditions, while columns marked “T1 are to be applied subsequently.  The exact instants on which these values shall be applied are described in the texts in this sub-clause.

Table 8.4.1.5-1

| Parameter | Unit | Cell 1 | Cell 2 | Cell 3 |
| --- | --- | --- | --- | --- |
|  |  | T0 | T1 | T0 | T1 | T0 | T1 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 1 | Ch. 1 |
|  | dB | 5.3 | 5.3 | 0.5 | 0.5 | Cell 3 is switched off | 3.3 |
| CPICH Ec/Io | dB | -12.1 | -13.5 | -16.9 | -18.3 |  | -15.5 |
| CPICH RSCP | dBm | -74.7 | -74.7 | -79.5 | -79.5 |  | -76.7 |

The UE is initially in idle mode and has selected cell 1 as the current cell.  The System Information Block type 11 message is modified from its default message contents, in order to prevent the UE’s reporting of CFN-SFN difference.  No measurement requirements are specified for the UE in any of the System Information Block type 11 or 12 messages.

SS then prompts the test operator to initiate an outgoing call of a supported traffic class.  When UE transmits a RRC CONNECTION REQUEST message on RACH, SS replies with RRC CONNECTION SETUP message.  Uplink and downlink DPCH physical channels are allocated.  Upon receiving RRC CONNECTION SETUP message, the UE shall transmit RRC CONNECTION SETUP COMPLETE message on DCCH and then moves to CELL_DCH state.  SS then sends a MEASUREMENT CONTROL message to UE.  In this message, the SS requests the establishment of an intra-frequency measurement task for the measurement of cell 2’s CPICH Ec/No.  At the same time, reporting of cell 2’s CPICH Ec/No is commanded with the reporting criteria set to “periodic reporting” and reporting interval set to 16 seconds.  The UE shall start transmitting MEASUREMENT REPORT messages at 16 seconds interval corresponding to the requested reporting event.

SS transmits PHYSICAL CHANNEL RECONFIGURATION message, triggering a switch of transport channels from DCH (UL)/DCH (DL) to RACH (UL)/FACH (DL).  After receiving this message, the UE shall reconfigure itself and reply with a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message on RACH.  SS acknowledges this message and the UE shall move to CELL_FACH state and read the System Information Block messages.  SS then monitors the uplink channels to verify that no MEASUREMENT REPORT messages are received.

SS reconfigures itself according to the settings in columns marked “T1” in table 8.4.1.5-1.  It then transmits System Information Block type 12 messages in cell 1, which indicates to include cell 3 into the neighbour cells monitoring list.  IEs ”Intra-frequency reporting quantity for RACH Reporting” and IE ”Maximum number of Reported cells on RACH” are also specified in these messages.  An event-triggered (event type 1a) reporting criterion is specified for intra-frequency measurements.  SS then pages for the UE using PAGING TYPE 1 message.  The UE shall respond with a CELL UPDATE message, which comprises measurement readings of CPICH Ec/No for cell 1 and cell 3.  Upon the receipt of CELL UPDATE message, SS replies with CELL UPDATE CONFIRM message on the downlink DCCH.  This message does not change the physical resources nor allocate any new RNTI identities.  SS transmits PHYSICAL CHANNEL RECONFIGURATION message again, allocating dedicated physical resources for both uplink and downlink directions to the UE.  The UE shall then send PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and return to CELL_DCH state.  SS listens to the uplink DCCH for MEASUREMENT REPORT messages.  SS verifies that all messages received pertain to the periodic measured value of cell 2’s CPICH Ec/No value.  UE shall not send any reports containing the measured values of cell 3.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 11 | UE is initially in idle mode in cell 1, and test operator is asked to make an outgoing call. |
| 2 | ( | RRC CONNECTION REQUEST |  |
| 3 | ( | RRC CONNECTION SETUP | Uplink and downlink DPCH resources are allocated. |
| 4 | ( | RRC CONNECTION SETUP COMPLETE | UE shall move to CELL_DCH state. |
| 5 | ( | MEASUREMENT CONTROL | SS requests for measurement and reporting of cell 2’s CPICH Ec/No value. |
| 6 | ( | MEASUREMENT REPORT | UE shall send periodic report at 16 seconds interval. SS waits for 2 consecutive reports. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS switches the physical resources to common physical channels. |
| 8 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall reconfigure its uplink and downlink channels before transiting to CELL_FACH state. |
| 9 | ( | System Information Block type 12 | SS reconfigures itself according to the settings stated in column “T1” of table 8.4.1.5-1. SIB type 12 indicates UE includes cell 3 into the monitored neighbour cell list. SS waits for 1 minute and verifies that no MEASUREMENT REPORT messages are detected on the uplink. |
| 10 | ( | PAGING TYPE 1 | SS pages for UE using the assigned U-RNTI identity. |
| 11 | ( | CELL UPDATE | UE shall transmit this message with measured results on RACH channels for cell 1 and cell 3 present in this message. |
| 12 | ( | CELL UPDATE CONFIRM | No changes in physical resource allocation and RNTI identities. |
| 13 | ( | PHYSICAL CHANNEL RECONFIGURATION | Allocates dedicated physical channels. |
| 14 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall transit to CELL_DCH state. |
| 15 | ( | MEASUREMENT REPORT | UE shall continue to report cell 2’s CPICH Ec/No value on a periodic basis. |

Specific Message Content

System Information Block type 11 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| SIB12 indicator FACH measurement occasion info Measurement control system information - Intra-frequency measurement system information - Inter-frequency measurement system information - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | FALSE Not Present Not Present Not Present Not Present Not Present Not Present |

RRC CONNECTION SETUP (Step 3)

Use the same message sub-type found in Annex A, which is entitled “Transition to CELL_DCH”.

MEASUREMENT CONTROL (Step 5)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info | 5 Setup Not Present Not Present Intra-frequency measurement Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE 0 CPICH Ec/No No report FALSE TRUE TRUE FALSE FALSE No report FALSE TRUE TRUE FALSE FALSE Not present Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Periodical reporting criteria Infinity 16 seconds Not Present |

MEASUREMENT REPORT (Step 6)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event results | Check to see if set to 5 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is present Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |

PHYSICAL CHANNEL RECONFIGURATION (Step 7)

Use the same message sub-type found in Annex A, which is entitled “(Packet to CELL_FACH from CELL_DCH in PS)”

System Information Block type 12 (Step 9)

| Information Element | Value/Remark |
| --- | --- |
| FACH measurement occasion info Measurement control system information - Intra-frequency measurement system information - Intra-frequency measurement identity - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Qoffsets,n - Maximum allowed UL TX power - HCS neighbouring cell information - Qqualmin, Qrxlevmin - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency measurement for RACH reporting - SFN-SFN observed time difference - Reporting quantity - Maximum number of reported cells on RACH - Reporting information for state CELL_DCH - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - CHOICE report criteria - Parameter required for each event - Intra-frequency event identity - Triggering condition 1 - Triggering condition 2 - Reporting range - Cells forbidden to affect reporting - CHOICE Mode - Primary CPICH info - Primary scrambling code - W - Hysteresis - Threshold used frequency - Reporting deactivation threshold - Replacement activation threshold - Time to trigger - Amount of reporting - Reporting Interval - Inter-frequency measurement system information - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | Not Present 6 Remove no intra-frequency cells Set to id of cell 3 0 dB 0 chips Set to same code as used for cell 3 Not Present FALSE FALSE 0dB 0dBm Not Present -20dB, -115dBm 0 CPICH Ec/No No report CPICH Ec/No Current cell + best neighbour No report FALSE TRUE TRUE FALSE FALSE No report FALSE TRUE TRUE FALSE FALSE Not present Intra-frequency measurement reporting criteria Only 1 reporting event is defined 1a Not Present Monitored set cells 3.0 dB Not present 0.0 FDD Set to scrambling code for cell 3 1.0 dB Not Present 7 Not Present 0 Infinity 8 seconds Not present Not present Not present Not present |

PAGING TYPE 1 (Step 10)

| Information Element | Value/Remarks |
| --- | --- |
| Page Record List - Page Record - CHOICE Paging originator - U-RNTI BCCH modification info | UTRAN Originator Set to same U-RNTI value as assigned in the RRC CONNECTION SETUP message Not Present |

CELL UPDATE (Step 11)

| Information Element | Value/Remarks |
| --- | --- |
| U-RNTI Integrity check info AM_RLC error indication (for C-plane) AM_RLC error indication (for U-plane) START List Cell update cause Protocol error info Measured results on RACH - Measurement result for current cell - CHOICE measurement quantity - CPICH Ec/No - Measurement results for monitored cells - SFN-SFN observed time difference - Primary CPICH info - Primary scrambling code - CHOICE measurement quantity - CPICH Ec/No Protocol error information | Check to see if same to value as in PAGING TYPE 1 message Check to see if it is absent Check to see if it is set to FALSE Check to see if it is set to FALSE Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if it is set to “Paging Response” Check to see if it is absent or set to FALSE Check to see if set to CPICH Ec/No Check to see if it is within acceptable range Not Checked Check to see if the same as cell 3’s code. Check to see if set to CPICH Ec/No Check to see if it is within acceptable range Check to see if it is absent |

PHYSICAL CHANNEL RECONFIGURATION (Step 13)

Use the same message sub-type found in Annex A, which is entitled “(Packet to CELL_DCH from CELL_FACH in PS)”

MEASUREMENT REPORT (Step 15)

| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event results | Check to see if set to 6 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is present Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |
| --- | --- |

8.4.1.5.5	Test Requirement

After step 5, the UE shall start to transmit MEASUREMENT REPORT messages at 16 seconds interval.  The message shall contain the measured result of cell 2’s CPICH Ec/No value.

After step 8, the UE shall not send any MEASUREMENT REPORT messages containing reporting quantities requested in MEASUREMENT CONTROL messages in step 5.

After step 10, the UE shall respond to the paging and transmit a CELL UPDATE message.  In this message, the measured values CPICH Ec/No for cell 1 and cell 3 shall be included.

After step 14, the UE shall follow measurement reporting mechanism specified in System Information Block type 12 messages sent in step 9.  It shall send MEASUREMENT REPORT messages containing estimates for cell 2’s CPICH Ec/No value.  The UE shall not transmit any MEASUREMENT REPORT messages, which report measurement quantities of cell 3.

#### 8.4.1.6  	Measurement Control and Report: Inter-frequency measurement for transition from CELL_DCH to CELL_FACH state

8.4.1.6.1		Definition

8.4.1.6.2	Conformance requirement

When transiting from CELL_DCH state to CELL_FACH state, the UE shall stop all measurement reporting activities related to inter-frequency measurements assigned in a MEASUREMENT CONTROL message.  After reaching CELL_FACH state, the UE shall begin to monitor neighbouring cells listed in the IE “inter-frequency cell info” specified in the System Information Block type 11 or 12 messages.

Reference

3GPP TS 25.331, clause 8.4.1.6.2

8.4.1.6.3	Test Purpose

To verify that UE ceases to transmit MEASUREMENT REPORT messages to report inter-frequency type measurements when moving from CELL_DCH state to CELL_FACH.  This requirement shall be observed even if the UE has detected that inter-frequency type measurement reporting criteria have been satisfied in CELL_FACH state.  To verify that the UE extracts information for inter-frequency measurement from System Information Block type 11 or 12 messages after reaching CELL_FACH state.

8.4.1.6.4	Method of test

Initial Condition

System Simulator: 2 cells – The initial configurations of the 2 cells in the SS should follow the values indicated in the columns marked “T0” in table 8.4.1.6-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-registered idle mode (state 2) or PS-registered idle mode (state 3) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.6-1 illustrates the downlink power to be applied for the 2 cells at various time instants of the test execution.  Columns marked “T0” denote the initial conditions, while columns marked “T1 are to be applied subsequently.  The exact instants on which these values shall be applied are described in the texts in this sub-clause.

Table 8.4.1.6-1

| Parameter | Unit | Cell 1 | Cell 4 |
| --- | --- | --- | --- |
|  |  | T0 | T1 | T0 | T1 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 2 |
|  | dB | 9.5 | -1.5 | -1.5 | 9.5 |
| CPICH Ec/Io | dB | -10.5 | -13.8 | -13.8 | -10.5 |
| CPICH RSCP | dBm | -70.5 | -81.5 | -81.5 | -70.5 |

The UE is initially in idle mode, after camping on cell 1.  SS prompts the test operator to initial an outgoing call for one of the supported traffic classes.  The System Information Block type 11 message is modified so that no measurement tasks are required of the UE.  The UE shall send a RRC CONNECTION REQUEST message on the uplink CCCH.  Upon receiving this message, SS allocates dedicated DPCH physical channels to the UE by transmitting RRC CONNECTION SETUP message. The UE shall reply by transmitting a RRC CONNECTION SETUP COMPLETE message.  SS then checks the IE ”Measurement Capability” of this message and verifies that the UE is capable of performing inter-frequency measurements under FDD mode.  After confirmation of the UE inter-frequency measurement capability, SS transmits PHYSICAL CHANNEL RECONFIGURATION message.  In this message, IE ”DPCH compressed mode info” is present, which indicates that the UE shall apply the given parameters for compressed mode operations.  The UE shall return a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message to acknowledge that compressed mode mechanism can be exercised.

SS then sends a MEASUREMENT CONTROL message to the UE, specifying that cell 4 be the measurement object for inter-frequency type measurement.  The periodic reporting criterion is selected for this measurement.  SS waits for 8 seconds to allow the periodic timer to expire.  The UE shall send a MEASUREMENT REPORT message containing measured result of cell 4’s measurement reporting quantity (CPICH Ec/No).  SS transmits PHYSICAL CHANNEL RECONFIGURATION message again, requesting the UE to switch from uplink and downlink DPCH to common physical channels.  The UE shall return a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and then move to CELL_FACH state.

SS modifies the contents of Master Information Block (MIB) and System Information Block (SIB) type 11.  In SIB 11, cell 4 is added to the neighbouring cell list in the “inter-frequency cell info” IE.  SS waits for 8 seconds to detect any possible uplink MEASUREMENT REPORT messages as a result of inter-frequency measurements.  SS then reconfigures the downlink transmission power settings of cell 1 and cell 4 according to the values stated in columns “T1” of Table 8.4.1.6-1.  SS waits for [x] seconds to allow the UE to perform cell re-selection.  The UE shall transmit a CELL UPDATE message on the uplink CCCH of cell 4, specifying the cause as “cell re-selection”.  SS replies with CELL UPDATE CONFIRM message on the downlink DCCH to complete the cell update procedure.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 11 | UE is initially in idle mode and camped onto cell 1. System Information Block type 11 is modified with respect to the default settings, in order to disable all measurement and reporting activities. |
| 2 |  |  | SS prompts the test operator to trigger an outgoing call for a supported traffic class |
| 3 | ( | RRC CONNECTION REQUEST |  |
| 4 | ( | RRC CONNECTION SETUP | Uplink and downlink DPCH resources are allocated. |
| 5 | ( | RRC CONNECTION SETUP COMPLETE | UE shall indicate that it’s capable of performing inter-frequency measurement for FDD mode. |
| 6 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS instructs UE to begin compressed mode operation. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall remain in CELL_DCH state. |
| 8 | ( | MEASUREMENT CONTROL | SS indicates that the CPICH Ec/No of cell 4 shall be monitored and reported. SS waits for 8 seconds. |
| 9 | ( | MEASUREMENT REPORT | UE shall transmit this message to report cell 4’s CPICH Ec/No value. |
| 10 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS changes the physical channel allocation to common channel configuration. |
| 11 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall moves to CELL_FACH state. |
| 12 | ( | Master Information Block, System Information Block type 11 | SS modifies MIB and SIB 11. Cell 4 is included in the neighbouring cells list for inter-frequency measurement |
| 13 |  |  | SS waits for 8 seconds to verify that no MEASUREMENT REPORT messages are detected. |
| 14 |  |  | SS changes the power settings for cell 1 and cell 4 according to columns marked “T1” of Table 8.4.1.6-1, and then waits for [x] seconds to allow the UE to re-select to a new cell. |
| 15 | ( | CELL UPDATE | UE shall determine that cell 4 has become the best cell and then perform cell re-selection procedure. |
| 16 | ( | CELL UPDATE CONFIRM |  |

Notes:

The value [x] seconds is TBD, after the cell re-selection duration is determined from TS 25.304.

Specific Message Content

System Information Block Type 11 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| References to other system information blocks FACH measurement occasion info - FACH Measurement occasion cycle length coefficient - Inter-frequency FDD measurement indicator - Inter-frequency TDD measurement indicator - Inter-RAT measurement indicators Measurement control system information - Intra-frequency measurement system information - Inter-frequency measurement system information - Inter-RAT measurement system information - Traffic volume measurement system information - UE Internal measurement system information | Not Present 2 FALSE FALSE Not Present Not Present Not Present Not Present Not Present Not Present |

RRC CONNECTION SETUP (Step 4)

Use the same message sub-type found in Clause 9 of TS 34.108, which is entitled “Transition to CELL_DCH”

RRC CONNECTION SETUP COMPLETE (Step 5)

| Information Element | Value/Remarks |
| --- | --- |
| START List - CN Domain Identity - START UE Radio access capability - ICS Version - PDCP capability - RLC capability - Transport channel capability - RF capability - Physical channel capability - UE multi-mode/multi-RAT capability - Security capability - LCS capability - Measurement capability - FDD measurements DL - TDD measurements DL - GSM measurements DL - GSM 900 DL - DCS 1800 DL - GSM 1900 DL - Multi-carrier measurement DL - FDD measurements UL - TDD measurements UL - GSM measurements UL - GSM 900 UL - DCS 1800 UL - GSM 1900 UL - Multi-carrier measurement UL UE system specific capability | Check to see if it is present for all supported CN domains Check to see if it is present for all supported CN domains Checked to see if set to ‘R99’ Not checked. Not checked. Not checked. Not checked. Not checked. Not checked. Not checked. Not checked. Checked to see if set to ‘TRUE’ Not checked. Not checked. Not checked. Not checked. Not checked. Not checked. Checked to see if set to ‘TRUE’ Not checked. Not checked. Not checked. Not checked. Not checked. Not checked. Not checked. |

PHYSICAL CHANNEL RECONFIGURATION (Step 6)

Use the same message sub-type found in Annex A, which is entitled “(Packet to CELL_DCH from CELL_DCH in PS)”, with the following exceptions in the IE(s) concerned:

| Information Element | Value/Remarks |
| --- | --- |
| Downlink information common for all radio links - Downlink DPCH info common for all RL - CHOICE Mode - Downlink DPCH power control information - DPC mode - DL rate matching restriction information - Spreading factor - Fixed or flexible position - TFCI existence - Number of bits for Pilot bits (SF=128, 256) - DPCH compressed mode info - TGPSI - TGPS Status Flag - TGCFN - Transmission gap pattern sequence configuration parameters - TGMP - TGPRC - TGCFN - TGSN - TGL1 - TGL2 - TGD - TGPL1 - TGPL2 - RPP - ITP - UL/DL Mode - Downlink compressed mode method - Uplink compressed mode method - Downlink frame type - DeltaSIR1 - DeltaSIRAfter1 - DeltaSIR2 - DeltaSIRAfter2 - TX Diversity Mode - SSDT information - S field - Code Word Set - Default DPCH Offset Value | FDD 0 (Single) Not Present Refer to the parameter set in TS 34.108 Flexible FALSE Not Present 1 Active 255 FDD Measurement 62 (Current CFN + (256 – TTI/10msec)) mod 256 8 10 5 15 35 35 Mode 1 Mode 1 DL SF/2 Not Present A 2.0 1.0 Not Present Not Present None Not Present 0 |

MEASUREMENT CONTROL (Step 8)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info | 15 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downlink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH Ec/No FALSE TRUE No report FALSE FALSE TRUE FALSE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not Present Periodic reporting criteria Infinity 8 seconds Not Present |

MEASUREMENT REPORT (Step 9)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to 15 Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 4 Check to see if set to the UARFCN of the downlink frequency for cell 4 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 4 Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent |

PHYSICAL CHANNEL RECONFIGURATION (Step 10)

Use the same message sub-type found in Annex A, which is entitled “(Packet to CELL_FACH from CELL_DCH in PS)”.2

Master Information Block (Step 12)

| Information Element | Value/Remarks |
| --- | --- |
| MIB value tag | 2 |

System Information Block type 11 (Step 12)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement control system information - Use of HCS - Cell_selection_and_reselection_-quality_measure - Intra-frequency measurement system information - Inter-frequency measurement system information - Inter-frequency cell info list - CHOICE Inter-frequency cell removal - New inter-frequency cells - Inter-frequency cell id - Frequency info - CHOICE mode - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - CHOICE Mode - Primary CPICH info - Primary scrambling code - Primary CPICH Tx power - Read SFN indicator - Cell selection and re-selection info - Inter-RAT measurement system information - Traffic volume measurement system information - UE Internal measurement system information | Not used CPICH_Ec/No Not Present No inter-frequency cells removed 0 FDD Set to uplink UARFCN for cell 4 Set to downlink UARFCN for cell 4 Not Present – use default of 0 dB Not Present FDD Set to the scrambling code of cell 4 Not Present FALSE Not Present Not Present Not Present Not Present |

CELL UPDATE (Step 15)

| Information Element | Value/Remarks |
| --- | --- |
| U-RNTI Integrity check info AM_RLC error indication (for C-plane) AM_RLC error indication (for U-plane) START List Cell update cause Protocol error info Measured results on RACH Protocol error information | Check to see if same to value as in RRC CONNECTION SETUP message Check to see if it is absent Check to see if it is set to FALSE Check to see if it is set to FALSE Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if it is set to “Cell Reselection” Check to see if it is absent or set to FALSE Check to see if it is absent Check to see if it is absent |

CELL UPDATE CONFIRM (Step 16)

Use the same message sub-type found in Annex A.

8.4.1.6.5	Test Requirement

After step 4 the UE shall transmit RRC CONNECTION SETUP COMPLETE message with the IE ”Measurement capability”, indicating that both uplink and downlink inter-frequency measurements for FDD mode are supported.

After step 8 the UE shall transmit MEASUREMENT REPORT message to report cell 4’s CPICH Ec/No value.

After step 11 the UE shall stop sending MEASUREMENT REPORT messages, which contain inter-frequency measured results for cell 4’s CPICH Ec/No value.

After step 14 the UE shall transmit CELL UPDATE message to inform that a cell reselection to cell 4 has occurred.

#### 8.4.1.7	Measurement Control and Report: Intra-frequency measurement for transition from CELL_FACH to CELL_DCH state

8.4.1.7.1		Definition

8.4.1.7.2	Conformance requirement

When transiting from CELL_FACH state to CELL_DCH state, the UE shall resume intra-frequency measurement if it has previously stored such a measurement context in CELL_DCH state, and if this measurement context is indicated to be resume in CELL_DCH state.  The UE shall also re-start the associated reporting activities for the resumed intra-frequency measurement.  If the UE has performed a cell reselection whilst out of CELL_DCH state, the UE shall not re-start intra-frequency measurement previously designated to be resumed in CELL_DCH state.

In the case when the UE is not assigned any measurement tasks, it shall continue to monitor the list of intra-frequency neighbouring cells stated in System Information Block type 11 or 12 messages.  It shall transmit MEASUREMENT REPORT messages when the reporting criteria (if specified in System Information Block type 11 or 12 messages) are met.  When in CELL_DCH state, the UE shall override existing measurement and reporting contexts obtained from listening to System Information Block type 11 or 12 messages, if a MEASUREMENT CONTROL message is received.  The UE shall then apply the new measurement and reporting parameters received in the MEASUREMENT CONTROL message.

Reference

3GPP TS 25.331, clause 8.4.1.7.1

8.4.1.7.3	Test Purpose

To confirm that UE resumes intra-frequency measurements and the associated reporting when it enters CELL_DCH state from CELL_FACH state, and that such measurement contexts (and optionally, the reporting context) have been stored for resumption in CELL_DCH state.  To confirm that the UE continues to monitor the intra-frequency neighbour cells i listed in the System Information Block type 11 or 12 messages, if no previously assigned measurements are present.  To confirm that the UE transmits MEASUREMENT REPORT messages if reporting conditions stated in System Information Block type 11 or 12 messages have been satisfied.  To confirm that a MEASUREMENT CONTROL message received in CELL_DCH state overrides the measurement and associated reporting contexts maintained in the UE by virtue of System Information Block type 11 or 12 messages.

8.4.1.7.4	Method of test

Initial Condition

System Simulator: 3 cells – The initial configurations of the 3 cells in the SS should follow the values indicated in the column marked “T0” in table 8.4.1.7-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-CELL_FACH_Initial (state 6-2) or PS-CELL_FACH_Initial (state 6-4) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.7-1 illustrates the downlink power to be applied for the 3 cells at various time instants of the test execution.  Column marked “T0” denotes the initial conditions, while columns marked “T1” are to be applied subsequently.  The exact instants on which these values shall be applied are described in the text in this sub-clause.

Table 8.4.1.7-1

| Para-meter | Unit | Cell 1 | Cell 2 | Cell 3 |
| --- | --- | --- | --- | --- |
|  |  | T0 | T1 | T0 | T1 | T0 | T1 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 1 | Ch. 1 |
|  | dB | 7.9 | -5.0 | 7.3 | 7.3 | 5.7 | 5.7 |
| CPICH Ec/Io | dB | -14.2 | -25.2 | -14.8 | -12.9 | -16.4 | -14.5 |
| CPICH RSCP | dBm | -72.1 | -85.0 | -72.7 | -72.7 | -74.3 | -74.3 |

The UE is brought to CELL_FACH state in cell 1, after it has successfully executed procedure P4 or P6 (depending on the CN domain supported by the UE) as specified in clause 7.4 of TS 34.108.  System Information Block type 12 message is changed with respect to the default message contents, specifying that cell 2 is to be included in the neighbouring cell list for intra-frequency measurement.  Event 1e is selected in IE ”Reporting information for state CELL_DCH”, and “Intra-frequency measurement quantity” is set to CPICH Ec/No.

SS send a PHYSICAL CHANNEL RECONFIGURATION message to UE, allocating dedicated physical channels on both uplink and downlink directions.  Upon receiving such a message, the UE shall return PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and then move to CELL_DCH state.  The UE shall send MEASUREMENT REPORT messages to indicate that the measured result of cell 2’s CPICH Ec/No value, as the measurement quantity has exceeded the threshold value in System Information Block type 12 messages.  After receiving the MEASUREMENT REPORT messages, SS transmits a MEASUREMENT CONTROL message in which it specifies that only intra-frequency measurement and periodic reporting for cell 3 ’s CPICH Ec/No shall be performed.  After receiving such a message, the UE shall transmit another set of MEASUREMENT REPORT messages.  SS verifies that only measurement readings for cell 3 ’s CPICH Ec/No are included in these messages.

Next, SS sends PHYSICAL CHANNEL RECONFIGURATION message to UE.  In this message, the physical channel resources are switched to common physical channels – PRACH for the uplink and S-CCPCH for the downlink.  The UE shall reply with a PHYSICAL CHANNEL RECONFIGURATION COMPLETE and transits to CELL_FACH.  SS waits for 16 seconds and checks the uplink RACH to confirm that no MEASUREMENT REPORT messages are received.  SS transmits MEASUREMENT CONTROL message on the downlink DCCH.  The key parameters specified in this message are: measurement command = ‘setup’, measurement type = ‘intra-frequency measurement’, measurement object = ‘cell 2’, reporting criteria = ‘periodic reporting’, measurement validity IE is present and “UE state” = “CELL_DCH”.  SS waits for 16 seconds, verifies that no MEASUREMENT REPORT messages are detected on the uplink DCCH, before sending another PHYSICAL CHANNEL RECONFIGURATION message, allocating DPCH physical channels to the UE.  UE shall then return to CELL_DCH state, start to monitor the neighbour cell specified by the SS in the latest MEASUREMENT CONTROL message while the UE was previously in CELL_FACH state.  The UE shall resume periodic reporting of cell 2’s CPICH RSCP measured results by sending MEASUREMENT REPORT messages.  Following the reception of the MEASUREMENT REPORT message, SS commands the UE to stop performing measurements and generation of reports for cell 2 CPICH RSCP.  Thereafter, SS verifies that no MEASUREMENT REPORT messages are detected.  After this requirement is satisfied, SS sends MEASUREMENT CONTROL on the downlink DCCH once more.  This message is identical to the one sent in step 10 (see specific message content).

In the next sequence, SS dispatches a PHYSICAL CHANNEL RECONFIGURATION message on the downlink DCCH.  In this message, common physical channel resources are assigned to the UE.  The UE shall respond with a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and then transit to CELL_FACH state.  SS monitor the uplink DCCH once more to verify that no MEASUREMENT REPORT messages are detected.  SS modifies the contents of Master Information Block and System Information Block type 12 messages, followed by a reconfiguration of the downlink transmission power of the respect cells according to the settings in columns “T1” in Table 8.4.1.7-1.  SS starts timer T305 and then waits for it to expire.  The UE shall discover an “out-of-service” condition and initiate a cell re-selection procedure.  This is verified in the SS when a CELL UPDATE message is received on the uplink CCCH with the “cell update cause” IE set to “cell reselection”.  SS transmits a CELL UPDATE CONFIRM message on the DCCH to end the cell update procedure.  Next, SS sends a PHYSICAL CHANNEL RECONFIGURATION message on the downlink DCCH, assigning DPCH channel in both uplink and downlink directions.  The UE shall respond with a PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and then return to CELL_DCH state.  SS checks that the UE does not generate any MEASUREMENT REPORT messages on the uplink DCCH.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 12 | UE is initially in CELL_FACH in cell1, after having successfully executed procedure P4 or P6, depending on the supported CN domain. Refer to clause 7.4 of TS 34.108 for details. System Information Block type 12 messages are changed according to the descriptions in “Specific Message Contents” sub-clause. |
| 2 | ( | PHYSICAL CHANNEL RECONFIGURATION | Allocates DPCH physical channels. |
| 3 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall move to CELL_DCH state. |
| 4 | ( | MEASUREMENT REPORT | Reports cell 2’s CPICH Ec/No measurement value. |
| 5 | ( | MEASUREMENT CONTROL | Specifies cell 3 as the measurement object for intra-frequency measurement. |
| 6 | ( | MEASUREMENT REPORT | UE shall report the estimated value for cell 3’s CPICH Ec/No reading only. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION | Allocates PRACH and S-CCPCH physical channels. |
| 8 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall move to CELL_FACH state. |
| 9 |  |  | SS waits for 16 seconds and checks that no MEASUREMENT REPORT messages are sent by UE. |
| 10 | ( | MEASUREMENT CONTROL | SS instructs the UE to perform intra-frequency measurement and reporting for cell 2. These activities should be resumed if the UE subsequently transits to CELL_DCH state again. |
| 11 |  |  | SS once again waits for 16 seconds and verifies that no MEASUREMENT REPORT messages are sent by UE. |
| 12 | ( | PHYSICAL CHANNEL RECONFIGURATION | DPCH physical channels are assigned to the UE in this message. |
| 13 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall return to CELL_DCH state. |
| 14 | ( | MEASUREMENT REPORT | UE begins to report cell 2’s measured results for CPICH RSCP again. |
| 15 | ( | MEASUREMENT CONTROL | Terminate all the intra-frequency measurement activity related to cell 2. |
| 16 |  |  | SS waits for 16 seconds and verifies that UE stop transmitting MEASUREMENT REPORT messages. |
| 17 | ( | MEASUREMENT CONTROL | This message is the same as in step 10 |
| 18 | ( | PHYSICAL CHANNEL RECONFIGURATION | Allocates PRACH and S-CCPCH physical channels. |
| 19 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall move to CELL_FACH state. |
| 20 |  |  | SS checks that no MEASUREMENT REPORT messages are received. |
| 21 | ( | Master Information Block System Information Block type 12 | System Information Block type 12 messages are modified to include cell 2 and cell 3 into neighbouring cells monitored list for intra-frequency type measurements. SS reconfigures the downlink transmission power settings for cell 1 to cell 3 according to columns “T1” in Table 8.4.1.7-1, runs timer T305, and then waits until T305 expires. |
| 22 | ( | CELL UPDATE | UE shall re-selects to cell 2 and then perform a cell update procedure. |
| 23 | ( | CELL UPDATE CONFIRM | UE shall stay in CELL_FACH state. |
| 24 | ( | PHYSICAL CHANNEL RECONFIGURATION | DPCH physical channels are assigned to the UE in this message. |
| 25 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall return to CELL_DCH state. |
| 26 |  |  | SS checks that no MEASUREMENT REPORT messages are received on uplink DCCH. |

Specific Message Content

System Information Block type 12 (Step 1)

| Information Element | Value/Remark |
| --- | --- |
| FACH measurement occasion info Measurement control system information - Intra-frequency measurement system information - Intra-frequency measurement identity - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency measurement for RACH reporting - Maximum number of reported cells on RACH - Reporting information for state CELL_DCH - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - CHOICE report criteria - Parameter required for each event - Intra-frequency event identity - Triggering condition 1 - Triggering condition 2 - Reporting range - Cells forbidden to affect reporting - CHOICE Mode - Primary CPICH Info - Primary scrambling code - W - Hysteresis - Threshold used frequency - Reporting deactivation threshold - Replacement activation threshold - Time to trigger - Amount of reporting - Reporting Interval - Reporting cell status - CHOICE reported cells - Maximum number of reported cells - Inter-frequency measurement system information - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | Not Present 10 Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE Not Present – use default values 0 CPICH Ec/No Not Present No report No report FALSE FALSE FALSE FALSE FALSE No report FALSE TRUE TRUE FALSE FALSE Not present Intra-frequency measurement reporting criteria 1e Not Present Monitored set cells Not present Not present FDD Set to the scrambling code of cell 2 Not present 0 dB -18 dB Not present Not present 0 Infinity 16 seconds Report cells within monitored set cells on used frequency 1 Not Present Not Present Not Present Not Present |

PHYSICAL CHANNEL RECONFIGURATION (Step 2, Step 12 and Step 24)

Use the same message sub-type found in Annex A, which is entitled “Packet to CELL_DCH from CELL_FACH in PS”

MEASUREMENT REPORT (Step 4)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results - CHOICE event result - Intra-frequency event identity - Cell measured event results - Primary CPICH info - Primary scrambling code | Check to see if set to 10 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is present Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s set to ‘Intra-frequency measurement event results’ Check to see if this IE is set to ‘1e’ Check to see if it’s the same code for cell 2 |

MEASUREMENT CONTROL (Step 5)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - Reporting cell status - Measurement validity - CHOICE report criteria - Parameters required for each event - Intra-frequency event identity - Triggering condition 1 - Triggering condition 2 - Reporting Range - Cells forbidden to affect Reporting range - CHOICE Mode - Primary CPICH Info - Primary Scrambling Code - W - Hysteresis - Reporting deactivation threshold - Replacement activation threshold - Reporting Threshold - Time to Trigger - Amount of reporting - Reporting interval - Reporting cell status - CHOICE reported cells - Maximum number of reported cells DPCH compressed mode status info | 11 Setup Not Present Not Present Intra-frequency measurement Remove no intra-frequency cells Set to id of cell 3 0 dB 0 chips Set to same code as used for cell 3 Not Present FALSE FALSE Not Present 0 CPICH Ec/No No report FALSE FALSE FALSE FALSE FALSE No report FALSE TRUE TRUE FALSE FALSE Not present Not present Not present Intra-frequency measurement criteria 1e Not Present Monitored set cells Not Present Not Present FDD Set to the same scrambling code for cell 3 Not Present 0 dB Not Present Not Present -19.5 dB 0 Infinity 16 seconds Report cells within monitored set cells on used frequency 1 Not Present |

MEASUREMENT REPORT (Step 6)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results - CHOICE event result - Intra-frequency event identity - Cell measured event results - Primary CPICH info - Primary scrambling code | Check to see if set to 11 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 3 Check to see if this IE is present absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s set to ‘Intra-frequency measurement event results’ Check to see if this IE is set to ‘1e’ Check to see if it’s the same code for cell 3 |

PHYSICAL CHANNEL RECONFIGURATION (Step 7 and 18)

Use the same message sub-type found in Annex A, which is entitled “Packet to CELL_FACH from CELL_DCH in PS”

MEASUREMENT CONTROL (Step 10 and 17)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Intra-frequency cell info list - CHOICE intra- frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - Reporting cell status - Measurement validity - UE state - CHOICE report criteria - Parameters required for each event - Intra-frequency event identity - Triggering condition 1 - Triggering condition 2 - Reporting Range - Cells forbidden to affect Reporting range - Primary CPICH Info - Primary Scrambling Code - W - Hysteresis - Reporting deactivation threshold - Replacement activation threshold - Reporting Threshold - Time to Trigger - Amount of reporting - Reporting interval - Reporting cell status - CHOICE reported cell - Maximum number of reported cells DPCH compressed mode status info | 12 Setup Not Present Not Present Intra-frequency measurement Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE Not Present 0 CPICH RSCP No report FALSE FALSE FALSE FALSE FALSE No report FALSE TRUE FALSE TRUE FALSE Not present Not present CELL_DCH Intra-frequency measurement criteria 1e Not Present Monitored set cells Not Present Not Present Set to the same scrambling code for cell 2 Not Present 0 dB Not Present Not Present -80 dBm 0 Infinity 16 seconds Report cells within monitored set cells on used frequency 1 Not Present |

MEASUREMENT REPORT (Step 14)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results - CHOICE event result - Intra-frequency event identity - Cell measured event results - Primary CPICH info - Primary scrambling code | Check to see if set to 12 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 2 Check to see if this IE is absent Check to see if this IE is present Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s set to ‘Intra-frequency measurement event results’ Check to see if this IE is set to ‘1e’ Check to see if it’s the same code for cell 2 |

MEASUREMENT CONTROL (Step 15)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE Measurement type DPCH compressed mode status info | 12 Release Not Present Not Present Not Present Not Present |

Master Information Block (Step 21)

| Information Element | Value/Remarks |
| --- | --- |
| MIB Value Tag | 2 |

System Information Block type 12 (Step 21)

| Information Element | Value/Remark |
| --- | --- |
| FACH measurement occasion info Measurement control system information - Use of HCS - Cell_selection_and_reselection_-quality_measure - Intra-frequency measurement system information - Intra-frequency measurement identity - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency measurement for RACH reporting - Maximum number of reported cells on RACH - Reporting information for state CELL_DCH - Inter-frequency measurement system information - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | Not Present Not used CPICH_Ec/No 13 Not Present Cell 2 and Cell 3 are added Remove no intra-frequency cells Set to id of cell 2 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE Not Present – use default values Set to id of cell 3 0 dB 0 chips Set to same code as used for cell 3 Not Present FALSE FALSE Not Present – use default values 0 CPICH Ec/No Not Present No report Not Present Not Present Not Present Not Present |

CELL UPDATE (Step 22)

| Information Element | Value/Remarks |
| --- | --- |
| U-RNTI - SRNC Identity - S-RNTI Integrity check info START List AM_RLC error indicator (for C-plane) AM_RLC error indicator (for U-plane) Cell Update Cause Protocol error indicator Measured results on RACH Protocol error information | Check to see if set to ‘0000 0000 0000 0001’ Check to see if set to ‘0000 0000 0000 0000 0000 0001’ Not checked Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE Check to see if set to ‘FALSE’ Check to see if set to ‘FALSE’ Check to see if set to ‘Cell Re-selection’ Check to see if it is absent or set to ‘FALSE’ Check to see if it is absent Check to see if it is absent |

CELL UPDATE CONFIRM (Step 23)

Use the default message content of the same message type in Annex A.

8.4.1.7.5	Test Requirement

After step 3 the UE shall report cell 2’s CPICH Ec/No value by transmitting MEASUREMENT REPORT messages.

After step 5 the UE shall delete all measurement and reporting contexts obtained from listening to System Information messages.  It shall transmit MEASUREMENT REPORT messages containing measured results of cell 3’s CPICH RSCP value only, in accordance to the contents of MEASUREMENT CONTROL message transmitted by SS in step 5.

After step 9 and step 11 the UE shall not transmit MEASUREMENT REPORT messages, which pertain to intra-frequency type measurement reporting.

After step 13 the UE shall resume the measurement and reporting activities as specified in MEASUREMENT CONTROL message received in step 10.  The UE shall transmit MEASUREMENT REPORT messages, containing measured results of cell 2’s CPICH RSCP value.

After step 15 the UE shall stop measurement activities pertaining to periodic reporting of cell 2’s CPICH RSCP, no MEASUREMENT REPORT messages shall be detectable by the SS on the uplink DCCH.

After step 21 the UE shall re-select to cell 2 and initiate a cell update procedure.  SS shall receive a CELL UPDATE message on the uplink CCCH of cell 2, with the “cell update cause” IE stated as “cell re-selection”.

After step 25 the UE shall not resume measurements and any associated reporting activities for cell 2’s CPICH RSCP, no MEASUREMENT REPORT messages shall be detectable by the SS in the uplink DCCH.

#### 8.4.1.8	Measurement Control and Report: Inter-frequency measurement for transition from CELL_FACH to CELL_DCH state

8.4.1.8.1		Definition

8.4.1.8.2	Conformance requirement

When transiting from CELL_FACH state to CELL_DCH state, the UE shall stop monitoring the list of inter-frequency neighbour cells indicated in System Information Block type 11 or 12 messages.  If the UE has a previously stored inter-frequency measurement context marked as ‘resume’ and for which the IE “UE state for reporting” has been assigned to “CELL_DCH”, it shall reinstate the suspended measurement and associated reporting activities after it has re-entered CELL_DCH state.  The UE shall be able to start or terminate inter-frequency measurements by decoding the “DPCH compressed mode status info” IE in MEASUREMENT CONTROL messages.

Reference

3GPP TS 25.331 clause 8.4.1.7.2

8.4.1.8.3	Test Purpose

To confirm that the UE erases all inter-frequency measurement contexts received from System Information Block type 11 or 12 while in CELL_FACH state, when it moves to CELL_DCH.  To confirm that the UE resumes inter-frequency measurements and reporting stored previously in the UE, after it moves to CELL_DCH state.  To confirm that the UE resumes inter-frequency measurement and reporting activities after it has received a MEASUREMENT CONTROL message specifying that a stored compressed mode pattern sequence be re-activated.

8.4.1.8.4	Method of test

Initial Condition

System Simulator: 3 cells – The initial configurations of the 3 cells in the SS should follow the values indicated in table 8.4.1.8-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-DCCH+DTCH_DCH (State 6-9) or PS-DCCH+DTCH_DCH (State 6-10) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.8-1 illustrates the downlink power to be applied for the 3 cells in this test.

Table 8.4.1.8-1

| Para-meter | Unit | Cell 1 | Cell 4 | Cell 5 |
| --- | --- | --- | --- | --- |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 2 | Ch. 2 |
|  | dB | 9.7 | 7.3 | 5.7 |
| CPICH Ec/Io | dB | -10.4 | -12.7 | -14.3 |
| CPICH RSCP | dBm | -70.3 | -72.7 | -74.3 |

The UE is in CELL_DCH state in cell 1, after successfully executing procedures P11 or P13 as specified in clause 7.4 of TS 34.108.  Next, SS transmits MEASUREMENT CONTROL message to request the UE to execute an inter-frequency measurement for cell 5.  The parameters of the reporting criteria are as follow: event-triggered with event identity =’2c’, reporting quantity = “CPICH RSCP”, threshold for non-used frequency = ‘-85 dBm’, hysteresis = ‘1.0dB’, time to trigger = ‘10 seconds’, amount of reporting = ‘1’ and reporting interval = ‘0’.  In the same message, IE ”Measurement validity” is present and “UE state” is assigned the value ‘CELL_DCH’.  SS checks that no MEASUREMENT REPORT messages are detected on the uplink DCCH after it has transmitted the MEASUREMENT CONTROL message.

Following this action, SS sends a PHYSICAL CHANNEL RECONFIGURATION message on the downlink DCCH and commands the UE to change its physical channel to PRACH and S-CCPCH.  SS modifies the content of System Information Block type 12 messages, such that cell 4 is included in the list of neighbouring cells to be monitored for inter-frequency measurements.  Once again, SS verifies that the UE does not transmit MEASUREMENT REPORT messages in the uplink direction.

SS sends PHYSICAL CHANNEL RECONFIGURATION message to allocate dedicated physical channels to the UE. In this message, SS commands the UE to start applying compressed mode mechanism for DPCH.  The UE shall reply with PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and then move to CELL_DCH state.  SS waits for 10 seconds.  The UE shall transmit MEASUREMENT REPORT message, containing the selected frequency quality estimate (in this case CPICH Ec/No) of cell 5.  SS verifies that this message does not contain measured results for cell 4.  After sending this message, the UE shall not transmit any more MEASUREMENT REPORT messages.

SS modifies the reporting criteria by transmitting a MEASUREMENT CONTROL message on the downlink DCCH using AM-RLC.  In this message, SS commands the UE to perform inter-frequency measurement and reporting for cell 5 using periodic reporting mechanism.  Upon receiving this message, the UE shall transmit MEASUREMENT REPORT message at 2 seconds interval.  In the next sequence, SS transmits a PHYSICAL CHANNEL RECONFIGURATION message and deactivates the compressed mode pattern sequence with “TGPSI” IE set to 1.  The UE shall respond by sending PHYSICAL CHANNEL RECONFIGURATION COMPLETE message and also stop the periodic reporting activities.   Following this, SS sends a MEASUREMENT CONTROL message and re-activates the compressed mode pattern sequence by using the “DPCH compressed mode status” IE.  SS confirms that the UE has reconfigured itself to start measurement reporting again.  The SS shall be able to receive MEASUREMENT REPORT messages continuously at 2 seconds interval.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The initial state of UE is in CELL_DCH state of cell 1, after executing procedure P11 or P13, depending on the supported CN domain. Refer to clause 7.4 of TS 34.108. |
| 2 | ( | MEASUREMENT CONTROL | SS specifies inter-frequency measurement and reporting parameters for cell 5, with “measurement validity” IE present and “UE state” set to “CELL_DCH”. |
| 3 |  |  | SS checks that no MEASUREMENT REPORT messages are detected on the uplink DCCH. |
| 4 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS allocates PRACH and S-CCPCH physical resources. |
| 5 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE shall moves to CELL_FACH state. |
| 6 | ( | System Information Block type 12 | SS modifies SIB 12 in order to include cell 4 into the neighbour cell list for inter-frequency measurements. |
| 7 |  |  | SS confirms that there are no transmissions of MEASUREMENT REPORT message in the uplink direction. |
| 8 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS allocates DPCH physical channels and specifies compressed mode parameters |
| 9 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE moves to CELL_DCH state. |
| 10 | ( | MEASUREMENT REPORT | UE shall resume inter-frequency measurement task for cell 5 and transmit this message to report the measured CPICH Ec/No value |
| 11 | ( | MEASUREMENT CONTROL | SS changes the reporting criteria for cell 5 to ‘periodic reporting’ |
| 12 | ( | MEASUREMENT REPORT | UE shall begin to transmit this message at 2 seconds interval. |
| 13 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS deactivates the currently used pattern sequence for compressed mode operation. |
| 14 | ( | PHYSICAL CHANNEL RECONFIGURATION COMPLETE | UE stays in CELL_DCH state. SS verifies that no MEASUREMENT REPORT messages are received. |
| 15 | ( | MEASUREMENT CONTROL | SS activates the pattern sequence stored by the UE. |
| 16 | ( | MEASUREMENT REPORT | SS checks that MEASURE-MENT REPORT messages are received at 2 seconds interval. |

Specific Message Content

MEASUREMENT CONTROL (Step 2)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - Measurement validity - UE State - Inter-frequency set update - CHOICE report criteria - Parameters required for each event - Inter-frequency event identity - Threshold used frequency - W used frequency - Hysteresis - Time to trigger - Reporting cell status - Parameters required for each non-used frequency - Threshold non used frequency - W non-used frequency DPCH compressed mode status info | 14 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 5 UARFCN of the uplink frequency for cell 5 UARFCN of the downlink frequency for cell 5 0 dB 0 chips Set to same code as used for cell 5 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH Ec/No FALSE TRUE No report FALSE TRUE FALSE TRUE FALSE Not present CELL_DCH Not Present Inter-frequency measurement reporting criteria 2c Not Present Not Present 1.0 dB 10 seconds Not Present -85 dBm 0.0 Not Present |

PHYSICAL CHANNEL RECONFIGURATION (Step 4)

Use the same message sub-type found in Annex A titled “(Packet to CELL_FACH from CELL_DCH in PS)”.

System Information Block type 12 (Step 6)

| Information Element | Value/Remark |
| --- | --- |
| FACH measurement occasion info - FACH Measurement occasion cycle length coefficient - Inter-frequency FDD measurement indicator - Inter-frequency TDD measurement indicator - Inter-RAT measurement indicators Measurement control system information - Intra-frequency measurement system information - Inter-frequency measurement system information - Inter-frequency cell info list - CHOICE inter-frequency cells removal - New inter-frequency info list - Inter-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Cell selection and Re-selection info - Inter-RAT measurement system information - Traffic volume measurement system information - UE internal measurement system information | 2 TRUE FALSE Not Present Not Present No inter-frequency cells removed Set to id of cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Not Present – use default values Not Present Not Present Not Present |

PHYSICAL CHANNEL RECONFIGURATION (Step 8)

Use the same message sub-type found in Annex A, which is entitled “(Packet to CELL_DCH from CELL_FACH in PS)”, with the following exceptions in the IE(s) concerned:

| Information Element | Value/Remarks |
| --- | --- |
| Downlink information common for all radio links - Downlink DPCH info common for all RL - CHOICE Mode - Downlink DPCH power control information - DPC mode - DL rate matching restriction information - Spreading factor - Fixed or flexible position - TFCI existence - Number of bits for Pilot bits (SF=128, 256) - DPCH compressed mode info - TGPSI - TGPS Status Flag - TGCFN - Transmission gap pattern sequence configuration parameters - TGMP - TGPRC - TGCFN - TGSN - TGL1 - TGL2 - TGD - TGPL1 - TGPL2 - RPP - ITP - UL/DL Mode - Downlink compressed mode method - Uplink compressed mode method - Downlink frame type - DeltaSIR1 - DeltaSIRAfter1 - DeltaSIR2 - DeltaSIRAfter2 - TX Diversity Mode - SSDT information - Default DPCH Offset Value | FDD 0 (Single) Not Present Refer to the parameter set in TS 34.108 Flexible FALSE Not Present 1 Active 255 FDD Measurement 62 (Current CFN + (256 – TTI/10msec)) mod 256 8 10 5 15 35 35 Mode 1 Mode 1 DL SF/2 Not Present A 2.0 1.0 Not Present Not Present None Not Present 0 |

MEASUREMENT REPORT (Step 10)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results - CHOICE event result - Inter-frequency event identity - Inter-frequency cells - Frequency Info - UARFCN (uplink) - UARFCN (downlink) - Non frequency related measurement event results - Primary CPICH Info - Primary Scrambling Code | Check to see if set to 14 Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 5 Check to see if set to the UARFCN of the downlink frequency for cell 5 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 5 Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent Inter-frequency event results Check to see if it’s set to ‘2c’ Check to see if set to the UARFCN of the uplink frequency for cell 5 Check to see if set to the UARFCN of the downlink frequency for cell 5 Check to see if set to the same code for cell 5 |

MEASUREMENT CONTROL (Step 11)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info | 14 Modify Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 5 UARFCN of the uplink frequency for cell 5 UARFCN of the downlink frequency for cell 5 0 dB 0 chips Set to same code as used for cell 5 Not Present FALSE FALSE Inter-frequency reporting criteria 1 CPICH Ec/No FALSE TRUE No report FALSE TRUE FALSE TRUE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not Present Not Present Periodic reporting criteria Infinity 2000 milliseconds Not Present |

MEASUREMENT REPORT (Step 12, 16)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss - CFN-SFN observed time difference Measured Results on RACH Event Results | Check to see if set to 14 Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 5 Check to see if set to the UARFCN of the downlink frequency for cell 5 Check to see if it is absent Check to see if set to the id of cell 5 Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 5 Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent |

PHYSICAL CHANNEL RECONFIGURATION (Step 13)

Use the same message transmitted in step 8 with the following modifications:

| Information Element | Value/Remarks |
| --- | --- |
| Downlink information common for all radio links - DPCH compressed mode info - TGPSI - TGPS Status Flag - TGCFN - Transmission gap pattern sequence configuration parameters | 1 Inactive 255 Not Present |

MEASUREMENT CONTROL (Step 15)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type DPCH compressed mode status info - Transmission gap pattern sequence - TGPSI - TGPS Flag - TGCFN | Any number except 14 Modify Not Present Not Present Not Present 1 Active 255 |

8.4.1.8.5	Test Requirement

After step 2 the UE shall not send any MEASUREMENT REPORT messages on the uplink DCCH of cell 1.

After step 9 the UE shall transmit a MEASUREMENT REPORT message, containing the measured results for cell 5’s CPICH Ec/No value.  The UE shall not transmit any messages pertaining to cell 4’s measurements.

After step 11 the UE shall send MEASUREMENT REPORT messages, which comprises cell 5’s CPICH Ec/No measured value at 2 seconds interval.  The “Event results” IE shall be omitted in these messages.

After step 14 the UE shall not transmit any MEASUREMENT REPORT messages.

After step 15 the UE shall resume the transmission of MEASUREMENT REPORT messages with identical contents as in those received after step 9.

#### 8.4.1.9  	Measurement Control and Report: Unsupported measurement in the UE

8.4.1.9.1		Definition

8.4.1.9.2	Conformance requirement

If the UTRAN indicates the UE to perform a measurement that is not supported in the UE, the UE shall keep the measurement configuration.  Then the UE shall transmit a MEASUREMENT CONTROL FAILURE message on the DCCH using AM RLC within 8 frames (excluding the effect of TTI mis-alignment).

Reference

3GPP TS 25.331 clause 8.4.1

8.4.1.9.3	Test purpose

To confirm that the UE transmits a MEASUREMENT CONTROL FAILURE message, with the value “unsupported measurement” specified in IE ”failure cause” when the SS commanded the UE to perform an unsupported measurement by sending a MEASUREMENT CONTROL message.

8.4.1.9.4	Method of test

Initial Condition

System Simulator: 1cell

UE: CS-DCCH_DCH (State 6-5) or PS-DCCH_DCH (State 6-7) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

[Editor’s note: It is assumed in this test that the UE under test does not possess any inter-RAT measurement capability.  The mandatory type(s) of measurement capability that should be implemented by the UE is to be discussed]

Test Procedure

The UE is in the CELL_DCH state. The SS transmits a MEASUREMEN CONTROL message which includes parameters (e.g. Measurement identity number: 2, measurement command: Setup, measurement type: inter-RAT measurements, measurement reporting mode: unacknowledged and periodical reporting, measurement object: inter-RAT cell information, measurement quantity: Signal strength, reporting quantity: RSSI on BCCH carrier). As the UE under test does not support inter-RAT measurement, it shall transmit a MEASUREMENT CONTROL FAILURE message on the uplink DCCH using AM RLC.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is in the CELL_DCH state. |
| 2 | ( | MEASUREMENT CONTROL | Including the parameters (e.g. Measurement identity number: 2, measurement command: Setup, measurement type: inter-RAT measurements, measurement reporting mode: unacknowledged and periodical reporting, measurement object: inter-RAT cell information, measurement quantity: Signal strength, reporting quantity: RSSI on BCCH carrier). |
| 3 | ( | MEASUREMENT CONTROL FAILURE | Which is set to “unsupported measurement” in IE “failure cause”. SS calculates the time interval between the transmissions of MEASUREMENT CONTROL message on the downlink DCCH to the uplink reception of MEASUREMENT CONTROL FAILURE on the uplink DCCH. SS verifies that the calculated time interval is within (8 frames + TTI) |

Specific Message Content

MEASUREMENT CONTROL (Step 2)

| Information Element | Value/Remark |
| --- | --- |
| RRC transaction identifier Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-RAT cell info list - CHOICE inter-RAT cell removal - New inter-RAT cells - Inter-RAT cell id - CHOICE Radio Access Technology - Cell selection and re-selection info - BSIC - BSIC ARFCN - Output power - Inter-RAT measurement quantity - CHOICE system - Measurement quantity - Filter Coefficient - BSIC verification required - Inter-RAT reporting quantity - UTRAN estimate quantity - CHOICE system - Pathloss - Observed time difference to GSM cell - GSM Carrier RSSI - Reporting cell status - CHOICE report criteria DPCH compressed mode status info | Select an arbitrary an integer between 0 and 3 2 Setup Unacknowledged mode Not Present Inter-RAT measurement Remove no inter-RAT cells 1 GSM Not Present Set to the BSIC code of cell 2 Set to the ARFCN assigned to cell 2 Not Present GSM GSM Carrier RSSI 0 Not required FALSE GSM FALSE FALSE TRUE Not Present No reporting Not Present |

MEASUREMENT CONTROL FAILURE (Step 3)

| Information Element | Value/Remarks |
| --- | --- |
| RRC transaction identifier Failure cause | Check if it is set to the same value of the same IE in the MEASUREMENT CONTROL message sent in Step 2. Check if it is set to “Unsupported measurement” |

8.4.1.9.5	Test requirement

After step 2 the UE shall identify the unsupported measurement element in the MEASUREMENT CONTROL message and transmit a MEASUREMENT CONTROL FAILURE.  In this message, the value “unsupported measurement” shall be specified in IE ”failure cause”.  SS shall be able to receive the MEASUREMENT CONTROL FAILURE message on the uplink DCCH, within a time interval of (8 frames + Transmission Time Interval) from the sending of the last transport block that contains the downlink MEASUREMENT CONTROL message.

#### 8.4.1.10 	Measurement Control and Report: Failure (Invalid Message Reception)

8.4.1.10.1	Definition

8.4.1.10.2	Conformance requirement

When the UE received a MEASUREMENT CONTROL message containing an unexpected conditional IE, it shall reply with a MEASUREMENT CONTROL FAILURE message stating the appropriate protocol error information.  The UE shall transmit the MEASUREMENT CONTROL FAILURE message at the latest of 8 frames (excluding the effect of TTI mis-alignment), after SS has sent the last transport block containing the downlink MEASUREMENT CONTROL message.  It shall maintain the monitoring and measurement reporting mechanism as in before the MEASUREMENT CONTROL message has been received.

Reference

3GPP TS 25.331 clause 8.4.1.9

8.4.1.10.3	Test Purpose

To confirm that the UE does not change its current monitoring and measurement settings after it has received an illegal MEASUREMENT CONTROL message, which contains an unexpected IE error.  To confirm that the UE resume its normal measurement reporting operations after transmitting MEASUREMENT CONTROL FAILURE message to the SS.

8.4.1.10.4	Method of test

Initial Condition

System Simulator: 1 cell.

UE: CS-DCCH_DCH (State 6-5) or PS-DCCH_DCH (State 6-7) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

The UE is initially brought to CELL_DCH.  SS transmits a MEASUREMENT CONTROL message to the UE, commanding it to start transmitting report messages for the reporting quantity “UE Transmitted Power”.  SS then waits for the MEASUREMENT RERORT message with the allocated measurement identity to arrive.  Then it transmits the MEASUREMENT CONTROL message again.  In this message, SS requests that the reporting activities for  “UE Transmitted Power” be stopped.  At the end of this message, SS appends an unknown information element.  When the UE receives this message, it shall reply with MEASURMENT CONTROL FAILURE message as it has detected a protocol error.  It shall not cease to report its own transmission power level using MEASUREMENT REPORT messages.

Expected Sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | The UE is CELL_DCH state in cell 1. |
| 2 | ( | MEASUREMENT CONTROL | SS transmits this message on downlink DCCH to instruct UE to start reporting the quantity “UE transmit power”. |
| 3 | ( | MEASUREMENT REPORT | UE shall send this message periodically at 32 seconds interval |
| 4 | ( | MEASURMENT CONTROL | SS sends a MEASUREMENT CONTROL message to request that UE stop the reporting activity. |
| 5 | ( | MEASUREMENT CONTROL FAILURE | UE shall maintain its current measurement context and send this message. SS calculates the time interval between the transmissions of MEASUREMENT CONTROL message in step 4 to the uplink reception of MEASUREMENT CONTROL FAILURE message. SS verifies that the calculated time interval is within (8 frames + TTI) |
| 6 | ( | MEASUREMENT REPORT | 32 seconds after step 3, UE shall continue to transmit this message to the SS. |

Specific Message Content

MEASUREMENT CONTROL (Step 2)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - UE internal measurement quantity - Measurement quantity - Filter coefficient - UE internal reporting quantity - UE Transmitted Power - UE Rx-Tx time difference CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info | 3 Setup Not Present Not Present UE internal measurement UE Transmitted Power 0 TRUE FALSE Periodical reporting criteria Infinity 32 seconds Not Present |

MEASUREMENT REPORT (Step 3)

| Information Element | Value/Remarks |
| --- | --- |
| Measurement identity Measured Results CHOICE measurement - UE Transmitted Power - UE Rx-Tx report entries Measured Results on RACH Event Results | Check to see if set to 3 Check to see if set to “UE internal measurement” Check to see if the reported power is compatible with RF class Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |

MEASUREMENT CONTROL (Step 4)

| Information Element | Value/Remark |
| --- | --- |
| RRC transaction identifier Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type DPCH compressed mode status info | Selects an arbitrary integer between 0 and 3 3 Stop Not Present Not Present Contains an arbitrary value Not Present |

MEASUREMENT CONTROL FAILURE (Step 5)

| Information Element | Value/Remark |
| --- | --- |
| RRC transaction identifier Failure cause Protocol error information | Check if it is set to the same value of the same IE in the MEASUREMENT CONTROL message sent in Step 4. Check to see if set to “protocol error” Check to see if set to “Message extension not comprehended” |

MEASUREMENT REPORT (Step 6)

Same as in the requirement for step 3

8.4.1.10.5	Test Requirement

After step 4 the UE shall transmit MEASUREMENT CONTROL FAILURE message, stating the IE ”failure cause” as “protocol error” and IE ”protocol error information” as “message extension not comprehended”.  SS shall be able to receive the MEASUREMENT CONTROL FAILURE message on the uplink DCCH, within a time interval of (8 frames + Transmission Time Interval) from the sending of the last transport block that contains the downlink MEASUREMENT CONTROL message in step 4.  The UE shall continue to send MEASUREMENT REPORT with the correct identity number and measurement result entries at approximately 32 seconds interval.

#### 8.4.1.11	Measurement Control and Report: Compressed Mode Configuration Failure during radio bearer reconfiguration procedure

8.4.1.11.1	Definition

8.4.1.11.2	Conformance requirement

During a radio bearer reconfiguration procedure, the UTRAN might request the activation of a new transmission gap pattern sequence configuration.  If the UE detects a runtime error due to overlapping compressed mode configuration (when transmission gap pattern sequences create transmission gaps in the same frame), it shall delete the transmission gap pattern sequence configuration associated with highest value of TGPSI.  The UE shall also terminate any inter-frequency measurements corresponding to the deleted transmission gap pattern sequence.  Finally, the UE shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM-RLC, with the cause value in IE "failure cause" set to "compressed mode runtime error".

Reference

3GPP TS 25.331  clause 8.2.2, clause 8.2.11, clause 8.6.6.15

8.4.1.11.3	Test purpose

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the uplink DCCH using AM RLC, if it receives a RADIO BEARER RECONFIGURATION message which includes IE “DPCH compressed mode info” that causes an illegal overlap involving more than one parallel transmission gap pattern sequences.  To confirm that the UE terminate any inter-frequency measurements corresponding to the deleted transmission gap pattern sequence

8.4.1.11.4	Method of test

Initial Condition

System Simulator: 2 cells – both cell 1 and cell 4 are active.  See Table 8.4.1.11-1 for the power settings.

UE: CS-DCCH+DTCH_DCH (State 6-9) or PS-DCCH+DTCH_DCH (State 6-10) as specified in TS34.108 clause 7.4, depending on the CN domain supported.

Test Procedure

Table 8.4.1.11-1 illustrates the downlink power to be applied for the 2 cells in this test case.

Table 8.4.1.11-1

| Parameter | Unit | Cell 1 | Cell 4 |
| --- | --- | --- | --- |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 2 |
|  | dB | 5.7 | 2.3 |
| CPICH Ec/Io | dB | -11.0 | -12.0 |
| CPICH RSCP | dBm | -74.3 | -77.7 |

The UE is in the CELL_DCH state in cell 1.  SS sends a MEASUREMENT CONTROL message on the downlink DCCH to request the UE to start inter-frequency measurement for cell 4’s CPICH Ec/No value.  Simultaneously, the stored transmission gap pattern sequence configuration associated with TGPSI=1 is indicated to be activated in this message.  Upon the reception of this message, the UE shall transmit MEASUREMENT REPORT messages periodically at 16 seconds interval to report cell 4’s measurement results.  Next, SS sends a second MEASUREMENT CONTROL message.  In this message, a new measurement task is to be established for the measurement and reporting of cell 4’s CPICH RSCP value on a periodic basis.  A deactivated transmission pattern gap sequence configuration (with TGPSI=2) is associated with this new measurement task.

The SS transmits a RADIO BEARER RECONFIGURATION message and commands the activation of transmission gap pattern sequence with TGPSI=2.  This is expected to result in the detection of a runtime error due to overlapping compressed mode configuration.  The UE then shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM-RLC.  In this message, the value of IE ” failure cause” shall be set to “compressed mode runtime error”.  The UE shall terminate all inter-frequency measurement tasks associated with TGPSI=2.  However, the UE shall continue to send MEASUREMENT REPORT messages to report cell 4’s CPICH Ec/No value, which is measured during the transmission gap created by compressed mode configuration corresponding to TGPSI=1.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | UE is initially in CELL_DCH state. |
| 2 | ( | MEASUREMENT CONTROL | Start inter-frequency measurements for cell 4’s CPICH Ec/No using transmission gap pattern sequence with TGPSI=1. |
| 3 | ( | MEASUREMENT REPORT | UE reports cell 4’s CPICH Ec/No readings periodically. |
| 4 | ( | MEASUREMENT CONTROL | Assign inter-frequency measurements for cell 4’s CPICH RSCP. This measurement task is associated with transmission gap pattern sequence with TGPSI=2, which has not been activated yet. |
| 5 | ( | RADIO BEARER RECONFIGURATION | SS specifies the parameters for transmission gap pattern sequence with TGPSI=2 and activate it simultaneously |
| 6 |  |  | UE shall delete transmission gap pattern sequence configuration associated with TGPSI=2. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | Failure cause shall be set to “Compressed mode runtime error” |
| 8 | ( | MEASUREMENT REPORT | The contents shall be the same as that in step 3. |

Specific Message Contents

MEASUREMENT CONTROL (Step 2)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 1 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH Ec/No FALSE TRUE No report FALSE FALSE TRUE FALSE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 1 Active 255 |

MEASUREMENT REPORT (Step 3 and 8)

| Information Element | Value/Remarks |
| --- | --- |
| Integrity check info | If integrity protection is activated, this IE shall be present and SS checks that the MAC-I value matches with the calculated X-MAC value. Else, this IE shall be absent. |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to “1” Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 4 Check to see if set to the UARFCN of the downlink frequency for cell 4 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 4 Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent |

MEASUREMENT CONTROL (Step 4)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 2 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH RSCP FALSE TRUE No report FALSE FALSE FALSE TRUE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 2 Inactive 255 |

RADIO BEARER RECONFIGURATION

The contents of RADIO BEARER RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| - DPCH compressed mode info |  |
| - TGPSI | 2 |
| - TGPS Status Flag | Active |
| - TGCFN | 255 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Integrity check info | If integrity protection is activated, this IE shall be present and SS checks that the MAC-I value matches with the calculated X-MAC value. Else, this IE shall be absent. |
| Failure cause | Checked to see if set to “compressed mode runtime error” |
| - Protocol error information | Checked to see if it is absent |
| - Deleted TGPSI | Checked to see if it is set to “2” |

8.4.1.11.5	Test requirement

After step 6 the UE shall keep transmission gap pattern sequence configuration associated with TGPSI=1.  It shall delete the transmission gap pattern sequence configuration associated with TGPSI=2, and delete the inter-frequency measurements corresponding to it.  It shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the uplink DCCH, with the IE “Failure cause” set to “Compressed mode runtime error”.

After step 7 the UE shall continue to send MEASUREMENT REPORT messages periodically, to report the CPICH Ec/No readings for cell 4.  However, no MEASUREMENT REPORT messages containing the CPICH RSCP readings for cell 4 shall be sent by the UE.

#### 8.4.1.12	Measurement Control and Report: Compressed Mode Configuration Failure during transport channel reconfiguration procedure

8.4.1.12.1	Definition

8.4.1.12.2	Conformance requirement

During a transport channel reconfiguration procedure, the UTRAN might request the activation of a new transmission gap pattern sequence configuration.  If the UE detects a runtime error due to overlapping compressed mode configuration (when transmission gap pattern sequences create transmission gaps in the same frame), it shall delete the transmission gap pattern sequence configuration associated with highest value of TGPSI.  The UE shall also terminate any inter-frequency measurements corresponding to the deleted transmission gap pattern sequence.  Finally, the UE shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM-RLC, with the cause value in IE "failure cause" set to "compressed mode runtime error".

Reference

3GPP TS 25.331  clause 8.2.2, clause 8.2.11, clause 8.6.6.15

8.4.1.12.3	Test purpose

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the uplink DCCH using AM RLC, if it receives a TRANSPORT CHANNEL RECONFIGURATION message which includes IE “DPCH compressed mode info” that causes an illegal overlap involving more than one parallel transmission gap pattern sequences.  To confirm that the UE terminate any inter-frequency measurements corresponding to the deleted transmission gap pattern sequence

8.4.1.12.4	Method of test

Initial Condition

System Simulator: 2 cells – both cell 1 and cell 4 are active.  See Table 8.4.1.11-1 in clause 8.4.1.11.4 for the power settings.

UE: CS-DCCH+DTCH_DCH (State 6-9) or PS-DCCH+DTCH_DCH (State 6-10) as specified in TS34.108 clause 7.4, depending on the CN domain supported.

Test Procedure

For this test case, the downlink transmission power settings should follow that specified in Table 8.4.1.11-1 in clause 8.4.1.11.4.

The UE is in the CELL_DCH state in cell 1.  SS sends a MEASUREMENT CONTROL message on the downlink DCCH to request the UE to start inter-frequency measurement for cell 4’s CPICH Ec/No value.  Simultaneously, the stored transmission gap pattern sequence configuration associated with TGPSI=1 is indicated to be activated in this message.  Upon the reception of this message, the UE shall transmit MEASUREMENT REPORT messages periodically at 16 seconds interval to report cell 4’s measurement results.  Next, SS sends a second MEASUREMENT CONTROL message.  In this message, a new measurement task is to be established for the measurement and reporting of cell 4’s CPICH RSCP value on a periodic basis.  A deactivated transmission pattern gap sequence configuration (with TGPSI=2) is associated with this new measurement task.

The SS transmits a TRANSPORT CHANNEL RECONFIGURATION message and commands the activation of transmission gap pattern sequence with TGPSI=2.  This is expected to result in the detection of a runtime error due to overlapping compressed mode configuration.  The UE then shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM-RLC.  In this message, the value of IE ” failure cause” shall be set to “compressed mode runtime error”.  The UE shall terminate all inter-frequency measurement tasks associated with TGPSI=2.  However, the UE shall continue to send MEASUREMENT REPORT messages to report cell 4’s CPICH Ec/No value, which is measured during the transmission gap created by compressed mode configuration corresponding to TGPSI=1.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | UE is initially in CELL_DCH state. |
| 2 | ( | MEASUREMENT CONTROL | Start inter-frequency measurements for cell 4’s CPICH Ec/No using transmission gap pattern sequence with TGPSI=1. |
| 3 | ( | MEASUREMENT REPORT | UE reports cell 4’s CPICH Ec/No readings periodically. |
| 4 | ( | MEASUREMENT CONTROL | Assign inter-frequency measurements for cell 4’s CPICH RSCP. This measurement task is associated with transmission gap pattern sequence with TGPSI=2, which has not been activated yet. |
| 5 | ( | TRANSPORT CHANNEL RECONFIGURATION | SS specifies the parameters for transmission gap pattern sequence with TGPSI=2 and activate it simultaneously |
| 6 |  |  | UE shall delete transmission gap pattern sequence configuration associated with TGPSI=2. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | Failure cause shall be set to “Compressed mode runtime error” |
| 8 | ( | MEASUREMENT REPORT | The contents shall be the same as that in step 3. |

Specific Message Contents

MEASUREMENT CONTROL (Step 2)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 1 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH Ec/No FALSE TRUE No report FALSE FALSE TRUE FALSE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 1 Active 255 |

MEASUREMENT REPORT (Step 3 and 8)

| Information Element | Value/Remarks |
| --- | --- |
| Integrity check info | If integrity protection is activated, this IE shall be present and SS checks that the MAC-I value matches with the calculated X-MAC value. Else, this IE shall be absent. |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to “1” Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 4 Check to see if set to the UARFCN of the downlink frequency for cell 4 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 4 Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent |

MEASUREMENT CONTROL (Step 4)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 2 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH RSCP FALSE TRUE No report FALSE FALSE FALSE TRUE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 2 Inactive 255 |

TRANSPORT CHANNEL RECONFIGURATION

The contents of TRANSPORT CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| - DPCH compressed mode info |  |
| - TGPSI | 2 |
| - TGPS Status Flag | Active |
| - TGCFN | 255 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Integrity check info | If integrity protection is activated, this IE shall be present and SS checks that the MAC-I value matches with the calculated X-MAC value. Else, this IE shall be absent. |
| Failure cause | Checked to see if set to “compressed mode runtime error” |
| - Protocol error information | Checked to see if it is absent |
| - Deleted TGPSI | Checked to see if it is set to “2” |

8.4.1.12.5	Test requirement

After step 6 the UE shall keep transmission gap pattern sequence configuration associated with TGPSI=1.  It shall delete the transmission gap pattern sequence configuration associated with TGPSI=2, and delete the inter-frequency measurements corresponding to it.  It shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the uplink DCCH, with the IE “Failure cause” set to “Compressed mode runtime error”.

After step 7 the UE shall continue to send MEASUREMENT REPORT messages periodically, to report the CPICH Ec/No readings for cell 4.  However, no MEASUREMENT REPORT messages containing the CPICH RSCP readings for cell 4 shall be sent by the UE.

#### 8.4.1.13	Measurement Control and Report: Compressed Mode Configuration Failure during physical channel reconfiguration procedure

8.4.1.13.1	Definition

8.4.1.13.2	Conformance requirement

During a physical channel reconfiguration procedure, the UTRAN might request the activation of a new transmission gap pattern sequence configuration.  If the UE detects a runtime error due to overlapping compressed mode configuration (when transmission gap pattern sequences create transmission gaps in the same frame), it shall delete the transmission gap pattern sequence configuration associated with highest value of TGPSI.  The UE shall also terminate any inter-frequency measurements corresponding to the deleted transmission gap pattern sequence.  Finally, the UE shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM-RLC, with the cause value in IE "failure cause" set to "compressed mode runtime error".

Reference

3GPP TS 25.331  clause 8.2.2, clause 8.2.11, clause 8.6.6.14

8.4.1.13.3	Test purpose

To confirm that the UE transmits a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the uplink DCCH using AM RLC, if it receives a PHYSICAL CHANNEL RECONFIGURATION message which includes IE “DPCH compressed mode info” that causes an illegal overlap involving more than one parallel transmission gap pattern sequences.  To confirm that the UE terminate any inter-frequency measurements corresponding to the deleted transmission gap pattern sequence

8.4.1.13.4	Method of test

Initial Condition

System Simulator: 2 cells – both cell 1 and cell 4 are active.  See Table 8.4.1.11-1 in clause 8.4.1.11.4 for the power settings.

UE: CS-DCCH+DTCH_DCH (State 6-9) or PS-DCCH+DTCH_DCH (State 6-10) as specified in TS34.108 clause 7.4, depending on the CN domain supported.

Test Procedure

For this test case, the downlink transmission power settings should follow that specified in Table 8.4.1.11-1 in clause 8.4.1.11.4.

The UE is in the CELL_DCH state in cell 1.  SS sends a MEASUREMENT CONTROL message on the downlink DCCH to request the UE to start inter-frequency measurement for cell 4’s CPICH Ec/No value.  Simultaneously, the stored transmission gap pattern sequence configuration associated with TGPSI=1 is indicated to be activated in this message.  Upon the reception of this message, the UE shall transmit MEASUREMENT REPORT messages periodically at 16 seconds interval to report cell 4’s measurement results.  Next, SS sends a second MEASUREMENT CONTROL message.  In this message, a new measurement task is to be established for the measurement and reporting of cell 4’s CPICH RSCP value on a periodic basis.  A deactivated transmission pattern gap sequence configuration (with TGPSI=2) is associated with this new measurement task.

The SS transmits a PHYSICAL CHANNEL RECONFIGURATION message and commands the activation of transmission gap pattern sequence with TGPSI=2.  This is expected to result in the detection of a runtime error due to overlapping compressed mode configuration.  The UE then shall transmit a PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the DCCH using AM-RLC.  In this message, the value of IE ” failure cause” shall be set to “compressed mode runtime error”.  The UE shall terminate all inter-frequency measurement tasks associated with TGPSI=2.  However, the UE shall continue to send MEASUREMENT REPORT messages to report cell 4’s CPICH Ec/No value, which is measured during the transmission gap created by compressed mode configuration corresponding to TGPSI=1.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 |  |  | UE is initially in CELL_DCH state. |
| 2 | ( | MEASUREMENT CONTROL | Start inter-frequency measurements for cell 4’s CPICH Ec/No using transmission gap pattern sequence with TGPSI=1. |
| 3 | ( | MEASUREMENT REPORT | UE reports cell 4’s CPICH Ec/No readings periodically. |
| 4 | ( | MEASUREMENT CONTROL | Assign inter-frequency measurements for cell 4’s CPICH RSCP. This measurement task is associated with transmission gap pattern sequence with TGPSI=2, which has not been activated yet. |
| 5 | ( | PHYSICAL CHANNEL RECONFIGURATION | SS specifies the parameters for transmission gap pattern sequence with TGPSI=2 and activate it simultaneously |
| 6 |  |  | UE shall delete transmission gap pattern sequence configuration associated with TGPSI=2. |
| 7 | ( | PHYSICAL CHANNEL RECONFIGURATION FAILURE | Failure cause shall be set to “Compressed mode runtime error” |
| 8 | ( | MEASUREMENT REPORT | The contents shall be the same as that in step 3. |

Specific Message Contents

MEASUREMENT CONTROL (Step 2)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 1 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH Ec/No FALSE TRUE No report FALSE FALSE TRUE FALSE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored set on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 1 Active 255 |

MEASUREMENT REPORT (Step 3 and 8)

| Information Element | Value/Remarks |
| --- | --- |
| Integrity check info | If integrity protection is activated, this IE shall be present and SS checks that the MAC-I value matches with the calculated X-MAC value. Else, this IE shall be absent. |
| Measurement identity Measured Results - CHOICE measurement - Inter-frequency measurement results - Frequency info - UARFCN (uplink) - UARFCN (downlink) - UTRA carrier RSSI - Inter-frequency cell measurement results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Event Results | Check to see if set to “1” Check to see if set to “Inter-frequency measured results list” Check to see if set to the UARFCN of the uplink frequency for cell 4 Check to see if set to the UARFCN of the downlink frequency for cell 4 Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if set to the same code for cell 4 Check to see if it is present Check to see if it is absent Check to see if it is absent Check to see if it is absent Check to see if it is absent |

MEASUREMENT CONTROL (Step 4)

| Information Element | Value/Remark |
| --- | --- |
| Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Inter-frequency cell info list - CHOICE inter-frequency cell removal - New inter-frequency info list - Inter-frequency cell id - Frequency info - UARFCN uplink (Nu) - UARFCN downlink (Nd) - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Inter-frequency measurement quantity - CHOICE reporting criteria - Filter Coefficient - Measurement quantity for frequency quality estimate - Inter-frequency reporting quantity - UTRA Carrier RSSI - Frequency quality estimate - Non frequency related cell reporting quantities - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell Identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting cell status - CHOICE reported cell - Maximum number of reported cells - Measurement validity - Inter-frequency set update - CHOICE report criteria - Amount of reporting - Reporting interval DPCH compressed mode status info - TGPSI - TGPS Status Flag - TGCFN | 2 Setup Not Present Not Present Inter-frequency measurement No inter-frequency cells removed Set to id of cell 4 UARFCN of the uplink frequency for cell 4 UARFCN of the downink frequency for cell 4 0 dB 0 chips Set to same code as used for cell 4 Not Present FALSE FALSE Inter-frequency reporting criteria 0 CPICH RSCP FALSE TRUE No report FALSE FALSE FALSE TRUE FALSE Report cells within active and/or monitored set on used frequency or within active and/or monitored cells on non-used frequency 2 Not present Not present Periodic reporting criteria Infinity 16 seconds 2 Inactive 255 |

PHYSICAL CHANNEL RECONFIGURATION

The contents of PHYSICAL CHANNEL RECONFIGURATION message in this test case is identical to the message sub-type title “Packet to CELL_DCH from CELL_DCH in PS” found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| - DPCH compressed mode info |  |
| - TGPSI | 2 |
| - TGPS Status Flag | Active |
| - TGCFN | 255 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |

PHYSICAL CHANNEL RECONFIGURATION FAILURE

| Information Element | Value/remark |
| --- | --- |
| Integrity check info | If integrity protection is activated, this IE shall be present and SS checks that the MAC-I value matches with the calculated X-MAC value. Else, this IE shall be absent. |
| Failure cause | Checked to see if set to “compressed mode runtime error” |
| - Protocol error information | Checked to see if it is absent |
| - Deleted TGPSI | Checked to see if it is set to “2” |

8.4.1.13.5	Test requirement

After step 6 the UE shall keep transmission gap pattern sequence configuration associated with TGPSI=1.  It shall delete the transmission gap pattern sequence configuration associated with TGPSI=2, and delete the inter-frequency measurements corresponding to it.  It shall transmit PHYSICAL CHANNEL RECONFIGURATION FAILURE message on the uplink DCCH, with the IE “Failure cause” set to “Compressed mode runtime error”.

After step 7 the UE shall continue to send MEASUREMENT REPORT messages periodically, to report the CPICH Ec/No readings for cell 4.  However, no MEASUREMENT REPORT messages containing the CPICH RSCP readings for cell 4 shall be sent by the UE.

#### 8.4.1.14	Measurement Control and Report: Cell forbidden to affect reporting range

8.4.1.14.1	Definition

8.4.1.14.2	Conformance requirement

When event 1A is ordered by the UTRAN in a MEASUREMENT CONTROL message, the UE shall send a MEASUREMENT REPORT message when a primary CPICH measured has entered the specified reporting range.  The UTRAN can request that a certain primary CPICH be forbidden to affect the reporting range used for event 1A measurement reporting.  However, the UE shall ignore such request from the UTRAN if two conditions are satisfied – (a) the primary CPICH concerned is included in the active set, and (b) all cells in the active set are defined as primary CPICH forbidden to affect the reporting range.

Reference

3GPP TS 25.331 clause 14.1.2.1, clause 14.1.5.4

8.4.1.14.3	Test Purpose

To confirm that the UE reports to the SS, if a primary CPICH currently measured by the UE enters the reporting range (event 1A).  The reporting range was specified in a MEASUREMENT CONTROL message received earlier.  To confirm that the UE ignores SS’s request to forbid the updating of reporting range, when (a) the primary CPICH concerned is one of the cells currently in active set and (b) all cells in the active sets are marked as primary CPICH forbidden to affect the reporting range.

8.4.1.14.4	Method of test

Initial Condition

System Simulator: 3 cells – The initial configurations of the 3 cells in the SS should follow the values indicated in the column marked “T0” in table 8.4.1.14-1.  The table is found in “Test Procedure” sub-clause.

UE: CS-DCCH_DCH (State 6-5) or PS-DCCH_DCH (State 6-7) in cell 1 as specified in clause 7.4 of TS 34.108, depending on the CN domain supported by the UE.

Test Procedure

Table 8.4.1.14-1 illustrates the downlink power to be applied for the 3 cells at various time instants of the test execution.  Column marked “T0” denotes the initial conditions, while columns marked “T1”, “T2”, “T3” and “T4” are to be applied subsequently.  The exact instants on which these values shall be applied are described in the text in this sub-clause.

Table 8.4.1.14-1

| Para-meter | Unit | Cell 1 | Cell 2 | Cell 3 |
| --- | --- | --- | --- | --- |
|  |  | T0 | T1 | T2 | T3 | T4 | T0 | T1 | T2 | T3 | T4 | T0 | T1 | T2 | T3 | T4 |
| UTRA RF Channel Number |  | Ch. 1 | Ch. 1 | Ch. 1 |
|  | dB | 9.5 | 9.5 | 9.5 | 9.5 | 9.5 | 4.0 | 4.0 | 4.0 | 14.5 | 14.5 | Cell 3 is switched off | 8.0 | 1.5 | 1.5 | 8.0 |
| CPICH Ec/Io | dB | -11.4 | -13.2 | -11.9 | -16.5 | -17.0 | -16.9 | -18.7 | -17.4 | -11.5 | -12.0 |  | -14.7 | -19.9 | -24.5 | -18.5 |
| CPICH RSCP | dBm | -70.5 | -70.5 | -70.5 | -70.5 | -70.5 | -76.0 | -76.0 | -76.0 | -66.5 | -66.5 |  | -72.0 | -78.5 | -78.5 | -72.0 |

The UE is initially in CELL_DCH state of cell 1.  SS then performs an active set update procedure by sending ACTIVE SET UPDATE REQUEST message on the downlink DCCH.  Cell 2 is to be added to the active set, according to the content of this downlink message.  The UE shall reply with an ACTIVE SET UPDATE COMPLETE message on the uplink DCCH, and include cell 2 to the active set when the activation time specified has elapsed.

SS configures itself according to the values in columns “T1” shown above.  SS then sends a MEASUREMENT CONTROL message to the UE, commanding the start of intra-frequency measurement for all 3 cells.  The intra-frequency measurement report criteria is set to event-triggered using event 1A.  The reporting range is set to 5 dB in the MEASUREMENT CONTROL message.  The UE shall send a MEASUREMENT REPORT on the uplink DCCH, which contains the CPICH RSCP reading for cell 3.

SS executes the active set update procedure again, but requesting that cell 3 be added to the active set this time.  The UE shall respond with ACTIVE SET UPDATE message on the uplink DCCH and then includes cell 3 into its current active set.  Following this, SS configures itself according to the values in columns “T2” shown above.  The UE should detect that CPICH RSCP of cell 3 has dropped out of the reporting range.

Next, SS configures itself according to the values in columns “T3” shown above.  SS then sends a MEASUREMENT CONTROL message to command that all cells in the active set are forbidden to update the reporting range for event 1A.

Finally, SS configures itself according to the values in columns “T4” shown above.  The UE shall proceed to update the reporting range as cell 2 has become the strongest cell.  Although the CPICH RSCP value of cell 3 has been restored, this value still falls outside the new reporting range.  Therefore, the UE shall not transmit a MEASUREMENT REPORT message on the uplink to report the triggering of event 1A.

Expected sequence

| Step | Direction | Message | Comment |
| --- | --- | --- | --- |
|  | UE | SS |  |  |
| 1 | ( | System Information Block type 11 | UE is initially in CELL_DCH state in cell 1. SIB 11 is modified to include both cell 2 and 5 into the monitored cell list. |
| 2 | ( | ACTIVE SET UPDATE | SS asks UE to add cell 2 into the active set |
| 3 | ( | ACTIVE SET UPDATE COMPLETE |  |
| 4 |  |  | SS configures itself according to the settings stated in column “T1” of Table 8.4.1.14-1. |
| 5 | ( | MEASUREMENT CONTROL | SS commands the start of measurement tasks for CPICH RSCP of cell 1, cell 2 and cell 3. All 3 cells are added under IE “Intra-frequency cell info list”. The reporting criteria is set to event-triggered using event type 1A, with reporting range = 5 dB. |
| 6 | ( | MEASUREMENT REPORT | UE shall report that cell 3 has entered the reporting range for event 1A. |
| 7 | ( | ACTIVE SET UPDATE | SS asks UE to add cell 3 into the active set |
| 8 | ( | ACTIVE SET UPDATE COMPLETE |  |
| 9 |  |  | SS configures itself according to the settings stated in column “T2” of Table 8.4.1.14-1. |
| 10 |  |  | SS configures itself according to the settings stated in column “T3” of Table 8.4.1.14-1. |
| 11 | ( | MEASUREMENT CONTROL | SS forbids all cells in active list to affect the reporting range |
| 12 |  |  | SS configures itself according to the settings stated in column “T4” of Table 8.4.1.14-1. |
| 13 |  |  | UE shall ignore the restrictions imposed by the messages received in step 11. It shall update the reporting range. SS verifies that no MEASUREMENT REPORT messages are received in the uplink direction |

Specific Message Contents

ACTIVE SET UPDATE (Step 2)

The contents of ACTIVE SET UPDATE message for this test step is identical to the same message found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Radio link addition information - Primary CPICH Info - Primary Scrambling Code - Downlink DPCH info for each RL - Primary CPICH usage for channel estimation - DPCH frame offset - Secondary CPICH info - DL channelisation code - Secondary scrambling code - CHOICE Spreading factor - Code Number - Scrambling code change - TPC Combination Index - SSDT Cell Identity - Close loop timing adjustment mode - TFCI Combining Indicator - SCCPCH information for FACH Radio link removal information | 0 Set to same code as assigned for cell 2 P-CPICH can be used. 0 chips Not Present This IE is repeated for all existing downlink DPCHs allocated to the UE Not Present 512 For each DPCH, assign the same code number in the current code given in cell 1. Not Present Not Present Not Present Not Present Not Present Not Present Not Present |

ACTIVE SET UPDATE COMPLETE (Step 3 and Step 8)

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier | Check to see if it is set to 0 |

MEASUREMENT CONTROL (Step 5)

The contents of MEASUREMENT CONTROL message for this test step is identical to the same message found in Annex A with the following exceptions:

| Information Element | Value/Remark |
| --- | --- |
| RRC transaction identifier Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Intra-frequency cell info list - CHOICE intra-frequency cell removal - New intra-frequency info list - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Intra-frequency cell id - Cell info - Cell individual offset - Reference time difference to cell - Primary CPICH Info - Primary Scrambling Code - Primary CPICH TX power - Read SFN Indicator - TX Diversity Indicator - Intra-frequency measurement quantity - Filter Coefficient - Measurement quantity - Intra-frequency reporting quantity - Reporting quantities for active set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for monitored set cells - SFN-SFN observed time difference reporting indicator - Cell synchronisation information reporting indicator - Cell identity reporting indicator - CPICH Ec/No reporting indicator - CPICH RSCP reporting indicator - Pathloss reporting indicator - Reporting quantities for detected cells - Reporting cell status - Measurement validity - CHOICE report criteria - Parameters required for each events - Intra-frequency event identity - Triggering conditions 1 - Triggering conditions 2 - Reporting range - Cells forbidden to affect reporting range - W - Hysteresis - Threshold used frequency - Reporting deactivation threshold - Replacement activation threshold - Time to trigger - Amount of reporting - Reporting interval - Reporting cell status DPCH compressed mode status info | 1 1 Setup Not Present Not Present Intra-frequency measurement Remove no intra-frequency 3 cells are specified – cell 1, cell 2 and cell 3 0 0 dB 0 chips Set to same code as used for cell 1 Not Present FALSE FALSE 1 0 dB 0 chips Set to same code as used for cell 2 Not Present FALSE FALSE 2 0 dB 0 chips Set to same code as used for cell 3 Not Present FALSE FALSE 0 CPICH RSCP No report FALSE FALSE FALSE TRUE FALSE No report FALSE FALSE FALSE FALSE FALSE Not present Not present Not present Intra-frequency measurement reporting criteria Only 1 event is specified 1a Not Present Active set cells 5.0 dB Not Present 0 0 dB Not Present 3 Not Present 0 msec 1 0 Not Present Not Present |

MEASUREMENT REPORT (Step 6)

| Information Element | Value/Remarks |
| --- | --- |
| RRC transaction identifier Measurement identity Measured Results - CHOICE measurement - Intra-frequency measured results - Cell measured results - Cell Identity - SFN-SFN observed time difference - Cell synchronisation information - Primary CPICH Info - Primary Scrambling Code - CPICH Ec/No - CPICH RSCP - Pathloss Measured Results on RACH Additional Measured Results Event Results | Check to see if set to 1 Check to see if set to 1 Check to see if set to “Intra-frequency measured results list” Check to see if it is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if it’s the same code for cell 3 Check to see if this IE is absent Check to see if this IE is present Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent Check to see if this IE is absent |

ACTIVE SET UPDATE (Step 7)

The contents of ACTIVE SET UPDATE message for this test step is identical to the same message found in Annex A with the following exceptions:

| Information Element | Value/remark |
| --- | --- |
| RRC transaction identifier Radio link addition information - Primary CPICH Info - Primary Scrambling Code - Downlink DPCH info for each RL - Primary CPICH usage for channel estimation - DPCH frame offset - Secondary CPICH info - DL channelisation code - Secondary scrambling code - CHOICE Spreading factor - Code Number - Scrambling code change - TPC Combination Index - SSDT Cell Identity - Close loop timing adjustment mode - TFCI Combining Indicator - SCCPCH information for FACH Radio link removal information | 0 Set to same code as assigned for cell 3 P-CPICH can be used. 0 chips Not Present This IE is repeated for all existing downlink DPCHs allocated to the UE Not Present 512 For each DPCH, assign the same code number in the current code given in cell 1. Not Present Not Present Not Present Not Present Not Present Not Present Not Present |

MEASUREMENT CONTROL (Step 11)

The contents of MEASUREMENT CONTROL message for this test step is identical to the same message found in Annex A with the following exceptions:

| Information Element | Value/Remark |
| --- | --- |
| RRC transaction identifier Measurement Identity Measurement Command Measurement Reporting Mode Additional measurements list CHOICE measurement type - Intra-frequency cell info list - Intra-frequency measurement quantity - Intra-frequency reporting quantity - CHOICE report criteria - Parameters required for each events - Intra-frequency event identity - Triggering conditions 1 - Triggering conditions 2 - Reporting range - Cells forbidden to affect reporting range - CHOICE Mode - Primary CPICH info - Primary scrambling code - CHOICE Mode - Primary CPICH info - Primary scrambling code - CHOICE Mode - Primary CPICH info - Primary scrambling code - W - Hysteresis - Threshold used frequency - Reporting deactivation threshold - Replacement activation threshold - Time to trigger - Amount of reporting - Reporting interval - Reporting cell status DPCH compressed mode status info | 1 1 Modify Not Present Not Present Intra-frequency measurement Not Present Not Present Not Present Intra-frequency measurement reporting criteria Only 1 event is specified 1a Not Present Active set cells 5.0 dB 3 cells – cell 1, cell 2 and cell 3 FDD Set to the same code as in cell 1 FDD Set to the same code as in cell 2 FDD Set to the same code as in cell 3 0 0 dB Not Present 3 Not Present 0 msec 1 0 Not Present Not Present |

8.4.1.14.5	Test requirement

After step 2, the UE shall transmit ACTIVE SET UPDATE COMPLETE message on the uplink DCCH to acknowledge the successful addition of cell 2 into the active set.  The UE shall be able to communicate with cell 2 in both the uplink and downlink directions after this step.

After step 5, the UE shall send a MEASUREMENT REPORT message on the uplink DCCH.  The message shall contain the measurement reading for cell 3’s CPICH RSCP.

After step 7, the UE shall transmit ACTIVE SET UPDATE COMPLETE message on the uplink DCCH to acknowledge the successful addition of cell 3 into the active set.  The UE shall be able to communicate with cell 3 in both the uplink and downlink directions after this step.

After step 12, the UE shall ignore the previous restriction imposed for the updating of reporting range.  It shall determine that cell 3’s RSCP value is not within the updated reporting range.  SS verifies that the UE does not send a MEASUREMENT REPORT message on the uplink DCCH to report cell 3’s RSCP value.

Annex A:
Default RRC Message Contents

This clause contains the default values of RRC messages, other than those specified in TS 34.108 clauses 6 and 9. Unless indicated otherwise in specific test cases, they shall be transmitted by the system simulator in RRC messages, and which are required to be received from the UE under test.

The necessary L3 messages are listed in alphabetic order, with the exception of the SYSTEM INFORMATION messages, where it is the information elements which are listed in alphabetic order (this is because some information elements occur in several SYSTEM INFORMATION types).

In this clause, decimal values are normally used. However, sometimes a hexadecimal value, indicated by an "H", or a binary value, indicated by a "B" is used.

# Default SYSTEM INFORMATION:

NOTE 1:	SYSTEM INFORMATION BLOCK TYPE 1 (except for PLMN type “GSM-MAP”), SYSTEM INFORMATION BLOCK TYPE 8, SYSTEM INFORMATION BLOCK TYPE 9, SYSTEM INFORMATION BLOCK TYPE 10, SYSTEM INFORMATION BLOCK TYPE 14, SYSTEM INFORMATION BLOCK TYPE 15 and SYSTEM INFORMATION BLOCK TYPE 16 messages are not used.

# Contents of ACTIVE SET UPDATE message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects one integer between 0 to 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| CN information info | Not Present |
| RB with PDCP information list | Not Present |
| Maximum allowed UL TX power | 33dBm |
| Radio link addition information | (This IE is repeated for addition RL number.) |
| - Primary CPICH info |  |
| - Primary scrambling code | The value is for additional cell |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - TFCI combining indicator | TRUE |
| - SCCPCH Information for FACH |  |
| - Secondary CCPCH info |  |
| - Selection Indicator | Not Present |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - Secondary CPICH info | Not Present |
| - Secondary scrambling code | 1 |
| - SSDT Indicator | FALSE |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Pilot symbol existence | FALSE |
| - TFCI existence | TRUE |
| - Fixed or Flexible Position | Flexible |
| - Timing offset | 0 |
| - TFCS | (This IE is repeated for TFC number for PCH and FACH.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set. |
| - Power offset information | Not Present |
| - FACH/PCH information |  |
| - TFS | (PCH) |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number.) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - TFS | (FACH) |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number.) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - References to system information blocks | Not Present |
| Radio link removal information | (This IE is repeated for removal RL number.) |
| - Primary CPICH info |  |
| - Primary scrambling code | The value is for removal cell |
| TX Diversity Mode | None |
| SSDT information | Not Present |

# Contents of ACTIVE SET UPDATE COMPLETE message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if it matches the same value used in the corresponding downlink ACTIVE SET UPDATE message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Uplink integrity protection activation info | Not checked |
| Radio bearer uplink ciphering activation time info | Not checked |
| RB with PDCP information list | Not checked |

# Contents of ACTIVE SET UPDATE FAILURE message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if it matches the same value used in the corresponding downlink ACTIVE SET UPDATE message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Failure cause | Value will be checked |

# Contents of CELL UPDATE message: TM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| U-RNTI | Checked to see if it is set to the following values |
| - SRNC identity | 0000 0000 0001B |
| - S-RNTI | 0000 0000 0000 0000 0001B |
| RRC transaction identifier | Checked to see if it is absent |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| START List | Checked to see if the ‘CN domain identity’ and ‘START’ IEs are present for all CN domains supported by the UE |
| - CN domain identity | Checked to see if it is one of the supported CN domains |
| - START | Checked to see if it is present |
| AM_RLC error indication (for c-plane) | Checked to see if it is set to ‘FALSE’ |
| AM_RLC error indication (for u-plane) | Checked to see if it is set to ‘FALSE’ |
| Cell update cause | See the test content |
| Failure cause | Checked to see if it is absent |
| RB timer indicator |  |
| - T314 expired | Checked to see if it is set to ‘FALSE’ |
| - T315 expired | Checked to see if it is set to ‘FALSE’ |
| Measured results on RACH | Not checked |

# Contents of CELL UPDATE CONFIRM message: UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| U-RNTI | If this message is sent on CCCH, use the following values. Else, this IE is absent. |
| - SRNC identity | 0000 0000 0001B |
| - S-RNTI | 0000 0000 0000 0000 0001B |
| RRC transaction identifier | Selects an arbitrary integer between 0 to 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | Not Present – use default value |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| RLC reset indicator (for C-plane) | FALSE |
| RLC reset indicator (for U-plane) | FALSE |
| CN information info | Not Present |
| URA identity | 0000 0000 0001B |
| RB information to release list | Not Present |
| RB information to reconfigure list | Not Present |
| RB information to be affected list | Not Present |
| RB with PDCP information list | Not Present |
| UL Transport channel information common for all transport channels | Not Present |
| Deleted TrCH information list | Not Present |
| - Deleted UL TrCH information |  |
| Added or Reconfigured TrCH information list | Not Present |
| - Added or Reconfigured UL TrCH information |  |
| CHOICE Mode | Not Present |
| DL Transport channel information common for all transport channels | Not Present |
| Deleted TrCH information list | Not Present |
| - Deleted DL TrCH information |  |
| Added or Reconfigured TrCH information list | Not Present |
| - Added or Reconfigured DL TrCH information |  |
| Frequency info | Not Present |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information per radio link list | Not Present |

# Contents of MEASUREMENT CONTROL message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an unused integer between 0 to 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - Message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Measurement Identity | 1 |
| Measurement Command | Setup |
| Measurement Reporting Mode |  |
| - Measurement Report Transfer Mode | Acknowledged mode RLC |
| - Measurement Reporting/Event Trigger Reporting Mode | Event Trigger |
| Additional measurement list |  |
| - CHOICE Measurement type |  |
| - Intra-frequency measurement |  |
| - Intra-frequency cell info |  |
| - New intra-frequency cell |  |
| - Intra-frequency cell-id | 0 |
| - cell info |  |
| - Cell individual offset | 0dB |
| - Reference time difference to cell | Not Present |
| - Primary CPICH info |  |
| - Primary scrambling code | 150 |
| - Primary CPICH Tx power | Not Present |
| - Read SFN number | FALSE |
| - TX Diversity indicator | FALSE |
| - Intra-frequency measurement quantity |  |
| - Filter coefficient | 0 |
| - Measurement quantity | CPICH RSCP |
| - Intra-frequency reporting quantity |  |
| - Reporting quantities for active set cells |  |
| - SFN-SFN observed time difference reporting indicator | No report |
| - Cell synchronisation information reporting indicator | FALSE |
| - Cell Identity reporting indicator | TRUE |
| - CPICH Ec/N0 reporting indicator | FALSE |
| - CPICH RSCP reporting indicator | TRUE |
| - Pathloss reporting indicator | FALSE |
| - Reporting quantities for monitored cells |  |
| - SFN-SFN observed time difference reporting indicator | No report |
| - Cell Identity reporting indicator | TRUE |
| - CPICH Ec/N0 reporting indicator | FALSE |
| - CPICH RSCP reporting indicator | TRUE |
| - Pathloss reporting indicator | FALSE |
| - Reporting quantities for detected set cells | Not Present |
| - Reporting cell status |  |
| - CHOICE reported cell | Report cell within active set and/or monitored cells on used frequency |
| - Maximum number of reported cells | 2 |
| - Measurement validity | Not Present |
| - CHOICE report criteria | Periodic reporting criteria |
| - Amount of reporting | Infinity |
| - Reporting interval | 64 sec |
| - Inter-RAT measurement | Not Present |
| - UP measurement | Not Present |
| - Traffic Volume measurement | Not Present |
| - Quality measurement | Not Present |
| - UE internal measurement | Not Present |
| CHOICE Measurement type | Intra-frequency measurement |
| - Intra-frequency cell info list | Not Present |
| - Intra-frequency measurement quantity | Not Present |
| - Intra-frequency cell reporting quantity | Not Present |
| - Report cell status | Not Present |
| - Measurement validity | Not Present |
| - CHOICE report criteria | No reporting |
| DPCH Compressed mode status info | Not Present |

# Contents of MEASUREMENT CONTROL FAILURE message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if it’s set to the identical value for the same IE in the downlink MEASUREMENT CONTROL message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Failure cause | See the test content |

# Contents of MEASUREMENT REPORT message: AM or UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Measurement identity number | 1 |
| Measured Results |  |
| - Intra-frequency measured results |  |
| - Cell measured results |  |
| - Cell Identity | 0000 0000 0000 0000 0000 0000 0010B |
| - SFN-SFN observed time difference | Not checked |
| - Cell synchronisation information | Not checked |
| - Primary CPICH info |  |
| - Primary scrambling code | 150 |
| - CPICH Ec/N0 | Not checked |
| - CPICH RSCP | The presence should be checked |
| - Pathloss | Not checked |
| Measured results on RACH | Not checked |
| Additional measured results | Not checked |
| Event results | Not checked |

# Contents of PAGING TYPE 1 message: TM (SMS in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Paging record |  |
| - CHOICE Used paging identity | CN identity |
| - Paging cause | Low Priority Signalling |
| - CN domain identity | CS domain |
| - CHOICE UE identity |  |
| - IMSI (GSM-MAP) | Set to the same octet string as in the IMSI stored in the USIM card |
| BCCH modification info | Not Present |

# Contents of PAGING TYPE 1 message: TM (SMS in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Paging record |  |
| - CHOICE Used paging identity | CN identity |
| - Paging cause | Low Priority Signalling |
| - CN domain identity | PS domain |
| - CHOICE UE identity |  |
| - IMSI (GSM-MAP) | Set to the same octet string as in the IMSI stored in the USIM card |
| BCCH modification info | Not Present |

# Contents of PAGING TYPE 2 message: AM (Speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Paging cause | Terminating Conversational Call |
| CN domain identity | CS domain |
| Paging record type identifier | Select the same type as in the IE “Initial UE Identity” in RRC CONNECTION REQUEST” message. |

# Contents of PHYSICAL CHANNEL RECONFIGURATION message: AM or UM (The others of speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identfier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.1 present 23-2. If integrity protection is indicated to be active, this IE is with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TPGS status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITPITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of PHYSICAL CHANNEL RECONFIGURATION message: AM or UM (Speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identfier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | FALSE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP |  |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of PHYSICAL CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_DCH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identfier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | Inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of PHYSICAL CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_DCH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identfier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | Inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of PHYSICAL CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_FACH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identfier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH power control info | Not Present |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio link list | Not Present |

# Contents of PHYSICAL CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_FACH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identfier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | 0000 0000 0000 0010B |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH power control info | Not Present |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio link list | Not Present |

# Contents of PHYSICAL CHANNEL RECONFIGURATION COMPLETE message: AM

| Message Type |  |
| --- | --- |
| RRC transaction identifier | Checked to see if it’s set to identical value of the same IE in the downlink PHYSICAL CHANNEL RECONFIGURATION message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Uplink integrity protection activation info | Not checked |
| COUNT-C activation time | The presence of this IE depends on the following 2 factors: (a) There exists RB(s) mapped to RLC-TM, (b) UE is transiting to CELL_DCH state after the reconfiguration procedure. Else, this IE is absent. |
| CHOICE mode | FDD |
| Radio bearer uplink ciphering activation time info | Not checked |
| RB with PDCP information list | Not checked |

# Contents of RADIO BEARER SETUP message: AM or UM (The others of speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If ciphering is indicated to be active, this IE present with the values of the sub IEs as stated below. Else, this IE is omitted. |
| - Ciphering mode command | Start |
| - Ciphering algorithm | Use one of the supported ciphering algorithms |
| - Ciphering activation time for DPCH | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| - Radio bearer downlink ciphering activation time info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| Signalling RB information to setup | Not Present |
| RAB information for setup |  |
| - RAB info |  |
| - RAB identity | 0000 0001B |
| - CN domain identity | CS domain |
| - NAS Synchronization Indicator | Not Present |
| - Re-establishment timer |  |
| - T314 | 20 seconds |
| - RB information to setup |  |
| - RB identity | 10 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | TM RLC |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 1 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| Added or Reconfigured UL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 6 |
| - CHOICE DL parameters | SameAsUL |
| UL TrCH identity | 1 |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - UL TrCH identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER SETUP message: AM or UM (Packet to CELL_DCH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If ciphering is indicated to be active, this IE present with the values of the sub IEs as stated below. Else, this IE is omitted |
| - Ciphering mode command | Start |
| - Ciphering algorithm | Use one of the supported ciphering algorithms |
| - Ciphering activation time for DPCH | Not Present |
| - Radio bearer downlink ciphering activation time info |  |
| - Radio bearer identity | 10 |
| - RLC sequence number | Current RLC SN + 2 |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| Signalling RB information to setup | Not Present |
| RAB information for setup |  |
| - RAB info |  |
| - RAB identity | 0000 0001B |
| - CN domain identity | PS domain |
| - NAS Synchronization Indicator | Not Present |
| - Re-establishment timer |  |
| - T314 | 20 seconds |
| - RB information to setup |  |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - Transport channel identity | 1 |
| - UL Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - MAC logical channel priority | 1 |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 1 |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - RLC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| Added or Reconfigured UL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC Size | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 6 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 10 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER SETUP message: AM or UM (Packet to CELL_DCH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If ciphering is indicated to be active, this IE present with the values of the sub IEs as stated below. Else, this IE is omitted. |
| - Ciphering mode command | Start |
| - Ciphering algorithm | Use one of the supported ciphering algorithms. |
| - Ciphering activation time for DPCH | Not Present |
| - Radio bearer downlink ciphering activation time info |  |
| - Radio bearer identity | 20 |
| - RLC sequence number | Current RLC SN + 2 |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| Signalling RB information to setup | Not Present |
| RAB information for setup |  |
| - RAB info |  |
| - RAB identity | 0000 0001B |
| - CN domain identity | PS domain |
| - NAS Synchronization Indicator | Not Present |
| - Re-establishment timer |  |
| - T314 | 20 seconds |
| - RB information to setup |  |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - CHOICE SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - RLC logical channel mapping indicator | Not Present |
| - Information for each multiplexing option |  |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - UL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - UL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH information |  |
| - Transport channel identity | 15 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 1 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH information |  |
| - Transport channel identity | 12 |
| - Transport channel identity | 13 |
| - Transport channel identity | 14 |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 6 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset |  |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER SETUP message: AM or UM (Packet to CELL_FACH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If ciphering is indicated to be active, this IE present with the values of the sub IEs as stated below. Else, this IE is omitted |
| - Ciphering mode command | start |
| - Ciphering algorithm | Use one of the supported ciphering algorithms |
| - Ciphering activation time for DPCH | Not Present |
| - Radio bearer downlink ciphering activation time info |  |
| - Radio bearer identity | 20 |
| - RLC sequence number | Current RLC SN + 2 |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| Signalling RB information to setup | Not Present |
| RAB information for setup |  |
| - RAB info | (AM DTCH for PS domain) |
| - RAB identity | 0000 0001B |
| - CN domain identity | PS domain |
| - NAS Synchronization Indicator | Not Present |
| - Re-establishment timer |  |
| - T314 | 20 seconds |
| - RB information to setup |  |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - CHOICE SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 6 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 4 |
| RB information to be affected | (TM CCCH uplink for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info | Not Present |
| RB information to be affected | (UM CCCH for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| - Downlink RLC logical channel info | Not Present |
| RB information to be affected | (TM BCCH for RRC) |
| - RB identity | 6 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 5 |
| - Downlink RLC logical channel info | Not Present |
| RB information to be affected | (TM PCCH for RRC) |
| - RB identity | 7 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | PCH |
| - Logical channel identity | 1 |
| - Downlink RLC logical channel info | Not Present |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Deleted UL TrCH information |  |
| - Transport channel identity | 1 |
| - Transport channel identity | 5 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Deleted DL TrCH information |  |
| - Transport channel identity | 6 |
| - Transport channel identity | 10 |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 12 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 14 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of RADIO BEARER SETUP message: AM or UM (Packet to CELL_FACH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If ciphering is indicated to be active, this IE present with the values of the sub IEs as stated below. Else, this IE is omitted |
| - Ciphering mode command | start |
| - Ciphering algorithm | Use one of the supported ciphering algorithms |
| - Ciphering activation time for DPCH | Not Present |
| - Radio bearer downlink ciphering activation time info |  |
| - Radio bearer identity | 20 |
| - RLC sequence number | Current RLC SN |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| Signalling RB information to setup | Not Present |
| RAB information for setup | (AM DTCH for PS domain) |
| - RAB info |  |
| - RAB identity | 0000 0001B |
| - CN domain identity | PS domain |
| - NAS Synchronization Indicator | Not Present |
| - Re-establishment timer |  |
| - T314 | 20 seconds |
| - RB information to setup |  |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - CHOICE SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 6 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 4 |
| RB information to be affected | (TM CCCH uplink for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| RB information to be affected | (UM CCCH for downlink RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| RB information to be affected | (TM BCCH for RRC) |
| - RB identity | 6 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 5 |
| RB information to be affected | (TM PCCH for RRC) |
| - RB identity | 7 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | PCH |
| - Logical channel identity | 1 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 12 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 14 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of RADIO BEARER RECONFIGURATION message: AM or UM (The others of speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to reconfigure list | Not Present |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 10 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 1 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB information to be affected | (TM DTCH) |
| - RB identity | 10 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size |  |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factor | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH information | Not Present |
| - Transport channel identity |  |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted DL TrCH information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | SameAsUL |
| - UL TrCH Identity | 5 |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | Inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info | 100 |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - Secondary scrambling code |  |
| - channelisation code |  |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RECONFIGURATION message: AM or UM (Speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to reconfigure list | Not Present |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB information to be affected | (DTCH TM) |
| - RB identity | 10 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| RB information to be affected | (DTCH TM) |
| - RB identity | 11 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 2 |
| - Logical channel identity | 8 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 7 |
| - Logical channel identity | 8 |
| RB information to be affected | (This IE is needed for 12.2 kbps and 10.2 kbps) |
| - RB identity | 12 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 3 |
| - Logical channel identity | 9 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 8 |
| - Logical channel identity | 9 |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH information | Not Present |
| - Transport channel identity |  |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | SameAsUL |
| - UL TrCH Identity | 5 |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | Inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - S field |  |
| - Code Word Set |  |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RECONFIGURATION message: AM or UM (Packet to CELL_DCH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to reconfigure list | Not Present |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB information to be affected | (AM DTCH) |
| - RB identity | 20 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH information |  |
| - Transport channel identity | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Additon |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted DL TrCH information |  |
| - Transport channel identity | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| -DPCCH Power offset | -6dB |
| -PC Preamble | 8slot |
| -Power Control Algorithm | Algorithm1 |
| -TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bits | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RECONFIGURATION message: AM or UM (Packet to CELL_DCH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to reconfigure list |  |
| - RB information to reconfigure | (UM DCCH for RRC) |
| - RB identity | 1 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for RRC) |
| - RB identity | 2 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 5 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - PDCP info | Not Present |
| - RLC info | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| - RB information to reconfigure | (AM DTCH) |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 6 |
| - Logical channel identity | 7 |
| - RB stop/continue | Not Present |
| RB information to be affected | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation |  |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH information |  |
| - Transport channel identity | 15 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 1 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH information |  |
| - Transport channel identity | 12 |
| - Transport channel identity | 13 |
| - Transport channel identity | 14 |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 6 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| -DPCCH Power offset | -6dB |
| -PC Preamble | 8slot |
| -Power Control Algorithm | Algorithm1 |
| -TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bits | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | Inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RECONFIGURATION message: AM or UM (Packet to CELL_FACH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to reconfigure list |  |
| - RB information to reconfigure | (UM DCCH for RRC) |
| - RB identity | 1 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for RRC) |
| - RB identity | 2 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 4 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DTCH) |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 7 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 6 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (TM CCCH uplink for RRC) |
| - RB identity | 0 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | TM RLC |
| - Transmission RLC discard | Not Present |
| - Segmentation indication | TRUE |
| - CHOICE Downlink RLC mode | TM RLC |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info | Not Present |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (UM CCCH downlink for RRC) |
| - RB identity | 0 |
| - PDCP info | Not Present |
| - CHOICE RLC info type |  |
| - CHOICE Uplink RLC mode | Not Present |
| - CHOICE Downlink RLC mode | UM RLC |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (TM BCCH for RRC) |
| - RB identity | 5 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | Not Present |
| - CHOICE Downlink RLC mode | TM RLC |
| - Segmentation Indication | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 5 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (TM PCCH for RRC) |
| - RB identity | 7 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | Not Present |
| - CHOICE Downlink RLC mode | TM RLC |
| - Segmentation Indication | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | PCH |
| - Logical channel identity | 1 |
| - RB stop/continue | Not Present |
| RB information to be affected | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Deleted UL TrCH information |  |
| - Transport channel identity | 1 |
| - Transport channel identity | 5 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Deleted DL TrCH information |  |
| - Transport channel identity | 6 |
| - Transport channel identity | 10 |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 12 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 14 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of RADIO BEARER RECONFIGURATION message: AM or UM (Packet to CELL_FACH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | 0000 0000 0000 0010B |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to reconfigure list |  |
| - RB information to reconfigure | (UM DCCH for RRC) |
| - RB identity | 1 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| - RB information to reconfigure | (AM DCCH for RRC) |
| - RB identity | 2 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 4 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (AM DTCH) |
| - RB identity | 20 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | Not Present |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 6 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 6 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (TM CCCH uplink for RRC) |
| - RB identity | 0 |
| - PDCP info | Not Present |
| - CHOICE RLC info | RLC info |
| - CHOICE Uplink RLC mode | TM RLC |
| - Transmission RLC Discard | Not Present |
| - Segmentation Indication | TRUE |
| - CHOICE Downlink RLC mode | Not Present |
| - Segmentation Indication |  |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info | Not Present |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (UM CCCH for RRC) |
| - RB identity | 0 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | Not Present |
| - CHOICE Downlink RLC mode | UM RLC |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (TM BCCH for RRC) |
| - RB identity | 6 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | Not Present |
| - CHOICE Downlink RLC mode | TM RLC |
| - Segmentation Indication | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 5 |
| - RB stop/continue | Not Present |
| - RB information to reconfigure | (TM PCCH for RRC) |
| - RB identity | 7 |
| - PDCP info | Not Present |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | Not Present |
| - CHOICE Downlink RLC mode | TM RLC |
| - Segmentation indication | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | PCH |
| - Logical channel identity | 1 |
| - RB stop/continue | Not Present |
| RB information to be affected | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Deleted UL TrCH information |  |
| - Transport channel identity | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFCS representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Deleted DL TrCH information |  |
| - Transport channel identity | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 12 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 14 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of RADIO BEARER RECONFIGURATION COMPLETE message: AM

| Message Type |  |
| --- | --- |
| RRC transaction identifier | Checked to see if the value is identical to the same IE in the downlink RADIO BEARER RECONFIGURATION COMPLETE message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Uplink integrity protection activation info | Not checked |
| COUNT-C activation time | The presence of this IE depends on the following 2 factors: (a) There exists RB(s) mapped to RLC-TM and (b) UE is transiting to CELL_DCH state after the reconfiguration procedure. Else, this IE is absent. |
| CHOICE mode | FDD |
| Radio bearer uplink ciphering activation time info | Not checked |
| RB with PDCP information list | Not checked |

Contents of RADIO BEARER RELEASE message: AM or UM (The others of speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to release |  |
| - RB identity | 10 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - RLC logical channel mapping indicator | Not Present |
| - Information for each multiplexing option |  |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factor | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH Information |  |
| - Transport channel identity | 1 |
| Added or Reconfigured UL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| CPCH set ID | Not Present |
| DRAC static information | Not Preaent |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 6 |
| Added or Reconfigured DL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | N/A |
| - TFCI existence | FALSE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RELEASE message: AM or UM (Speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| Signalling Connection release indication | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to release |  |
| - RB identity | 10 |
| RB information to release |  |
| - RB identity | 11 |
| RB information to release |  |
| - RB identity | 12 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factor | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH Information |  |
| - Transport channel identity | 1 |
| Deleted UL TrCH Information |  |
| - Transport channel identity | 2 |
| Deleted UL TrCH Information |  |
| - Transport channel identity | 3 |
| Added or Reconfigured UL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| CPCH set ID | Not Present |
| DRAC static information | Not Preaent |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 6 |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 7 |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 8 |
| Added or Reconfigured DL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - UL TrCH Identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | N/A |
| - TFCI existence | FALSE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RELEASE message: AM or UM (Packet to CELL_DCH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| Signalling Connection release indication | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to release |  |
| - RB identity | 20 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - RLC logical channel mapping indicator | Not Present |
| - Information for each multiplexing option |  |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted UL TrCH Information |  |
| - Transport channel identity | 1 |
| Added or Reconfigured UL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 5 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| CPCH set ID | Not Present |
| DRAC static information | Not Preaent |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters |  |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 6 |
| Added or Reconfigured DL TrCH information | If TrCH reconfiguration is executed then this is needed(e.g The rate of SRB for DCCH is changed.). |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | N/A |
| - TFCI existence | FALSE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RELEASE message: AM or UM (Packet to CELL_DCH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| Signalling Connection release indication | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to release |  |
| - RB identity | 20 |
| RB information to release |  |
| - RB identity | 6 |
| RB information to release |  |
| - RB identity | 7 |
| RB information to release |  |
| - RB identity | 0 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 100 |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | DCH |
| - UL Transport channel identity | 5 |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | DCH |
| - DL Transport channel identity | 10 |
| - Logical channel identity | 4 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Siz | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factor |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Deleted UL TrCH Information | 15 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| CPCH set ID | Not Present |
| DRAC static information | Not Preaent |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 12 |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 13 |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 14 |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| - Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | N/A |
| - TFCI existence | FALSE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of RADIO BEARER RELEASE message: AM or UM (Packet to CELL_FACH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| Signalling Connection release indication | Not Present |
| URA identity | Not Present |
| RAB information to reconfigure list | Not Present |
| RB information to release |  |
| - RB identity | 20 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - DL Transport channel identity | 1 |
| - Logical channel identity | 4 |
| RB information to be affected | (TM CCCH uplink for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info | Not Present |
| RB information to be affected | (UM CCCH downlink for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| RB information to be affected | (TM BCCH for RRC) |
| - RB identity | 6 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 5 |
| RB information to be affected | (TM PCCH for RRC) |
| - RB identity | 7 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | PCH |
| - Logical channel identity | 1 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Deleted UL TrCH Information |  |
| - Transport channel identity | 1 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| CPCH set ID | Not Present |
| DRAC static information | Not Preaent |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Deleted DL TrCH Information | 6 |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
|  | 14 |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of RADIO BEARER RELEASE message: AM or UM (Packet to CELL_FACH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| Signalling Connection release indication | Not Present |
| URA identity | Not Present |
| RAB information to be reconfigured list | Not Present |
| RB information to release |  |
| - RB identity | 20 |
| RB information to be affected | (UM DCCH for RRC) |
| - RB identity | 1 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| RB information to be affected | (AM DCCH for RRC) |
| - RB identity | 2 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - UL Transport channel identity | 1 |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| RB information to be affected | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| RB information to be affected | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 4 |
| RB information to be affected | (TM CCCH uplink for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 5 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 1 |
| - Downlink RLC logical channel info | Not Present |
| RB information to be affected | (UM CCCH downlink for RRC) |
| - RB identity | 0 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 6 |
| RB information to be affected | (TM BCCH for RRC) |
| - RB identity | 6 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 5 |
| RB information to be affected | (TM PCCH for RRC) |
| - RB identity | 7 |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | PCH |
| - Logical channel identity | 1 |
| RB with PDCP information list | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Deleted UL TrCH Information | 15 |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| CPCH set ID | Not Present |
| DRAC static information | Not Preaent |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Deleted DL TrCH Information |  |
| - Transport channel identity | 12 |
| Added or Reconfigured DL TrCH information | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |
|  | Primary CPICH may be used |
|  | Not Present |

# Contents of UTRAN MOBILITY INFORMATION message: AM or UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| New U-RNTI | See the test content |
| New C-RNTI | See the test content |
| UE Timers and constants in connected mode |  |
| - T301 | 2000 milliseconds |
| - N301 | 2 |
| - T302 | 4000 milliseconds |
| - N302 | 3 |
| - T304 | 1000 milliseconds |
| - N304 | 3 |
| - T305 | 60 minutes |
| - T307 | 50 seconds |
| - T308 | 320 milliseconds |
| - T309 | 8 seconds |
| - T310 | 320 milliseconds |
| - N310 | 5 |
| - T311 | 500 milliseconds |
| - T312 | 5 seconds |
| - N312 | 200 |
| - T313 | 10 seconds |
| - N313 | 200 |
| - T314 | 20 seconds |
| - T315 | 30 seconds |
| - N315 | 200 |
| - T316 | 50 seconds |
| - T317 | 1800 seconds |
| CN information info | Not Present |
| URA identity | Not present |
| RB with PDCP information list | Not Present |

# Contents of UTRAN MOBILITY INFORMATION CONFIRM message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if it matches the value of the same IE in downlink UTRAN MOBILITY INFORMATION message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| COUNT-C activation time | The presence of this IE depends on the following 2 factors: (a) There exists RB(s) mapped to RLC-TM, (b) UE is transiting to CELL_DCH state after the reconfiguration procedure. Else, this IE is absent. |
| Uplink integrity protection activation info | Not checked |
| Radio bearer uplink ciphering activation time info | Not checked |
| RB with PDCP information list | Not checked |

# Contents of RRC CONNECTION REJECT message: UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Initial UE identity | Set to the UE’s IMSI (GSM-MAP) or TMSI. |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Rejection cause | Unspecified |
| Wait Time | 0 |
| Redirection info | Not Present |

# Contents of RRC CONNECTION SETUP message: UM (Transition to CELL_FACH)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Initial UE identity | Reference to TS34.108 clause 6.10 Parameter Set |
| RRC transaction identifier | Arbitrarily select a integer between 0 and 3 |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI |  |
| - SRNC identity | 0000 0000 0001B |
| - S-RNTI | 0000 0000 0000 0000 0001B |
| New C-RNTI | 0000 0000 0000 0001B |
| RRC state indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | 5 (2 to 12) |
| Capability update requirement |  |
| - UE radio access capability update requirement | FALSE |
| - System specific capability update requirement | Not Present |
| Signalling RB information to setup | (UM DCCH for RRC) |
| - RB identity | 1 |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | UM RLC |
| - Transmission RLC discard |  |
| - SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - CHOICE Downlink RLC mode | UM RLC |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 1 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 2 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 1 |
| Signalling RB information to setup | (AM DCCH for RRC) |
| - RB identity | 2 |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 2 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 3 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 2 |
| Signalling RB information to setup | (AM DCCH for NAS_DT High priority) |
| - RB identity | 3 |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 3 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 4 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 3 |
| Signalling RB information to setup | (AM DCCH for NAS_DT Low priority) |
| - RB identity | 4 |
| - CHOICE RLC info type | RLC info |
| - CHOICE Uplink RLC mode | AM RLC |
| - Transmission RLC discard |  |
| - SDU discard mode | Max DAT retransmissions |
| - MAX_DAT | 4 |
| - Timer_MRW | 100 |
| - MaxMRW | 4 |
| - Transmission window size | 8 |
| - Timer_RST | 500 |
| - Max_RST | 4 |
| - Polling info |  |
| - Timer_poll_prohibit | 200 |
| - Timer_poll | 200 |
| - Poll_SDU | 1 |
| - Last transmission PU poll | TRUE |
| - Last retransmission PU poll | TRUE |
| - Poll_Windows | 99 |
| - CHOICE Downlink RLC mode | AM RLC |
| - In-sequence delivery | TRUE |
| - Receiving window size | 8 |
| - Downlink RLC status info |  |
| - Timer_status_prohibit | 200 |
| - Timer_EPC | 200 |
| - Missing PU indicator | TRUE |
| - RB mapping info |  |
| - Information for each multiplexing option |  |
| - RLC logical channel mapping indicator | Not Present |
| - Number of uplink RLC logical channels | 1 |
| - Uplink transport channel type | RACH |
| - Logical channel identity | 4 |
| - CHOICE RLC size list | All |
| - MAC logical channel priority | 5 |
| - Downlink RLC logical channel info |  |
| - Number of downlink RLC logical channels | 1 |
| - Downlink transport channel type | FACH |
| - Logical channel identity | 4 |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 14 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of RRC STATUS message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Identification of received message | Not Present |
| - Received message type |  |
| - RRC transaction identifier |  |
| Protocol error information |  |
| - Protocol error cause | Value will be checked. |

# Contents of SECURITY MODE FAILURE message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if the value is the identical to the same IE in the downlink SECURITY MODE COMMAND message. |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Failure cause | Value will be checked |

# Contents of TRANSPORT CHANNEL RECONFIGURATION message: AM or UM (The others of speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP info | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factors |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | SameAsUL |
| - UL TrCH Identity | 5 |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of TRANSPORT CHANNEL RECONFIGURATION message: AM or UM (Speech in CS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factors |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | SameAsUL |
| - UL TrCH Identity | 5 |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| - DPCCH power offset | -6dB |
| - PC Preamble | 8slot |
| - Power Control Algorithm | Algorithm1 |
| - TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bit | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of TRANSPORT CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_DCH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factors |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE TFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - CHOICE Transport channel type | Dedicated transport channels |
| - TFS |  |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| -DPCCH Power offset | -6dB |
| -PC Preamble | 8slot |
| -Power Control Algorithm | Algorithm1 |
| -TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bits | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Not Present |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - S field |  |
| - Code Word Set |  |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of TRANSPORT CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_DCH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_DCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE Gain Factors | Signalled Gain Factors |
| - Gain factor βc | 0 |
| - Gain factor βd | 0 |
| - Reference TFC ID | Not Present |
| - Power offset Pp-m | 0dB |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 1 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | Not Present |
| - CHOICE DL parameters |  |
| - DL DCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 6 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Dedicated transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Transmission Time Interval | Not Present |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target |  |
| - BLER Quality value | -6.3 |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| Uplink DPCH info |  |
| -Uplink DPCH power control info |  |
| -DPCCH Power offset | -6dB |
| -PC Preamble | 8slot |
| -Power Control Algorithm | Algorithm1 |
| -TPC step size | 1dB |
| - Scrambling code type | Long |
| - Scrambling code number | 0 (0 to 16777215) |
| - Number of DPDCH | Not Present(1) |
| - spreading factor | SF is reference to TS34.108 clause 6.10 Parameter Set |
| - TFCI existence | TRUE |
| - Number of FBI bits | Not Present(0) |
| - Puncturing Limit | Reference to TS34.108 clause 6.10 Parameter Set |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links |  |
| - Downlink DPCH info common for all RL |  |
| - Timing indicator | Maintain |
| - CFN-targetSFN frame offset | Not Present |
| - Downlink DPCH power control information |  |
| - DPC mode | 0 (single) |
| - DL rate matching restriction information | Not Present |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Fixed or Flexible Position | Flexible |
| - TFCI existence | TRUE |
| - Number of bits for Pilot bits(SF=128,256) | Reference to TS34.108 clause 6.10 Parameter Set |
| - DPCH compressed mode info |  |
| - TGPSI | 1 |
| - TGPS Status Flag | inactive |
| - TGCFN | (Current CFN + (256 – TTI/10msec)) mod 256 |
| - Transmission gap pattern sequence configuration parameters |  |
| - TGMP | FDD Measurement |
| - TGPRC | 62 |
| - TGSN | 8 |
| - TGL1 | 10 |
| - TGL2 | 5 |
| - TGD | 15 |
| - TGPL1 | 35 |
| - TGPL2 | 35 |
| - RPP | Mode 1 |
| - ITP | Mode 1 |
| - UL/DL Mode | DL |
| - Downlink compressed mode method | SF/2 |
| - Uplink compressed mode method | Not Present |
| - Downlink frame type | A |
| - DeltaSIR1 | 2.0 |
| - DeltaSIRafter1 | 1.0 |
| - DeltaSIR2 | Not Present |
| - DeltaSIRafter2 | Not Present |
| - TX Diversity mode | None |
| - SSDT information | Not Present |
| - Default DPCH Offset Value | 0 |
| Downlink information for each radio links |  |
| - Primary CPICH info |  |
| - Primary scrambling code | 100 |
| - PDSCH with SHO DCH info | Not Present |
| - PDSCH code mapping | Not Present |
| - Downlink DPCH info for each RL |  |
| - Primary CPICH usage for channel estimation | Primary CPICH may be used |
| - DPCH frame offset | 0 chips |
| - Secondary CPICH info | Not Present |
| - DL channelisation code |  |
| - Secondary scrambling code | 1 |
| - Spreading factor | Reference to TS34.108 clause 6.10 Parameter Set |
| - Code number | SF-1(SF is reference to TS34.108 clause 6.10 Parameter Set) |
| - Scrambling code change | No change |
| - TPC combination index | 0 |
| - SSDT Cell Identity | -a |
| - Closed loop timing adjustment mode | Not Present |
| - Secondary CCPCH info | Not Present |
| - TFCS | Not Present |
| - FACH/PCH information | Not Present |
| - References to system information blocks | Not Present |

# Contents of TRANSPORT CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_FACH from CELL_DCH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 5 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size |  |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information | Not Present |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 10 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 2 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 3 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 4 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel list | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links |  |

# Contents of TRANSPORT CHANNEL RECONFIGURATION message: AM or UM (Packet to CELL_FACH from CELL_FACH in PS)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| Activation time | (256+CFN-(CFN MOD 8 + 8))MOD 256 |
| New U-RNTI | Not Present |
| New C-RNTI | 0000 0000 0000 0010B |
| RRC State indicator | CELL_FACH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | Not Present |
| RB with PDCP information | Not Present |
| UL Transport channel information for all transport channels |  |
| - TFC subset | (This IE is repeated for TFC number.) |
| - Allowed Transport Format combination | 0 to MaxTFCValue-1 (MaxTFCValue is refer to TS34.108 clause 6.10 Parameter Set.) |
| - PRACH TFCS | Not Present |
| - CHOICE mode | FDD |
| - UL DCH TFCS | Not Present |
| Added or Reconfigured UL TrCH information |  |
| - Transport channel identity | 15 |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| DRAC static information | Not Present |
| DL Transport channel information common for all transport channel |  |
| - SCCPCH TFCS | (This IE is repeated for TFC number.) |
| - Normal |  |
| - TFCI Field 1 information |  |
| - CHOICE CTFC representation | Addition |
| - TFCS addition information |  |
| - CHOICE CTFC Size | Number of bits used must be enough to cover all combinations of CTFC from clause 6.10. |
| - CTFC information | Refer to TS34.108 clause 6.10 Parameter Set |
| - Power offset information |  |
| - CHOICE DL parameters | Independent |
| - DL DCH TFCS | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 12 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 13 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
| Added or Reconfigured DL TrCH information |  |
| - Transport channel identity | 14 |
| - CHOICE DL parameters | Independent |
| - TFS |  |
| - CHOICE Transport channel type | Common transport channels |
| - Dynamic Transport format information | (This IE is repeated for TFI number) |
| - RLC Size | Reference to TS34.108 clause 6.10 Parameter Set |
| - Number of TBs and TTI List | (This IE is repeated for TFI number.) |
| - Number of Transport blocks | Reference to TS34.108 clause 6.10 Parameter Set |
| - CHOICE mode | FDD |
| - CHOICE Logical Channel List | ALL |
| - Semi-static Transport Format information |  |
| - Transmission time interval | Reference to TS34.108 clause 6.10 Parameter Set |
| - Type of channel coding | Reference to TS34.108 clause 6.10 Parameter Set |
| - Coding Rate | Reference to TS34.108 clause 6.10 Parameter Set |
| - Rate matching attribute | Reference to TS34.108 clause 6.10 Parameter Set |
| - CRC size | Reference to TS34.108 clause 6.10 Parameter Set |
| - DCH quality target | Not Present |
| - Transparent mode signalling info | Not Present |
|  | Common transport channels |
|  | (This IE is repeated for TFI number) |
|  | Reference to TS34.108 clause 6.10 Parameter Set |
| Frequency info |  |
| - UARFCN uplink(Nu) | Reference to TS34.108 clause 6.10 Parameter Set |
| - UARFCN downlink(Nd) | Reference to TS34.108 clause 6.10 Parameter Set |
| Maximum allowed UL TX power | 33dBm |
| CHOICE channel requirement | Not Present |
| CHOICE Mode | FDD |
| - Downlink PDSCH information | Not Present |
| Downlink information common for all radio links | Not Present |
| Downlink information for each radio links | Not Present |

# Contents of TRANSPORT CHANNEL RECONFIGURATION COMPLETE message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if the value is identical to the same IE in the downlink TRANSPORT CHANNEL RECONFIGURATION message |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| Uplink integrity protection activation info | Not checked |
| COUNT-C activation time | The presence of this IE depends on the following 2 factors: (a) There exists RB(s) mapped to RLC-TM and (b) UE is transiting to CELL_DCH state after the reconfiguration procedure. Else, this IE is absent. |
| Radio bearer uplink ciphering activation time info | Not checked |
| RB with PDCP information list | Not checked |

# Contents of TRANSPORT FORMAT COMBINATION CONTROL message: AM or UM (in CELL_DCH)

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - Message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC Message sequence number | SS provides the value of this IE, from its internal counter. |
| DPCH TFCS in Uplink |  |
| - Allowed Transport format combination index | 0 (The TFC is constructed from ALL TF0) |

# Contents of UE CAPABILITY ENQUIRY message: AM or UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Arbitrarily selects an integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - Message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC Message sequence number | SS provides the value of this IE, from its internal counter. |
| Capability update requirement |  |
| - UE radio access capability update requirement | TRUE |
| - System specific capability update requirement list | UE only supports 1 system |
| - System specific capability update requirement | GSM |

# Contents of UE CAPABILITY INFORMATION message: AM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| RRC transaction identifier | Checked to see if the value is identical to the same IE in the downlink UE CAPABILITY ENQUIRY message. |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| UE radio access capability | Value will be checked. Stated capability must be compatible with 34.123-2 (ICS statements) and the user settings |
| - ICS Version |  |
| - PDCP Capability |  |
| - RLC Capability |  |
| - Transport channel capability |  |
| - RF Capability |  |
| - Physical channel capability |  |
| - UE multi-mode/multi-RAT capability |  |
| - Security Capability |  |
| - LCS Capability |  |
| - Measurement capability |  |
| UE system specific capability | Value will be checked. UE must include the classmark information for the supported RAT |

# Contents of UE CAPABILITY INFORMATION CONFIRM message: UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - Message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC Message sequence number | SS provides the value of this IE, from its internal counter. |

# Contents of URA UPDATE message: TM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| U-RNTI |  |
| - SRNC identity | 0000 0000 0001B |
| - S-RNTI | 0000 0000 0000 0000 0001B |
| RRC transaction identifier | Checked to see if it is absent |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE shall be present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs shall be absent. |
| - Message authentication code | This IE is checked to see if it is present. The value is compared against the XMAC-I value computed by SS. |
| - RRC Message sequence number | This IE is checked to see if it is present. The value is used by SS to compute the XMAC-I value. |
| URA update cause | See the test content |
| Protocol error indicator | Checked to see if it is absent or set to ‘FALSE’ |
| Protocol error information | Checked to see if it is absent |

# Contents of URA UPDATE CONFIRM message: UM

| Information Element | Value/remark |
| --- | --- |
| Message Type |  |
| U-RNTI | If this message is sent on CCCH, use the following values. Else, this IE is absent. |
| - SRNC identity | 0000 0000 0001B |
| - S-RNTI | 0000 0000 0000 0000 0001B |
| RRC transaction identifier | Arbitrarily selects and integer between 0 and 3 |
| Integrity check info | The presence of this IE is dependent on IXIT statements in TS 34.123-2. If integrity protection is indicated to be active, this IE is present with the values of the sub IEs as stated below. Else, this IE and the sub-IEs are omitted. |
| - message authentication code | SS calculates the value of MAC-I for this message and writes to this IE. |
| - RRC message sequence number | SS provides the value of this IE, from its internal counter. |
| Integrity protection mode info | Not Present |
| Ciphering mode info | Not Present |
| New U-RNTI | Not Present |
| New C-RNTI | Not Present |
| RRC state indicator | URA_PCH |
| UTRAN DRX cycle length coefficient | Not Present |
| CN information info | Not Present |
| URA identity | See the test content |
| RB with PDCP information list | Not Present |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.