| 3GPP TSG-T WG2 SWG3#10 Paris, France 21st – 25th January 2002 | T2M020110 |
| --- | --- |
| CR-Form-v5 |
| CHANGE REQUEST |
| ( | 23.140 | CR | CRNum | ( rev | - | ( Current version: | 5.1.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE | x | Radio Access Network |  | Core Network |  |
| Title: ( | Alignment of 3GPP TS 23.140 with 3GPP TS 26.140 |
| Source: ( | Siemens AG |
| Work item code: ( | MESS5-MMS |  | Date: ( | 24.01.2002 |
| Category: ( | C |  | Release: ( | REL-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | In R’99 and REL-4 of MMS, the set of media formats and codecs for MMS was defined in 3GPP TS 23.140. For Release 5 the responsibility for the definition of media formats and codecs for MMS was shifted to SA4. SA4 created a new specification, 3GPP TS 26.140, based on those parts of 3GPP TS 23.140 which currently define media formats and codecs. As result of this shift of responsibility these parts of 3GPP TS 23.140 need consequently to be replaced by references to 3GPP TS 26.140. |
| Summary of change: ( | Those parts of 3GPP TS 23.140 which currently define media formats and codecs are replaced by references to the newly created specification for MMS media formats and codecs, 3GPP TS 26.140. |
| Consequences if ( not approved: | Duplicate definition of the set of media formats and codecs for MMS which, eventually, might result in inconsistencies between 3GPP TS 23.140 and 3GPP TS 26.140. |
| Clauses affected: ( | 2, 5.1.2 |
| Other specs ( | x | Other core specifications ( | 3GPP TS 26.140 |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( | The changes made are according to the agreement reached on BT tdoc T2-010801 at T2#14 and based on current version 1.0.0 of 3GPP TS 26.140. |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 22.140: "Multimedia Messaging Service; Stage 1".

[2]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[3]	WAP Forum: "Wireless Application Environment Specification, Version 1.2", WAP-WAESpec-19991104, . URL: http://www.wapforum.org/.

[4]	3GPP TS 23.057: "Mobile Execution Environment (MExE); Functional description; Stage 2".

[5]	IETF; STD 0011 (RFC 2822): "Internet Message Format", URL: http://www.ietf.org/rfc/rfc2822.txt.

[6]	IETF; RFC 2046: "Multipurpose Internet Mail extension (MIME) Part Two: Media Types", URL: http://www.ietf.org/rfc/rfc2046.txt.

[7]	The Unicode Consortium: "The Unicode Standard", Version 2.0, Addison-Wesley Developers Press, 1996.URL: http://www.unicode.org/.

[8]	ANSI X3.4, 1986: "Information Systems; Coded Character Set 7 Bit; American National Standard Code for Information Interchange".

[9]	ISO/IEC 8859-1:1998: "Information Processing; 8-bit Single-Byte Coded Graphic Character Sets; Part 1: Latin Alphabet No. 1".

[10]	IETF; RFC 2279: "UTF-8, A Transformation format of ISO 10646", URL: http://www.ietf.org/rfc/rfc2279.txt.

[11]	3GPP TS 24.011: "Point-to-Point (PP) Short Message Service (SMS) support on mobile radio interface".

[12]	obsolete

[13]	obsolete

[14]	obsolete

[15]	obsolete

[16]	obsolete

[17]	obsolete

[18]	obsolete

[19]	obsolete

[20]	obsolete

[21]	obsolete

[22]	IETF; STD 0010 (RFC 2821): "Simple Mail Transfer Protocol", URL: http://www.ietf.org/rfc/rfc2821.txt.

[23]	WAP Forum (November 1999): "WAP Wireless Session Protocol", WAP-WSP-19991105- , URL: http://www.wapforum.org/.

[24]	WAP Forum (November 1999): "WAP Push Access Protocol", WAP-PAP-19991108, URL: http://www.wapforum.org/.

[25]	WAP Forum (November 1999): "WAP User Agent Profile Specification", WAP-UAProf-19991110, URL: http://www.wapforum.org/.

[26]	W3C Recommendation 22 February 1999 "Resource Description Framework (RDF) Model and Syntax Specification", URL: http://www.w3.org/TR/REC-rdf-syntax.

[27]	WAP Forum (November 1999): "WAP Wireless Markup Language Specification, Version 1.2 ", WAP-WML-19991104, URL: http://www.wapforum.org/.

[28]	W3C Recommendation 15-June-1998: "Synchronized Multimedia Integration Language (SMIL) 1.0 Specification" - http://www.w3.org/TR/REC-smil/.

[29]	WAP Forum (November 1999): "WAP Wireless Transport Layer Security Specification", WAP-WTLS-19991105, URL: http://www.wapforum.org/.

[30]	WAP Forum (November 1999): "WAP Identity Module Specification", WAP-WIM-19991105, URL: http://www.wapforum.org/.

[31]	ITU-T Recommendation T.37 (06/98): "Procedures for the transfer of facsimile data via store-and-forward on the Internet".

[32]	ITU-T Recommendation T.30 (1996): "Procedures for document facsimile transmission in the general switched telephone network".

[33]	IETF; RFC 2421 (Sept. 1998): "Voice Profile for Internet Mail – version 2, VPIM" , URL: http://www.ietf.org/rfc/rfc2421.txt.

[34]	IETF; STD 0053 (RFC 1939): "POP 3, Post Office Protocol - Version 3" , URL: http://www.ietf.org/rfc/rfc1939.txt.

[35]	IETF; RFC 1730 (December 1994): "IMAP4, Internet Message Access Protocol - Version 4" , URL: http://www.ietf.org/rfc/rfc1730.txt..

[36]	Adobe Systems: "Tag Image File Format (TIFF), Version 6", URL:, http://www.adobe.com.

[37]	3GPP TR 23.039: "Interface protocols for the connection of Short Message Service Centres (SMSCs) to Short Message Entities (SMEs)".

[38]	obsolete

[39]	obsolete

[40]	3GPP TS 26.233: "End-to-end transparent streaming Service (PSS); General Description".

[41]	3GPP TS 26.234: "End-to-end transparent streaming Service (PSS); Protocols and Codecs".

[42]	IETF; Internet Draft: "TCP over 2.5G and 3G Wireless Networks"; URL: http://search.ietf.org/internet-drafts/draft-ietf-pilc-2.5g3g-03.txt

NOTE: 	Reference [42] has to be replaced by the appropriate RFC number once the Internet draft is approved within the IETF.

[43]	WAP Forum: "Wireless profiled TCP", WAP-225-TCP-20010331-a, URL: http://www.wapforum.org

[44]	IETF; RFC 2045: "Multipurpose Internet Mail Extensions (MIME) Part One: Format of Internet Message Bodies", URL: http://www.ietf.org/rfc/rfc2045.txt

[45]	IETF; RFC 2047: "Multipurpose Internet Mail Extensions (MIME) Part Three: Message Header Extensions for Non-ASCII-Text", URL: http://www.ietf.org/rfc/rfc2047.txt.

[46]	IETF; RFC 2048: "Multipurpose Internet Mail Extensions (MIME) Part Four: Registration Procedures", URL: http://www.ietf.org/rfc/rfc2048.txt.

[47]	IETF; RFC 2049: "Multipurpose Internet Mail Extensions (MIME) Part Five: Conformance Criteria and Examples", URL: http://www.ietf.org/rfc/rfc2049.txt.

[48]	IETF; RFC 2616: “Hypertext Transfer Protocol, HTTP/1.1”, URL: http://www.ietf.org/rfc/rfc2616.txt.

[49]	IETF; STD 13 (RFC 1034, 1035): "Domain Names -- concepts and facilities", "Domain names – implementation and specification", URL: http://www.ietf.org/rfc/rfc1034.txt, http://www.ietf.org/rfc/rfc1035.txt.

[50]	IETF; STD 14 (RFC 947): "Multi-network broadcasting within the Internet", URL: http://www.ietf.org/rfc/rfc947.txt.

[51]	IETF; RFC 2076: "Common Internet Message Headers", URL: http://www.ietf.org/rfc/rfc2076.txt.

[52]	IETF; RFC 1893: "Enhanced Mail System Status Codes", URL: http://www.ietf.org/rfc/rfc1893.txt.

[53]	IETF; RFC 1327: "Mapping between X.400(1988)/ISO 10021 and RFC 822", URL: http://www.ietf.org/rfc/rfc1327.txt.

[54]	3GPP TS 29.061: "Interworking between the Public Land Mobile Network (PLMN) supporting Packet Based Services and Packet Data Networks (PDN)"

[55]	WAP-183-ProvCont, Provisioning Content, URL: http://www.wapforum.org

[56]	WAP-209-MMSEncapsulation, MMS Encapsulation Protocol, URL: http://www.wapforum.org

[57]	3GPP TS 26.140: "Multimedia Messaging Service; Media formats and codecs".

NOTE: 	Reference [57] is work in progress in the 3GPP TSG SA WG 4 (3GPP TSG SA approval is scheduled to 03/2002).

…

# 5	Functional Description of Involved MMS Elements

## 5.1	MMS User Agent

…

### 5.1.2	Minimum set of supported formats

Multiple media elements shall be combined into a composite single MM using MIME multipart format as defined in RFC 2046 [6]. The media type of a single MM element shall be identified by its appropriate MIME type whereas the media format shall be indicated by its appropriate MIME subtype.

In order to guarantee a minimum support and compatibility between multimedia messaging capable terminals, an MMS User Agent shall support:

- Interoperability with SMS

- Text

An MMS User Agent may support:

- Speech

- Audio

- Synthetic audio

- Still Image

- Bitmap graphics

- Video

- Vector graphics

- File Format for dynamic media

- Media synchronization and presentation format

#### 5.1.2.1	Interoperability with SMS

In order to guarantee SMS interoperability, SMS 3GPP TS 24.011 [11] RP-DATA RPDU encapsulation defined in clause 7.3.1 shall be supported. MIME type "application/x-sms" shall be used for this purpose.

NOTE:	SMS MIME type shall be used as soon as the MIME registration has been completed.

#### 5.1.2.2	Text

Text coding inside MMS shall be done according to [57].

#### 5.1.2.3	Speech

Speech coding inside MMS shall be done according to [57].

#### 5.1.2.4	Audio

Audio coding inside MMS shall be done according to [57].

#### 5.1.2.5	Synthetic audio

Synthetic audio coding inside MMS shall be done according to [57].

#### 5.1.2.6	Still Image

Still image coding inside MMS shall be done according to [57].

#### 5.1.2.7	Bitmap graphics

Bitmap graphics coding inside MMS shall be done according to [57].

#### 5.1.2.8	Video

Video coding inside MMS shall be done according to [57].

#### 5.1.2.9	Vector graphics

Vector graphics coding inside MMS shall be done according to [57].

#### 5.1.2.10	File Format for dynamic media

Support for file formats for dynamic media inside MMS shall be according to [57].

#### 5.1.2.11	Media synchronization and presentation format

Support for media synchronization and presentation format inside MMS shall be according to [57].

## 5.2	MMS Relay/Server

…

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.