| 3GPP TSG-T2 SWG3#11 Seattle, USA 29th April – 2nd May 2002 | T2M02137 |
| --- | --- |
| CR-Form-v5 |
| CHANGE REQUEST |
| ( | 23.140 | CR | CRNum | ( rev | - | ( Current version: | 5.2.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | X |
| Title: ( | MM7 Stage 3 Definition |
| Source: ( | Comverse |
| Work item code: ( | MESS5-MMS |  | Date: ( | 14 April, 2002 |
| Category: ( | B |  | Release: ( | Rel-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | In order to complete the workitem for Release 5 of MMS the group has defined the Stage 2 of MM7 and now must complete the work by specifying the Stage-3 based on the decision of the group using SOAP as the interface Protocol. |
| Summary of change: ( | Definition of the protocol and specification of the SOAP Schema that will be used for MM7 communication |
| Consequences if ( not approved: | Very important workitem will not be completed |
| Clauses affected: ( | Section 6.9 – specifying the protocols that will be used for MM7 Section 8.7 – new sections with specification of the Stage 3 Section 2 – added references for SOAP and other RFCs used |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( | Based on CR for Stage 2 that should be approved in T2#16 |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 22.140: "Multimedia Messaging Service; Stage 1".

[2]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[3]	WAP Forum: "Wireless Application Environment Specification, Version 1.2", WAP-WAESpec-19991104, . URL: http://www.wapforum.org/.

[4]	3GPP TS 23.057: "Mobile Execution Environment (MExE); Functional description; Stage 2".

[5]	IETF; STD 0011 (RFC 2822): "Internet Message Format", URL: http://www.ietf.org/rfc/rfc2822.txt.

[6]	IETF; RFC 2046: "Multipurpose Internet Mail extension (MIME) Part Two: Media Types", URL: http://www.ietf.org/rfc/rfc2046.txt.

[7]	The Unicode Consortium: "The Unicode Standard", Version 2.0, Addison-Wesley Developers Press, 1996.URL: http://www.unicode.org/.

[8]	ANSI X3.4, 1986: "Information Systems; Coded Character Set 7 Bit; American National Standard Code for Information Interchange".

[9]	ISO/IEC 8859-1:1998: "Information Processing; 8-bit Single-Byte Coded Graphic Character Sets; Part 1: Latin Alphabet No. 1".

[10]	IETF; RFC 2279: "UTF-8, A Transformation format of ISO 10646", URL: http://www.ietf.org/rfc/rfc2279.txt.

[11]	3GPP TS 24.011: "Point-to-Point (PP) Short Message Service (SMS) support on mobile radio interface".

[12]	3GPP TS 26.090: "Mandatory Speech Codec speech processing functions; AMR Speech Codec Transcoding Functions".

[13]	3GPP TS 26.093 (V3.1.0): "Mandatory Speech Codec speech processing functions; AMR Speech Codec; Source Controlled Rate Operation".

[14]	ISO/IEC 11172-3:1993: "Information technology; Coding of moving pictures and associated audio for digital storage media at up to about 1,5 Mbit/s; Part 3: Audio" (MP3, MPEG1-Audio, MPEG2-Audio)

[15]	MIDI Manufacturers Association Incorporated, Los Angeles, California: “MIDI Sample Dump Standard (SDS)”; URL: http://www.midi.org.

[16]	ISO/IEC 14496-2:1999/FDAM4, ISO/IEC JTC1/SC 29/WG11 N3904, Pisa, January, 2001

[17]	ITU-T Recommendation T.81 | ISO/IEC 10918-1:1994: "Information technology; Digital compression and coding of continuous-tone still images: Requirements and guidelines".

[18]	Compuserve Incorporated, Columbus, Ohio (1990): "Graphics Interchange Format (Version 89a)".

[19]	ISO/IEC 14496-2:1999: "Information technology; Coding of audio-visual objects; Part 2: Visual".

[20]	ITU-T Recommendation H.263 (1998): "Video coding for low bit rate communication".

[21]	ITU-T Recommendation H.263 (1998): "Video coding for low bit rate communication - Annex X, Profiles and Levels Definition"

[22]	IETF; STD 0010 (RFC 2821): "Simple Mail Transfer Protocol", URL: http://www.ietf.org/rfc/rfc2821.txt.

[23]	WAP Forum (November 1999): "WAP Wireless Session Protocol", WAP-WSP-19991105- , URL: http://www.wapforum.org/.

[24]	WAP Forum (November 1999): "WAP Push Access Protocol", WAP-PAP-19991108, URL: http://www.wapforum.org/.

[25]	WAP Forum (November 1999): "WAP User Agent Profile Specification", WAP-UAProf-19991110, URL: http://www.wapforum.org/.

[26]	W3C Recommendation 22 February 1999 "Resource Description Framework (RDF) Model and Syntax Specification", URL: http://www.w3.org/TR/REC-rdf-syntax.

[27]	WAP Forum (November 1999): "WAP Wireless Markup Language Specification, Version 1.2 ", WAP-WML-19991104, URL: http://www.wapforum.org/.

[28]	W3C Recommendation 15-June-1998: "Synchronized Multimedia Integration Language (SMIL) 1.0 Specification" - http://www.w3.org/TR/REC-smil/.

[29]	WAP Forum (November 1999): "WAP Wireless Transport Layer Security Specification", WAP-WTLS-19991105, URL: http://www.wapforum.org/.

[30]	WAP Forum (November 1999): "WAP Identity Module Specification", WAP-WIM-19991105, URL: http://www.wapforum.org/.

[31]	ITU-T Recommendation T.37 (06/98): "Procedures for the transfer of facsimile data via store-and-forward on the Internet".

[32]	ITU-T Recommendation T.30 (1996): "Procedures for document facsimile transmission in the general switched telephone network".

[33]	IETF; RFC 2421 (Sept. 1998): "Voice Profile for Internet Mail – version 2, VPIM" , URL: http://www.ietf.org/rfc/rfc2421.txt.

[34]	IETF; STD 0053 (RFC 1939): "POP 3, Post Office Protocol - Version 3" , URL: http://www.ietf.org/rfc/rfc1939.txt.

[35]	IETF; RFC 1730 (December 1994): "IMAP4, Internet Message Access Protocol - Version 4" , URL: http://www.ietf.org/rfc/rfc1730.txt..

[36]	Adobe Systems: "Tag Image File Format (TIFF), Version 6", URL:, http://www.adobe.com.

[37]	3GPP TR 23.039: "Interface protocols for the connection of Short Message Service Centres (SMSCs) to Short Message Entities (SMEs)".

[38]	ISO/IEC TR 13818-5:1997/Amd 1:1999 "Advanced Audio Coding (AAC)"

[39]	IETF; Internet draft: "RTP payload format and file storage format for AMR and AMR-WB audio";  URL: http://search.ietf.org/internet-drafts/draft-ietf-avt-rtp-amr-10.txt..

NOTE: 	Reference [39] is work in progress in IETF/AVT working group and to be replaced by the appropriate RFC number once the Internet draft is approved within the IETF (IESG approval is scheduled to spring/summer 2001).

[40]	3GPP TS 26.233: "End-to-end transparent streaming Service (PSS); General Description".

[41]	3GPP TS 26.234: "End-to-end transparent streaming Service (PSS); Protocols and Codecs".

[42]	IETF; Internet Draft: "TCP over 2.5G and 3G Wireless Networks"; URL: http://search.ietf.org/internet-drafts/draft-ietf-pilc-2.5g3g-03.txt

NOTE: 	Reference [42] has to be replaced by the appropriate RFC number once the Internet draft is approved within the IETF.

[43]	WAP Forum: "Wireless profiled TCP", WAP-225-TCP-20010331-a, URL: http://www.wapforum.org

[44]	IETF; RFC 2045: "Multipurpose Internet Mail Extensions (MIME) Part One: Format of Internet Message Bodies", URL: http://www.ietf.org/rfc/rfc2045.txt

[45]	IETF; RFC 2047: "Multipurpose Internet Mail Extensions (MIME) Part Three: Message Header Extensions for Non-ASCII-Text", URL: http://www.ietf.org/rfc/rfc2047.txt.

[46]	IETF; RFC 2048: "Multipurpose Internet Mail Extensions (MIME) Part Four: Registration Procedures", URL: http://www.ietf.org/rfc/rfc2048.txt.

[47]	IETF; RFC 2049: "Multipurpose Internet Mail Extensions (MIME) Part Five: Conformance Criteria and Examples", URL: http://www.ietf.org/rfc/rfc2049.txt.

[48]	IETF; RFC 2616: “Hypertext Transfer Protocol, HTTP/1.1”, URL: http://www.ietf.org/rfc/rfc2616.txt.

[49]	IETF; STD 13 (RFC 1034, 1035): "Domain Names -- concepts and facilities", "Domain names – implementation and specification", URL: http://www.ietf.org/rfc/rfc1034.txt, http://www.ietf.org/rfc/rfc1035.txt.

[50]	IETF; STD 14 (RFC 947): "Multi-network broadcasting within the Internet", URL: http://www.ietf.org/rfc/rfc947.txt.

[51]	IETF; RFC 2076: "Common Internet Message Headers", URL: http://www.ietf.org/rfc/rfc2076.txt.

[52]	IETF; RFC 1893: "Enhanced Mail System Status Codes", URL: http://www.ietf.org/rfc/rfc1893.txt.

[53]	IETF; RFC 1327: "Mapping between X.400(1988)/ISO 10021 and RFC 822", URL: http://www.ietf.org/rfc/rfc1327.txt.

[54]	3GPP TS 29.061: "Interworking between the Public Land Mobile Network (PLMN) supporting Packet Based Services and Packet Data Networks (PDN)"

[55]	WAP-183-ProvCont, Provisioning Content, URL: http://www.wapforum.org

[56]	WAP-209-MMSEncapsulation, MMS Encapsulation Protocol, URL: http://www.wapforum.org

[57]	IETF; RFC 1870: “SMTP Service Extension for Message Size Declaration”, URL: http://www.ietf.org/rfc/rfc1870.txt

[58]	IETF; RFC 1652: “SMTP Service Extension for 8bit-MIME transport”, URL: http://www.ietf.org/rfc/rfc1652.txt

[59]	3GPP TS 32.235: "Charging Management; Charging Data Description for Application Services".

[60]	IETF, RFC 2915: “The Naming Authority Pointer (NAPTR) DNS Resource Record”, URL: http://www.ietf.org/rfc/rfc2915.txt

[61]	IETF, RFC 2916: “E.164 number and DNS”, URL: http://www.ietf.org/rfc/rfc2916.txt

[62]	3GPP TS 29.002: "Mobile Application Part (MAP) specification".

[63]	3GPP TS 22.066: "Support of Mobile Number Portability (MNP); Service description. Stage 1".

[64]	3GPP TS 23.066: "Support of Mobile Number Portability (MNP); Technical realization. Stage 2".

[65]	IETF; RFC 2617 "Access Authentication", URL:http://www.ietf.org/rfc/rfc2617.txt

[66]	IETF; RFC 2246 "TLS protocol, version 1.0" , URL:http://www.ietf.org/rfc/rfc2246.txt

[67]	3GPP TS 31.102 "Characteristics of the USIM Application".

[68]	W3C Note 08 May 2000 "Simple Object Access Protocol (SOAP) 1.1", URL: http://www.w3.org/TR/SOAP

[69]	W3C Note 11 December 2000 "SOAP Messages with Attachments", URL: http://www.w3.org/TR/SOAP-attachments

[70]	IETF; RFC 2376: "XML Media Type", URL: http://www.ietf.org/rfc/rfc2376.txt.

[71]	IETF; RFC 2387: "The MIME Multipart/Related Content Type", URL: http://www.ietf.org/rfc/rfc2387.txt.

[72]	IETF; RFC 2111: "Content-ID and Message-ID Uniform Resource Locators", URL: http://www.ietf.org/rfc/rfc2111.txt.

[73]	IETF; RFC 2557: "MIME Encapsulation of Aggregate Documents, such as HTML (MHTML)", URL: http://www.ietf.org/rfc/rfc2557.txt.

[74]	IETF; RFC 2617 “Access Authentication”, URL:http://www.ietf.org/rfc/rfc2617.txt

## 6.9	MM7: MMS Relay/Server – MMS VAS Applications

Reference point MM7 is used to transfer MMs from MMS Relay/Server to MMS VAS applications and to transfer MMs from MMS VAS applications to MMS Relay/Server. This reference point shall be based  on SOAP 1.1[68] using a HTTP transport layer.  Future releases may update this protocol decision to use a standardized version of SOAP and support additional transport layer implementations.

## 8.7	Technical realisation of MMS on reference point MM7

### 8.7.8 Implementation of the MM7 Abstract Messages

The interface between a VASP and the MMS Relay/Server, over the MM7 reference point, will be implemented using SOAP 1.1[68] as the formatting language.  The VASP and the MMS Relay/Server shall be able to play dual roles of sender and receiver of SOAP messages.  HTTP [48] shall be used as the transport protocol of the SOAP messages. The SOAP message shall bind to the HTTP request/response model by providing SOAP request parameters in the body of the HTTP POST request and the SOAP response in the body of the HTTP response.

#### 8.7.8.1 SOAP Message Format and Encoding Principles

The following principles will be used in the design of the SOAP implementation of the MM7 interface:

- The XML Schema that will be defined should be modular – to allow hiding of implementation details and reuse of common components.

- The XML Schema that will be defined should be extensible – to allow future enhancements and extensions.

- The schema will be based on the W3C SOAP 1.1 schema and will be published by the 3GPP.  The schema will include an indication of the version of the MM7 specification that is supported.

- The MM7 SOAP messages shall consist of a SOAP envelope, SOAP Header element and SOAP body element, as described in [68].

- The information elements of the MM7 abstract messages are divided into two major groups – control information and messaging information.  The control information will be encoded in the SOAP Header elements and the messaging information will be encoded in the SOAP Body elements.

- The control information will be divided into generic control information that will include the – Transaction ID, Message Type, and MM7 Version Information Elements and these will be encoded within a SOAP Header element named MM7Header.  The authentication information will be organized into two SOAP Header elements – VASPHeader [VASP ID, VAS ID, Sender Address Information Elements] and RSHeader [MMS Relay/Server ID Information Element].

- The SOAP body element shall contain the messaging elements within an element that is named for the abstract message that is being implemented, e.g. Submit.REQ will be encapsulated in an XML element named “Submit.REQ”.  Each information element will be defined as a SOAP element with an appropriate type and value range.

- XML element names shall use Upper Camel Case convention, where words are concatenated to form an element name with the first letter of each word in upper case (e.g. EarliestDeliveryTime).  The only exception to this rule is where an acronym (e.g. VASP) is used  - in such cases all of the letters of the acronym will be in upper case (e.g. VASPHeader).

- The SOAP payload will be of content type “text/xml”. If multimedia content is included then the payload will be of type “multipart/related” with the Start parameter set to point to the SOAP envelope that will be the first part of the multipart payload.  The multimedia content will be formatted as a single part attachment to the SOAP message as specified in [69].  The SOAP body will include a single reference to the content part of the MIME.

#### 8.7.8.1.1 Binding to HTTP

MM7 request messages will be transferred in an HTTP POST request of media type “text/xml”[70] for requests that do not carry multimedia content or of media type “multipart/related”[71] for requests that include multimedia content.   The SOAP envelope will be the first part of the MIME message.

If multimedia content is included in the request it will be encoded as a single MIME part that will be the second part of the HTTP POST content.  This content will have Content-Type and Content-ID fields.  The Content-ID will be referenced by the MM7 request <content> element using the format specified in [69].  The Content-Type should be the type of the MM content, e.g. image/jpeg, multipart/ related, etc.

For specific examples see the section describing SOAP HTTP examples.

#### 8.7.8.1.2 Access Authentication

HTTP provides several optional challenge-response authentication mechanisms, which can be used by the MMS Relay/Server to challenge the VASP request and by the VASP to provide authentication information. The MMS Relay/Server shall use the mechanisms defined in RFC 2617[74],” basic” and “digest” authentication to authenticate the VASP during each session established for message submission. The VASP will be required to issue a username and password before any transactions will be allowed by the MMS Relay/Server.

The VASP may optionally require authentication from the MMS Relay/Server for transactions that are intiated by the MMS Relay/Server.  The exact nature of these authentication procedures are not dictated by this document, however the MMS Relay/Server may supply its identification as part of the request information in the RS Header element.

#### 8.7.8.1.3 SOAPAction Header Field

The SOAPAction HTTP request header field [68] should be set to the NULL string (i.e. “”). If, for implementation reasons, it is necessary to enter a value for this header field then the value may indicate the intent of the HTTP request.

#### 8.7.8.2 MM7 Addressing Considerations

In order to bind properly to HTTP, the MMS Relay/Server and the VASP shall be adressable by a URL type address [48]. This address shall be placed in the host header field in the HTTP POST method.   The VASP will identify itself using one (or more) of three possible identifiers – the VASP identification number, the VAS identification number, or a MM1 compliant address.  The MMS Relay/Server must translate the identifcation of the VASP to an appropriate address format for transfer across other reference points, e.g. address as defined in section 7.2.2 for messages sent on MM1.

The MMS Relay/Server must also translate addresses that originate from the MM1 interface into the appropriate URL of the VASP, for example when an MM7_deliver.REQ  results from a MM1_submit.REQ from the MMS User Agent.  The format of the MM1 address is defined in section 7.2.2 of this specification.

In the SOAP body, when the recipient MMS User Agent is addressed, the address-encoding scheme for MM1 shall be used.  For these purposes the VASP will be identified by a MM1 addressable address.

#### 8.7.8.3 Fault Reporting

The MM7 response messages will be carried within a HTTP response as a SOAP message.  The response may carry errors at three levels:

- network errors will be indicated by the HTTP level, e.g. as an HTTP 403 “Server not found”

- request processing errors – when a PDU arrives to the server but cannot be handled, e.g. incompatible protocol version, failure to comply with XML schema – these errors will usually be reported by a generic error message (sections 8.7.9.13 and 8.7.9.14).

- MMS errors indicate errors at the application level, e.g. server congestion or replace not possible

All error responses will be reported with three XML elements in the response –

- StatusCode will indicate a numerical code that identifies different classes of error or successful completion of the operation.  The StatusCode will be a four-digit number of which the two high-order digits will be defined in section 8.7.8.3.1, the two low-order digits are implementation specific.

- StatusText, an optional field, that contains a predetermined text description of the numerical code that indicates the general type of the error.

- Details, optionally, gives particular details of the error, e.g. indicates the address that cannot be resolved or message-id that is not recognized.

The first two digits of the code will be defined in section 8.7.8.3.1.  The low-order two digits will be implementation specific.

#### 8.7.8.3.1 Request Status Codes

The StatusText element (for application-level situations) shall be used to carry a human readable explanation of the error or success situation, e.g. partial success. In addition to this there will be status codes consisting of a four digit numeric value. The two high-order digits of the status code indicates the classification of the error as follows:

00xx  Success

This code indicates that the request was executed completely

01xx Partial success

This code indicates that the request was executed partially but some parts of the request could not be completed.  Lower order digits and the optional Details element may indicate what parts of the request were not completed.

21xx Operation restricted

The request was refused due to lack of permission to execute the command.

22xx Address Error

The address supplied in the request was not in a recognized format or the MMS Relay/Server ascertained that the address was not valid for the network because it was determined not to be serviced by this MMS Relay/Server. When used in response-result, and multiple recipients were specified in the corresponding push submission, this status code indicates that at least one address is incorrect.

23xx Address Not Found

The address supplied in the request could not be located by the MMS Relay/Server. This code is returned when an operation is requested on a previously submitted message and the MMS Relay/Server can not find the message for the address specified.

25xx Multimedia content corrupt

The server could not parse the MIME content that was attached to the SOAP and indicated by the Content element.

26xx Message ID Not Found

This code is returned when an operation is requested on a previously submitted message and the MMS Relay/Server cannot find the message for the message ID specified.

30xx Server Error

The server failed to fulfill an apparently valid request.

33xx Not Possible

The request could not be carried out because it is not possible. This code is normally used as a result of a cancel or status query on a message that is no longer available for cancel or status. The MMS Relay/Server has recognized the message in question, but it cannot fulfill the request because the message is already complete or status is no longer available.

35xx Multiple Addresses Not Supported

The MMS Relay/Server does not support this operation on multiple recipients. The operation MAY be resubmitted as multiple single recipient operations.

51xx Unknown message

Reported by the VASP when receiving a delivery or read report for a message whose ID is not recognized by the VASP.

60xx VASP Server error

The server failed to fulfill an apparently valid request.

61xx Message rejected

Reported by the VASP for requests that were received from the MMS Relay/Server but could not be completed.

71xx Improper identification

Identification header of the request does not uniquely identify the client (either the VASP or MMS Relay/Server).

81xx Unsupported version

The version indicated by the MM7Version element is not supported by the server.

82xx Unsupported operation

The server does not supported the request indicated by the MessageType element in the header of the message.

83xx Validation error

The SOAP and XML structures could not be parsed, mandatory fields are missing, or the message-format is not compatible to the format specified.  Details field may specify the parsing error that caused this status.

90xx Service error

The operation caused a server (either MMS Relay/Server or VASP) failure and should not be resent.

91xx Service unavailable

This indication may be sent by the server when service is temporarily unavailable, e.g. when server is busy

Status codes are extensible. The VASP and the MMS Relay/Server must understand the class of a status code. Unrecognized codes shall be treated as the x000 code for that class. The two high-order digits should be assigned according to the following classifications: 0xxx – indicate success in the operation, 2xxx are generated by the MMS Relay/Server for client errors, 3xxx are generated by the MMS Relay/Server to indicate server errors, 5xxx are generated by the VASP for client errors, 6xxx are generated by VASP server errors, 7xxx indicate validation errors, 8xxx indicate unsupported features, and 9xxx indicated top-level errors.  The two low-order digits of the status code are reserved for implementation specific codes,

### 8.7.9 Mapping of Information Elements to SOAP Elements

The following subsections detail the mapping of the information elements of the abstract messages to SOAP elements.  The full XML Schema definition of the interface appears in Annex D of this document.

#### 8.7.9.1 MM7_submit.REQ mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Submit.REQ In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| VASP ID | SOAP Header | VASPID | VASPHeader group |
| VAS ID | SOAP Header | VASID | VASPHeader group |
| Sender Address | SOAP Header | ApplicationAddress | VASPHeader group |
| Recipient Address | SOAP Body | To, CC, Bcc | At least one of these elements must appear |
| Service code | SOAP Body | ServiceCode | Information supplied for billing purposes – exact format is implementation dependent |
| Linked ID | SOAP Body | LinkedID | Message-ID of linked message |
| Message class | SOAP Body | MessageClass | Enumeration – possible values: Informational, Advertisement, Auto |
| Date and time | SOAP Body | Date |  |
| Time of Expiry | SOAP Body | ExpiryDate |  |
| Earliest delivery time | SOAP Body | EarliestDeliveryTime |  |
| Delivery report | SOAP Body | DeliveryReport | Boolean: True or False |
| Read reply | SOAP Body | ReadReply | Boolean: True or False |
| Reply-Charging | SOAP Body | ReplyCharging | Boolean: True or False |
| Reply-Deadline | SOAP Body | ReplyDeadline | Date format – absolute or interval |
| Reply-Charging-Size | SOAP Body | ReplyChargingSize |  |
| Priority | SOAP Body | Priority | Enumeration – possible values: High, Normal, Low |
| Subject | SOAP Body | Subject |  |
| Adaptations | SOAP Body | AllowAdaptations | Boolean: True or False |
| Content type | MIME header – Attachment | Content-Type |  |
| Content | SOAP Body | Content | href:cid |

#### 8.7.9.2 MM7_submit.RES mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Submit.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Message ID | SOAP Body | MessageID |  |
| Request Status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Request Status Text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

Sample message submission

POST /mms-rs/mm7 HTTP/1.1
Host: mms.omms.com
Content-Type: multipart/related; boundary=”NextPart_000_0028_01C19839.84698430"; type=text/xml;
	start=”</tnn-200102/mm7-submit>”
Content-Length: nnnn
SOAPAction: “”

-- NextPart_000_0028_01C19839.84698430 --
Content-Type:text/xml; charset=”utf-8”
Content-ID: </tnn-200102/mm7-submit>

<?xml version=’1.0’ ?>
<env:Envelope xmlns:env="http:// schemas.xmlsoap.org/soap /soap-envelope"> 
      <env:Header>
		<mm7:MM7Header xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>
      			<TransactionID>vas00001-sub</TransactionID>
			<MessageType>Submit.REQ</MessageType>

<MM7Version>5.3.0</MM7Version>
		</mm7:MM7Header>
		<mm7:VASPHeader xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>
			<VASPID>TNN</VASPID>
			<VASID>News</VASID>
		</mm7:VASPHeader>
	</env:Header>	<env:Body>
		<mm7:Submit.REQ xmlns:mm7="//www.3gpp.org/MMS/Rel5/MM7”>
			<Recipients>
				<To>7255441234</To>
				<Cc>7255442222@OMMS.com</Cc>
				<Cc>7255443333</Cc>
				<Cc>7255444444@OMMS.com</Cc>
			</Recipients>
			<ServiceCode>gold-sp33-im42</ServiceCode>
			<LinkedID>mms00016666</LinkedID>
			<MessageClass>Informational</MessageClass>
			<Date>2002-01-02T09:30:47-05:00</Date>
			<ExpiryDate>P90D</ExpiryDate>
			<EarliestDeliveryTime>2002-01-02T09:30:47-05:00</EarliestDeliveryTime>
			<DeliveryReport>true</DeliveryReport>
			<ReadReply>true</ReadReply>
			<Priority>Normal</Priority>
			<Subject>News for today</Subject>
			<AllowAdaptations>true</AllowAdaptations>
			<Content href="cid:SaturnPics-01020930@news.tnn.com"/>
		</mm7:Submit.REQ>
	</env:Body></env:Envelope>-- NextPart_000_0028_01C19839.84698430 --
Content-Type: multipart/mixed; boundary=”StoryParts 74526 8432 2002-77645”

Content-ID:< SaturnPics-01020930@news.tnn.com>

-- StoryParts 74526 8432 2002-77645 --

Content-Type: text/plain; charset="us-ascii"

Science news, new Saturn pictures...

-- StoryParts 74526 8432 2002-77645 --

Content-Type: image/gif;

Content-ID:<saturn.gif>

R0lGODdhZAAwAOMAAAAAAIGJjGltcDE0OOfWo6Ochbi1n1pmcbGojpKbnP/lpW54fBMTE1RYXEFO

…

-- StoryParts 74526 8432 2002-77645 --

--_NextPart_000_0028_01C19839.84698430--

The response message is sent by the MMS Relay/Server back to the VASP for the VAS application in a HTTP Response message.

HTTP/1.1  200 OK

Content-Type: text/xml; charset=”utf-8”

Content-Length: nnnn

<? xml  version=’1.0’ ?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/soap-envelope">

<env:Header>

<mm7:MM7Header xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<TransactionID>vas00001-sub</TransactionID>

<MessageType>Submit.RES</MessageType>

<MM7Version>5.3.0</MM7Version>

</mm7:MM7Header>
	</env:Header>
	<env:Body>

<MessageID>041502073667</MessageID>

<Status>

<StatusCode>2000</StatusCode>

<StatusText> Message Sent</StatusText>

</Status>

</env:Body>
</env:Envelope>

#### 8.7.9.3 MM7_deliver.REQ Mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Deliver.REQ In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| MMS Relay/Server ID | SOAP Header | MMSRelayServerID | RSHeader group |
| Linked ID | SOAP Body | LinkedID |  |
| Sender address | SOAP Body | Sender |  |
| Recipient address | SOAP Body | Recipients (To, Cc, Bcc) | If none appear then Sender Address is used |
| Date and time | SOAP Body | Date |  |
| Reply-Charging-ID | SOAP Body | ReplyChargingID | Should correspond to an ID that appeared in previous MM7_submit.REQ |
| Priority | SOAP Body | Priority | Enumeration – possible values: High, Normal, Low |
| Subject | SOAP Body | Subject |  |
| Content type | MIME header of attachment | Content-Type |  |
| Content | SOAP Body | Content | href:cid |

#### 8.7.9.4 MM7_deliver.RES

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Deliver.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Service code | SOAP Header | ServiceCode | VASPHeader group |
| Request status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Request status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

Sample Deliver request and response

POST /mms/weather.xml HTTP/1.1

Host: www.yahoo.com

Content-Type: multipart/related; boundary=”NextPart_000_0125_01C19839.7237929064"; type=text/xml;

start=”</cmvt256/mm7-deliver>”

Content-Length: nnnn

SOAPAction: “”

-- NextPart_000_0125_01C19839. 7237929064 --

Content-Type:text/xml; charset=”utf:8”

Content-ID: </cmvt256/mm7-submit>

<? xml version=’1.0’ ?>

<env:Envelope xmlns:env="http:// schemas.xmlsoap.org/soap /soap-envelope">

<env:Header>

<mm7:MM7Header xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<TransactionID>vas00324-dlvr</TransactionID>

<MessageType>Deliver.REQ</MessageType>

<MM7Version>5.3.0</MM7Version>

</mm7:MM7Header>

<mm7:RSHeader xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<MMSRelayServerID>240.110.75.34</MMSRelayServerID>

</mm7:RSHeader>

</env:Header>

<env:Body>

<!-- Example of MM7_deliver.REQ -->

<mm7:Deliver.req xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7”>

<Sender>97254265781@OMMS.com</Sender>

<LinkedID>wthr8391</LinkedID>

<Date>2002-04-15T14:35:21-05:00</Date>

<Priority>Normal</Priority>

<Subject>Weather Forecast</Subject>

<Content href=cid:forecast-location200102-86453/>

</env:Body>

</env:Envelope>

-- NextPart_000_0125_01C19839. 7237929064 --

Content-Type:text/plain;charset=”utf-8”

Content-ID:<forecast-location2000102-86453>

Los Angeles, Calif, USA 
--_NextPart_000_0125_01C19839. 7237929064--

The deliver response message might look like this (with an application error code):

HTTP/1.1  200 OK

Content-Type: text/xml; charset=”utf-8”

Content-Length: nnnn

<? xml version=’1.0’ ?>

<env:Envelope xmlns:env="http://schemas.xmlsoap.org/soap/soap-envelope">

<env:Header>

<mm7:MM7Header xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<TransactionID>vas00324-dlvr</TransactionID>

<MessageType>Deliver.RES</MessageType>

<MM7Version>5.3.0</MM7Version>

</mm7:MM7Header>

</env:Header>

<env:Body>

<mm7:Deliver.res xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7”>

<ServiceCode>wthr-badl-6521</ServiceCode>

<Status>

<StatusCode>4101</StatusCode>

<StatusText>Service Unavailable</ServiceText>

<Detail>Location not covered in service </Detail>

</Status>

</mm7:Deliver.res>

</env:Body></env:Envelope>

#### 8.7.9.5 MM7_cancel.REQ mapping

| Information Element | Location | Element-name |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Cancel.REQ In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| VASP ID | SOAP Header | VASPID | VASPHeader group |
| VAS ID | SOAP Header | VASID | VASPHeader group |
| Sender Address | SOAP Header | ApplicationAddress | VASPHeader group |
| Message ID | SOAP Body | MessageID |  |

#### 8.7.9.6 MM7_cancel.RES mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Cancel.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Request status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Request status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

The following shows an interchange of a MM7_cancel.REQ and MM7_cancel.RES to illustrate a SOAP message that does not include a multimedia content part.

POST /mms-rs/mm7 HTTP/1.1

Host: mms.omms.com

Content-Type: text/xml; charset=”utf-8”

Content-Length: nnnn

SOAPAction: “3GPP/MMSR5/MM7/cancel”

<env:Envelope xmlns:env="http:// schemas.xmlsoap.org/soap /soap-envelope">

<env:Header>

<mm7:MM7Header xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<TransactionID>vas0000--can</TransactionID>

<MessageType>Cancel.REQ</MessageType>

<MM7Version>5.3.0</MM7Version>

</mm7:MM7Header>

<mm7:VASPHeader xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<VASPID>TNN</VASPID>

<VASID>Reminder</VASID>

</mm7:VASPHeader>

</env:Header>

<env:Body>

<mm7:Cancel.REQ xmlns:mm7="//www.3gpp.org/MMS/Rel5/MM7”>

<MessageID>mms000222222</MessageID>

</mm7:Cancel.REQ>

</env:Body>

</env:Envelope>

HTTP/1.1  200 OK

Content-Type: text/xml; charset=”utf-8”

Content-Length: nnnn

<env:Envelope xmlns:env="http:// schemas.xmlsoap.org/soap /soap-envelope">

<env:Header>

<mm7:MM7Header xmlns:mm7=”//www.3gpp.org/MMS/Rel5/MM7” env:mustUnderstand=”1”>

<TransactionID>vas0000--can</TransactionID>

<MessageType>Cancel.RES</MessageType>

<MM7Version>5.3.0</MM7Version>

</mm7:MM7Header>

</env:Header>

<env:Body>

<Status>

<StatusCode>0000</StatusCode>

<StatusText>Message canceled</StatusText>

</Status>

</env:Body>

</env:Envelope>

#### 8.7.9.7 MM7_replace.REQ mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Replace.REQ In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| VASP ID | SOAP Header | VASPID | VASPHeader group |
| VAS ID | SOAP Header | VASID | VASPHeader group |
| Sender address | SOAP Header | ApplicationAddress | VASPHeader group |
| Message ID | SOAP Body | MessageID |  |
| Service code | SOAP Header | ServiceCode | Charging group |
| Date and time | SOAP Body | Date |  |
| Earliest delivery time | SOAP Body | EarliestDeliveryTime |  |
| Read reply | SOAP Body | ReadReply | Boolean – true or false |
| Adapatations | SOAP Body | AllowAdaptations | Boolean – true or false |
| Content type | MIME part Header | Content-Type |  |
| Content | SOAP Body | Content | href:cid |

#### 8.7.9.8 MM7_replace.RES mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | Transaction-ID | MM7Header group |
| Message-Type | SOAP Header | Message-Type | MM7Header group Value is Replace.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7-Version | Transaction group Value is number of this specification, e.g. 5.2.0 |
| Request status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Request status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

#### 8.7.9.9 MM7_delivery_report.REQ mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Delivery-Report.REQ In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| MMS Relay/Server ID | SOAP Header | MMSRelayServerID | RSHeader group |
| Message ID | SOAP Body | MessageID |  |
| Recipient address | SOAP Body | Recipient |  |
| Sender address | SOAP Body | Sender |  |
| Date and time | SOAP Body | Date |  |
| MM Status | SOAP Body | MMStatus | Enumeration – possible values: Expired, Retrieved, Rejected, Indeterminate, Forwarded |
| Status text | SOAP Body | StatusText |  |

#### 8.7.9.10 MM7_delivery_report.RES mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Delivery-Report.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Request Status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Request Status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

#### 8.7.9.11 MM7_read_reply.REQ mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Read-Reply.REQ In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| MMS Relay/Server ID | SOAP Header | MMSRelayServerID | RSHeader group |
| Message ID | SOAP Body | MessageID |  |
| Recipient address | SOAP Body | Recipient |  |
| Sender address | SOAP Body &HTTP POST URL | Sender |  |
| Date and time | SOAP Body | Date |  |
| Read Status | SOAP Body | MMStatus | Enumeration – possible values: Indeterminate, Read, Deleted without Read |
| Status text | SOAP Body | StatusText |  |

#### 8.7.9.12 MM7_read_reply.RES mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is Read-Reply.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Request status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Request status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

#### 8.7.9.13 MM7_RS_error.RES mapping

| Information Element | Location | ElementName |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | TransactionID | MM7Header group |
| Message-Type | SOAP Header | MessageType | MM7Header group Value is RS_Error.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Error status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Error status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

#### 8.7.9.14 MM7_VASP_error.RES mapping

| Information Element | Location | Element-name |  |
| --- | --- | --- | --- |
| Transaction ID | SOAP Header | Transaction-ID | MM7Header group |
| Message-Type | SOAP Header | Message-Type | MM7Header group Value is VASP-Error.RES In addition defined as Root element of SOAP Body |
| MM7 Version | SOAP Header | MM7-Version | MM7Header group Value is number of this specification, e.g. 5.2.0 |
| Error status | SOAP Body | StatusCode | See section 8.7.8.4 |
| Error status text | SOAP Body | StatusText & Details | See section 8.7.8.4 |

Annex X (informative): MM7 XML Schema

<?xml version="1.0" encoding="UTF-8"?>

<!-- edited with XML Spy v4.2 U (http://www.xmlspy.com) by Arie Gofer (Comverse) -->

<xs:schema targetNamespace="//www.3gpp.org/MMS/Rel5/MM7" xmlns:mm7="//www.3gpp.org/MMS/Rel5/MM7" xmlns:xs="http://www.w3.org/2001/XMLSchema" elementFormDefault="qualified" attributeFormDefault="unqualified">

<xs:element name="MM7Header" type="mm7:MM7Header">

<xs:annotation>

<xs:documentation>Generic header for Relay/Server originated PDUs</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="VASPHeader" type="mm7:VASPHeader">

<xs:annotation>

<xs:documentation>Generic header for VASP originated PDUs</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="RSHeader" type="mm7:RSHeader">

<xs:annotation>

<xs:documentation>Generic header for VASP originated PDUs</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Submit.REQ" type="mm7:Submit.REQ">

<xs:annotation>

<xs:documentation>VASP to MMS : Sending MM from the VASP to one or more recipients</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Submit.RES" type="mm7:Submit.RES">

<xs:annotation>

<xs:documentation>MMS  to VASP: Response to a VASP after MM submission request</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Deliver.REQ" type="mm7:Deliver.REQ">

<xs:annotation>

<xs:documentation>MMS to VASP : Delivery of MM from the MMSC to the VASP </xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Deliver.RES" type="mm7:Deliver.RES">

<xs:annotation>

<xs:documentation>VASP to MMS : Response to a message delivered to the VASP from the relay</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Cancel.REQ" type="mm7:Cancel.REQ">

<xs:annotation>

<xs:documentation>VASP  to MMS: Request to cancel a message submission </xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Cancel.RES" type="mm7:simpleResponsePDUType">

<xs:annotation>

<xs:documentation>MMS  to VASP: Response to a VASP after MM cancellation request </xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Replace.REQ" type="mm7:Replace.REQ">

<xs:annotation>

<xs:documentation>VASP  to MMS: Request to replace a message which was submitted </xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="Replace.RES" type="mm7:simpleResponsePDUType">

<xs:annotation>

<xs:documentation>MMS  to VASP: Response to a VASP after MM replace request </xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="DeliveryReport.REQ" type="mm7:DeliveryReport.REQ">

<xs:annotation>

<xs:documentation>MMS to VASP : Delivery Report from one of the MM recipients</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="DeliveryReport.RES" type="mm7:simpleResponsePDUType">

<xs:annotation>

<xs:documentation>VASP to MMS: Response to a delivery report delivered to the VASP</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="ReadReply.REQ" type="mm7:ReadReply.REQ">

<xs:annotation>

<xs:documentation>MMS to VASP : Delivery Report from one of the MM recipients</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="ReadReply.RES" type="mm7:simpleResponsePDUType">

<xs:annotation>

<xs:documentation>VASP to MMS: Response to a read reply delivered to the VASP</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="RSError.RES" type="mm7:simpleResponsePDUType">

<xs:annotation>

<xs:documentation>MMS to VASP: Error response to a any bad request sent to the Relay/Server</xs:documentation>

</xs:annotation>

</xs:element>

<xs:element name="VASPError.RES" type="mm7:simpleResponsePDUType">

<xs:annotation>

<xs:documentation>VASP to MMS: Error response to a any bad request sent to the VASP</xs:documentation>

</xs:annotation>

</xs:element>

<xs:complexType name="MM7Header">

<xs:all>

<xs:element name="TransactionID" type="xs:NMTOKEN"/>

<xs:element name="MM7Version" type="mm7:versionType"/>

<xs:element name="MessageType" type="mm7:PDUType"/>

</xs:all>

</xs:complexType>

<xs:complexType name="VASPHeader">

<xs:all>

<xs:element name="VASPID" type="mm7:entityIDType" minOccurs="0"/>

<xs:element name="VASID" type="mm7:entityIDType" minOccurs="0"/>

<xs:element name="ApplicationAddress" type="xs:string" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="RSHeader">

<xs:all>

<xs:element name="MMSRelayServerID" type="mm7:entityIDType" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="Submit.REQ">

<xs:all>

<xs:element name="Recipients" type="mm7:recipientsType"/>

<xs:element name="ServiceCode" type="mm7:serviceCodeType" minOccurs="0"/>

<xs:element name="LinkedID" type="mm7:messageIDType" minOccurs="0"/>

<xs:element name="MessageClass" type="mm7:messageClassType" default="Informational" minOccurs="0"/>

<xs:element name="Date" type="xs:dateTime" minOccurs="0"/>

<xs:element name="ExpiryDate" type="mm7:relativeOrAbsoluteDateType" minOccurs="0"/>

<xs:element name="EarliestDeliveryTime" type="mm7:relativeOrAbsoluteDateType" minOccurs="0"/>

<xs:element name="DeliveryReport" type="xs:boolean" minOccurs="0"/>

<xs:element name="ReadReply" type="xs:boolean" minOccurs="0"/>

<xs:element name="ReplyCharging" type="xs:boolean" minOccurs="0"/>

<xs:element name="ReplyDeadline" type="mm7:relativeOrAbsoluteDateType" minOccurs="0"/>

<xs:element name="ReadChargingSize" type="xs:positiveInteger" minOccurs="0"/>

<xs:element name="Priority" type="mm7:priorityType" minOccurs="0"/>

<xs:element name="Subject" type="xs:string" minOccurs="0"/>

<xs:element name="AllowAdaptations" type="xs:boolean" default="true" minOccurs="0"/>

<xs:element name="Content" type="mm7:contentReferenceType" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="Submit.RES">

<xs:all>

<xs:element name="MessageID" type="mm7:messageIDType" minOccurs="0"/>

<xs:element name="Status" type="mm7:responseStatusType"/>

</xs:all>

</xs:complexType>

<xs:complexType name="Deliver.REQ">

<xs:all>

<xs:element name="LinkedID" type="mm7:messageIDType" minOccurs="0"/>

<xs:element name="Sender" type="mm7:addressType"/>

<xs:element name="Recipients" type="mm7:recipientsType" minOccurs="0"/>

<xs:element name="Date" type="xs:dateTime" minOccurs="0"/>

<xs:element name="ReplyChargingID" type="mm7:messageIDType"/>

<xs:element name="Priority" type="mm7:priorityType" minOccurs="0"/>

<xs:element name="Subject" type="xs:string" minOccurs="0"/>

<xs:element name="Content" type="mm7:contentReferenceType" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="Deliver.RES">

<xs:all>

<xs:element name="ServiceCode" type="mm7:serviceCodeType" minOccurs="0"/>

<xs:element name="Status" type="mm7:responseStatusType"/>

</xs:all>

</xs:complexType>

<xs:complexType name="Cancel.REQ">

<xs:all>

<xs:element name="MessageID" type="mm7:messageIDType"/>

</xs:all>

</xs:complexType>

<xs:complexType name="Replace.REQ">

<xs:all>

<xs:element name="MessageID" type="mm7:messageIDType"/>

<xs:element name="ServiceCode" type="mm7:serviceCodeType" minOccurs="0"/>

<xs:element name="Date" type="xs:dateTime" minOccurs="0"/>

<xs:element name="EarliestDeliveryTime" type="mm7:relativeOrAbsoluteDateType" minOccurs="0"/>

<xs:element name="ReadReply" type="xs:boolean" minOccurs="0"/>

<xs:element name="AllowAdaptations" type="xs:boolean" minOccurs="0"/>

<xs:element name="Content" type="mm7:contentReferenceType" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="DeliveryReport.REQ">

<xs:all>

<xs:element name="MessageID" type="mm7:messageIDType"/>

<xs:element name="Recipient" type="mm7:addressType"/>

<xs:element name="Sender" type="mm7:addressType"/>

<xs:element name="Date" type="xs:dateTime"/>

<xs:element name="MMStatus" type="mm7:mmDeliveryStatusType"/>

<xs:element name="StatusText" type="xs:string" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="ReadReply.REQ">

<xs:all>

<xs:element name="MessageID" type="mm7:messageIDType"/>

<xs:element name="Recipient" type="mm7:addressType"/>

<xs:element name="Sender" type="mm7:addressType"/>

<xs:element name="Date" type="xs:dateTime"/>

<xs:element name="MMStatus" type="mm7:mmReadStatusType"/>

<xs:element name="StatusText" type="xs:string" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:complexType name="simpleResponsePDUType">

<xs:annotation>

<xs:documentation>Any simple response sent </xs:documentation>

</xs:annotation>

<xs:all>

<xs:element name="Status" type="mm7:responseStatusType"/>

</xs:all>

</xs:complexType>

<xs:complexType name="responseStatusType">

<xs:annotation>

<xs:documentation>Status information conveyed in responses</xs:documentation>

</xs:annotation>

<xs:all>

<xs:element name="StatusCode" type="mm7:statusCodeType"/>

<xs:element name="StatusText" type="xs:string" minOccurs="0"/>

<xs:element name="Details" type="mm7:anyDataType" minOccurs="0"/>

</xs:all>

</xs:complexType>

<xs:simpleType name="mmDeliveryStatusType">

<xs:annotation>

<xs:documentation>Statuses for MM7_delivery_report</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:enumeration value="Expired"/>

<xs:enumeration value="Retrieved"/>

<xs:enumeration value="Rejected"/>

<xs:enumeration value="Indeterminate"/>

<xs:enumeration value="Forwarded"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="mmReadStatusType">

<xs:annotation>

<xs:documentation>Statuses for MM7_read_reply</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:enumeration value="Indeterminate"/>

<xs:enumeration value="Read"/>

<xs:enumeration value="Deleted"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="messageIDType">

<xs:annotation>

<xs:documentation>Message ID</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:NMTOKEN"/>

</xs:simpleType>

<xs:simpleType name="addressType">

<xs:annotation>

<xs:documentation>Any address (RFC822 / MMS etc.)</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string"/>

</xs:simpleType>

<xs:complexType name="serviceCodeType" mixed="true">

<xs:annotation>

<xs:documentation>Used to identify the specific service given for billing purposes</xs:documentation>

</xs:annotation>

<xs:complexContent mixed="true">

<xs:extension base="mm7:anyDataType"/>

</xs:complexContent>

</xs:complexType>

<xs:simpleType name="entityIDType">

<xs:annotation>

<xs:documentation>String used to identify the VAS, VASP and relays</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:NMTOKEN"/>

</xs:simpleType>

<xs:complexType name="recipientsType">

<xs:annotation>

<xs:documentation>At least one of To,CC,Bcc</xs:documentation>

</xs:annotation>

<xs:sequence maxOccurs="unbounded">

<xs:choice>

<xs:element name="To" type="mm7:addressType"/>

<xs:element name="Cc" type="mm7:addressType"/>

<xs:element name="Bcc" type="mm7:addressType"/>

</xs:choice>

</xs:sequence>

</xs:complexType>

<xs:simpleType name="messageClassType">

<xs:annotation>

<xs:documentation>Message class</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:enumeration value="Personal"/>

<xs:enumeration value="Informational"/>

<xs:enumeration value="Advertisement"/>

<xs:enumeration value="Auto"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="priorityType">

<xs:annotation>

<xs:documentation>Priority of MM</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:enumeration value="Normal"/>

<xs:enumeration value="High"/>

<xs:enumeration value="Low"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="PDUType">

<xs:annotation>

<xs:documentation>MM7 PDU type</xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:enumeration value="Submit.REQ"/>

<xs:enumeration value="Submit.RES"/>

<xs:enumeration value="Cancel.REQ"/>

<xs:enumeration value="Cancel.RES"/>

<xs:enumeration value="Replace.REQ"/>

<xs:enumeration value="Replace.RES"/>

<xs:enumeration value="Deliver.REQ"/>

<xs:enumeration value="Deliver.RES"/>

<xs:enumeration value="DeliveryReport.REQ"/>

<xs:enumeration value="DeliveryReport.RES"/>

<xs:enumeration value="ReadReply.REQ"/>

<xs:enumeration value="ReadReply.RES"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="relativeOrAbsoluteDateType">

<xs:annotation>

<xs:documentation>Date which can be relative or absolute</xs:documentation>

</xs:annotation>

<xs:union memberTypes="xs:dateTime xs:duration"/>

</xs:simpleType>

<xs:simpleType name="versionType">

<xs:annotation>

<xs:documentation>Version number in the format of x.y.z </xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:enumeration value="5.3.0"/>

</xs:restriction>

</xs:simpleType>

<xs:simpleType name="statusCodeType">

<xs:annotation>

<xs:documentation>request status resonse codes in RES </xs:documentation>

</xs:annotation>

<xs:restriction base="xs:string">

<xs:pattern value="[0-9]{4}"/>

</xs:restriction>

</xs:simpleType>

<xs:complexType name="contentReferenceType">

<xs:annotation>

<xs:documentation>content element including only href</xs:documentation>

</xs:annotation>

<xs:attribute name="href" type="xs:anyURI" use="required"/>

</xs:complexType>

<xs:complexType name="anyDataType" mixed="true">

<xs:annotation>

<xs:documentation>Any element and attribute </xs:documentation>

</xs:annotation>

<xs:complexContent mixed="true">

<xs:restriction base="xs:anyType">

<xs:sequence>

<xs:any processContents="lax" minOccurs="0" maxOccurs="unbounded"/>

</xs:sequence>

</xs:restriction>

</xs:complexContent>

</xs:complexType>

</xs:schema>

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.