| 3GPP TSG-T2 SWG3#11 Seattle, USA 29th April – 2nd May 2002 | T2M020151 |
| --- | --- |
| CR-Form-v5 |
| CHANGE REQUEST |
| ( | 23.140 | CR | CRNum | ( rev | - | ( Current version: | 5.2.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | X |
| Title: ( | Correction to MM7 Stage 2 on Address Visibility in Sender and Recipient IEs |
| Source: ( | NOKIA |
| Work item code: ( | MESS5-MMS |  | Date: ( | May 1st, 2002 |
| Category: ( | F |  | Release: ( | REL-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | MM7 Stage 2 is incomplete in its description how informational and control level addressing is handled |
| Summary of change: ( | Information about address level handling is included. |
| Consequences if ( not approved: | MM7 Stage 2 would be unclear with certain specifics in MM7 Stage 3 |
| Clauses affected: ( | 7.2.3, 8.7.1.3, 8.7.1.4, 8.7.2.3, 8.7.2.4 |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

### 7.2.3	Address Formats on MM7

The MMS addressing model on MM7 contains two addresses: The address of the originator MMS User Agent or VAS/VASP and the address(es) of the recipient MMS User Agent(s) or VAS/VASP.

The reference point MM7 shall support E.164 (MSISDN) addresses and e-mail addresses (RFC2822). In addition Short Codes should be supported.

In the case of a multimedia message terminated at the VAS/VASP, the recipient(s)' address(es) may be the VAS/VASP address or the intended recipient(s)’ address and the originator's address shall be user's address (e.g. MSISDN address) or a user's terminal address. For this release the user's terminal addresses (e.g. terminal IP addresses) are not supported.

In the case of a multimedia message originated from the VAS/VASP, the originator's address may be the VAS/VASP address and the recipient(s)' address(es) shall be either a user's address or a user's terminal address. For this release the user's terminal addresses (e.g. terminal IP addresses) are not supported. The VASP's responsibility is to format these addresses before it submits the message to the MMS Relay/Server. The user’s address shall be E.164 (MSISDN) address or e-mail address (RFC2822). Additionally, it shall be possible to control which recipient(s) address(es) are utilized for actual routing and which are conveyed as informational only to be displayed to the recipient MMS User Agent.

The reference point MM7 defines also other addressing like information elements: VASP ID, VAS ID and MMS Relay/Server ID. These fields are used only to identify VASP, VAS and MMS Relay/Server and are not used for addressing purpose.

NOTE: 	The users’ addresses refered to above may be replaced by appropriate coded addresses in order not to harm the users’ privacy.

…

#### 8.7.1.3	Features

Authorisation: The VASP must supply its own identifier or the VAS identifier as part of the request.

Addressing: The VASP may direct the MM to a one or more subscribers or to a distribution list. In the addressing, it may be indicated whether a recipient address is meant for informational purposes only or to be used for routing or other processing purposes as well. The originator of a submitted MM may be indicated in addressing-relevant information field(s) of the MM7_submit.REQ

Version: The MM7 protocol shall provide unique means to identify the version supported by both the MMS Relay/Server and VASP.

Message Type: The type of message used on reference point MM7 indicating MM7_submit.REQ and MM7_submit.RES as such.

Transaction Identification: The VASP shall provide an unambiguous transaction identification within an MM7_submit.REQ. The MM7_submit.RES shall unambiguously refer to the corresponding MM7_submit.REQ using the same transaction identification.

Linked message identification: The VASP will supply a message identifier when submitting a message, that defines a correspondence to a previous message that was delivered by the MMS Relay/Server to the VASP

Message class,  priority, and subject: The VASP may qualify the MM further by adding a message class, a priority and/or subject to the MM7_submit.REQ.

Service code:  The VASP may mark the content of the message with a service code that may be transferred by the MMS Relay/Server in the form of charging information for use by the billing system to properly bill the user for the service being supplied.

Time stamping: The VASP may time stamp the MM.

Time constraints: The VASP may request an earliest desired time of delivery of the MM. The VASP may request a time of expiry for the MM

Reply-Charging: The originator VASP may indicate that it wants to pay for a reply-MM and convey the reply-charging limitations (e.g. the latest time of submission and/or the maximum size of a reply-MM) in the MM7_submit.REQ.

Delivery reporting: The VASP may request a delivery report for the MM

Read reporting: The VASP may request a read-reply report when the user has viewed the MM.

Content adaptation restriction: The VASP may request that the content of the MM will not be subjected to content adaptation.

Content type: The MIME type of the multimedia content shall always be identified in the MM7_submit.REQ.

Content: The VASP may add content in the MM7_submit.REQ.

Message identification: The MMS Relay/Server shall always provide a message identification for an MM, which it has accepted for submission in the MM7_submit.RES.

Request status: The MMS Relay/Server shall indicate the status of the MM7_submit.REQ in the associated MM7_submit.RES. The reason code given in the status information element of the MM7_submit.RES may be supported with an explanatory text further qualifying the status.

…

#### 8.7.1.4	Information Elements

Table 48: Information elements in the MM7_submit.REQ .

| Information element | Presence | Description |
| --- | --- | --- |
| Transaction ID | Mandatory | The identification of the MM7_submit.REQ/ MM7_submit.RES pair. |
| Message type | Mandatory | Identifies this message as a MM7_submit request. |
| MM7 version | Mandatory | Identifies the version of the interface supported by the VASP |
| VASP ID | Optional | Identifier of the VASP for this MMS Relay/Server. |
| VAS ID | Optional | Identifier of the originating application. |
| Sender address | Optional | The address of the MM originator. |
| Recipient address | Mandatory | The address of the recipient MM. Multiple addresses are possible or the use of the alias that indicates the use of a distribution list. It is possible to mark an address to be used only for informational purposes. |
| Service code | Optional | Information supplied by the VASP which may be included in charging information. The syntax and semantics of the content of this information are out of the scope of this specification. |
| Linked ID | Optional | This identifies a correspondence to a previous valid message delivered to the VASP. |
| Message class | Optional | Class of the MM (e.g. advertisement, information service, accounting) |
| Date and time | Optional | The time and date of the submission of the MM (time stamp). |
| Time of Expiry | Optional | The desired time of expiry for the MM. |
| Earliest delivery time | Optional | The earliest desired time of delivery of the MM to the recipient. |
| Delivery report | Optional | A request for delivery report. |
| Read reply | Optional | A request for confirmation via a read report to be delivered as described in section 8.1 |
| Reply-Charging | Optional | A request for reply-charging. |
| Reply-Deadline | Optional | In case of reply-charging the latest time of submission of replies granted to the recipient(s). |
| Reply-Charging-Size | Optional | In case of reply-charging the maximum size for reply-MM(s) granted to the recipient(s). |
| Priority | Optional | The priority (importance) of the message. |
| Subject | Optional | The title of the whole multimedia message. |
| Adaptations | Optional | Indicates if VASP allows adaptation of the content (default True) |
| Content type | Mandatory | The content type of the MM’s content. |
| Content | Optional | The content of the multimedia message |

…

#### 8.7.2.3	Features

Authentication: The MMS Relay/Server may supply its own identifier as part of the request.

Addressing: All relevant address information for the delivery of the message to the VASP – including the addressing information from the original message and from the MMS Relay/Server should be included in the relevant information elements of MM7_deliver.REQ. In the addressing, it may be indicated whether a certain recipient address is meant for informational purposes only or to be used for routing or other processing purposes as well.

Version: The MM7 protocol shall provide unique means to identify the version supported by both the MMS Relay/Server and VASP.

Message Type: The type of message used on reference point MM7 indicating MM7_deliver.REQ and MM7_deliver.RES as such.

Transaction Identification: The VASP shall provide an unambiguous transaction identification within a request. The response shall unambiguously refer to the corresponding request using the same transaction identification.

Message priority and subject: The MMS Relay/Server may qualify the MM further by adding a priority and/or subject to the MM7_deliver.REQ.  This information will originate from the end-user’s original request.

Linked message identification: The MMS Relay/Server will supply an identifier for the request that may be used by the VASP.

Service code:  The VASP may mark the response to the message with a service code that will be transferred to the charging information for use by the billing system to properly bill the user for the service being supplied.

Time stamping: The MM may include a time stamp indicating the time of original submission.

Reply-Charging: In case of reply-charging when the reply-MM is submitted within the MM7_deliver.REQ MMS Relay/Server should indicate that the message is free-of-charge reply.

Content type: The MIME type of the multimedia content shall always be identified in the MM7_deliver.REQ.

Content: The originator of the MM may supply content that is delivered to the VASP in the MM7_deliver.REQ.

Request status: The MMS Relay/Server shall indicate the status of the request in the associated response. The reason code given in the status information element of the response may be supported with an explanatory text further qualifying the status.

#### 8.7.2.4	Information Elements

Table 51: Information elements in the MM7_deliver.REQ .

| Information element | Presence | Description |
| --- | --- | --- |
| Transaction ID | Mandatory | The identification of the MM7_deliver.REQ/ MM7_deliver.RES pair. |
| Message type | Mandatory | Identifies this message as a MM7_deliver request. |
| MM7 version | Mandatory | Identifies the version of the interface supported by the MMS Relay/Server |
| MMS Relay/Server ID | Optional | Identifier of the MMS Relay/Server |
| Linked ID | Optional | Identifier that may be used by the VASP in a subsequent MM7_submit.REQ |
| Sender address | Mandatory | The address of the MM originator. |
| Recipient address | Optional | The address(es) of the intended recipients of the subsequent processing by the VASP or the original recipient address(es). It is possible to mark an address to be used only for informational purposes. |
| Date and time | Optional | The time and date of the submission of the MM (time stamp). |
| Reply-Charging-ID | Optional | In case of reply-charging when the reply-MM is submitted within the MM7_deliver.REQ this is the identification of the original MM that is replied to. |
| Priority | Optional | The priority (importance) of the message. |
| Subject | Optional | The title of the whole MM. |
| Content type | Mandatory | The content type of the MM’s content. |
| Content | Optional | The content of the multimedia message |

…

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.