## Slide 1: Vision & Priorities for next generation network access technology based on activities of HORIZON JU-SNS ORIGAMI research project
Source: Fibercop
With HORIZON-JU-SNS ORIGAMI project

## Slide 2: Current issues to be solved
In the current RAN architecture we identified two areas that can be redesigned towards 6G
Barrier: removing silo-style interaction among domains
  Providing Service Based supports to all domains (Access Network included)
Barrier: poor interoperability at the RAN
  Introduce a data driven architecture to access computing facilities
We propose two architectural modules applied to RAN and associated UCs that remove these barriers

## Slide 3: SBA and CCL for RAN
Requirements | Flexibility & Scalability
SBA | To tear down the silo-based design of different network domains, integrating one single bus to link them all
CCL | will democratize access to extremely heterogeneous computing resources and will boost resource sharing with reliability guarantees, encouraging green transition, sustainability and greater accessibility

## Slide 4: GSBA into the RAN
Bringing GSBA to the RAN enables a finer control
  More interoperable operation between c-plane components and u-plane functions
  At the RAN level, it requires to define the network functionalities to be defined as a service
Cloud Infrastructure
GSBA
UE-NAS
DU-U
RU
RU
DU-C
CU-C
CU-U
F1-u
NG-u
Fronthaul
UE
NRF
To Other Core NFs
To Management Functions
To UPF
Management
RT
Resource Broker
Non-RT
Which part of the RAN to be considered for SB migration will depend on performance requirements of each network function (e.g., the very stringent requirements for fronthaul traffic could make this approach unfeasible for the DU-RU interaction)

## Slide 5: Advantages for the GSBA-based RAN operation
Introducing SBA into the RAN brings several benefits to network operations and management.
  Improved Scalability: Service-based architectures (SBA) decouple network functions into modular services, allowing networks to scale dynamically based on demand. This flexibility is essential for handling traffic spikes or expanding capacity without significant hardware investments.
  Enhanced Flexibility and Modularity: The modular design of SBA enables independent development, deployment, and management of network functions. This approach supports agile updates and innovation without disrupting the entire network (e.g., SBA could simplify the possibility of introducing new AI/ML algorithms and related services for their lifecycle).
  Improved Automation and Orchestration: SBA supports advanced automation tools and orchestration frameworks. By using programmable interfaces and machine-readable APIs, networks can automate tasks like resource allocation, fault detection, and recovery.
  Better Resource Management: Fine-grained control over individual services enables better monitoring and allocation of resources.
  Resilience and Reliability: SBA supports fault-tolerant designs where failures in one service do not cascade across the network. This architecture improves the overall reliability and uptime of the network.
  Future-Proofing: With its modular and API-driven approach, SBA is well-suited to adapt to evolving standards, protocols, and technologies, ensuring long-term relevance and reduced need for overhauls

## Slide 6: SBA use case: Interoperable Machine Learning Models Improving RAN Energy Efficiency
This use case will leverage the GSBA for AI models and services lifecycle management enabling faster and more reliable Network Intelligence to manage 6G network operations effectively.
  It offers highly accurate and optimized ML models and network NI solutions for energy saving.
  It will strategically leverage the conflict resolution mechanisms, KPMs and data exposed by the GSBA to provide in real-time energy management policies.

## Slide 7: Compute Continuum Layer
The Compute Continuum Layer (CCL)
  CCL Broker: Abstractions of heterog. computing resources
  CCL ctrl: Compute-aware NF-control & management
Real-time CCL-x interfaces
  Sub-ms latency is expected
Compute awareness is required in NF control
  To avoid saturation of computing resources
  To provide compute latency guarantees
Library|Driver
LPU 1
request
request
response
response
PPU 1 (e.g., FPGA, GPU, ASIC or SIMD CPU)
PPU M (e.g., FPGA, GPU, ASIC or SIMD CPU)
…
Library|Driver
LPU M
request
request
response
response
…
Abstraction
Layer
Resource Broker
DU-U
request
response
…
DU-C
CCL-P
CCL-P
CCL-S
CCL-S
GSBA
CCL-P
CCL-S

## Slide 8: Proposal
To evaluate the feasibility for the migration of the RAN architecture toward the Service-Based approach (SBA) for 6G Release 20.
To evaluate the feasibility for introduction of a CCL layer in the RAN for 6G Release 20.

## Slide 9: References
ORIGAMI Project. Deliverable D2.1: Initial report on requirements and definition of KVIs and KPIs (Final). Zenodo. https://doi.org/10.5281/zenodo.12580929
L. Lo Schiavo et al. 2024. CloudRIC: Open Radio Access Network (O-RAN) Virtualization with Shared Heterogeneous Computing. In Proceedings of the 30th Annual International Conference on Mobile Computing and Networking (ACM MobiCom '24). Association for Computing Machinery, New York, NY, USA, 558–572. https://doi.org/10.1145/3636534.3649381
L. L. Schiavo et al. "YinYangRAN: Resource Multiplexing in GPU-Accelerated Virtualized RANs," IEEE INFOCOM 2024 - IEEE Conference on Computer Communications, Vancouver, BC, Canada, 2024, pp. 721-730, doi: 10.1109/INFOCOM52122.2024.10621380.
Gines Garcia-Aviles et al. 2021. Nuberu: reliable RAN virtualization in shared platforms. In Proceedings of the 27th Annual International Conference on Mobile Computing and Networking (MobiCom '21). Association for Computing Machinery, New York, NY, USA, 749–761. https://doi.org/10.1145/3447993.3483266
L. E. Chatzieleftheriou et al "Towards 6G: Architectural Innovations and Challenges in the ORIGAMI Framework," 2024 Joint European Conference on Networks and Communications & 6G Summit (EuCNC/6G Summit), Antwerp, Belgium, 2024, pp. 1139-1144, doi: 10.1109/EuCNC/6GSummit60053.2024.10597105.
R. C. Bello et al "Time-based coordination in Intent-driven management for Vehicular Service Orchestration," 2024 Joint European Conference on Networks and Communications & 6G Summit (EuCNC/6G Summit), Antwerp, Belgium, 2024, pp. 872-876, doi: 10.1109/EuCNC/6GSummit60053.2024.10597096.